| CHANGE REQUEST |
| --- |
| Group Name:* | WG2 |
| Source:* | Alcatel-Lucent, Telecom Italia |
| Format:* | ARC#11 |
| Date:* | 2014-05-30 |
| Contact:* | Omar Elloumi, Alcatel-Lucent, omar.elloumi@alcatel-lucent.com Enrico Scarrone |
| Reason for Change/s:* | CSE-ID and AE-ID identifiers formats |
| CR against: Release* | 1 |
| CR against: TS/TR* | TS-0001 v0.6.1 |
| Clauses/Sub Clauses* | 7.1 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

During ARC10-bis (adhoc meeting) several discussion took place around the uniqueness CSE-ID and AE-ID, ACP as well as AE-ID instantiation for multi user application.

Here are the three issue addressed:

- When the AE-ID and the CSE-ID are stored in the ACP, the format (Hierarchical /non-hierarchical URI) becomes relevant because the CSE is currently not able to convert the two formats. Considering that such ACP can refer to application that are using one or the other format, it can happen that ACP are not able to work correctly. It is therefore proposed to fix these formats in a way that the CSE can translate the two rappresentations one each other, and apply the ACP correctly.

- The need to have identifiers that are globally unique to assure global communication, can impact negatively constrained devices, making the identifiers relatively long. For such reason is proposed to shorten the URI to the local domain information when appropriate.

- Applications that allow multiple end-users to login via specific credential (e.g. a shared health monitoring machine) are supported via multiple AE registrations, one for each end-user.

## -----------------------Start of change 1-------------------------------------------

### 7.1.1	M2M Service Provider Identifier (M2M-SP-ID)

An M2M Service Provider shall be uniquely identified by the M2M Service Provider Identifier (M2M-SP-ID). This is a static value assigned to the Service Provider.

### 7.1.2	Application Entity Identifier (AE-ID)

An Application Entity Identifier (AE-ID) uniquely identifies an AE resident on an M2M Node, or an AE that requests to interact with an M2M Node. An AE-ID shall identify an Application Entity for the purpose of all interactions within the M2M System. The AE-ID shall include the Application ID (see clause 7.1.3).

### The AE-ID is globally unique but when used internally to a specific M2M SP domain, it is sufficient to keep it unique within such M2M Service Provider domain, and that it is extended to become globally unique when used outside the M2M SP boundaries. The IN-CSE shall perform this adding or removing identifierportions according to clause 7.1.x.7.1.3	Application Identifier (App-ID)

This is equivalent to the application name and is not guaranteed to be globally unique on its own.

This identifier may be supported via a single or multiple registration authorities/entities. The definition and assignment of such an identifier is out of scope of this document.

NOTE:  Detailed format and structure of the App-ID is not specified in the present document.  Who assigns the App-ID is not specified in the present document.

### 7.1.4	CSE Identifier (CSE-ID)

A CSE shall be identified by a globally unique identifier, the CSE-ID, when instantiated within an M2M node in the M2M System. The CSE-ID is globally unique but when used internally to a specific M2M SP domain, it is sufficient to keep it unique within such M2M Service Provider domain, and that it is extended to become globally unique when used outside the M2M SP boundaries. The IN-CSE shall perform this adding or removing identifierportions according to clause 7.1.x.

The CSE-ID shall identify the CSE for the purpose of all interactions from/to the CSE within the M2M System.

When a multi-user application is used (an application where different users can enter credential), there shall be a separate registration for each user, an AE-ID shall be assigned for each user following registration.

## -------------------------End of change 1-------------------------------------------

## -----------------------Start of change 2-------------------------------------------

### 7.1.x	M2M-SP-ID, CSE-ID and AE-ID use for identifiers

As a general rule, the identifiers of AEs, CSEs and resources are globally unique, but to optimize their use, expecially in relation to costrained devices, the identifiers shall be  shorten when the their scope can bederived form their context of use by the CSEs and the AEs.

7.1.x.1 Global uniqueness

The identifiers of CSE-IDs shall be made globally unique by the concatenation of M2M-SP-ID and CSE-ID.

The identifiers of AEs shall be made globally unique by the concatenation of the globally unique CSE-ID with the AE-ID.

The identifiers of resources shall be made globally unique by the concatenation of globally unique CSE-ID with the App-ID+Inst-ID.

#### 7.1.x.1 Shorten identifiers equivalence

CSE-ID, AE, Resources: the M2M-SP-ID shall be omitted when used to refer to AEs, CSEs and Resources in the domain they belong to. M2M-SP-ID shall be present when used to refer to AEs, CSEs and Resources in a different domain.

AE: the CSE-ID shall be omitted when used on Mca to refer to the AE that is serve by that particular Mca instantiation, shall be present when used to refer to any other CSEs or other Resources.

CSEs and AEs shall be able to derive the shorten identifiers from the complete identifiers and viceversa, by knowing that all the shorten identifiers refer to the M2M SP domain where the specific CSE or AR is operating.

#### 7.1.x.1 Structured and non structured URI: identifier equivalence concatenation rules

CSEs and AEs shall be able to derive the AE and the CSE identifiers in the case of use of structured URI from theuUnstructured ones and viceversa expecially when operating on ACP.

| AE-ID | EQUIVALENT REPRESENTATIONS |
| --- | --- |
|  | Unstructured URI | Structured URI |
|  | App-ID+Inst-ID | App-ID+Inst-ID |
|  | CSE-ID+App-ID+Inst-ID | CSE-ID/App-ID+Inst-ID |
|  | M2M-SP-ID+CSE-ID+App-ID+Inst-ID | M2M-SP-ID/CSE-ID/App-ID+Inst-ID |
| CSE-ID | EQUIVALENT REPRESENTATIONS |
|  | Unstructured URI | Structured URI |
|  | CSE-ID | CSE-ID |
|  | M2M-SP-ID+CSE-ID | M2M-SP-ID/CSE-ID |

Note: “+” in this table means a separator to be detailed in the protocols.  The identifier length isnot fixed.

7.1.x.1 Summary of identifier by interfaces

The AE and CSE shall follow thecases as described in thefollowing tables:

| Mca |
| --- |
| AE to CSE communications: from attribute | App-ID+Inst-ID (all cases) |
| CSE to AE communications: from attribute | CSE-ID (to refer to CSEs in the same domain) M2M-SP-ID+CSE-ID (to refer to CSEs in a different domain domain, unstructured URI case) M2M-SP-ID/CSE-ID (to refer to CSEs in a different domain domain, structured URI case) |
| AE to CSE communications: to attribute | CSE-ID/Resource (to refer to CSEs in the same domain) M2M-SP-ID+CSE-ID+Resource (to refer to CSEs in a different domain domain, unstructured URI case) M2M-SP-ID/CSE-ID/Resource (to refer to CSEs in a different domain domain, unstructured URI case) |
| CSE to AE communications: to attribute | App-ID+Inst-ID (all cases) |
| Note: “+” in this table means a separator to be detailed in the protocols. The identifier length isnot fixed. | Mcc | Mcc’ |
| from is AE | CSE-ID+App-ID+Inst-ID (unstructured URI case) CSE-ID/App-ID+Inst-ID (structured URI case) | M2M-SP-ID+CSE-ID+App-ID+Inst-ID (unstructured URI case) M2M-SP-ID/CSE-ID/App-ID+Inst-ID (structured URI case) The M2M-SP-ID component shall be added by the IN CSE of the originator side |
| from is CSE | CSE-ID (all cases) | M2M-SP-ID+CSE-ID (unstructured URI case) M2M-SP-ID/CSE-ID (structured URI case) The M2M-SP-ID component shall be added by the IN CSE of the originator side |
| to is AE | CSE-ID/App-ID+Inst-ID CSE-ID+App-ID+Inst-ID M2M-SP-ID/CSE-ID/App-ID+Inst-ID M2M-SP-ID+CSE-ID+App-ID+Inst-ID | M2M-SP-ID+CSE-ID+App-ID+Inst-ID (unstructured URI case) M2M-SP-ID/CSE-ID/App-ID+Inst-ID (structured URI case) The M2M-SP-ID component shall be removed by the IN CSE of the receiver side |
| to is a resource on a CSE | CSE-ID/Resource (to refer to CSEs in the same domain) M2M-SP-ID+CSE-ID+Resource (to refer to CSEs in a different domain domain, unstructured URI case) M2M-SP-ID/CSE-ID/Resource (to refer to CSEs in a different domain domain, structured URI case) | M2M-SP-ID+CSE-ID/Resource (unstructured URI case) M2M-SP-ID/CSE-ID/Resource (structured URI case) The M2M-SP-ID component shall be removed by the IN CSE of the receiver side |

Note: “+” in this table means a separator to be detailed in the protocols.  The identifier length isnot fixed.

## -----------------------End of change 2-------------------------------------------

## -----------------------Start of change 3-------------------------------------------

#### 9.6.2.1	originatorPrivileges

The following originator privilege types shall be considered for access control policy check.

Table 9.6.2.1-1: originatorPrivileges types

| Name | Description |
| --- | --- |
| Domain | FQDN domain |
| originator identifier | CSE-ID or AE-ID which represent a originator identity. M2M-SP-ID shall be included when bthe AE or the CSE are belonging to a different domain respect to the one of the ACP resource |
| Token | Access token usually provided as query parameter |
| All | All originators |
| Role | A role name associated with the URL the a Service Subscription resource where such role is defined |

## -----------------------End of change 3-------------------------------------------