| CHANGE REQUEST |
| --- |
| Group Name:* | WG2 Architecture |
| Source:* | Ericsson |
| Format:* | ARC11 |
| Date:* | 2014-05-30 |
| Contact:* | George Foti |
| Reason for Change/s:* | There is a need to provide guidelines for creating application instances and handling as well application specific information for multi-user applications. |
| CR against: Release* | Release-1 |
| CR against: TS/TR* | TS-0001 v0.7.0 |
| Clauses/Sub Clauses* | 7.1.2 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

1	Introduction

This contribution proposes adding some guidelines for how the system creates application instance ID as well as support for multi-user applications

* * * Start of 1st Change * * *

### 7.1.2	Application Entity Identifier (AE-ID)

An Application Entity Identifier (AE-ID) uniquely identifies an AE resident on an M2M Node, or an AE that requests to interact with an M2M Node. An AE-ID shall identify an Application Entity for the purpose of all interactions within the M2M System.

It is the responsibility of the M2M Service Provider to ensure that the AE-ID is globally unique. The AE-ID shall include the Application ID (see clause 7.1.3).

To that effect there are 2 cases:

Case 1: The AE itself provides its own AE-ID and shall include it at registration, for example it can be pre-provisioned in the AE

Case 2: The AE does not provide an AE-ID In this case the local CSE shall create the AE-ID upon successful AE registration and return it to the AE.

For case 1, how global uniqueness of such identifier is achieved is left to implementation of the AE. An example on how to achieve uniqueness is by appending the CSE-ID of the Local CSE to the non-global AE-ID. (see below how the local CSE can ensure global uniqueness of an AE provisioned AE-ID)

For case2, the local CSE should assume that the App-Inst-ID is made up of two parts, the first part shall include the Application ID (see clause 7.1.3). If the registered AE included an application token in its registration request, then the local CSE shall append that token before the Application ID. The second part is implementation adependent.

For either of the above cases, it is the responsibility of the local CSE to ensure global uniqueness of the AE-ID used withn the M2M system. This could be achieved by including the local CSE-ID. However in case 1, the local CSE shall maintain a mapping between the AE provisioned AE-ID, and the local CSE corresponding AE-ID used within the MM system for the duration of the registration..

* * * End of 1st Change * * *

* * * Start of 2ndChange * * *

# Table 9.6.5-2: Attributes of <AE> resource

| Attribute Name of <AE> | Multiplicity | RW/ RO/ WO | Description | <AEAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1 where this common attribute is described. | NA |
| parentID | 1 | RO | See clause 9.6.1 where this common attribute is described. | NA |
| expirationTime | 1 | RW | See clause 9.6.1 where this common attribute is described. | MA |
| accessControlPolicyIDs | 1 | RW | See clause 9.6.1 where this common attribute is described. | MA |
| creationTime | 1 | RW | See clause 9.6.1 where this common attribute is described. | NA |
| lastModifiedTime | 1 | RO | See clause 9.6.1 where this common attribute is described. | NA |
| labels | 0..1 | RO | See clause 9.6.1 where this common attribute is described. | MA |
| announceTo | 1 | RW | See clause 9.6.1 where this common attribute is described. | NA |
| announcedAttribute | 1 | RW | See clause 9.6.1 where this common attribute is described. | NA |
| name | 1 | RO | The (usually human readable) name of the application, as declared by the application developer (e.g., "HeatingMonitoring") | OA |
| App-ID | 1 | RO | Application Identifier | OA |
| AE-ID | 1 | RO | The identifier of the Application Entity (see clause 7.1.2). | OA |
| pointOfAccess | 0..n | RW | The list of addresses for communicating with the registered Application Entity over Mca reference point via the transport services provided by Underlying Network (e.g., IP address, FQDN, URI). This attribute shall be accessible only by the AE and the hosting CSE. | OA |
| ontologyRef | 0..1 | RW | A reference (URI) of the ontology used to represent the information that is managed and understood by the AE; to be passed to the AE. | OA |
| nodeLink | 0..1 | RO | A reference (URI) of a <node> resource that stores the node specific information. | OA |
| ApplicatioToken | 0..1 | RW | An application token that is to be included in the AE-ID returned by the CSE to the application for subsequent use |  |

* * * End of 2nd Change * * *

* * * Start of 3rd Change * * *

Figure 9.6.5-1: Structure of <AE> resource

Editor's Note: To update the picture to include "application tioken”

* * * End of 3rd Change * * *