| CHANGE REQUEST |
| --- |
| Group Name:* | WG2 |
| Source:* | TELECOM Italia |
| Format:* | ARC#11 |
| Date:* | 2014-06-01 |
| Contact:* | Enrico Scarrone |
| Reason for Change/s:* | Correction to changes in 1384r1 |
| CR against: Release* | 1 |
| CR against: TS/TR* | TS-0001 v0.6.1 |
| Clauses/Sub Clauses* | 9.6.2 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

## -----------------------Start of change 1-------------------------------------------

### 9.6.2	Resource Type accessControlPolicy

The <accessControlPolicy> resource is comprised of  privileges and selfPrivileges attributes which represents a set of access control rules  defining which entities (defined as accessControlOriginators) have the privilege to perform  certain operations (defined as accessContolOperations) within specified contexts (defined as accessControlContexts) and are used by the CSEs in making access decision to specific resources.

Each access control rule defines what is allowed,. So for sets of Access control rules an operation is permitted if it is permitted by some/any of the access control rules in the set. As a consequence, a combination of access control rules will never be conflicting.

For a resource that is not of <accessControlPolicy> resource type, the common attribute accessControlPolicyIDs (defined in table 9.6.1-1) contains a list of identifiers which link that resource to <accessControlPolicy> resources. The CSE access decision for such a resource shall follow the evaluation of the set of access control rules expressed by the privileges attributes defined in the identified <accessControlPolicy> resources.

The selfPrivileges attribute represents the set of access control rules for the resource <accessControlPolicy> itself.

The CSE access decision for <accessControlPolicy>  resource shall follow the evaluation of the set of access control rules expressed by the selfprivileges attributes defined in the identified <accessControlPolicy> resource itself.

The Access Control Policies shall be used by the CSE to control access to the resources as specified in this TS and in TS-0003 [TS0003].

The ACP is designed to fit different access control models, such as access control lists, role or attribute based access control.

The ACP associate accessControlOriginators with the privilege to perform certain operation within a given context, that maps in the definition of a role. Multiple ACP can associated to the same resource, allowing to operate on such resource according to different roles.

Figure 9.6.2-1: Structure of <accessControlPolicy> resource

The <accessControlPolicy> resource shall contain the child resource in table 9.6.2-1.

# Table 9.6.2-1: Child resources of <accessControlPolicy> resource

| Child Resource Name of <accessControlPolicy> | Child Resource Type | Multiplicity | Description | <accessControlPolicyAnnc> Child Resource Type |
| --- | --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 | <subscriptionAnnc> |

This resource shall contain the attributes in Table 9.6.2-2.

# Table 9.6.2-2: Attributes of <accessControlPolicy> resource

| Attribute Name of <accessControlPolicy> | Multiplicity | RW/ RO/ WO | Description | <accessControlPolicyAnnc> Attribute |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1 where this common attribute is described. | MA |
| parented | 1 | RO | See clause 9.6.1 where this common attribute is described. | NA |
| expirationTime | 1 | RW | See clause 9.6.1 where this common attribute is described. | MA |
| Labels | 0..1 | RW | See clause 9.6.1 where this common attribute is described. | MA |
| creationTime | 1 | RO | See clause 9.6.1 where this common attribute is described. | NA |
| lastModifiedTime | 1 | RO | See clause 9.6.1 where this common attribute is described. | NA |
| announceTo | 1 | RW | See section 9.6.1 where this common attribute is described. | NA |
| announcedAttribute | 1 | RW | See section 9.6.1 where this common attribute is described. | NA |
| privileges | 1 | RW | Represent a set of access control rules that applies to resources referencing this <accessControlPolicy> resource using the accessControlPolicyID attribute. | MA |
| selfPrivileges | 1 | RW | Represent the Set of access control rules that apply to the <accessControlPolicy> resource itself. | MA |

The set of access control rules represented in privileges and selfPrivileges attributes are comprised of 3-tuples  (accessControlOriginators, accessControlContexts, accessControlOperations) with parameters shown in Table 9.6.2-3 which are further described in the following clauses.

If privileges  contains no 3-tuples than this represent an empty set of the access control rules

The selPrivileges  shall contain at least one 3-tuples.

The CSE access granting mechanism shall follow the procedure described in TS-0003 [TS0003] in clause 7.1 (Authorization and access control).

Table 9.6.2-3: Parameters in access-control-rule-tuples

| Name | Description |
| --- | --- |
| accessControlOriginators | See 9.6.2.1 |
| accessControlContexts | See 9.6.2.2 |
| accessControlOperations | See 9.6.2.3 |

#### 9.6.2.1	accessControlOriginators

The accessControlOriginators is a mandatory parameter in an access-control-rule-tuple represents the set of Originators shall be allowed using this access control rule. The set of Originators is described by a list of parameters, where the types of the parameter can vary within the list. Table 9.6.2.1-1 describes the supported types of parameters in accessControlOriginators. The following originator privilege types shall be considered for access control policy check.

Table 9.6.2.1-1: Types of Parameters in accessControlOriginators

| Name | Description |
| --- | --- |
| Domain | A SP domain or SP subdomain |
| originatorIdentifier | CSE-Id or AE-ID which represent a originator identity |
| all | Any originators are allowed to access the resource within the accessControlOriginators constraints |

#### 9.6.2.2	accessControlContexts

The accessControlContexts is an optional parameter  in an access-control-rule-tuple that contains a list, where each element of the list, when present, represents a context that is is permitted using this access control rule. Each request contexts is described by a set of parameters, where the types of the parameter can vary within the set. Table 9.6.2.2-1 describes the supported types of parameters in accessControlContexts.

The following originator accessControlContexts shall be considered for access control policy check by the CSE..

Table 9.6.2.2-1: Types of Parameters in accessControlContexts

| Name | Description |
| --- | --- |
| accessControlTimeWindow | Represents a time window constraint which is compared against the time that Authorization Decision is made. |
| accessControlLocationRegion | Represents a location region constraint which is compared against the location of the Originator of the request |
| accessControlIpAddress | Represents an IP address constraint or IP address block constraint which is compared against the IP address of the Originator of the request |

#### 9.6.2.3	accessControlOperations

The accessControlOperations is a mandatory parameter in an access-control-rule-tuple that represents the set of operations that are authorized using this access control rule. Table 9.6.2.3-1 describes the supported set of operations that are authorized by accessControlOperations.

The following accessControlOperations shall be considered for access control policy check by the CSE..

Table 9.6.2.3-1: Types of parameters in accessControlOperations

| Name | Description |
| --- | --- |
| RETRIEVE | Privilege to retrieve the content of an addressed resource |
| CREATE | Privilege to create a child resource |
| UPDATE | Privilege to update the content of an addressed resource |
| DELETE | Privilege to delete an addressed resource |
| DISCOVER | Privilege to discover the resource |
| NOTIFY | Privilege to receive a notification |

## -----------------------End of change 1-------------------------------------------

# Comments

This is repeated below. Delete this.

I think this sentence is not necessary as we said above that access control rule is defined within a specified context, with attributes listed in accessControlcontext.

This appears to repeat the text for two paragraphs prior to this paragraph.

RESOLUTION: link, announceTo and announcedAttribute are common attributes. They should not be shown in this figure. No action required

Changed To maintain consistency with privileges description

RESOLUTION: Why are mechanisms for announcing noted here. I gather announcement is dealt with in Clause 10.2.18. No action required

This doesn't sound like normative text. Delete

We should not impose that this is a "Flag" since that is a stage 3 issue. Enough to say we describe the operations see clause 9.6.2.3.

RESOLUTION: This is a stage 3 detail. No action required