| CHANGE REQUEST |
| --- |
| Group Name:* | ARC |
| Source:* | InterDigital Communications |
| Format:* | ARC #12 |
| Date:* | <2014-07-28> |
| Contact:* | Catalina Mladin, InterDigital, Catalina.Mladin@InterDigital.com |
| Reason for Change/s:* | Updates for <mgmtCmd> resource: R01 addresses changes requested by the MAS group: resolve editor’s note 10.3.9.3 only by removing quote marks, move of the proposed text 1 for section 10.1.3 to a different CR (ARC-2014-1507), alignment to ARC-2014-1427R01 table format of operations. R02 corrects editorials such as capitalizing Mca, Mcc , aligns text in tables 10.2.9.6-1 and 10.2.9.7-1, clarifies the originators in tables 10.2.9.5-1 and 10.2.9.5-2. R03 corrects the term “remote entity” to “managed entity” throughout. Also the comments about future ARC decision impacts have been removed |
| CR against: Release* | 1 |
| CR against: TS/TR* | oneM2M-TS-0001 , V-0.8.0 |
| Clauses/Sub Clauses* | 9.6.16 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Issues addressed in this CR:

- Editor’s Note  [10.3.9.3] : MAS group proposes to address this note by deleting the quotation marks around <mgmtcmd> in section 10.3.9 . This is absosbed by issue C below in R01 and R02 versions of the document.

- Editor’s Note [10.2.9.6.b]  has been addressed in table 10.2.9.6-1

- To update section 10.2.9  with the latest table format (ARC-2014-1427R01)

### -----------------------Start of proposed text 1 -------------------------------------------

### 10.2.9	External Management Operations through <mgmtCmd>

#### 10.2.9.1	Introduction

This clause describes how RESTful management operations may be performed using <mgmtCmd> resources over the Mca and Mcc reference points.  The <mgmtCmd> resource, together with its attributes or sub-resources, may be used in the process of translating between RESTful operations and management commands and procedures from existing management technologies (e.g. BBF TR-069 [i.4]). These procedures can then be performed on the managedentity, using the Management Adapter and the procedures described in the following clauses.

#### 10.2.9.2	Create <mgmtCmd>

A CREATE request is used by an Originator to create a specific <mgmtCmd> resource in a hosting CSE.

The created <mgmtCmd> resource will be mapping a RESTful method to management commands and/or procedures which may be translated from existing management protocols (e.g. BBF TR-069 [i.4]). At run-time the hosting CSE can expose the translated commands, over the Mcc reference point, to the managedentities (i.e. ASN/MN-CSE).

The Originator may be:

An AE registered to the IN-CSE.

The CSE on the managed entity: In this case, the CSE transforms supported management command into the <mgmtCmd> resource representation, then requests the hosting CSE to create the corresponding <mgmtCmd> resource.

NOTE 1:	The hosting IN-CSE in the network domain may also create the <mgmtCmd> resource locally by itself. The details are out of scope. Then an AE can discover the created <mgmtCmd> and manipulate it.

NOTE 2:	The <mgmtCmd> resource could also be created in the hosting CSE by other offline provisioning means that are out of scope.

The Receiver  shall be an IN-CSE.

# Table 10.2.9.2-1: <mgmtCmd> CREATE

| <mgmtCmd> CREATE |
| --- |
| Associated reference point | Mcc, Mca |
| Information on Request message | All attributes of the <mgmtCmd> resource. The mandatory and/or optional attributes defined in clause 9.6.16, as needed |
| Pre-Processing at Originator | According to clause 10.1.1 with the following: The CSE on the originating node shall first collect local management command. |
| Processing at the Receiver | According to clause 10.1.1 with the following: The Receiver CSE shall maintain the mapping between the created <mgmtCmd> resource and the corresponding nonRESTful commands represented by the "cmdType" attribute of <mgmtCmd> resource |
| Information on Response message | According to clause 10.1.1 with the following specific information: cn: URI of created <mgmtCmd> resource |
| Post-processing at Originator | According to clause 10.1.1 |
| Exceptions | According to clause 10.1.1 |

#### 10.2.9.3	Retrieve <mgmtCmd>

This procedure shall be used for retrieving all or part information from a previously created <mgmtCmd> resource on a target CSE.

The Originator may be:

An AE.

A CSE.

The Receiver  shall be an IN-CSE.

# Table 10.2.9.3-1: <mgmtCmd> RETRIEVE

| <mgmtCmd> RETRIEVE |
| --- |
| Associated reference point | Mcc, Mca |
| Information on Request message | According to clause 10.1.2, with the mandatory and/or optional attributes defined in clause 9.6.16, as needed. |
| Pre-processing at the Originator | According to clause 10.1.2 |
| Pre-Processing at the Receiver | According to clause 10.1.2 |
| Information on Response message | According to clause 10.1.2 |
| Post-Conditions | According to clause 10.1.2 |
| Exceptions | According to clause 10.1.2 |

#### 10.2.9.4	Update <mgmtCmd>

This procedure shall be used for updating all or part information of an existing <mgmtCmd> resource with new attributes.

The Originator may be:

An AE.

A CSE.

The Receiver  shall be an IN-CSE.

# Table 10.2.9.4-1: <mgmtCmd> UPDATE

| <mgmtCmd> UPDATE |
| --- |
| Associated reference point | Mcc, Mca |
| Information on Request message | According to clause 10.1.3, including mandatory and/or optional attributes defined in clause 9.6.16, as needed. |
| Pre-Conditions | According to clause 10.1.3 |
| Pre-processing at the Originator | According to clause 10.1.3 |
| Post-processing at the Receiver | According to clause 10.1.3 |
| Post-Conditions | According to clause 10.1.3 |
| Exceptions | According to clause 10.1.3 |

#### 10.2.9.5	Delete <mgmtCmd>

This procedure shall be used for deletion an existing <mgmtCmd> resource on a hosting CSE. An AE may also use this procedure to cancel any initiated <execInstance> of an <mgmtCmd> if applicable.

The Originator may be:

The CSE on the manageable entity: In this case, the CSE issues the request to the hosting CSE to hide the corresponding management command from being exposed by the <mgmtCmd> resource.

An AE: In this case, the AE requests the hosting CSE to delete the <mgmtCmd> resource from the hosting CSE and cancel all initiated <execInstance> of an <mgmtCmd> if applicable.

NOTE 1:	The hosting CSE in the network domain could also delete an <mgmtCmd> resource locally by itself. This internal procedure is out of scope.

NOTE 2:	The <mgmtCmd> resource could also be deleted in the hosting CSE by other offline provisioning means, which are out of scope.

If the Originator is an AE and there is any initiated <execInstance> under the <mgmtCmd> that can be cancelled by a corresponding management command. The hosting CSE shall also issue the management command to the managed entity to cancel those initiated <execInstance> based on existing management protocol (i.e. BBF TR-069 [i.4]). Then the CSE shall respond to the originator with the appropriate generic responses.

The Receiver  shall be an IN-CSE.

# Table 10.2.9.5-1: <mgmtCmd> DELETE by ASN-CSE or MN-CSE

| <mgmtCmd> DELETE by ASN-CSE or MN-CSE |
| --- |
| Associated reference point | Mcc |
| Information on Request message | According to clause 10.1.4 |
| Pre-Processing at the Originator Conditions | According to clause 10.1.4 with the following: Before issuing a DELETE request to the IN-CSE, the originating CSE may perform cancelling of the corresponding management command locally. |
| Post-Processing at the Receiver | According to clause 10.1.4 with the following: The Receiver IN-CSE shall verify if there are any initiated <execInstance> commands under the <mgmtCmd> which are cancellable by using a corresponding management command. If there are, the Receiver IN-CSE shall issue the management command to the managed entity to cancel those initiated <execInstance> based on existing management protocol (i.e. BBF TR-069 [i.4]). The <mgmtCmd> resource shall be deleted from the repository of the Receiver IN-CSE Then the Receiver IN-CSE shall respond to the Originator ASN-CSE or MN-CSE with the appropriate responses. |
| Information on Response message | According to clause 10.1.4 |
| Post-Conditions | According to clause 10.1.4 |
| Exceptions | According to clause 10.1.4 with the following: If the deletion is not allowed or the specific <mgmtCmd> resource does not exist, there is no local processing in the Receiver IN-CSE and a proper error code shall be returned to the Originator ASN-CSE or MN-CSE If the corresponding initiated commands cannot be deleted from the managed entity due to some reason (e.g. not found) a response with the proper indication shall be returned to the Originator ASN-CSE or MN-CSE |

# Table 10.2.9.5-2: <mgmtCmd> DELETE by an AE

| <mgmtCmd> DELETE by an AE |
| --- |
| Associated Reference Points | Mca |
| Information on Request message | According to clause 10.1.4 |
| Pre-Processing at the Originator | According to clause 10.1.4 |
| Post-Processing at the Receiver | According to clause 10.1.4 with the following: If there is any initiated <execInstance> under <mgmtCmd> and it is cancellable, the Receiver IN-CSE shall cancel those initiated <execInstance> from the managed entity using corresponding management procedures in existing management protocol (i.e. CancelTransfer RPC in BBF TR-069 [i.4]) The <mgmtCmd> resource shall be deleted from the repository of the Receiver IN-CSE |
| Information on Response message | According to clause 10.1.4 |
| Post-Conditions | According to clause 10.1.4 |
| Exceptions | According to clause 10.1.4 with the following: If the deletion is not allowed or the specific <mgmtCmd> resource does not exist, there is no local processing in the Receiver IN-CSE and a proper error code shall be returned to the Originator AE If the corresponding initiated commands cannot be deleted from managed entity due to some reason (e.g. not found) a response with the proper indication shall be returned to the Originator AE |

#### 10.2.9.6	Execute <mgmtCmd>

The Execute procedure is used by an Originator for execution of a specific management command on a managedentity, through an existing <mgmtCmd> resource on the hosting CSE.The Originator shall request to execute a specific management command which is represented by an existing <mgmtCmd> resource by using an UPDATE operation.

The Originator shall be an AE.

The Receiver shall be an IN-CSE.

[10.2.9.6.a]  Editor's note: The definition of Execute is to be for FFS in clause 10.1.

# Table 10.2.9.6-1: <mgmtCmd> EXECUTE

| <mgmtCmd> EXECUTE |
| --- |
| Associated reference Points | Mca |
| Information on Request message | According to clause 10.1.3, with the following ( see attributes defined in clause 9.6.16): The UPDATE request shall address the execEnable attribute with a predefined value to trigger the EXECUTE action.. |
| Pre-Processing at the Originator | Originator needs to execute a management command on a managed entity using a <mgmtCmd> resource at the Receiver by using an UPDATE operation. After issuing the execution request, the Originator may request to retrieve the execution result or status from <execInstance> sub-resources of the <mgmtCmd>by using a RETRIEVE method as described in clause 10.2.9.3. See also clause 10.1.3 |
| Post-Processing at the Receiver | According to clause 10.1.3 with the following The Receiver shall check if the Originator has the WRITE permission on the addressed <mgmtCmd> resource. Upon successful validation, the hosting CSE shall perform command conversion and mapping, and send the converted management command to execute with the provided arguments on the remote entity based on existing device management protocol (i.e. BBF TR 069 [i.4]). Then the hosting CSE shall create for each target a corresponding <execInstance> resource under <mgmtCmd> and shall respond to the originator with the appropriate generic responses. It shall also provide in the response the URL of the created <execInstance> resource. If the execTarget attribute of the addressed <mgmtCmd> addresses a group, the hosting CSE shall create corresponding <execInstance> resources for each target in the group and provide the corresponding URLs in the response. Upon receiving from any remote entity a management notification (i.e. BBF TR-069 [i.4] "Inform" message) regarding the execution result or status, the hosting CSE may update the corresponding <execInstance> sub-resource locally. |
| Post-Processing at the Receiver | According to clause 10.1.3, with additional processing which is dependent on the type of the command and execution status. The following actions may occur in any order after the command execution is finished: The managed entity may send responses including execution results to the Receiver CSE, who will store the execution results in corresponding <execInstance> resource. The Originator AE may use normal RETRIEVE procedure to retrieve the execution results or status of an <execInstance>. After receiving a RETRIEVE request from the Originator AE, the Receiver CSE can retrieve the execution status or results on the managed entity using existing management protocol A response shall be returned to the Originator AE. |
| Exceptions | If the execution is not allowed or the specified <mgmtCmd> resource does not exist, no further processing is required on the Receiver CSE, and a proper error code shall be returned to the Originator AE in the message response. If the corresponding management command cannot be executed on the managed entity, an error code shall be returned with the response to Originator AE. |

#### 10.2.9.7	Cancel <execInstance>

The Cancel procedure is used by an originating AE to disable/stop/cancel an initiated management command execution on the remote entity, through an existing <execInstance> resource on the hosting CSE.

The Originator shall be an AE.

The Receiver shall be an IN-CSE.

# Table 10.2.9.7-1: <execInstance> CANCEL

| <execInstance> CANCEL |
| --- |
| Associated reference Points | Mca |
| Information on Request message | According to clause 10.1.3, with the following ( see attributes defined in clause 9.6.17): The UPDATE request shall address the execDisable attribute with a predefined value in order to trigger the CANCEL action, |
| Pre-Processing at the Originator | Originator needs to disable/stop/cancel an initiated management command execution on the managed entity using an <execInstance> sub-resource at the Receiver, by using an UPDATE operation. See also clause 10.1.3 |
| Post-Processing at the Receiver | The Receiver shall check if the Originator has the WRITE permission on the addressed <execInstance> resource. Then, the Receiver shall check if the management operation is initiated and cancellable. Upon successful validation, the Receiver IN-CSE shall perform command conversion and mapping, then use existing management protocol (i.e. BBF TR-069 [i.4]) to cancel the corresponding management command execution initiated on the managed entity The Receiver IN-CSE shall respond to the originator with the appropriate responses. |
| Information on Response message | According to clause 10.1.3 |
| Post-Conditions | According to clause 10.1.3 |
| Exceptions | If the <execInstance> has not been initiated, is already complete or it is not cancellable ,or the specified <execInstance> resource does not exist in the Receiver IN-CSE, the post processing on Receiver CSE shall be skipped and a proper error code shall be returned to Originator in the Response message |

#### 10.2.9.8	Retrieve <execInstance>

This procedure shall be used for retrieving all or part information from an <execInstance> sub-resource on a target CSE.

The Originator shall be an AE.

The Receiver shall be an IN-CSE.

# Table 10.2.9.8-1: <execInstance> RETRIEVE

| <execInstance> RETRIEVE |
| --- |
| Associated Reference Points | Mca |
| Information on Request message | According to clause 10.1.2, with the mandatory and/or optional attributes defined in clause 9.6.17, as needed. |
| Pre-Processing at the Originator | Originator needs to create a resource. |
| Post-Processing at the Receiver | According to clause 10.1.2, with the following: If the retrieval is allowed, the Receiver IN-CSE can retrieve the execution status or results on the managed entity using existing management protocol (i.e. BBF TR-069 [i.4]) If the retrieval is allowed, the addressed attributes of the <execInstance> resource shall be retrieved from the repository of the Receiver IN-CSE |
| Information on Response message | According to clause 10.1.2 |
| Post-Conditions | According to clause 10.1.2 |
| Exceptions | If the retrieval is not allowed or the specific <execInstance> resource does not exist in the Receiver IN-CSE, there is no local processing on the Receiver CSE and a proper error code shall be returned to Originator AE in the Response Message |

#### 10.2.9.9	Delete <execInstance>

The DELETE request is used by an originating AE to delete an existing <execInstance> resource on a Receiver IN-CSE.

The originator shall be an AE.

NOTE 1:	The Receiver IN- CSE in the network domain could also delete an <execInstance> resource locally by itself. This internal procedure is out of scope.

NOTE 2:	The <execInstance> resource could also be deleted in the Receiver IN-CSE by other offline provisioning means that are out of scope.

Receiver: The Receiver shall check if the Originator has the DELETE permission on the addressed <execInstance> resource. Upon successful validation, the hosting CSE shall remove the resource from its repository. If  a corresponding managemnt command has been initiated and is pending finished on the managedentity, and the management command is cancellable, the hosting CSE shall use existing management protocols (i.e. BBF TR-069 [i.4] CancelTransfer RPC) to cancel the corresponding management currently initiated at the managedentity. Then the CSE shall respond to the originator with the appropriate generic responses.

The hosting CSE shall be an IN-CSE.

# Table 10.2.9.9-1: <execInstance> DELETE

| execInstance> DELETE |
| --- |
| Associated Reference Point | Mca |
| Information on Request message | According to clause 10.1.4. |
| Pre-Processing at the Originator | According to clause 10.1.4 . |
| Post-Processing at the Receiver | According to clause 10.1.4 with the following: If the <execInstance> has not been initiated, is already complete or it is not cancellable, the <execInstance> resource shall be deleted from the repository of the IN-CSE. If the <execInstance> is pending and it is cancellable, the Receiver IN-CSE shall first cancel the <execInstance> from the managedentity using corresponding management procedures in existing management protocol (i.e. CancelTransfer RPC in BBF TR-069 [i.4]). Afterwards, the <execInstance> resource shall be deleted from the repository of the Receiver IN-CSE. If the corresponding initiated commands cannot be successfully cancelled on the managed entity for some reason, the <execInstance> resource shall be still deleted. Then the Receiver IN-CSE shall respond to the Originator with the appropriate generic responses. |
| Information on Response message | According to clause 10.1.5 |
| Post-Conditions | According to clause 10.1.5 |
| Exceptions | If the deletion is not allowed or the specific <execInstance> resource does not exist on the Receiver IN-CSE, there is no processing at the Receiver and a proper error code shall be returned to the Originator. |

### ----------------------- End of proposed text 1 -------------------------------------------