| CHANGE REQUEST |
| --- |
| Group Name:* | WG2 ARC |
| Source:* | Interdigital |
| Format:* | ARC |
| Date:* | <2014-07-15> |
| Contact:* | Guang Lu, InterDigital, Guang.Lu@InterDigital.com |
| Reason for Change/s:* | The interface between M2M IN node to Charging server is diameter based. To align the ACA (Accounting answer) message as specified in oneM2M-TS-0001 - V-0.8.0 to RFC 6733 (Diameter base protocol), the ACA message structure needs to be revised. |
| CR against: Release* | 0.8 (oneM2M Functional Architecture Baseline Draft) |
| CR against: TS/TR* | oneM2M-TS-0001 - V-0.8.0 |
| Clauses/Sub Clauses* | Table 12.2.5.3.2-1 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Table 12.2.5.3.2-1  in oneM2M-TS-0001 - V-0.8.0 illustrates the basic structure of an ACA message generated by the charging server. The interface between M2M IN node and charging server is based on diameter protocol. However, the ACA message contents as described in oneM2M-TS-0001 - V-0.8.0 is not aligned to RFC 6733 (Diameter Base Protocol).

- Diameter Base Protocol - RFC 6733, section 6.6 mentions that “The Destination-Realm AVP MUST NOT be present in Answer messages.” On the other hand, oneM2M-TS-0001 - V-0.8.0, Table 12.2.5.3.2-1  mentions the Destination-Realm AVP as Mandatory. Hence there is a change required in oneM2M-TS-0001 - V-0.8.0, Table 12.2.5.3.2-1  for Destination-Realm AVP (removal).

- Diameter Base Protocol - RFC 6733, section 7.1 mentions that “All Diameter answer messages defined in IETF applications MUST include one Result-Code AVP”.On the other hand, oneM2M-TS-0001 - V-0.8.0, Table 12.2.5.3.2-1  does not mention the Result-code AVP in ACA messages. Hence there is a change required in oneM2M-TS-0001 - V-0.8.0, Table 12.2.5.3.2-1  for Result-code AVP (addition).

### -----------------------Start of change 1-------------------------------------------

##### 12.2.5.3.2	Accounting-Answer Message

The following table illustrates the basic structure of an ACA message generated by the charging server as a response to an ACR message.

Table 12.2.5.3.2-1: Accounting-Answer (ACA) message contents

| Information element | Category | Description |
| --- | --- | --- |
| Session-Id | M | Same as table 12.2.5.3.1-1 |
| Origin-Host | M | Same as table 12.2.5.3.1-1 |
| Origin-Realm | M | Same as table 12.2.5.3.1-1 |
| Accounting-Record-Type | M | Same as table 12.2.5.3.1-1 |
| Accounting-Record-Number | M | Same as table 12.2.5.3.1-1 |
| Acct-Application-Id | OC | Same as table 12.2.5.3.1-1 |
| Error-Reporting-Host | OC | Included only if the host that inserted the error is different from the Origin-Host |
| Event-Timestamp | O | Same as table 12.2.5.3.1-1 |
| Proxy-Info | OC | Same as table 12.2.5.3.1-1 |
| Proprietary Information | O | Same as table 12.3.5.3.1-1 |
| Result-Code | M | Indicates whether a particular request was completed successfully or whether an error occurred |
| OC This is a parameter that, if provisioned by the operator to be present, shall be included in the CDRs when the required conditions are met. In other words, an OC parameter that is configured to be present is a conditional parameter. |

### -----------------------End of change 1---------------------------------------------