| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG2 |
| Title:* | TS-0007 Mca Registration Services |
| Source:* | George Foti, Ericsson, George.Foti@ericsson.com |
| Contact: | George Foti, Ericsson, George.Foti@ericsson.com |
| Date:* | 2014-09-15 |
| Abstract:* |  |
| Agenda Item:* |  |
| Work item(s): | TS-0007 WI |
| Document(s) Impacted* | TS-0007 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Update TS for inclusion |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M. Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

Contents

6	M2M Services	3

6.1	Introduction	3

6.X	Registration Services	4

6.X.1	Overview	4

6.X.2	Service Capabilities	4

6.X.2.1	registerAE	4

6.X.2.2	refreshAERegistration	6

6.X.2.3	deregisterAE	8

6.Y	Registration Administration Services	10

6.Y.1	Overview	10

6.Y.2	Service Capabilities	10

6.Y.2.1	getRegistrationStatus	11

6.Y.2.2	revokeAERegistration	13

6.Y.2.3.	subscribeInitialAERegistrationEvent	15

6.Y.2.4	unsubscribeInitialAERegistrationEvent	17

6.X.2.5	getInitialSubscriptionAERegistrationEvents	19

7.3	Infrastructure Component (INF)	20

7.3.1	INF to Service Cross Reference	20

7.7	Service Exposure (SE)	20

7.7.1	Service Exposure to Service Cross Reference	20

s

-----------------------Start of change 1---------------------------

# 6	M2M Services

This clause describes the M2M Services provided by the M2M Services Platform.

## 6.1	Introduction

The M2M Services defined in this clause are utilized by the Business Services described in the Annexes of this specification.

Figure 6.1-1: oneM2M Services

## 6.X	Registration Services

### 6.X.1	Overview

The Registration service provides the ability for:

- Initial Registration of an AE

- Refresh an existing Registration of an AE

- AE initiated termination of an existing Registration

### 6.X.2	Service Capabilities

Editors Note: The fetching of the service profile is FFS in all operations involving such a step

Editors Note: The validation that the AE-ID is associated with the service profile is FFS in all operations involving such a step

#### 6.X.2.1	registerAE

This service capability enables an AE or a third party provisioned with the proper authorization to register with the M2M System. This service capability shall be restricted across the Mca reference point.

##### 6.X.2.1.1	Pre-conditions

The AE has not registered with the M2M System.

The common request attributes for the Mca reference point contains the Application Entity (AE-ID) that the Originator has requested to be used for future exchanges between the AE and the M2M System.

##### 6.X.2.1.2	Signature

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| pointOf Access | IN | NO | The point of Access of the registered AE. |
| applicationId | IN | NO | The Application Identifer (App-ID). |
| expirationTime | IN | NO | The expiration time of the registration as requested by the Originator |
| aeId | OUT | NO | AE-ID is provided back in the response |
| responseType | OUT | NO | Unique response types for this service: AE successfully registered AE not successfully registered |

Table 6.X.2.1.2-1 Registration – registerAE capability

##### 6.X.2.1.3	Services Interaction

The interactions of service capabilities required for this service capability:

- Issue the request to Supporting Services to validate the service profile, authorize the request and record the event.

- Send a notification for a first-time application registration on the device in the event there is a subscription

Figure 6.X.2.1.3-1 Registration – registerAE Diagram

##### 6.X.2.1.4	Post-Conditions

AE is registered and can start using service capabilities

The returned AE-ID shall be used in any subsequent operation related to that application

##### 6.X.2.1.5	Exceptions

Not Applicable

##### 6.X.2.1.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.X.2.1.7	oneM2M Resource Interworking

This service capability interworks with the following oneM2M Resource operations:

- Create AE

#### 6.X.2.2	refreshAERegistration

This service capability enables an AE or a third party provisioned with the proper authorization to refresh an existing registration with the M2M System. This service capability shall be restricted to the Mca and Msc reference points.

##### 6.X.2.2.1	Pre-conditions

The AE has successfully registered with the M2M System.

The common request attributes for the Mca and Msc reference points contains the Application Entity (AE-ID) that the Originator has requested to be used for future exchanges between the AE and the M2M System.

##### 6.X.2.2.2	Signature

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| pointOfAccess | IN | YES | The point of Access of the registered AE. POA is optional only if identical to the one in the refreshed registration |
| expirationTime | IN | NO | The expiration time of the registration as requested by the Originator. |
| responseType | OUT | NO | Unique response types for this service: AE successfully refreshed Registration Does not exist |

Table 6.X.2.2.2-1 refreshAERegistration capability

##### 6.X.2.2.3	Service Interactions

The interactions of service capabilities required for this service capability:

- Issue the request to Supporting Services to validate the service profile, authorize the service request and record the event.

Figure 6.X.2.2.3-1 Registration – refreshAERegistration Diagram

##### 6.X.2.2.4	Post-Conditions

Not Applicable

##### 6.X.2.2.5	Exceptions

Not Applicable

##### 6.X.2.2.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.X.2.2.7	oneM2M Resource Interworking

This service capability interworks with the following oneM2M Resource operations:

- Update AE

#### 6.X.2.3	deregisterAE

This service capability enables an AE or a third party provisioned with the proper ACP to deregister from the M2M System. This service capabaility shall be restricted to the Mca reference points.

##### 6.X.2.3.1	Pre-conditions

The AE successfully registered with the M2M System.

The common request attributes for the Mca and Msc reference points contains the Application Entity (AE-ID) that the Originator has requested to be used for future exchanges between the AE and the M2M System.

##### 6.X.2.3.2	Signature

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| responseType | OUT | NO | Unique response types for this service: AE successfully De-registsred Registration Does not exist |

Table 6.X.2.3.2-1 Registration – deregisterAE capability

##### 6.X.2.3.3	Service Interactions

The interactions of service capabilities required for this service capability:

- Issue the request to Supporting Services to validate the service peofile, authorize the request and record the event.

Figure 6.X.2.3.3-1 Registration – deregisterAE Diagram

##### 6.X.2.3.4	Post-Conditions

AE is no longer registsred and cannot use any services.

##### 6.X.2.3.5	Exceptions

Not Applicable

Transaction Pattern: Participation allowed

##### 6.X.2.3.6	oneM2M Resource Interworking

This service capability interworks with the following oneM2M Resource operations:

- Delete AE

### 6.Y	Registration Administration Services

### 6.Y.1	Overview

The Registration administration service provides the ability for:

- Retrieve the AE’s Registration status

- Revoke an AE existing Registration

- Permit subscriptions to AE Registration events

### 6.Y.2	Service Capabilities

Editors Note: The fetching of the service profile is FFS in all operations involving such a step

Editors Note: The validation that the AE-ID is associated with the service profile is FFS in all operations involving such a step

#### 6.Y.2.1	getRegistrationStatus

This service capability enables a third party authorized for this operation, to retrieve the registration status for an AE. This service capability is limited to the Msc reference point

##### 6.Y.2.1.1	Pre-conditions

The common request attributes for the Msc reference point contains the Application Entity (AE-ID) that the Originator has requested to be used for future exchanges between the AE and the M2M System.

##### 6.Y.2.1.2	Signature

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| pointOf Access | OUT | NO | The point of Access of the registered AE. |
| applicationId | OUT | NO | The Application Identifer (App-ID). |
| expirationTime | OUT | NO | The expiration time of the registration as requested by the Originator. |
| responseType | OUT | NO | Unique response types for this service: AE successfully Retrieved Registration does not exist |

Table 6.Y.2.1.2-1 Registration – getRegistrationStatus capability

##### 6.Y.2.1.3	Service Interaction

The interactions of service capabilities required for this service capability:

- Issue the request to Service Subscription Adminstration to fetch the service profile for the registered AE-ID

Figure 6.Y.2.1.3-1 Registration – getRegistrationStatus Diagram

##### 6.Y.2.1.4	Post-Conditions

Not Applicable

##### 6.Y.2.1.5	Exceptions

Not Applicable

##### 6.Y.2.1.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.Y.2.1.7	oneM2M Resource Interworking

This service capability interworks with the following oneM2M Resource operations:

- Read AE

#### 6.Y.2.2	revokeAERegistration

This service capability enables a third party authorized for this operation to revoke an existing AE registration. This service capabaility shall be restricted to the Msc reference points

##### 6.Y.2.2.1	Pre-conditions

The AE successfully registered with the M2M System.

The common request attributes for the Msc reference point contains the Application Entity (AE-ID) that the Originator has requested to be used for future exchanges between the AE and the M2M System.

##### 6.Y.2.2.2	Signature

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| responseType | OUT | NO | Unique response types for this service: AE successfully De-registsred Registration does not exist |

Table 6.Y.2.2.2-1 revokeAERegistration capability

##### 6.Y.2.2.3	Service Interaction

The interactions of service capabilities required for this service capability:

- Issue the request to the Service Subscription Adminstration to fetch  the service profile.

Figure 6.Y.2.2.3-1 Registration – revokeAERegistration Diagram

##### 6.Y.2.2.4	Post-Conditions

AE is no longer registsred and cannot use any services

##### 6.Y.2.2.5	Exceptions

Not Applicable

##### 6.Y.2.2.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.Y.2.2.7	oneM2M Resource Interworking

This service capability interworks with the following oneM2M Resource operations:

- Delete AE

#### 6.Y.2.3.	subscribeInitialAERegistrationEvent

This service capability enables a third party that is authorized to subscribe to the initial (first time ony) registration of an AE on all devices. This capability shall be restricted to the Msc reference point

##### 6.Y.2.3.1	Pre-conditions

Not Applicable

##### 6.Y.2.3.2	Signature

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| applicationId | IN | NO | The Application Identifier (App-ID) |
| subscriptionId | OUT | YES | Return subscriptionId in case of a success. |
| responseType | OUT | NO | Unique response types for this service: successfully subscribed not successfully subscribed |

6.Y.2.3.2-1 subscribeInitialAERegistrationEvent capabilty

##### 6.Y.2.3.3	Service Interaction

The interactions of service capabilities required for this service capability:

- Issue the request to the Service Subscription Adminsitration to retrieve the service profile.

Figure 6.Y.2.3.3-1 Registration – subscribeInitialAERegistrationEvent Diagram

##### 6.Y.2.3.4	Post-Conditions

An event is created

##### 6.Y.2.3.5	Exceptions

Not Applicable

##### 6.Y.2.3.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.Y.2.3.7	oneM2M Resource Interworking

Not Applicable

#### 6.Y.2.4	unsubscribeInitialAERegistrationEvent

This service capability enables a third party having the ACP for this operation to remove an existing subscription against an AE initial registration. This capability shall be restricted to the Msc reference point.

##### 6.X.2.4.1	Pre-conditions

Not Applicable

##### 6.X.2.4.2	Signature

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| subscriptionId | IN | NO | The subscriptionId for the AE initial registration event. |
| responseType | OUT | NO | Unique response types for this service: Successfully unsubscribed Subscription does not exist |

Table 6.Y.2.4.2-1 unsubscribeInitialAERegistrationEvent capability

##### 6.X.2.4.3	Service Interaction

The interactions of service capabilities required for this service capability:

- Issue the request to the Service Subscription Adminstration tofetch the service profile.

Figure 6.Y.2.4.3-1 Registration – unsubscribeInitialAERegistrationEvent Diagram

##### 6.X.2.4.4	Post-Conditions

Subscription to AE no longer exists for the originator

##### 6.X.2.4.5	Exceptions

Not Applicable

##### 6.X.2.4.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.X.2.4.7	oneM2M Resource Interworking

Not Applicable

#### 6.X.2.5	getInitialSubscriptionAERegistrationEvents

This service capability enables a third party authorized for this operation to request a list of subscriptions against an initial registration AE. This capability shall be restricted to the Msc reference point.

##### 6.X.2.5.1	Pre-conditions

Not applicable

##### 6.X.2.5.2	Signature - getInitialSubscriptionAERegistrationEvents

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| applicationId | IN | NO | The Application Instance Identifier (App-ID) |
| subscriptionIds | OUT | NO | List of subscriptionIds associated with that event |
| responseType | OUT | NO | Unique response types for this service: AE successfully de-registered Registration does not exist |

Table 6.Y.2.5.2-1 Registration - getInitialSubscriptionAERegistrationEvents capability

##### 6.X.2.5.3	Service Interaction

The interactions of service capabilities required for this service capability:

- Issue the request to the Service Subscription Administration to fetch the service profile

Figure 6.Y.2.5.3-1 Registration – getInitialSubscriptionAERegistrationEvents Diagram

##### 6.X.2.5.4	Post-Conditions

Not Applicable

##### 6.X.2.5.5	Exceptions

Not Applicable

##### 6.X.2.5.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.X.2.5.7	oneM2M Resource Interworking

Not Applicable

-----------------------Start of change 2 ------------------------

## 7.3	Infrastructure Component (INF)

The INF Component provides Services that are exposed to other M2M Service Components across the Msc reference point. The Services within the INF Component are common and utility type Services needed to enable other M2M Services.

## 7.3.1	INF to Service Cross Reference

Authorization: All Service Capabilities

ServiceSubscription: retrieveAuthorization

Registration Services: registerAE, refreshAERegistration, deregisterAE

## 7.7	Service Exposure (SE)

The SE Component acts as the primary interface for AEs to interact with the M2M Service Layer across the Mca reference point.

## 7.7.1	Service Exposure to Service Cross Reference

SE Data Exchange: All Service Capabilities

Service Subscription: getBroker

Broker: publish, subscribe

Service Subscription Administration: getServiceSubscription, addDeviceToServiceSubscription, deleteDeviceFromServiceSubscription, getDevicesForServiceSubscription, addApplicationsToServiceSubscription, deleteApplicationsFromServiceSubscription, getApplicationsForServiceSubscription

Management Adapter: All Service Capabilities

- Registration Services: registerAE, refreshAERegistration, deregisterAE

-----------------------Start of change 3---------------------------

Remove service-Subscription-ID from the entire TS

# Comments

Same comment the authorization needs to go a supporting service.

Also need a supporting service flow that invokes this across the Msc.

We also probably want to send a notification on this as well.

Wouldnt there be post conditions on regristration similar to register?

I don’t understand this.

Do we just need to have the Supporting service authorize and account?

What the is entity that is to receive the request?

What is the internal processing that is necessary.