| CHANGE REQUEST |
| --- |
| Group Name:* | WG2 Architecture |
| Source:* | Ericsson |
| Format:* | ARC13 |
| Date:* | 2014-09-14 |
| Contact:* | George Foti |
| Reason for Change/s:* | Annex G is missing resource types defined in the spec. and should be allocated service roles identifiers to govern their usage |
| CR against: Release* | Release-1 |
| CR against: TS/TR* | TS-0001 v1.1.0 |
| Clauses/Sub Clauses* | Annex G |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

## ----------------------------------first change---------------------------

# Annex G (informative): List of M2M Services

This annex provides a list of M2M Services supported in this document as well as the list of associated roles mapped to each M2M Service.

Table G-1: M2M Services

| M2M Service (name) | M2M-Serv-ID | Roles |
| --- | --- | --- |
| Application and service management | 01 | 001-Software management |
| Device management | 02 | 002-Device Configuration 003-Device Diagnostics and Monitoring 004-Device Firmware Management 005-Device Topology |
| Location | 03 | 006-Location |
| Data exchange | 04 | 007-Basic data |
| Device onboarding | 05 | 008-onboarding |
| Security | 06 | 009-Security Administration |
| Groups | 07 | 010 – Groups Management |
| Statistics | 08 | 011 – Statistical Collections |

Use of M2M Service Subscription across M2M Service Provider domains is subject to M2M Service Providers agreement.

The following table provides an example of mapping of Service Roles to resource types and operations. Such a table is to be configured by the SP to allow for the validation of requests according to the service subscription.

Table G-2: Mapping of Service Roles to Resource Types/Allowed Operations

| Service Role | Resource Type/Allowed Operations |
| --- | --- |
| 001: Software management | mgmtObj / CRUD mgmtCmd / CRUD software / CRUD |
| 002: Device Configuration | mgmtObj / CRUD mgmtCmd / CRUD deviceInfo / CRUD |
| 003: Device Diagnostics and Monitoring | mgmtObj / CRUD mgmtCmd / CRUD deviceInfo / CRUD deviceCapability / CRUD |
| 004: Device Firmware Management | mgmtObj / CRUD mgmtCmd / CRUD firmware / CRUD |
| 005: Device Topology | mgmtObj / CRUD mgmtCmd / CRUD areaNwkInfo / CRUD areaNwkDeviceInfo / CRUD |
| 006: Location | locationPolicy / CRUD container / CRUD subscription / CRUD |
| 007: Basic data | container / CRUD subscription / CRUD |
| 008: onboarding | m2mServiceSubscriptionProfile / CRUD serviceSubscribedNode / CRUD |
| 009: Security Administration | accessControlPolicy / CRUD |
| 010 - Group Management | group / CRUD fanOutPoint / vrirtual resource |
| 011 - Statistical Collections | statsConfig / CRUD eventConfig / CRUD statsCollect / CRUD |

## ---end of First change---------------------------

# Comments

Why is this an example.

We need to define service roles for all what is defined in Resoiurce types. These are missing

- Group Management

- Accounting and Statistics related resources