| CHANGE REQUEST |
| --- |
| Group Name:* | WG2 Architecture |
| Source:* | Ericsson |
| Format:* | ARC13 |
| Date:* | 2014-09-15 |
| Contact:* | George Foti |
| Reason for Change/s:* | The current section on M2M identifiers contains some errors that requires fixing |
| CR against: Release* | Release-1 |
| CR against: TS/TR* | TS-0001 v1.1.0 |
| Clauses/Sub Clauses* | 7 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

## ----------------------------------first change---------------------------

# 7	M2M Entities and Object Identification

## 7.1	M2M Identifiers

This clause provides a list of identifiers required for the purpose of interworking within the oneM2M architectural model.

An M2M identifier is a sequence of characters used to refer to a an entity (such as CSE, AE, …), a resource (such as defined in clause 9) or an object (such as an M2M Service Provider or an M2M Node)  defined in oneM2M. An M2M identifier has a consistent meaning when applied (i.e. it refers consistently to the same resource, entity or object for the duration of their lifetime, as defined in the clause 7.2) in a particular context.

An M2M identifier can be either:

- An absolute M2M identifier, in which case it is globally unique and shall be a Unified Resource Identifier (URI) as specified in the IETF RFC 3986 [i.12]. The URI scheme to use for this URI (clause 3.1 of RFC3986 [i.12]) shall be independent of any actual protocol bindings used and is defined in TS-0004 [i.2]. See table in clause 7.2 for details on the format of absolute identifiers.

- A relative M2M identifier, in which case it shall be understood in a particular context, as specified in the IETF clause 4.2 of RFC 3986 [i.12]. See table in clause in the clause 7.2 for details on the format of relative identifiers.

One identifier shall not be assigned to two or more different entities.

It is assumed that the Application Identifier (App-ID) and the CSE Identifier (CSE-ID) have been assigned initially and are known before an M2M System boots up.

Further to being absolute or relative, an M2M identifier can be either “hierarchical” (i.e. it adheres to a predefined structure for URIs) or “non-hierarchical” (i.e. it does not adhere to a predefined structure for URIs):

Hierarchical URI: a hierarchical URI has its path portion defining the entire relationship for the target resource within the resource structure. This is a structured representation of the resources within a CSE where the parent relationship chain is embedded in the resource address.

EXAMPLE 1:	<scheme>://IN-CSEID.m2m.myoperator.org/CSE123/myAppX/myContainerY.

Non-Hierarchical URI: a non-hierarchical URI does not have its path portion reflecting the entire relationship for the target resource within the resource structure. The actual parent relationship chain is not known a priori from reading the path portion of the URI and the hosting CSE needs to resolve the logical location of the target resource in the chain of relationships within the resource structure following links. That path portion of the URL can be of any depth.

EXAMPLE 2:	"<scheme>://IN-CSEID.m2m.myoperator.org/CSEBase/mCY" where the same container of the previous example is directly addressed.

EXAMPLE 3:	"<scheme>://IN-CSEID.m2m.myoperator.org/some/path/mCY" where the same container of the previous example is also directly addressed.

EXAMPLE 4:	"<scheme>://IN-CSEID.m2m.myoperator.org/sc07" where the same container of the previous example is also directly addressed.

### 7.1.1	M2M Service Provider Identifier (M2M-SP-ID)

An M2M Service Provider shall be uniquely identified by the M2M Service Provider Identifier (M2M-SP-ID). This is a static value assigned to the Service Provider.

### 7.1.2	Application Entity Identifier (AE-ID)

An Application Entity Identifier (AE-ID) uniquely identifies an AE resident on an M2M Node, or an AE that requests to interact with an M2M Node. An AE-ID shall identify an Application Entity for the purpose of all interactions within the M2M System.

The AE-ID is globally unique and when used internally within a specific M2M SP domain, it is sufficient to be unique within that M2M Service Provider domain. It is extended to become globally unique when used outside the M2M Service Provider boundaries. The IN-CSE shall perform this task of adding or removing identifier portions (identifying the M2M SP) according to clause 7.2.

Additionally the AE-ID, when used in the context of a specific CSE where the AE is registered, it is sufficient to be unique within the scope of that specific CSE. It is extended to become M2M Service Provider unique when used outside such specific CSE.

The hosting CSE of the AE shall perform this task of adding or removing the identifier portions according to clause 7.2.

### 7.1.3	Application Identifier (App-ID)

This is equivalent to the application name and is not guaranteed to be globally unique on its own.

This identifier may be supported via a single or multiple registration authorities/entities. The definition and assignment of such an identifier is out of scope of this document.

NOTE:	Detailed format and structure of the App-ID is not specified in the present document.

### 7.1.4	CSE Identifier (CSE-ID)

A CSE shall be identified by a globally unique identifier, the CSE-ID, when instantiated within an M2M Node in the M2M System.

The CSE-ID is globally unique but when used internally within a specific M2M SP domain it is sufficient to be unique within that M2M Service Provider domain. It is extended to become globally unique when used outside the M2M Service Provider boundaries. The IN-CSE shall perform this task of adding or removing the identifier portions according to clause 7.2.

The CSE-ID shall identify the CSE for the purpose of all interactions from/to the CSE within the M2M System.

### 7.1.5	M2M Node Identifier (M2M-Node-ID)

An M2M Node, hosting a CSE and/or Application(s) shall be identified by a globally unique identifier, the M2M-Node-ID.

The M2M System shall allow the M2M Service Provider to set the CSE-ID and the M2M-Node-ID to the same value.

The M2M-Node-ID enables the M2M Service Provider to bind a CSE-ID to a specific M2M Node.

Examples of allocating a globally unique M2M-Node-ID include the use of Object Identity (OID) and IMEI. For details on OID, see annex H.

### 7.1.6	M2M Service Subscription Identifier (M2M-Sub-ID)

The M2M-Sub-ID enables the M2M Service Provider to bind application(s), M2M Nodes, CSEs and services identified by service identifiers, as well as administrative information, such as billing address etc., to a particular M2M Service Subscription between an M2M subscriber and the M2M Service Provider. The M2M-Sub-ID is unique for every M2M subscriber.

The M2M Service Subscription Identifier has the following characteristics:

belongs to the M2M Service Provider;

identifies the subscription to an M2M Service Provider;

enables communication with the M2M Service Provider;

can differ from the M2M Underlying Network Subscription Identifier.

There can be multiple M2M Service Subscription Identifiers per M2M Underlying Network subscription.

The M2M-Sub-ID shall not be exposed over any interface.

### 7.1.7	M2M Request Identifier (M2M-Request-ID)

The M2M-Request-ID tracks a Request initiated by an AE over the Mca reference point, and by a CSE over the Mcc reference point, if applicable, end to end. It is also included in the Response to the Request over the Mca or Mcc reference points.

To enable an AE to track Requests and corresponding Responses over the Mca reference point, AEs shall include a distinct M2M Request Identifier per request over the Mca Reference point to the CSE for any initiated request.

The CSE shall make such M2M Request Identifier unique by appending the CSE-relative AE-ID (see clause 7.2) to it.

If the CSE creates an M2M Request Identifier, then the CSE shall maintain a binding between the M2M Request Identifier received from the AE and the M2M Request Identifier it created in its interactions towards other peer CSEs. The CSE shall include the M2M Request Identifier received from the AE in its Response to the AE. This binding shall be maintained by the CSE until the Request message sequence is completed. Note that the Request initiated by the CSE could be the result of an application Request, or a request initiated autonomously by the CSE to fulfil a service.

In case an IN-CSE needs to send a request to a receiving CSE that is not reachable over any of the underlying networks, the IN-CSE initiates the procedure for "waking up" the Node hosting the receiving CSE by using procedures such as device triggering over the Mcn reference point. For Device Triggering, the triggering reference number to co-relate device triggering response is independent of the M2M Request Identifier. An IN-CSE may use the same value of an M2M-Request-Identifier in an incoming request for the triggering reference number in its interaction with the underlying network.

A CSE receiving a Request from a peer CSE shall include the received M2M Request Identifier in all additional Requests unspanned (i.e. 1:1) it has to generate (including propagation of the incoming Request) and that are associated with the incoming Request, where applicable.

If a Receiver CSE receives a request from an Originator for which another request with the same Request Identifier is already pending, the request shall be rejected. Otherwise – even if the same Request Identifier was already used by the same Originaor some time in the past, the request shall be treated as a new request.

### 7.1.8	M2M External Identifier (M2M-Ext-ID)

The M2M-Ext-ID is used by an M2M Service Provider (M2M SP) when services targeted to a CSE, identified by a CSE-ID, are requested from the Underlying Network.

The M2M External Identifier allows the Underlying Network to identify the M2M Device (e.g., ASN, MN) associated with the CSE-ID. To that effect, the Underlying Network maps the M2M-Ext-ID to the Underlying Network specific Identifier it allocated to the target M2M Device. In addition, the M2M SP shall maintain the association between the CSE-ID, the M2M-Ext-ID and the identity of the Underlying Network.

Both pre-provisioned and dynamic association between the CSE-ID with the M2M-Ext-ID are supported.

NOTE 1:	For each CSE-ID, there is only one M2M-Ext-ID for a specific UNetwork-ID. Hence an M2M SP interworking with multiple Underlying Networks has different M2M-Ext-IDs associated with the same CSE-ID, one per Underlying Network and selects the appropriate M2M-Ext-ID for any service request it initiates towards an Underlying Network.

NOTE 2:	The mapping by the Underlying Network of the M2M-Ext-ID to the M2M Device is Underlying Network specific.

NOTE 3:	The Underlying Network provider and the M2M Service Provider collaborate for the assignment of an M2M-Ext-ID to each CSE identified by CSE-ID. At the same time, the Underlying Network provider maintains association of the M2M-Ext-ID with the Underlying Network specific Identifier allocated to the M2M device that hosts such CSE.

For pre-provisioned M2M-Ext-IDs, the M2M-Ext-ID along with the associated CSE-ID shall be made available at the Infrastructure Node. The CSE at M2M device does not need to have knowledge of the M2M-Ext-ID assigned to it.

For dynamic M2M-Ext-IDs, the M2M-Ext-ID specific to the Underlying Network shall be made available at the M2M device in the Field Domain. Such M2M-Ext-ID shall be conveyed to the IN-CSE during CSE Registration.

### 7.1.9	Underlying Network Identifier (UNetwork-ID)

The UNetwork-ID is used for identifying an Underlying Network. UNetwork-ID is a static value and unique within a M2M Service Provider domain.

One or more Underlying Networks may be available at an M2M Node offering different sets of capabilities, availability schedules etc. Based on the "policy" information at the Node and the capabilities offered by the available Underlying Networks, appropriate Underlying Network can be chosen by using UNetwork-ID. For example, based on "policy", scheduling of traffic triggered by a certain event category in certain time periods may be allowed over Underlying Network "WLAN" but may not be allowed over Underlying Network "2G Cellular".

### 7.1.10	Trigger Recipient Identifier (Trigger-Recipient-ID)

The Trigger-Recipient-ID is used when device triggering services are requested from the Underlying Network, to identify an instance of an ASN/MN-CSE on an execution environment, to which the trigger is routed. For example, when 3GPP device triggering is used, the Trigger-Recipient-ID maps to the Application-Port-Identifier (TS 123 682 [i.17]).

NOTE 1:	For pre-provisioned M2M-Ext-IDs, Trigger-Recipient-ID is provisioned at the Infrastructure Node along with the M2M-Ext-ID and the associated CSE-ID.

NOTE 2:	For dynamic M2M-Ext-IDs, Trigger-Recipient-ID specific to the Underlying Network is provisioned at each M2M device in the Field Domain. Such Trigger-Recipient-ID is conveyed to the IN-CSE during CSE Registration.

### 7.1.11	M2M Service Identifier (M2M-Serv-ID)

The M2M-Serv-ID is an identifier of a M2M Service offered by an M2M SP. It is an essential part of the M2M Service Subscription which stores a set of M2M-Serv-IDs pertaining to the set of subscribed services. Beyond the set of services depicted in this specification it shall be possible for an M2M Service Provider to offer other services. Those will be identified by means of M2M SP specific M2M-Serv-IDs.

### 7.1.12	Service Role identifier (SRole-ID)

In each M2M Service, one or multiple M2M Service Role(s) shall be defined by the M2M Service Provider. An M2M Service Role is defined as a set of privileges pertaining to resource types which are associated with M2M Service. See Annex G for examples of M2M Service Provider defined Service Roles.

### 7.1.13	M2M Service Profile Identifier (M2M-Service-Profile-ID)

An M2M Service Profile Identifier defines M2M Services and/or M2M Service Roles (see Annex G) and AEs applicable to M2M Nodes. Every M2M Service Profile is allocated an identifier so it can be retrieved for verification purposes.

The M2M-Service-Profile-ID enables the M2M Service Provider to bind AE(s) and M2M Service identifiers and/or M2M Service Roles identifiers to M2M nodes.

An M2M-Service-Profile-ID shall be allocated to every M2M Node

The M2M Service Profile Identifier has the following characteristics:

belongs to the M2M Service Provider;

dentifies the M2M services and/or M2M Service Roles and AEs applicable to an M2M node

## 7.2	M2M-SP-ID, CSE-ID and AE-ID and resource Identifier formats

As a general rule, the identifiers of AEs, CSEs and resources are globally unique. In order to optimize their use, the identifiers shall be shortened when their scope can be derived from their context of use by the CSEs and the AEs.  Such shortened identifiers are defined as 'relative' identifiers.

TheM2M system shall use the identifiers M2M-SP-ID, CSE-ID and AE-ID and resource identifiers according to the formats and the rules specified in the following table (table 7.2-1).

Table 7.2-1: Identifiers formats and use

|  | Identifier Name | Format | Rule of use |
| --- | --- | --- | --- |
| M2M-SP-ID format |  | Fully qualified domain name Examples: <scheme>://www.m2mprovider.com <scheme>://globalm2m.org Note: the <scheme> part, as stated in clause 7.1, is unique and protocol-independent | When The M2M-SP-ID is used, the FQDN format applies |
| AE-ID EQUIVALENT formats | CSE-relative-AE-ID (with respect to the context of the CSE hosting the AE) | The CSE-relative AE Identifier is a sequence of characters that may include any of the unreserved characters defined in the clause 2.3 of the RFC3986 [i.12], as well as the slash character. It shall not start with the slash character. The CSE-relative AE Identifier is unique within the context of the CSE. | On the Mca reference point: to refer to AEs that are hosted by the directly attached (Registrar) CSE. The hosting CSE is responsible for guaranteeing that the CSE-Relative-AE-ID is unique in the context of the hosting CSE. |
|  | SP-relative -AE-ID (with respect to the context of the SP hosting the AE) | /[CSE-ID]/CSE-relative-AE-ID It begins with a slash character, as specified in clause 4.2 of RFC3986 [i.12] under “absolute-path reference”. | On the Mca and Mcc reference points: to refer to AEs that are hosted by the M2M Service Provider domain to which AE is attached. |
|  | Absolute AE-ID | M2M-SP-ID/SP-relative-AE-ID The absolute AE-ID shall conform to the URI format as defined in the IETF RFC 3986 [i.12]. | On the Mca and Mcc reference points: to refer to AEs that are hosted by a different M2M Service Provider domain with respect to the one to which the AE is attached and on the Mcc’ reference point for all the AEs |
| CSE-ID EQUIVALENT formats | SP-relative-CSE-ID (with respect to the context of the SP hosting the CSE) | The SP-relative-CSE-ID is a sequence of characters that may include any of the unreserved characters defined in the clause 2.3 of the RFC3986 [i.12], as well as the slash character. It shall not start with the slash character. The SP-relative-CSE-ID is unique within the context of the SP | On the Mca and Mcc reference points: to refer to CSEs that are hosted by the same M2M Service Provider domain |
|  | Absolute CSE-ID | M2M-SP-ID/SP-relative-CSE-ID The absolute AE-ID shall conform to the URI format as defined in the IETF RFC 3986 [i.12]. | On Mca and Mcc reference points: to refer to CSEs that are hosted by different M2M Service Provider domains and on the Mcc’ reference point for all the CSEs |
| Resource identifier equivalent formats | CSE-relative Resource ID | The CSE-relative Resource Identifier is a sequence of characters that may include any of the unreserved characters defined in the clause 2.3 of the RFC3986 [i.12], as well as the slash character. It shall not start with the slash character. The CSE-relative Resource Identifier is unique in the context of the CSE. Examples: container123 containers/c123 a1b2c3d4b0b00f0fa66a123456789abc a1b2c3d4-b0b0-0f0f-a66a-123456789abc cont/ b0b0-0f0f-a66a-123456789abc |  |
|  | SP-relative Resource ID (with respect to the context of the M2M Service Provider hosting the CSE) | The SP-relative Resource identifier is an absolute-path relative reference (beginning with a single slash), as defined in clause 4.2 of RFC3986 [i.12]. The SP-relative Resource Identifier is unique in the context of the Service Provider. /SP-relative-CSE-ID/SP-relative Resource ID | On the Mca and Mcc reference points: to refer to resources that are hosted by the same M2M Service Provider domain |
|  | Absolute Resource ID | M2M-SP-ID/SP-relative-Resource-ID | On Mca and Mcc reference points: to refer to resources that are hosted by a different M2M Service Provider domain and on the Mcc’ reference point for all the resources |

NOTE: This table still needs to be further fixed and be given more examples.

As a consequence, the hosting CSE shall convert the AEs global and relative identifier according to table 7.1.12-1 when a request is transmitted across the Mcc and Mca reference points.

As a consequence, the IN-CSE shall convert the AEs, CSEs and resource global and relative identifiers according to table 7.1.12-1when a request is transmitted across the Mcc’ reference point.

## 7.3	M2M Identifiers lifecycle and characteristics

# Table 7.3-1: M2M Identifiers lifecycle and characteristics

| Identifier | Assigned by | Assigned to | Assigned during | Lifetime | Uniqueness | Used during | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- |
| M2M Service Provider Identifier | Out of scope | AE, CSE | Out of scope | Out of scope | Global | Provisioning |  |
| Application Entity Identifier | AE or Registrar CSE | AE | AE start-up | Application Entity Registration | Global | - Application Entity Registration - Security Context Establishment - All other operations initiated by the AE | Security requirements apply for Security Context Establishment |
| Application Identifier | Out of scope | Out of scope | Pre-provisioned | Out of scope | Specific to M2M service deployment | - Application Entity registration |  |
| CSE Identifier | M2M SP | CSE | Security Provisioning | Life of the CSE | Global | - Information flows (clause 10) - Security Context Establishment | Security requirements apply for Security Context Establishment |
| M2M Node Identifier | Out of Scope | ALl M2M Nodes | Pre-provisioned | Life of the M2M Node | Global | - Device Management Not used for an ADN | Needs to be Read Only |
| M2M Subscription Identifier | M2M SP, Out of Scope | Application Entities, and one or more CSEs belonging to the same M2M subscriber | At service signup | Life of the M2M Service Subscription with the M2M Service Provider | Global | - Charging and Information Recorded - Role based access control - Authentication | Multiple CSEs can be allocated the same M2M Subscription Identifier |
| M2M Service Profile Identifier | M2M SP | Every M2M Node | At service signup | Life of M2M Service Subscriptions with the M2M Service Provider | Global for roaming cases otherwise local | Information Flows (Clause 10) | The ID has to be pre-provsioned after signup, but may need to be updated during the subscription lifetime due to changes in the subercibed services |
| M2M-Request-ID | Mcc: CSE Mca: Application Entity | A request initiated by an AE or CSE | Mcc: When a request is initiated by a CSE, or handling of a request received by a CSE. Mca: When a request is initiated by an AE | Equal to the lifetime of the Request and its corresponding Response | Mcc: Global Mca: Local or global | Requests and corresponding responses |  |
| External Identifier | Jointly between the Underlying Network provider and M2M SP. | M2M Node belonging to a CSE that wants to utilize services of the Underlying Network. | Administrative Agreement. | Life of the CSE. | Local or global, decided by the specific Underlying Network provider | Requests initiated by a CSE over the Mcn reference point, where applicable. | Pre-Provisioned Mode: Made available at the Infrastructure Node. Dynamic Mode: Made available at M2M device. Conveyed to IN-CSE during CSE Registration. |
| Underlying Network Identifier | M2M SP | Underlying Networks | Pre-provisioned | Life of the agreement by the M2M SP with the Underlying Network | Local to M2M SP domain | UL Network selection |  |
| Trigger Recipient Identifier | Execution Environment | ASN/MN-CSE | ASN/MN-CSE start-up or wake-up | Life of the CSE | Execution Environment-wide | Device Triggering procedures, where applicable | Pre-Provisioned Mode: Made available at Infrastructure Node along with M2M-Ext-ID. Dynamic Mode: Made available at M2M device. Conveyed to IN-CSE during CSE Registration along with M2M-Ext-ID. |
| M2M Service Identifier | M2M Service Provider, Out of Scope | A service defined by the M2M Service Provider which consists of a set of functions defined by this document. | Out of Scope | Out of Scope | Local to the M2M Service Provider | For M2M Service Subscription |  |
| SRole-ID | M2M Service Provider | M2M Service Provider sets the set of service roles that a subscriber can choose from. M2M service subscription lists one or multiple subscribed to service roles. | Out of Scope | Out of scope | M2M Service Provider | Access Control Policy, M2M service subscription management |  |

## ---end 1st change---------------------------

## ----------------------------------second change---------------------------

#### 10.1.1.1	Non-registration related CREATE procedure

This procedure is valid for all resources which are not related to registration.

Originator requests to create a resource by using the CREATE method. See clause 8.1.2 for the parameters to be included in the Request message.

Registrar CSE, when the Originator is an AE, shall validate the create request based on the resource type (ty) against the M2M Service Subscription Profile of the AE (validation is done against serviceRoles attribute)

Hosting CSE If the request is allowed by the given privileges, the Receiver shall create the resource.

# Figure 10.1.1.1-1: Procedure for CREATEing a Resource

Step 001: The Originator shall send the following parameters in the CREATE Request message:

op: 	C (Create);

to: 	URI of the target resource where the new resource should be created (parent resource);

# fr: 	ID of the Originator (either the AE or CSE);

[10.1.1.1.b] Editor's Note: AE or CSE may not have the ID upon its registration request. Alternative information for fr is FFS.

ty:	Type of resource to be created;

nm:	optional name of the resource to be provided by the Originator, where permitted by the resource type as specified in clause 9.6.

NOTE:	Some of the resources defined in clause 9.6 have a predefined name. For these resources the parameter nm is not applicable.

cn: 	attributes of the resource to be provided by the Originator. Of particular importance for the CREATE Request message is the common attribute resourceType (clause 9.6.1) which identifies the type of the resource to be Created.

[10.1.1.1.c] Editor's Note: which parameters are deducted to be mandatory/optional in the request is for FFS. Clause 8.1 should provide a generic mechanism to identify mandatory params for a request by looking at how the resource is defined. E.g. If the attribute in the resource definition is identified as mandatory and it is of type RW, then it is also intended as mandatory in the request.

[10.1.1.1.d] Editor's Note: references to elements defined in sect 8 have been added here. They may be removed if we decide to move sect 8.1.2-4 to stage 3 doc. In this case, these references will be removed and sect 1 of this document would replace sect 8.1.2-4 in the TS-0001.

Step 002: The Receiver shall:

- Check if the Originator has the appropriate privileges for performing the request. Privileges are part of the attribute accessControlPolicyIDs of the targeted resource. In case that such an attribute does not exist, the Receiver shall check the accessControlPolicyIDs of the parent resource.

[10.1.1.1.e] Editor's Note: how far should the Receiver go back to a parent to look for an accessControlPolicyIDs is FFS

- Verify that the suggested nm, if provided by the Originator in the Create Request message, does not already exist  among child resources of the target resource. If nm is not provided by the Originator, assign nm.

Assign a resource identifier (see resourceID attribute in common attribute table 9.6.1-1) to the resource to be created.

Assign/modify default values for certain mandatory attributes of the resource, where allowed by the resource itself and if not provided by the Originator itself.

the Receiver shall assign a value to the following common attributes specified in clause 9.6.1:

a)	parentID;

b)	creationTime;

c)	expirationTime: if not provided by the Originator, the Receiver shall assign the maximum value possible (within the restriction of the Receiver policies). If the value provided by the Originator cannot be supported, due to either policy or subscription restrictions, the Receiver will assign a new value.

d)	lastModifiedTime: which is equals to the creationTime;

e)	Any other RO (Read Only) attributes within the restriction of the Receiver policies.

On successful validation of the Create Request, the Receiver shall create the requested resource.

Step 003: The Receiver shall respond with a Response message that shall contain the following parameters:

to:	Optional. ID of the Originator. In case this is a response carrying the result of an operation triggered by a non-blocking request , rd information can be used.

# fr:	Optional. ID of the Receiver.

cn:	URI and optionally the content of the created resource. The Receiver shall provide the content if the created resource contains attributes which were modified by the Receiver in step 002.

See clauses 8.1.3 and 8.1.4 for the parameters to be included in the Response message.

# General Exceptions:

- The Originator does not have the privileges to create a resource on the Receiver. The Receiver responds with an error.

The resource with the specified name (if provided) already exists at the Receiver. The Receiver responds with an error.

The provided information in cn is not accepted by the Receiver (e.g. missing mandatory parameter). The Receiver responds with an error.

## ---end 2nd change---------------------------

# Comments

Very strange term. A node boots up but what does an M2M system mean her

Nowhere do we say how this ID is used. We have in section 10.1.1.1. a verification against the profile. We need tobe more explicit on how the servicSRole-ID is checked in that section

Are we not missing the rekative CSE-ID here