| CHANGE REQUEST |
| --- |
| Group Name:* | ARC#13 |
| Source:* | Qualcomm Inc. (TIA) |
| Format:* | Plenary |
| Date:* | 2014-09-15 |
| Contact:* | Phil Hawkes, Qualcomm, phawkes@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com Wolfgang Granzov, Qualcomm phawkes@qti.qualcomm.com |
| Reason for Change/s:* | New definitions for AE Identifiers required to support persistent identifiers |
| CR against: | TS-0001 and v1.1.0 |
| Clauses/Sub Clauses Affected* | 7.1.2, 7.2, 7.3, 3.1, 3.2 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the changes into TS-0001 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Do not conflict with the content of an already approved text, by modification, deletion or the addition of an editor’s note.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

ARC and SEC met at SEC#12.2 to discuss the need for persistent identifiers for Application Entities. At that meeting it was generally agreed that persistent identifiers for Application Entities are required. This CR replaces the current AE-ID definition with three types of AE identifiers that will support the various uses of AE identifiers that are required in oneM2M.

Note that the new Application Entity Service-Provider-Issued Persistent-Identity (AE-SPI-PID) can be used in cases where the AE might change which CSE it is registered to. In order for messages to sent to the AE, the messages will need to include the CSE-ID of the CSE to which the AE is currently registered. We plan to submit another CR describing mechanisms allowing an CSE can find out the CSE-ID of the AE’s current Registrar CSE (in the cases where the AE has an AE-SPI-PID).

### -----------------------Start of change 1-------------------------------------------

### 7.1.2	Application Entity Identifiers

#### 7.1.2.1	Types of Application Entity Identifier

There are three types of Application Entity identifier:

- Application Entity Leased Identifier (AE-LID). This is a small CSE-relative identity “leased” to the Application Entity by the Registrar CSE upon registration and which is associated with the Application Entity for only as long as the Application Entity does not let the registration expire. Once the registration expires, then the AE-LID can be leased to another Application Entity. The AE-LID is provides a small identity for communication with the Registrar CSE and with other Application Entities registered to this Registrar CSE.

- Application Entity Service-Provider-Issued Persistent Identifier (AE-SPI-PID). This is a persistent M2M SP-relative identity issued by an IN-CSE (on behalf of the M2M SP) to an Application Entities that is hosted on Application Dedicated Node (ADN) only. The AE-SPI-PID can be used as a persistent identifier for the Application Entity, but does not identify the Registrar CSE of the Application Entity. The current Registrar CSE of the Application entity with an AE-SPI-PID can be obtained by querying the IN-CSE.

- Application Entity Registrar Issued Persistent Identifier (AE-RI-PID). This is a persistent CSE-relative identity issued by the Registrar CSE to Application Entities that are hosted on the same node as the Registrar CSE. The combination of the AE-RI-PID and the CSE-ID of the Registrar CSE can be used as a persistent identifier for the Application Entity that has the added bonus of identifier the Registrar CSE of the Application Entity.

#### 7.1.2.2	Application Entity Leased Identifier (AE-LID)

An Application Entity Leased Identifier (AE-LID) is assigned by the CSE to an AE upon registration to the CSE. An AE-LID is assigned to at most one AE at any given time. An AE continues to be associated with an AE-LID for as long as the Application Entity does not let its registration (with the CSE) expire. If the registration expires, then the AE’s “lease” on the AE-LID ends, and the AE-LID can be assigned to another AE (that is, the AE-LID can be recycled).

All AE are issued an AE-LID upon registration.

The AE-LID has the following properties

- Since an AE-LID can be recycled, a CSE needs only as many AE-LID as the number of AE that are expected to be registered simultaneously – and this allows the AE-LID to remain relatively small is size.

- The combination of the AE-LID with the CSE-ID of the Registrar CSE provides an identity for an AE that is unique within the scope of the M2M SP, but which is not guaranteed to be persistent. Other entities cannot assume that the AE-LID will be associated with the AE after the expiry of the current registration.

An AE-LID, or combination of AE-LID and CSE-ID of the Registrar CSE, can be useful in scenarios where

- A small identifier is desirable, and

- The identifier is required only for the lifetime of the current registration.

An AE-LID, or combination of AE-LID and CSE-ID of the Registrar CSE, can be problematic in scenarios where the identifier is required only for the lifetime of the current registration (for example, in <accessControlPolicy>, <subscription> or <group> resources). In such scenarios, an AE-RI-PID or AE-SPI-PID should be used – see clauses 7.1.2.3 and 7.1.2.4.

#### 7.1.2.3	Application Entity Registrar- Issued Persistent Identifier (AE-RI-PID)

An Application Entity Registrar-Issued Persistent Identifier (AE-RI-PID) is assigned by the Registrar CSE to an AE if requested by the AE. An AE-RI-PID is unique within the scope of that CSE and is persistent, that is, it can never be assigned to another AE.

An AE issued an AE-RI-PID only if requested by the AE. Not all AE will have an associated AE-RI-PID.

The AE-RI-PID has the following properties

- While the AE is registered to this CSE CSE, then the combination of the AE-RI-PID with the CSE-ID of the Registrar CSE provides an identity for an AE that is

  - unique within the scope of the M2M SP and

  - Provides all information needed in the “to” parameter of a message intended for the AE.

- If the AE deregisters from the CSE that issued the AE-RI-PID and registers to another CSE, then

  - The combination of the AE-RI-PID (from the previous Registrar CSE) the CSE-ID of the previous Registrar CSE no longer provides the information needed in the “to” parameter of a message intended for the AE - so this combination is not persistent.

  - The combination of the AE-RI-PID (from the previous Registrar CSE) the CSE-ID of the new Registrar CSE is no longer guaranteed to be unique.

- Since an AE-RI-PID cannot be recycled, a CSE needs as many AE-RI-PID as the number of persistent AE that are expected to be registered over all time.

An AE-RI-PID is useful in all scenarios for which an AE-LID is useful (either on its own, or in combination with the CSE-ID of the Registrar CSE).

The combination of AE-RI-PID and CSE-ID of the Registrar CSE, can be useful in scenarios where both of the following requirements are met.

- The AE is very unlikely to change its Registrar CSE. For example

  - An AE hosted on the same device as the Registrar CSE,

  - An AE on an ADN which will always register to a single Registrar CSE.

- A persistent identifier is required.

For example, the combination of AE-RI-PID and CSE-ID of the Registrar CSE can be useful for

- Identifying an AE in <accessControlPolicy>, <subscription> and <group> resources.

- Identifying an AE in the “to” parameter of a message intended for the AE.

#### Identifying an AE in the “from” parameter of a message from the AE.

#### The combination of AE-RI-PID and CSE-ID of the Registrar CSE can be problematic in scenarios requiring a persistent AE, but where the AE is likely to frequently changes its Registrar CSE (for example, AEs on ADNs that are mobile and frequently change which MN-CSE they are registered to). In such scenarios, an AE-SPI-PID should be used – see clause 7.1.2.4.

#### 7.1.2.4	Application Entity Service-Provider-Issued Persistent Identifier (AE-SPI-PID)

An Application Entity Service-Provider-Issued Persistent Identifier (AE-SPI-PID) is a persistent M2M SP-relative identity issued by an IN-CSE (on behalf of the M2M SP) to an Application Entity. Once an AE has been issued a particular AE-SPI-PID, then no other AE is permitted to be identified with that AE-SPI-PID.  Once an AE is issued an AE-SPI-PID, then the AE-SPI-PID is provided to the Registrar CSE during registration.

The AE-SPI-PID is intended to be used in scenarios requiring a persistent identifier, but where an AE-RI-PID is not appropriate because the AE is likely to frequently change its Registrar CSE.

An AE is issued an AE-SPI-PID only if requested by the AE. Not all AE will request an AE-SPI-PID

The AE-SPI-PID (on its own) has the following properties

- Since an AE-SPI-PID cannot be recycled, an M2M SP needs to support as many AE-SPI-PID as the number of AE within the M2M SP system. This may a very large number. Consequently, the AE-SPI-PID may grow relatively large in size.

- An AE-SPI-PID provides an identity for an AE that is unique within the scope of the M2M SP and that is guaranteed to be persistent, regardless of which CSE the AE registers with.

An AE-SPI-PID (on its own) is useful in all scenarios for which an AE-LID (on its own) is useful.

The AE-SPI-PID (on its own or in combination with the M2M-SP-ID) can be used in scenarios where an identifier might be required for more than the lifetime of the current registration and where an AE-RI-PID is not appropriate. For example, AE-SPI-PID can be useful for identifying an AE in:

- <accessControlPolicy>, <subscription> and <group> resources.

- Identifying an AE in the “from” parameter of a request from the AE, if the response is not expected back shortly after the request.

The combination of AE-SPI-PID with the CSE-ID of the AE’s current Registrar CSE has the following properties:

- The combination of AE-SPI-PID and the CSE-ID of the CSE to which the AE s currently registered provides all information needed in the “to” parameter of a message intended for the AE

The combination of AE-SPI-PID with the CSE-ID of the AE’s current Registrar CSE is useful in all scenarios for which the combination of the AE-LID with the CSE-ID of the AE’s current Registrar CSE is useful.

The combination of the AE-SPI-PID with the CSE-ID of the AE’s current Registrar CSE can be useful in scenarios where an AE (possessing an AE-SPI-PID) and its current Registrar CSE needs to be identified. For example, the combination of the AE-SPI-PID with the CSE-ID of the AE’s current Registrar CSE can be useful for identifying an AE in:

- The “from” parameter of a message from the AE, if the response is expected back shortly time after the request.

- Identifying an AE in the “to” parameter of a message intended for the AE.

<Select the text from the latest baseline TS or TR.

Turn  "Track Changes" off.

Paste the existing text from the baseline.

Turn "Track Changes" on.

Make the proposed changes.

If the text is new text, turn on "Track Changes" and start typing>

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

## 7.2	M2M-SP-ID, CSE-ID and AE-ID and resource Identifier formats

As a general rule, the identifiers of AEs, CSEs and resources are globally unique. In order to optimize their use, the identifiers shall be shortened when their scope can be derived from their context of use by the CSEs and the AEs.  Such shortened identifiers are defined as 'relative' identifiers.

TheM2M system shall use the identifiers M2M-SP-ID, CSE-ID and AE-ID and resource identifiers according to the formats and the rules specified in the following table (table 7.2-1).

Table 7.2-1: Identifiers formats and use

|  | Format Name | Format | Rule of use |
| --- | --- | --- | --- |
| M2M-SP-ID format |  | Fully qualified domain name Examples: <scheme>://www.m2mprovider.com <scheme>://globalm2m.org Note: the <scheme> part, as stated in clause 7.1, is unique and protocol-independent | When The M2M-SP-ID is used, the FQDN format applies |
| AE-ID EQUIVALENT formats | CSE-relative-AE-ID (with respect to the context of the CSE hosting the AE) | The CSE-relative AE Identifier is a sequence of characters that may include any of the unreserved characters defined in the clause 2.3 of the RFC3986 [i.x], as well as the slash character. It shall not start with the slash character. The CSE-relative AE Identifier is unique within the context of the CSE. The CSE-relative AE Identifier may be an AE-LID, AE-RI-PID or AE-SPI-PID (see clause 7.1.2) | In “to” and “from” parameters of messages on the Mca reference point: to refer to AEs that are hosted by the directly attached (Registrar) CSE. The hosting CSE is responsible for guaranteeing that the CSE-Relative-AE-ID is unique in the context of the hosting CSE. |
|  | SP-relative -AE-ID (with respect to the context of the SP hosting the AE) | /[CSE-ID]/CSE-relative-AE-ID It begins with a slash character, as specified in clause 4.2 of RFC3986 [i.12] under “absolute-path reference”. | In “to” and “from” parameters of messages on the Mca and Mcc reference points: to refer to AEs that are hosted by the M2M Service Provider domain to which AE is attached. |
|  | Absolute AE-ID | M2M-SP-ID/SP-relative-AE-ID The absolute AE-ID shall conform to the URI format as defined in the IETF RFC 3986 [i.12]. | In “to” and “from” parameters of messages on the Mca and Mcc reference points: to refer to AEs that are hosted by a different M2M Service Provider domain with respect to the one to which the AE is attached and on the Mcc’ reference point for all the AEs |
|  | Persistent Absolute AE-ID | M2M-SP-ID/[CSE-ID]/[AE-RI-PID] or M2M-SP-ID/”persistentAeId”/[AE-SPI-PID] | In <accessControlPolicy>, <subscription>, <group>, <m2mServiceSubscriptionProfile> : where persistent AE identifiers are needed. |
| CSE-ID EQUIVALENT formats | SP-relative-CSE-ID (with respect to the context of the SP hosting the CSE) | M2M-SP-ID/SP-relative-AE-ID The absolute AE-ID shall conform to the URI format as defined in the IETF RFC 3986 [i.12]. | On the Mca and Mcc reference points: to refer to CSEs that are hosted by the same M2M Service Provider domain |
|  | Absolute CSE-ID | M2M-SP-ID/SP-relative-CSE-ID | On Mca and Mcc reference points: to refer to CSEs that are hosted by different M2M Service Provider domains and on the Mcc’ reference point for all the CSEs |
| Resource identifier equivalent formats | CSE-relative Resource ID | The CSE-relative Resource Identifier is a sequence of characters that may include any of the unreserved characters defined in the clause 2.3 of the RFC3986 [i.12], as well as the slash character. It shall not start with the slash character. The CSE-relative Resource Identifier is unique in the context of the CSE. Examples: container123 containers/c123 a1b2c3d4b0b00f0fa66a123456789abc a1b2c3d4-b0b0-0f0f-a66a-123456789abc cont/ b0b0-0f0f-a66a-123456789abc |  |
|  | SP-relative Resource ID (with respect to the context of the M2M Service Provider hosting the CSE) | The SP-relative Resource identifier is an absolute-path relative reference (beginning with a single slash), as defined in clause 4.2 of RFC3986 [i.12]. The SP-relative Resource Identifier is unique in the context of the Service Provider. | On the Mca and Mcc reference points: to refer to resources that are hosted by the same M2M Service Provider domain |
|  | Absolute Resource ID | M2M-SP-ID/SP-relative-Resource-ID | On Mca and Mcc reference points: to refer to resources that are hosted by a different M2M Service Provider domain and on the Mcc’ reference point for all the resources |

NOTE: This table still needs to be further fixed and be given more examples.

As a consequence, the hosting CSE shall convert the AEs global and relative identifier according to table 7.1.12-1 when a request is transmitted across the Mcc and Mca reference points.

As a consequence, the IN-CSE shall convert the AEs, CSEs and resource global and relative identifiers according to table 7.1.12-1when a request is transmitted across the Mcc’ reference point.

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3-------------------------------------------

## 7.3	M2M Identifiers lifecycle and characteristics

# Table 7.3-1: M2M Identifiers lifecycle and characteristics

| Identifier | Assigned by | Assigned to | Assigned during | Lifetime | Uniqueness | Used during | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- |
| M2M Service Provider Identifier | Out of scope | AE, CSE | Out of scope | Out of scope | Global | Provisioning |  |
| Application Entity Lesed Identifier (AE-LID) | Registrar CSE | AE | Registration if no current AE-LID is assigned | Application Entity Registration | - Registrar. - Can be used by another AE if Registration expires | - Application Entity Re- Registration - All other operations initiated by the AE where a persistent AE identifier is not needed |  |
| Application Entity Registrar-Issued Persistent-Identifier (AE-RI-PID) | Registrar CSE | AE | Initial Registration (may be deferred if desired) | Persistent. | - Registrar - Cannot ever be used by another AE | - Application Entity Re-Registration - All other operations where a persistent AE identifier is needed -access control, subscription and group operations | Intended for cases where AE will not register to other CSEs See clause 7.1.2.3. |
| Application Entity Service-Provider-Issued Persistent-Identifier (AE-SPI-PID) | IN-CSE (on behalf of M2M-SP) | AE | - Pre-assigned in coordination with Subscriber - Following initial registration (may be deferred if desired) | Persistent | M2M-SP - Cannot ever be used by another AE |  | Intended for cases where AE might register to other CSEs (e.g. nomadic). See clause 7.1.2.4. |
| Application Entity Credential Identity | Various. Out of scope | ADN-AE or all AE on a single ADN might share AE Credential in some cases | Pre-provisioning or Security Provisioning | Lifetime of the credential – typically close to the lifetime of the AE. | Global | Security Context Establishment | - Security requirements apply for Security Context Establishment - Registrar associates w/ AE-LID, AE-SPI-PID. |
| Application Identifier | Out of scope | Out of scope | Pre-provisioned | Out of scope | Specific to M2M service deployment | - Application Entity registration |  |
| CSE Identifier | M2M SP | CSE | Security Provisioning | Life of the CSE | Global | - Information flows (clause 10) - Security Context Establishment | Security requirements apply for Security Context Establishment |
| M2M Node Identifier | Out of Scope | M2M Node hosting CSE | Pre-provisioned | Life of the M2M Node | Global | - Device Management | Needs to be Read Only |
| M2M Subscription Identifier | M2M SP, Out of Scope | Application Entities, and one or more CSEs belonging to the same M2M subscriber | At service signup | Life of the M2M Service Subscription with the M2M Service Provider | Global | - Charging and Information Recorded - Role based access control - Authentication | Multiple CSEs can be allocated the same M2M Subscription Identifier |
| M2M Service Profile Identifier | M2M SP | Every M2M Node | At service signup | Life of M2M Service Subscriptions with the M2M Service Provider | Global for roaming cases otherwise local | Information Flows (Clause 10) | The ID has to be pre-provsioned after signup, but may need to be updated during the subscription lifetime due to changes in the subercibed services |
| M2M-Request-ID | Mcc: CSE Mca: Application Entity | A request initiated by an AE or CSE | Mcc: When a request is initiated by a CSE, or handling of a request received by a CSE. Mca: When a request is initiated by an AE | Equal to the lifetime of the Request and its corresponding Response | Mcc: Global Mca: Local or global | Requests and corresponding responses |  |
| External Identifier | Jointly between the Underlying Network provider and M2M SP. | M2M Node belonging to a CSE that wants to utilize services of the Underlying Network. | Administrative Agreement. | Life of the CSE. | Local or global, decided by the specific Underlying Network provider | Requests initiated by a CSE over the Mcn reference point, where applicable. | Pre-Provisioned Mode: Made available at the Infrastructure Node. Dynamic Mode: Made available at M2M device. Conveyed to IN-CSE during CSE Registration. |
| Underlying Network Identifier | M2M SP | Underlying Networks | Pre-provisioned | Life of the Underlying Network | Local to M2M SP domain | UL Network selection |  |
| Trigger Recipient Identifier | Execution Environment | ASN/MN-CSE | ASN/MN-CSE start-up or wake-up | Life of the CSE | Execution Environment-wide | Device Triggering procedures, where applicable | Pre-Provisioned Mode: Made available at Infrastructure Node along with M2M-Ext-ID. Dynamic Mode: Made available at M2M device. Conveyed to IN-CSE during CSE Registration along with M2M-Ext-ID. |
| M2M Service Identifier | M2M Service Provider, Out of Scope | A service defined by the M2M Service Provider which consists of a set of functions defined by this document. | Out of Scope | Out of Scope | Local to the M2M Service Provider | For M2M Service Subscription |  |
| SRole-ID | M2M Service Provider | M2M Service Provider sets the set of service roles that a subscriber can choose from. M2M service subscription lists one or multiple subscribed to service roles. | Out of Scope | Out of scope | M2M Service Provider | Access Control Policy, M2M service subscription management |  |

### -----------------------End of change 3---------------------------------------------

### -Start of changes to Definitions Symbols Abbreviations Acronyms ---- please add in the new definitions in the appropriate location in the text-

# 3	Definitions, symbols, abbreviations  and acronyms

## 3.1	Definitions

Application Entity Credential Identifier: Identifier for the credential being used to authenticate the Application Entity. An  Application Entity Credential Identity can have various formats, depending on the kind of credential. There may be some scenarios where all Application Entities on an Application Dedicated Node share a common credential (for example, if using the Generic Bootstrapping Architecture or a Device Certificate)

Editor’s note: references needed.

Application Entity Leased Identifier: CSE-relative identity “leased” to the Application Entity by the Registrar CSE upon registration and which is associated with the Application Entity for only as long as the Application Entity does not let the registration expire

Application Entity Registrar-Issued Persistent-Identifier: persistent CSE-relative identity issued by the Registrar CSE to Application Entities that are hosted on the same node as the Registrar CSE.

Application Entity Service-Provider-Issued Persistent-Identifier: a persistent M2M SP-relative identity issued by an IN-CSE (on behalf of the M2M SP) to an Application Entities that is hosted on Application Dedicated Node (ADN) only.

## 3.2	Abbreviations and Acronyms

For the purposes of the present document, the following abbreviations and acronyms apply:

2G	Second Generation

3GPP	3rd Generation Partnership Project

3GPP2	3rd Generation Partnership Project 2

AAA	Authentication, Authorization, Accounting

AAAA	Authentication, Authorization, Accounting and Auditing

A/AAAA	IPv4/IPv6 DNS records that are used to map hostnames to an IP address

ACA	Accounting Answer

ACR	Accounting Request

ADN	Application Dedicated Node

ADN-AE	AE which resides in the Application Dedicated Node

AE	Application Entity

AE-LID	Application Entity Leased Identifier

AE-RI-PID	Application Entity Registrar-Issued Persistent-Identifier

AE-SPI-PID	Application Entity Service-Provider-Issued Persistent-Identifier

AID CSF	Addressing and Identification CSF

Annc	Announced

API	Application Program Interface

AS	Application Server

ASM CSF	Application and Service Layer Management CSF

ASN	Application Service Node

ASN-AE	Application Entity that is registered with the CSE at Application Service Node

ASN-CSE	CSE which resides in the Application Service Node

BBF	BroadBand Forum

CDR	Charging Data Record

CF	Configuration Function

CHF	Charging Function

CM	Conditional Mandatory

CMDH 	Communication Management and Delivery Handling

COSEM	Companion Specification for Energy Metering

CRUD	Create Retrieve Update Delete

CRUDN	Create Retrieve Update Delete Notify

CSE	Common Services Entity

CSE-ID	Common Service Entity Identifier

CSE-PoA	CSE Point of Access

CSF	Common Services Function

DCF	Device Configuration Function

DDMF	Device Diagnostics and Monitoring Function

DFMF	Device Firmware Management Function

DHCP	Dynamic Host Configuration Protocol

DIS CSF	Discovery CSF

DM	Device Management

DMF	Diagnostic and Monitoring Function

DMG CSF	Device Management CSF

DMR	Data Management and Repository

DNS	Domain Name Server

DTMF	Device Topology Management Function

EF	Enabler Function

FFS	For Further Study

FQDN	Fully Qualified Domain Name

GMG CSF	Group Management CSF

GPRS	General Packet Radio Service

GPS	Global Positioning System

GSMA	GSM Association (Global System for Mobile Communications Association)

HA/LMA	Home Agent/Local Mobility Agent

HAAA	Home AAA

HLR	Home Location Register

HPLMN	Home Public Land Mobile Network

HSS	Home Subscriber Server

HTTP	HyperText Transfer Protocol

IMEI	International Mobile Equipment Identity

IMS	IP Multimedia System

IMSI	International Mobile Subscriber Identity

IN	Infrastructure Node

IN-AE	Application Entity that is registered with the CSE in the Infrastructure Node

IN-CSE	CSE which resides in the Infrastructure Node

IN-DMG	Infrastructure Node Device ManaGement

IN-DMG-MA	Infrastructure Node Device ManaGement Management Adapter

IP	Internet Protocol

IPE	Interworking Proxy application Entity

ISO	International Organization for Standardization

ITU-T	ITU Telecommunication Standardization Sector

IWF	InterWorking Function

JNI	Java Native Interface

LOC	Location

LOC CSF	Location CSF

LWM2M	Lightweight M2M

M2M	Machine to Machine

M2M-IWF	M2M InterWorking Function

M2M-Sub-ID	M2M service Subscription Identifier

MA	Mandatory Announced

Mca	Reference Point for M2M Communication with AE

Mcc	Reference Point for M2M Communication with CSE

Mcc'	Reference Point for M2M Communication with CSE of different M2M Service Provider

Mch	Reference Point for M2M Communication with external charging server

Mcn	Reference Point for M2M Communication with NSE

MIP	Mobile IP

MN	Middle Node

MN-AE	Application Entity that is registered with the CSE in Middle Node

MN-CSE	CSE which resides in the Middle Node

MSISDN	Mobile Subscriber International Subscriber Directory NumberMTC	Machine Type Communications

NA	Not Announced

NAT	Network Address Translation

NSE	Network Service Entity

NSSE CSF	Network Service Exposure, Service Execution and Triggering CSF

OA	Optional Announced

OID	Object Identifier

OMA	Open Mobile Alliance

OMA-DM	Open Mobile Alliance Device Management

OSI	Open Service Initiative or Open Service Interconnection

PDSN	Packet Data Serving Node

PMIP	Proxy Mobile IP

PoA	Point of Access

PPP	Point to Point Protocol

RAM	Random Access Memory

REG	Registration

REG CSF	Registration CSF

RFC	Request for Comments

RO	Read Only

RPC	Remote Procedure Calls

RW	Read Write

SCA	Service Charging and Accounting

SCA CSF	Service Charging and Accounting CSF

SCS	Services Capability Server

SDO	Standards Developing Organization

SEC	Security

SEC CSF	Security CSF

SIP	Session Initiation Protocol

SLA	Service Level Agreement

SMF	Software Monitoring Function

SMS	Short Messaging Service

SP	Service Provider

SP-ID	Service Provider Identifier

SSM 	Service Session Management

SSM CSF	Service Session Management CSF

SUB CSF	Subscription and Notification CSF

TBD	To Be Determined

Tsms	Interface between Short Message Entity (SME) and Short Message Service Center (SMS SC)

Tsp	Interface between Service Capability Server (SCS) and Machine Type Communication (MTC) InterWorking Function

# UE	User Equipment

UL	UpLink

URI	Uniform Resource Identifier

URL	Uniform Resource Locator

URN	Uniform Resource Name

WLAN	Wireless Local Area Network

WO	Write Once

### ---End of changes to Definitions, Symbols, Abbreviations, Acronyms ---

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Does this change request avoid conflict with the content of an already approved text, by modification, deletion or the addition of an editor’s note?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change  include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?