| CHANGE REQUEST |
| --- |
| Group Name:* | ARC#13 |
| Source:* | Qualcomm Inc. (TIA) |
| Format:* | Plenary |
| Date:* | 2014-09-22 |
| Contact:* | Wolfgang Granzow, wgranzow@qti.qualcomm.com Josef Blanz, jblanz@qti.qualcomm.com |
| Reason for Change/s:* | Clarification on use of square brackets for attribute and resource type names |
| CR against: Release* | Release-1 |
| CR against: TS/TR* | TS-0001 v1.1.0 |
| Clauses/Sub Clauses* | 9.5, 9.6, D.1 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR proposes clarifications about the usage of square brackets in attribute and resource type names (see also email discussion on the ARC email reflector under subject “Problem with the use of '[' and ']' convention”).

It is proposed that the square brackets shall be used to define “specializations” of attribute names and resource type names (currently inconsistently called “sub-resources” or “instances” of the <mgmtObj> resource).

The changes proposed here include renaming of the 1st column of the Tables which for each resource type  define the child resources and attributes and replacing of “[variable]“ with “variable”.

If agreed this change will need to be applied to all corresponding Tables in clause  9.5, 9.6 and Annex D of TS-0001. This is an editorial change that could be implemented rather easily by applying a global replace of the respective text.

### -----------------------Start of change 1-------------------------------------------

## 9.5	Resource Type Specification Conventions

The following conventions are used for the specification of resources.

Resources are specified via a tabular notation and the associated graphical representation as follows:

The resources are specified in association with a CSE. The resources are the representation in the CSE of the components and elements within the oneM2M System. Other CSEs, AEs, application data representing sensors, commands, etc. are known to the CSE by means of their resource representation. Resource, Child Resource and Attributes are defined in clause 3.1 and are restated below for readability.

Resource: A Resource is a uniquely addressable entity in oneM2M architecture. A resource is transferred and manipulated using CRUD operations (see clause 10.1). A resource can contain child resource(s) and attribute(s).

Child Resource: It is a sub-resource of another resource that is its parent resource. The parent resource contains references to the child resources(s).

Attribute: Stores information pertaining to the resource itself.

The set of attributes, which are common to all resources, are not detailed in the graphical representation of a resource.

Resource names and attribute names are strings in lower case. In case of a composed name, the subsequent word(s) start with a capital letter; e.g. accessControlPolicy, creationTime, expirationTime.

Resource type names and attribute names are written in italic form in this document.

A string containing a resource type name in italic delimited with '<' and '>', e.g. <resourceType>, is used as an abbreviation referring to for the type of a resource. For example the text “a <container> resource” could be used as an abbreviation for “a resource of type container”.

A string delimited with '[' and ']', e.g. [resourceName], is a reference to attribute(s) that can be specialized or a specialized resource type.

  - Attributes that can be specialized only occur in resource types that can be specialized.

  - A specialization of a resource type is done by defining specific names and descriptions of the attributes that can be specialized from the base resource type.

The resources are specified as shown below.

Figure 9.5-1: <resourceType> representation convention

The resource specification provides the graphical representation for the resource as the figure 9.5-1. The graphical representation of a resource shows the multiplicity of the attributes and child resources. The set of attributes, which are common to all resources are not detailed in the graphical representation of a resource. The following graphical representations are used for representing the attributes and child resources:

Square boxes are used for the resources;

Square boxes with round corners are used for attributes.

Child resources in a <resourceType> are detailed as shown in table 9.5-1.

The child resource table for an announce-able <resourceType> resource includes an additional column titled '<resourceTypeAnnc> Child Resource Types', indicating the type of announced resources. See the clause 9.6.26 for further details.

An announced resource may have child resources, and such child resources can be of type normal or announced. When a resource is announced, the associated child resources are announced independently of the original resource, as needed by the resource announcing CSE. The child resources at the announced resource are of the child resource Announced type.

When child resources at the announced resource are created locally by the remote CSE, the child resources are of normal child resource type.

# Table 9.5-1: Child Resources of <resourceType>

| Child Resources name | Child Resource Type | Multiplicity | Description | <resourceTypeAnnc> Child Resource Types |
| --- | --- | --- | --- | --- |
| <Fill in the name of Child Resource1 if a fixed name is required or [variable] if no fixed name is required> | <Fill in the type of Child Resource1> | <Fill in Multiplicity> | See clause <XRef> <clause> where the type of this child resource is described. | <Fill the child resource type for the announced resource. It can be none or <crTypeAnnc> or <crType>; where the <crType> is the child resource type of the original Child Resource1. |
| <Fill in the name of Child ResourceN if a fixed name is required or [variable] if no fixed name is required> | <Fill in the type of Child ResourceN> | <Fill in Multiplicity> | See clause <XRef> <clause> where the type of this child resource is described. | <Fill the child resource type for the announced resource. It can be none or <crTypeAnnc> or <crType>; where the <crType> is the child resource type of the original Child ResourceN. |

Attributes in a <resourceType> are detailed as shown in table 9.5-2

The attributes table for announce-able <resourceType> resource includes an additional column titled 'Attributes for <resourceTypeAnnc>', indicating the attributes that are to be announced for that <resourceType>. See the clause 9.6.26 for further details.

# Table 9.5-2: Attributes of <resourceType> resource

| Attributes name | Multiplicity | RW/ RO/ WO | Description | <resourceTypeAnnc> (MA/OA/NA) |
| --- | --- | --- | --- | --- |
| <Fill in name of Common Attribute1> | <Fill in Multiplicity> | <Fill in RW or RO or WO> | Provide description of this attribute - to be moved later to a common attribute clause. | <Fill in MA or OA or NA> |
| <Fill in name of Common AttributeN> | <Fill in Multiplicity> | <Fill in RW or RO or WO> | Provide description of this attribute - to be moved later to a common attribute clause. | <Fill in MA or OA or NA> |
| <Fill in name of Resource Specific Attribute1> | <Fill in Multiplicity> | <Fill in RW or RO or WO> | Provide description of this attribute - to be moved later to a central attribute table that also defines the type of the attribute, allowed ranges etc. | <Fill in MA or OA or NA> |
| <Fill in name of Resource-Specific AttributeN> | <Fill in Multiplicity> | <Fill in RW or RO or WO> | Provide description of this attribute - to be moved later to a central attribute table that also defines the type of the attribute, allowed ranges etc. | <Fill in MA or OA or NA> |

In case of misalignment of the graphical representation of a resource and the associated tabular representation, tabular representation shall take precedence.

The access modes for attributes can assume the following values:

Read/Write (RW): all operations are allowed for the attribute (Create/Update/Retrieve/Delete/Notify).

Read Only (RO): the value of the attribute is set by the hosting CSE when the resource is Created. Such an attribute can only be read.

Write Once (WO): the value of the attribute is set when the resource is Created based on information from the Originator. Such an attribute can then only be read.

The multiplicity, both for the child resources and the attributes can have the following values:

A value of "0" indicates that the child resource/attribute is not present.

A value of "1" indicates that the child resource/attribute is present.

A value of "0..1" indicates that the child resource/attribute could not be present. If present, it can have an instance of one only.

A value of "0..n" indicates that the child resource could not be present. If present, multiple instances are supported.

A value of "1..n" indicates that the child resource is always present. It has at least one instance and can have multiple instances.

An attribute multiplicity post-fixed with (L) indicates that it is a list of values.

The attributes for <resourceTypeAnnc> in the attribute table can have the following set of values:

MA (Mandatory Announced): Such attributes in the original resource are announced to the announced resources. The content of such announced attributes is the same as the content of the original resource.

OA (Optional Announced): Such attributes in the original resource may be announced to the announced resources depending on the contents of the announcedAttribute attribute at the original resource. The content of such announced attributes is of the same as the content of the original attributes.

NA (Not Announced): Such attributes are not announced to the announced resources.

### -----------------------End of change 1-------------------------------------------

### -----------------------Start of change 2-------------------------------------------

### 9.6.15	Resource Type mgmtObj

The <mgmtObj> resource contains management data which represents individual M2M management functions. It represents a general structure to map to external management technology e.g. OMA DM [i.5], BBF TR-069 [i.4] and LWM2M [i.6] data models. Each instance of <mgmtObj> resource shall be mapped to single external management technology.

Figure 9.6.15-1: Structure of <mgmtObj> resource

The <mgmtObj> resource shall contain the child resource specified in table 9.6.15-1.

# Table 9.6.15-1: Child resources of <mgmtObj> resource

| Child Resource name | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| variable | <subscription> | 0..n | See clause 9.6.8 |

The <mgmtObj> resource shall contain the attributes specified in table 9.6.15-2.

# Table 9.6.15-2: Attributes of <mgmtObj> resource

| Attributes name | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | WO | See clause 9.6.1 where this common attribute is described |
| resourceID | 1 | WO | See clause 9.6.1 where this common attribute is described. |
| parentID | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| expirationTime | 1 | RW | See clause 9.6.1 where this common attribute is described |
| accessControlPolicyIDs | 1 (L) | RW | See clause 9.6.1 where this common attribute is described |
| creationTime | 1 | RO | See clause 9.6.1 where this common attribute is described |
| lastModifiedTime | 1 | RO | See clause 9.6.1 where this common attribute is described |
| Labels | 0..1 | RO | See clause 9.6.1 where this common attribute is described |
| mgmtDefinition | 1 | WO | Specifies the type of <mgmtObj> resource e.g. software, firmware, memory. The list of the value of the attribute can be seen in Annex D. |
| objectIDs | 0..1 | WO | Contains the list URNs that uniquely identify the external management technology data models used for this <mgmtObj> resource as well as the managed function and version it represents. This attribute shall be provided during the creation of the <mgmtObj> resource and shall not be modifiable afterwards. If the <mgmtObj> resource is mapped to multiple external management technology data models, this attribute shall list all URNs for each mapped external management technology data model. This is mandatory for the <mgmtObj>, for which the data model is not specified by oneM2M but mapped from external management technology data model specified in other device management protocols. |
| objectPaths | 0..1 | WO | Contains the list of local paths of the external management object instances on the managed entity which is represented by the <mgmtObj> resource in the hosting CSE. This attribute shall be provided during the creation of the <mgmtObj>, so that the hosting CSE can correlate the created <mgmtObj> with the external management object instance on the managed entity for further management operations. It shall not be modifiable after creation. The format of this attribute shall be a local external management object path in the form as specified by existing management protocols. (e.g. "./anyPath/Fw1" in OMA DM [i.5], "Device.USBHosts.Host.3." in BBF TR-069 [i.4]). The combination of the objectPath and the objectID attribute, allows to address the external technology data models. |
| mgmtLink | 0..1 (L) | RW | This attribute contains reference to a list of other <mgmtObj> resources in case a hierarchy of <mgmtObj> is needed |
| [objectAttribute] | 0..1 (L) | RW | Each [objectAttribute] is mapped from a leaf node of a hierarchical structured management object (including oneM2M data model and the existing management data models) based on the mapping rules below the table. |
| Description | 0..1 | RW | Text format description of <mgmtObj>. |

When mapping resources from management technologies to a corresponding <mgmtObj> resource, the following rules shall apply:

- The root resource of external management objects maps to a specialization of the <mgmtObj> resource. Specializations of the <mgmtObj> resource are denoted in square brackets according to the conventions given in clause 9.5. The specializations of the <mgmtObj> resource are specified in Annex D.

- For the child resource of the root resource of specific technology:

- Rule1: If the child external management object cannot have another child external management object, the external management object maps to specializations of the [objectAttribute] attribute of the <mgmtObj> resource with the same resource name.

- Rule2: If the child external management object can have another child external management object, the external management object maps to a new <mgmtObj> resource.  The URI of the new <mgmtObj> resource is stored as an mgmtLink attribute of the <mgmtObj> resource which is mapped from the parent external management object.

### -----------------------End of change 2-------------------------------------------

### -----------------------Start of change 3-------------------------------------------

### 9.6.18	Resource Type node

The <node> resource represents specific information that provides properties of an M2M Node that can be utilized by other oneM2M operations. The <node> resource has specializations of the <mgmtObj> as its child resources.  These resources represent the Node's context information (e.g. memory and battery), network topology, device information, device capability etc. The <mgmtObj> resources are also resources to perform management of the Nodes.

This node specific information stored in these resources such as [memory] and [battery] can be obtained either by the existing device management technologies (OMA DM [i.5], BBF TR-069 [i.4]) or any other way (e.g. JNI [i.21]). Since <mgmtObj> resource type represents the management functions, their specializations represent sub-typesof the <mgmtObj> resource type.

For the case when the <node> resource belongs to an ADN, please see the description of nodeLink attribute in the <AE> resource (clause 9.6.5).

Figure 9.6.18-1: Structure of <node> resource

The <node> resource shall contain the child resources specified in table 9.6.18-1.

Table 9.6.18-1: Child resources of <node> resource

| Child Resource name | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| variable | <mgmtObj> as defined in the specialization [memory] | 0..1 | This resource provides the memory (typically RAM) information of the node. (e.g. the amount of total volatile memory), See clause D.4. |
| variable | <mgmtObj> as defined in the specialization [battery] | 0..n | The resource provides the power information of the node. (e.g. remaining battery charge). See clause D.7. |
| variable | <mgmtObj> with mgmtDefinition of as defined in the specialization value [areaNwkInfo] | 0..1 | This resource describes the list of Nodes attached behind the MN node and its physical or underlying relation among the nodes in the M2M Area Network. This attribute is defined in case the Node is MN. See clause D.5. |
| variable | <mgmtObj> as defined in the specialization [areaNwkDeviceInfo] | 0..n | This resource describes the information about the Node in the M2M Area Network. See clause D.6. |
| variable | <mgmtObj> as defined in the specialization [firmware] | 0..1 | This resource describes the information about the firmware of the Node include name, version etc, See clause D.2. |
| [variable] | <mgmtObj> as defined in the specialization [software] | 0..n | This resource describes the information about the software of the Node. See clause D.3. |
| variable | <mgmtObj> as defined in the specialization [deviceInfo] | 0..n | The resource contains information about the identity, manufacturer and model number of the device. See clause D.8. |
| variable | <mgmtObj> as defined in the specialization [deviceCapability] | 0..n | The resource contains information about the capability supported by the Node. See clause D.9. |
| variable | <mgmtObj> as defined in the specialization [reboot] | 0..1 | The resource is the place to reboot or reset the Node. See clause D.10. |
| variable | <mgmtObj> as defined in the specialization [eventLog] | 0..1 | The resource contains the information about the log of events of the Node. See clause D.11. |
| variable | <mgmtObj> as defined in the specialization [cmdhPolicy] | 0..n | The resource(s) contain(s) information about CMDH policies that are applicable to the CMDH processing on the CSE hosted on the node represented by this <ndoe> resource and identified by the hostedCSEID attribute of this <node> resource. . See clause D.12. |
| variable | <mgmtObj> as defined in the specialization [activeCmdhPolicy] | 0..1 | This resource defines which of the present [cmdhPolicy] resource(s) shall be active for the CMDH processing on the CSE hosted on the node represented by this <node> resource and identified by the hostedCSEID attribute of this <node> resource. See clause D.12. |
| variable | <subscription> | 0..n | See clause 9.6.8 |

The <node> resource shall contain the attributes specified in table 9.6.18-2.

# Table 9.6.18-2: Attributes of <node> resource

| Attribute name | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| resourceID | 1 | WO | See clause 9.6.1 where this common attribute is described. |
| parentID | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| expirationTime | 1 | RW | See clause 9.6.1 where this common attribute is described. |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1 where this common attribute is described. |
| creationTime | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| lastModifiedTime | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| Labels | 0..1 | RW | See clause 9.6.1 where this common attribute is described. |
| nodeID | 1 | RW | The M2M-Node-ID of the node which is represented by this <node> resource. |
| hostedCSEID | 0..1 | RW | The CSE-ID of the <CSEBase> resource or the <remoteCSE> resource that is hosted on the node represented this <node> resource. |

### -----------------------End of change 3-------------------------------------------

### -----------------------Start of change 4-------------------------------------------

# Annex D (normative):
<mgmtObj> Resource Specializations Description

# D.1	oneM2M Management Functions

This clause describes the management functions supported by oneM2M. These functions are fulfilled by defining specializations of <mgmtObj> resources. These specializations can be regarded  as “sub-types”of the <mgmtObj> resource type with specific designing to support different management capabilities through operations defined by oneM2M. These specializations are service layer information models for the purpose of management. They can be used within the M2M service layer or they can be further mapped to existing management technologies such as OMA DM [i.5], OMA LWM2M [i.6] and BBF TR-069 [i.4] to enable the management of devices with OMA or BBF compliant management clients.

NOTE:	The resources defined in this Annex D represent specializations of the <mgmtObj> resource. The mgmtDefinition attribute carries the name of the resource type specialization. The names of instantiations of these resource specializations are not fixed.

### -----------------------End of change 4-------------------------------------------