| CHANGE REQUEST |
| --- |
| Group Name:* | WG2 |
| Source:* | Seongyoon Kim, LG Electronics, seongyoon.kim@lge.com Shelby Kiewel (skiewel@iconectiv.com) |
| Format:* | ARC |
| Date:* | 2014-09-15 |
| Contact:* | Seongyoon Kim, LG Electronics, seongyoon.kim@lge.com |
| Reason for Change/s:* | To clean up AE-ID and App-ID |
| CR against: Release* | Pre-release |
| CR against: TS/TR* | TS-0001 v0.8.0 |
| Clauses/Sub Clauses* | 7.1.14, 7.1.3, 7.1.2, 7.2 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or (missing) functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

- Make App-ID unique

In ARC specification, App-ID is specified as just a string and it doesn’t guarantee any uniqueness. However, the usages of App-ID are CMDH(applying the same policy to the same App) and statistics(used for billing mainly). So this document suggests App-ID to be unique within oneM2M domain.

## -----------------------Start of change 1-------------------------------------------

### 7.1.3	Application Identifier (App-ID)

There are two types of App-ID: registration authority defined App-ID (registered App-ID) and non-registered App-ID. The establishment of the registered App-ID is guaranteed to be globally unique; the non-registered App-ID is not guaranteed to be globally unique. The detail format is described in clause 7.2.

## -----------------------End of change 1-------------------------------------------

## -----------------------Start of change 2-------------------------------------------

## 7.2	M2M-SP-ID, CSE-ID, App-ID and AE-ID and resource Identifier formats

As a general rule, the identifiers of AEs, CSEs and resources are globally unique. In order to optimize their use, the identifiers shall be shortened when their scope can be derived from their context of use by the CSEs and the AEs.  Such shortened identifiers are defined as 'relative' identifiers.

TheM2M system shall use the identifiers M2M-SP-ID, CSE-ID, App-ID and AE-ID and resource identifiers according to the formats and the rules specified in the following table (table 7.2-1).

Table 7.2-1: Identifiers formats and use

|  | Format Name | Format | Rule of use |
| --- | --- | --- | --- |
| M2M-SP-ID format |  | Fully qualified domain name Examples: <scheme>://www.m2mprovider.com <scheme>://globalm2m.org Note: the <scheme> part, as stated in clause 7.1, is unique and protocol-independent | When The M2M-SP-ID is used, the FQDN format applies |
| AE-ID EQUIVALENT formats | CSE-relative-AE-ID (with respect to the context of the CSE hosting the AE) | The CSE-relative AE Identifier is a sequence of characters that may include any of the unreserved characters defined in the clause 2.3 of the RFC3986 [i.x], as well as the slash character. It shall not start with the slash character. The CSE-relative AE Identifier is unique within the context of the CSE. | On the Mca reference point: to refer to AEs that are hosted by the directly attached (Registrar) CSE. The hosting CSE is responsible for guaranteeing that the CSE-Relative-AE-ID is unique in the context of the hosting CSE. |
|  | SP-relative -AE-ID (with respect to the context of the SP hosting the AE) | /[CSE-ID]/CSE-relative-AE-ID It begins with a slash character, as specified in clause 4.2 of RFC3986 [i.12] under “absolute-path reference”. | On the Mca and Mcc reference points: to refer to AEs that are hosted by the M2M Service Provider domain to which AE is attached. |
|  | Absolute AE-ID | M2M-SP-ID/SP-relative-AE-ID The absolute AE-ID shall conform to the URI format as defined in the IETF RFC 3986 [i.12]. | On the Mca and Mcc reference points: to refer to AEs that are hosted by a different M2M Service Provider domain with respect to the one to which the AE is attached and on the Mcc’ reference point for all the AEs |
| CSE-ID EQUIVALENT formats | SP-relative-CSE-ID (with respect to the context of the SP hosting the CSE) | M2M-SP-ID/SP-relative-AE-ID The absolute AE-ID shall conform to the URI format as defined in the IETF RFC 3986 [i.12]. | On the Mca and Mcc reference points: to refer to CSEs that are hosted by the same M2M Service Provider domain |
|  | Absolute CSE-ID | M2M-SP-ID/SP-relative-CSE-ID | On Mca and Mcc reference points: to refer to CSEs that are hosted by different M2M Service Provider domains and on the Mcc’ reference point for all the CSEs |
| Resource identifier equivalent formats | CSE-relative Resource ID | The CSE-relative Resource Identifier is a sequence of characters that may include any of the unreserved characters defined in the clause 2.3 of the RFC3986 [i.12], as well as the slash character. It shall not start with the slash character. The CSE-relative Resource Identifier is unique in the context of the CSE. Examples: container123 containers/c123 a1b2c3d4b0b00f0fa66a123456789abc a1b2c3d4-b0b0-0f0f-a66a-123456789abc cont/ b0b0-0f0f-a66a-123456789abc |  |
|  | SP-relative Resource ID (with respect to the context of the M2M Service Provider hosting the CSE) | The SP-relative Resource identifier is an absolute-path relative reference (beginning with a single slash), as defined in clause 4.2 of RFC3986 [i.12]. The SP-relative Resource Identifier is unique in the context of the Service Provider. | On the Mca and Mcc reference points: to refer to resources that are hosted by the same M2M Service Provider domain |
|  | Absolute Resource ID | M2M-SP-ID/SP-relative-Resource-ID | On Mca and Mcc reference points: to refer to resources that are hosted by a different M2M Service Provider domain and on the Mcc’ reference point for all the resources |
| App-ID format | App-ID | Either “R[authority-ID]/[registered-App-ID]” or “N[non-registered-App-ID]” If the first letter is “R”, then authority-ID and registered-App-ID are assigned by the registration authority. The registered-App-ID is managed by the owner of authority-ID. If the first letter is “N”, then non-registered-App-ID is not registred by the registration autority. | AE Registration Procedure described in clause 10.1.1.2.2. |

NOTE: This table still needs to be further fixed and be given more examples.

## -----------------------End of change 2-------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?