| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG2 |
| Title:* | TS-0001 addressing resources hosted on remote CSEs |
| Source:* | InterDigital |
| Contact: | Guang.Lu@InterDigital.com, Dale.Seed@InterDigital.com |
| Date:* | 2014-09-15 |
| Abstract:* |  |
| Agenda Item:* |  |
| Work item(s): | TS-0001 WI |
| Document(s) Impacted* | TS-0001 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | If agreed, update TS for inclusion |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Rationale

This contribution clarifies how an AE can address resources that are hosted on a remote CSE such that its local CSE is able to re-target the request to the remote CSE.  These details are currently missing from TS-0001

### -----------------------Start of change 1-------------------------------------------

## 9.3.3 Addressing Resources Hosted by Remote CSEs

When addressing a resource hosted on a remote CSE, an originator shall construct a URI which targets its  registrar CSE and which also includes the CSE-ID of  the remote CSE hosting the targeted resource.  For example, an AE can send a request with the following URI to its registrar CSE (i.e. CSE1) in order to target a resource hosted on a remote CSE (i.e. CSE2).

URI = scheme:/fullyqualifieddomainnameofCSE1/CSE-ID2/path/to/remote/resource; or

URI = scheme://<ip-address of CSE1>:<port of CSE1>/CSE-ID2/path/to/remote/resource.

When CSE1 receives a request it can parse this URI and detect that a local resource is not being targeted.  It can then check whether CSE-ID2 matches any of the CSE-ID attributes within the remoteCSE resources it hosts.  If a match is found, CSE1 can re-target the request to the corresponding CSE using the CSE-ID and pointOfContact information of the matching remoteCSE resource.  For example, CSE1 can re-target the request to the following URI.

URI = scheme:/fullyqualifieddomainnameofCSE2/CSE-ID2/path/to/remote/resource; or

URI = scheme://<ip-address of CSE2>:<port of CSE2>/ CSE-ID2/path/to/remote/resource.

### -----------------------End of change 2-------------------------------------------