| oneM2M Technical Specification |
| --- |
| Document Number | TS-0007 -V0.7.0 |
| Document Name: | Service Components |
| Date: | 2014-December-18 |
| Abstract: | This document specifies the M2M Services provided by the M2M Services Platform, the integration and interworking of the M2M Services functional architecture of the oneM2M Services Platform and informatively illustrates the use of the M2M Services within the context of complex business services. |

This Specification is provided for future development work within oneM2M only. The Partners accept no liability for any use of this Specification.

The present document has not been subject to any approval process by the oneM2M Partners Type 1. Published oneM2M specifications and reports for implementation should be obtained via the oneM2M Partners' Publications Offices.

About oneM2M

The purpose and goal of oneM2M is to develop technical specifications which address the need for a common M2M Service Layer that can be readily embedded within various hardware and software, and relied upon to connect the myriad of devices in the field with M2M application servers worldwide.

More information about oneM2M may be found at: http//www.oneM2M.org

Copyright Notification

No part of this document may be reproduced, in an electronic retrieval system or otherwise, except as authorized by written permission.

The copyright and the foregoing restriction extend to reproduction in all media.

© 2014, oneM2M Partners Type 1 (ARIB, ATIS, CCSA, ETSI, TIA, TTA, TTC).

All rights reserved.

Notice of Disclaimer & Limitation of Liability

The information provided in this document is directed solely to professionals who have the appropriate degree of experience to understand and interpret its contents in accordance with generally accepted engineering or other professional standards and applicable regulations. No recommendation as to products or vendors is made or should be implied.

NO REPRESENTATION OR WARRANTY IS MADE THAT THE INFORMATION IS TECHNICALLY ACCURATE OR SUFFICIENT OR CONFORMS TO ANY STATUTE, GOVERNMENTAL RULE OR REGULATION, AND FURTHER, NO REPRESENTATION OR WARRANTY IS MADE OF MERCHANTABILITY OR FITNESS FOR ANY PARTICULAR PURPOSE OR AGAINST INFRINGEMENT OF INTELLECTUAL PROPERTY RIGHTS. NO oneM2M PARTNER TYPE 1 SHALL BE LIABLE, BEYOND THE AMOUNT OF ANY SUM RECEIVED IN PAYMENT BY THAT PARTNER FOR THIS DOCUMENT, WITH RESPECT TO ANY CLAIM, AND IN NO EVENT SHALL oneM2M BE LIABLE FOR LOST PROFITS OR OTHER INCIDENTAL OR CONSEQUENTIAL DAMAGES. oneM2M EXPRESSLY ADVISES ANY AND ALL USE OF OR RELIANCE UPON THIS INFORMATION PROVIDED IN THIS DOCUMENT IS AT THE RISK OF THE USER.

# Contents

Contents	1

6.4	Data Exchange	6

6.4.1	Overview	6

6.4.1.1	Subscribe-Publish-Notify Data Exchange	6

6.4.1.1.1	Supporting Rules	6

6.4.1.2	Request-Response Data Exchange	7

6.4.1.2.1	Supporting Rules	7

6.4.2	Service Capabilities	7

6.4.2.1	subscribe	7

6.4.2.1.1	Pre-conditions	7

6.4.2.1.2	Signature - subscribe	7

6.4.2.1.3	Service Interactions	8

6.4.2.1.4	Post-Conditions	9

6.4.2.1.5	Exceptions	9

6.4.2.1.6	Policies for Use	9

6.4.2.1.7	oneM2M Resource Interworking	9

6.4.2.2	publish	10

6.4.2.2.1	Pre-conditions	10

6.4.2.2.2	Signature – publish	10

6.4.2.2.3	Service Interactions	10

6.4.2.2.4	Post-Conditions	11

6.4.2.2.5	Exceptions	11

6.4.2.2.6	Policies for Use	11

6.4.2.2.7	oneM2M Resource Interworking	11

6.4.2.3	notify	12

6.4.2.3.1	Pre-conditions	12

6.4.2.3.2	Signature – notify	12

6.4.2.3.3	Post-Conditions	12

6.4.2.3.4	Exceptions	12

6.4.2.3.5	Policies for Use	12

6.4.2.3.6	oneM2M Resource Interworking	12

6.4.2.4	sendMessage	13

6.4.2.4.1	Pre-conditions	13

6.4.2.4.2	Signature – sendMessage	13

6.4.2.4.3	Service Interactions	13

6.4.2.4.4	Post-Conditions	14

6.4.2.4.5	Exceptions	14

6.4.2.4.6	Policies for Use	14

6.4.2.4.7	oneM2M Resource Interworking	14

6.2	Service Subscription	15

6.2.2	Service Capabilities	15

6.2.2.6	associateAEWithServiceSubscription	15

6.2.2.6.1	Pre-conditions	15

6.2.2.6.2	Signature – associateAEWithServiceSubscription	15

6.2.2.6.3	Service Interactions	15

6.2.2.6.4	Post-Conditions	16

6.2.2.6.5	Exceptions	16

6.2.2.6.6	Policies for Use	16

6.2.2.6.7	oneM2M Resource Interworking	16

6.2.2.7	disassociateAEFromServiceSubscription	17

6.2.2.7.1	Pre-conditions	17

6.2.2.7.2	Signature – disassociateAEFromServiceSubscription	17

6.2.2.7.3	Service Interactions	17

6.2.2.7.4	Post-Conditions	17

6.2.2.7.5	Exceptions	17

6.2.2.7.6	Policies for Use	17

6.2.2.7.7	oneM2M Resource Interworking	18

6.2.2.8	refreshAEAssociationWithServiceSubscription	19

6.2.2.8.1	Pre-conditions	19

6.2.2.8.2	Signature – refreshAEAssociationWithServiceSubscription	19

6.2.2.8.3	Service Interactions	19

6.2.2.8.4	Post-Conditions	19

6.2.2.8.5	Exceptions	19

6.2.2.8.6	Policies for Use	19

6.2.2.8.7	oneM2M Resource Interworking	20

6.9	Service Subscription Administration	21

6.9.1	Overview	21

6.9.1.1	Service Subscription Entity	21

6.9.1.1.1	Service Subscription Filter Criteria	21

6.9.1.2	M2M Node Entity for Service Subscription	21

6.9.1.2.1	M2M Node Filter Criteria	22

6.9.1.3	Application Rule	22

6.9.1.3.1	Application Rule Filter Criteria	23

6.9.2	Service Capabilities	23

6.9.2.1	createServiceSubscription	23

6.9.2.1.1	Pre-conditions	23

6.9.2.1.2	Signature – createServiceSubscription	23

6.9.2.1.3	Service Interactions	23

6.9.2.1.4	Post-Conditions	24

6.9.2.1.5	Exceptions	24

6.9.2.1.6	Policies for Use	24

6.9.2.1.7	oneM2M Resource Interworking	24

6.9.2.2	deleteServiceSubscription	25

6.9.2.2.1	Pre-conditions	25

6.9.2.2.2	Signature – deleteServiceSubscription	25

6.9.2.2.3	Service Interactions	25

6.9.2.2.4	Post-Conditions	25

6.9.2.2.5	Exceptions	25

6.9.2.2.6	Policies for Use	25

6.9.2.2.7	oneM2M Resource Interworking	26

6.9.2.3	updateServiceSubscription	27

6.9.2.3.1	Pre-conditions	27

6.9.2.3.2	Signature – updateServiceSubscription	27

6.9.2.3.3	Service Interactions	27

6.9.2.3.4	Post-Conditions	27

6.9.2.3.5	Exceptions	27

6.9.2.3.6	Policies for Use	27

6.9.2.3.7	oneM2M Resource Interworking	28

6.9.2.4	addRoleToServiceSubscription	29

6.9.2.4.1	Pre-conditions	29

6.9.2.4.2	Signature – addRoleToServiceSubscription	29

6.9.2.4.3	Service Interactions	29

6.9.2.4.4	Post-Conditions	29

6.9.2.4.5	Exceptions	29

6.9.2.4.6	Policies for Use	29

6.9.2.4.7	oneM2M Resource Interworking	30

6.9.2.5	deleteRoleFromServiceSubscription	31

6.9.2.5.1	Pre-conditions	31

6.9.2.5.2	Signature – deleteRoleFromServiceSubscription	31

6.9.2.5.3	Service Interactions	31

6.9.2.5.4	Post-Conditions	31

6.9.2.5.5	Exceptions	31

6.9.2.5.6	Policies for Use	31

6.9.2.5.7	oneM2M Resource Interworking	31

6.9.2.6	getServiceSubscription	32

6.9.2.6.1	Pre-conditions	32

6.9.2.6.2	Signature – getServiceSubscription	32

6.9.2.6.3	Service Interactions	32

6.9.2.6.4	Post-Conditions	32

6.9.2.6.5	Exceptions	32

6.9.2.6.6	Policies for Use	32

6.9.2.6.7	oneM2M Resource Interworking	33

6.9.2.7	addNodeToServiceSubscription	34

6.9.2.7.1	Pre-conditions	34

6.9.2.7.2	Signature – addNodeToServiceSubscription	34

6.9.2.7.3	Service Interactions	34

6.9.2.7.4	Post-Conditions	34

6.9.2.7.5	Exceptions	34

6.9.2.7.6	Policies for Use	34

6.9.2.7.7	oneM2M Resource Interworking	35

6.9.2.8	deleteNodesFromServiceSubscription	36

6.9.2.8.1	Pre-conditions	36

6.9.2.8.2	Signature – deleteNodesFromServiceSubscription	36

6.9.2.8.3	Service Interactions	36

6.9.2.8.4	Post-Conditions	36

6.9.2.8.5	Exceptions	36

6.9.2.8.6	Policies for Use	36

6.9.2.8.7	oneM2M Resource Interworking	37

6.9.2.9	getNodesForServiceSubscription	38

6.9.2.9.1	Pre-conditions	38

6.9.2.9.2	Signature – getNodesForServiceSubscription	38

6.9.2.9.3	Service Interactions	38

6.9.2.9.4	Post-Conditions	38

6.9.2.9.5	Exceptions	38

6.9.2.9.6	Policies for Use	38

6.9.2.9.7	oneM2M Resource Interworking	39

6.9.2.10	createApplicationRule	40

6.9.2.10.1	Pre-conditions	40

6.9.2.10.2	Signature – createApplicationRule	40

6.9.2.10.3	Service Interactions	40

6.9.2.10.4	Post-Conditions	41

6.9.2.10.5	Exceptions	41

6.9.2.10.6	Policies for Use	41

6.9.2.10.7	oneM2M Resource Interworking	41

6.9.2.11	deleteApplicationRules	42

6.9.2.11.1	Pre-conditions	42

6.9.2.11.2	Signature – deleteApplicationRules	42

6.9.2.11.3	Service Interactions	42

6.9.2.11.4	Post-Conditions	42

6.9.2.11.5	Exceptions	42

6.9.2.11.6	Policies for Use	42

6.9.2.11.7	oneM2M Resource Interworking	43

6.9.2.12	getApplicationRules	44

6.9.2.12.1	Pre-conditions	44

6.9.2.12.2	Signature – getApplicationRules	44

6.9.2.12.3	Service Interactions	44

6.9.2.12.4	Post-Conditions	44

6.9.2.12.5	Exceptions	44

6.9.2.12.6	Policies for Use	44

6.9.2.12.7	oneM2M Resource Interworking	45

6.9.2.13	updateNodeForServiceSubscription	46

6.9.2.13.1	Pre-conditions	46

6.9.2.13.2	updateNodeForServiceSubscription	46

6.9.2.13.3	Service Interactions	46

6.9.2.13.4	Post-Conditions	46

6.9.2.13.5	Exceptions	46

6.9.2.13.6	Policies for Use	46

6.9.2.13.7	oneM2M Resource Interworking	47

6.9.2.14	updateApplicationRule	48

6.9.2.14.1	Pre-conditions	48

6.9.2.14.2	Signature – updateApplicationRule	48

6.9.2.14.3	Service Interactions	48

6.9.2.14.4	Post-Conditions	49

6.9.2.14.5	Exceptions	49

6.9.2.14.6	Policies for Use	49

6.9.2.14.7	oneM2M Resource Interworking	49

6.11	Registration	50

6.11.1	Overview	50

6.11.2	Service Capabilities	50

6.11.2.1	registerAE	50

6.11.2.1.1	Pre-conditions	50

6.11.2.1.2	Signature – registerAE	50

6.11.2.1.3	Services Interaction	50

6.11.2.1.4	Post-Conditions	51

6.11.2.1.5	Exceptions	51

6.11.2.1.6	Policies for Use	51

6.11.2.1.7	oneM2M Resource Interworking	51

6.11.2.2	refreshAERegistration	52

6.11.2.2.1	Pre-conditions	52

6.11.2.2.2	Signature – refreshAERegistration	52

6.11.2.2.3	Service Interactions	52

6.11.2.2.4	Post-Conditions	53

6.11.2.2.5	Exceptions	53

6.11.2.2.6	Policies for Use	53

6.11.2.2.7	oneM2M Resource Interworking	53

6.11.2.3	deregisterAE	54

6.11.2.3.1	Pre-conditions	54

6.11.2.3.2	Signature – deregisterAE	54

6.11.2.3.3	Service Interactions	54

6.11.2.3.4	Post-Conditions	55

6.11.2.3.5	Exceptions	55

6.11.2.3.6	oneM2M Resource Interworking	55

6.12	Registration Administration	56

6.12.1	Overview	56

6.12.2	Service Capabilities	56

6.12.2.1	getRegistrationStatus	56

6.12.2.1.1	Pre-conditions	56

6.12.2.1.2	Signature – getRegistrationStatus	56

6.12.2.1.3	Service Interaction	56

6.12.2.1.4	Post-Conditions	57

6.12.2.1.5	Exceptions	57

6.12.2.1.6	Policies for Use	57

6.12.2.1.7	oneM2M Resource Interworking	57

6.12.2.2	revokeAERegistration	58

6.12.2.2.1	Pre-conditions	58

6.12.2.2.2	Signature – revokeAERegistration	58

6.12.2.2.3	Service Interaction	58

6.12.2.2.4	Post-Conditions	58

6.12.2.2.5	Exceptions	58

6.12.2.2.6	Policies for Use	58

6.12.2.2.7	oneM2M Resource Interworking	59

6.12.2.3	subscribeInitialAERegistrationEvent	60

6.12.2.3.1	Pre-conditions	60

6.12.2.3.2	Signature – subscribeInitialAERegistrationEvent	60

6.12.2.3.3	Service Interaction	60

6.12.2.3.4	Post-Conditions	60

6.12.2.3.5	Exceptions	60

6.12.2.3.6	Policies for Use	60

6.12.2.3.7	oneM2M Resource Interworking	61

6.12.2.4	unsubscribeInitialAERegistrationEvent	62

6.12.2.4.1	Pre-conditions	62

6.12.2.4.2	Signature – unsubcribeInitialAERegistrationEvent	62

6.12.2.4.3	Service Interaction	62

6.12.2.4.4	Post-Conditions	62

6.12.2.4.5	Exceptions	62

6.12.2.4.6	Policies for Use	62

6.12.2.4.7	oneM2M Resource Interworking	63

Annex F (Informative): Registration Services	64

F.1	Overview	64

F.2	Mca Registration Service Processing and Supporting Services	64

F.2.1	Message Exchanges	64

F.2.1.2	Service Capabilities	64

F.2.1.2.1	registerAE	64

F.2.1.2.2	refreshAERegistration	66

F.2.1.2.3	deregisterAE	68

## 6.4	Data Exchange

### 6.4.1	Overview

The Data Exchange service provides the ability to exchange payloads between AEs across the Mca Reference Point using supported data exchange patterns. This service utilizes an underlying transport adapter to provide the transportation functions.

The supported data exchange patterns are:

Subscribe-Publish-Notify

Request-Response

#### 6.4.1.1	Subscribe-Publish-Notify Data Exchange

This data exchange pattern permits AEs to subscribe to publication resources. When an AE publishes data to a specific publication resource, the AEs that have subscribed to the publication resource are notified of the publication by receiving the published data.

##### 6.4.1.1.1	Supporting Rules

A publication resource is an entity that represents the mechanism used by underlying publish and subscribe protocols which represent one or more queues in the underlying protocol. A publication resource in the data exchange service provides capabilities to reference one or more queues in the underlying protocol using a tree mechanism where wildcards are placed to represent all elements of the tree branch or leaf.

###### 6.4.1.1.1.1	Publication Resources

When a AE publishes a payload to a publication resource, the publication resource is evaluated to obtain the leaf node of the tree. The AEs that have subscribed to leaf nodes of the tree receive the message via the notify M2M Service Capability.

###### 6.4.1.1.1.2	Delivery Policy

As part of the notify M2M Service Capability the Service Layer attempts to honor the delivery policy of the subscriber and publisher. The delivery policy is the attempt by the Service Layer to provide a reliable delivery of the payload that was published using the mechanisms of the underlying Broker. The reliable delivery of a payload is defined in the deliveryPolicy type.

| Attribute | Description |
| --- | --- |
| retryLimit | The number of retries by the Broker to connected subscribers before assuming failure of the notification. |

Table 6.4.1.1.1..2-1 Type: deliveryPolicy

###### 6.4.1.1.1.3	Message Retainment Policy

When a message is published, the M2M Service Layer, using the resources of the underlying Broker, attempts to retain messages according to a retainment policy. Retainment of messages permits AEs that are subscribed to the publication resource but not connected to the underlying Broker to receive messages, up to the retainLimit once the AE connects to the Broker. The message retainment policy is defined in the retainmentPolicy type.

| Attribute | Description |
| --- | --- |
| retainLimit | The maximum number of messages retained by the Broker for a subscriber that is not connected to the underlying Broker. |

Table 6.4.1.1.1..3-1 Type: retainmentPolicy

###### 6.4.1.1.1.4	Service Subscription Integration

In order for the Data Exchange Service to take advantage of the underlying transport, there shall be an association between the AE Resource and the identifier of the underlying transport within the context of the M2M Service Subscription.

#### 6.4.1.2	Request-Response Data Exchange

This data exchange pattern permits AEs to synchronously send messages to other AEs utilizing the underlying transport.

##### 6.4.1.2.1	Supporting Rules

Messages are sent to from an AE to another AE via the Service Layer. When sending a message the originating AE can provide a delivery policy to be used by the transport adapter when sending the message to the target AE.

###### 6.4.1.1.2.2	Delivery Policy

As part of the message sending capability the Service Layer attempts to honor the delivery policy of the message Originator. The delivery policy is the attempt by the Service Layer to provide a reliable delivery of the payload that was sent using the mechanisms of the transport adapter. The reliable delivery of a payload is defined in the deliveryPolicy type.

| Attribute | Description |
| --- | --- |
| retryLimit | The number of retries by the transport adapter to target AEs before assuming failure of the notification. |

Table 6.4.1.1.2.2-1 Type: deliveryPolicy

###### 6.4.1.1.2.3	Service Subscription Integration

In order for the Data Exchange Service to take advantage of the underlying transport, there shall be an association between the target AE and the identifier of the underlying transport within the context of the M2M Service Subscription.

### 6.4.2	Service Capabilities

#### 6.4.2.1	subscribe

This service capability provides the ability for AEs to subscribe to receive payloads based on a publication resource.

As part of the subscription, the subscribing AE can provide delivery and retainment policies to enhance the robustness of the notification to AEs that have subscribed to the publication resource identified in the request.

##### 6.4.2.1.1	Pre-conditions

The pre-conditions for Mca Received Requests are met.

A correlation between a M2M Service Subscription, publication resource, subscribing AE and Broker exist.

##### 6.4.2.1.2	Signature - subscribe

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| publicationResource | IN | NO | The publication resource. See 6.4.1.1.1.1 |
| deliveryPolicy | IN | YES | The delivery policy when notifying the subscriber. See 6.4.1.1.1.2 |
| retainmentPolicy | IN | YES | The retainment policy for unconnected subscribers. See 6.4.1.1.1.3 |
| responseType | OUT | YES | Unique response types for this service. Note: Consumed services also provide response types. Exception: Request may not have been completed |

Table 6.4.2.1.2-1 Data Exchange Service – subscribe capability

##### 6.4.2.1.3	Service Interactions

The interactions of service capabilities required for this service capability:

- Issue the subscribe request to the Supporting Service to validate the request and obtain the Broker instance for the subscription request.

- Issue the request to the broker to subscribe the AE-ID for the publication resource

- Issue the subscribe complete subscription request to the Supporting Service

Figure 6.4.2.1.3-1 Data Exchange Service – subscribe capability

##### 6.4.2.1.4	Post-Conditions

Not Applicable

##### 6.4.2.1.5	Exceptions

Not Applicable

##### 6.4.2.1.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.4.2.1.7	oneM2M Resource Interworking

This service capability interworks with the following oneM2M Resource operations that are interworked are:

Not Applicable

#### 6.4.2.2	publish

This service capability provides the ability for AEs to publish payloads to a leaf node of a publication resource.

As part of the publication, the publishing AE can provide a delivery policy to enhance the robustness of the publication to AEs that have subscribed to the Resource identified in the request.

##### 6.4.2.2.1	Pre-conditions

The pre-conditions for Mca Received Requests are met.

A correlation between a M2M Service Subscription, resource to publish the payload, publishing AE and Broker exist.

##### 6.4.2.2.2	Signature – publish

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| toResource | IN | NO | The leaf node of a publication resource. See 6.4.1.1.1.1 |
| deliveryPolicy | IN | YES | The delivery policy when notifying the subscriber. See 6.4.1.1.1.2 |
| payload | IN | NO | The payload to published. |
| responseType | OUT | YES | Unique response types for this service. Note: Consumed services also provide response types. Exception: Request may not have been completed |

Table 6.4.2.2.2-1 Data Exchange Service – publish capability

##### 6.4.2.2.3	Service Interactions

The interactions of service capabilities required for this service capability:

- Issue the publish request to the Supporting Service to validate the request

- Issue the request to the broker to publish the payload from the publishing AE to the resource in the request

- Issue the complete publication request to the Supporting Service

Figure 6.4.2.2.3-1 Data Exchange Service –publish (In-Out) capability

##### 6.4.2.2.4	Post-Conditions

Not Applicable

##### 6.4.2.2.5	Exceptions

Not Applicable

##### 6.4.2.2.6	Policies for Use

Message Exchange Patterns: In-Out, In-Only

The In-Only message exchange pattern would return a transport layer acknowledgement if supported by the underlying transport layer protocol. Response types or Exceptions are not returned in this message exchange pattern.

Transaction Pattern: Participation allowed

##### 6.4.2.2.7	oneM2M Resource Interworking

This service capability interworks with the following oneM2M Resource operations that are interworked are:

Not Applicable

#### 6.4.2.3	notify

This service capability provides the ability to notify AEs that have subscribed to the publication resource identified in a publish request.

##### 6.4.2.3.1	Pre-conditions

A correlation between a M2M Service Subscription, subscribed AE, publication resource and Broker exist.

##### 6.4.2.3.2	Signature – notify

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| fromResource | IN | NO | The leaf node of a publication resource. See 6.4.1.1.1.1 |
| deliveryPolicy | IN | YES | The delivery policy when notifying the subscriber. See 6.4.1.1.1.2 |
| payload | IN | NO | The Payload of the message to notify to the AE |
| responseType | OUT | YES | Unique response types for this service. Note: Consumed services also provide response types. Exception: Request may not have been completed |

Table 6.4.2.3.2-1 Data Exchange Service – notify capability

##### 6.4.2.3.3	Post-Conditions

Not Applicable

##### 6.4.2.3.4	Exceptions

Not Applicable

##### 6.4.2.3.5	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.4.2.3.6	oneM2M Resource Interworking

This service capability interworks with the following oneM2M Resource operations that are interworked are:

Not Applicable

#### 6.4.2.4	sendMessage

This service capability provides the ability for AEs to send messages to a target AE.

As part of the message send request, the originating AE can provide a delivery policy to enhance the robustness of the message to the AE.

##### 6.4.2.4.1	Pre-conditions

The pre-conditions for Mca Received Requests are met.

A correlation between a M2M Service Subscription, Originating AE and Transport Adapter exist.

##### 6.4.2.4.2	Signature – sendMessage

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| deliveryPolicy | IN | YES | The delivery policy when sending to the target AE. See 6.4.1.1.2.2 |
| payload | IN | NO | The payload to be sent. |
| responseType | OUT | YES | Unique response types for this service. Note: Consumed services also provide response types. Exception: Request may not have been completed |

Table 6.4.2.4.2-1 Data Exchange Service – sendMessage capability

##### 6.4.2.4.3	Service Interactions

The interactions of service capabilities required for this service capability:

- Issue the sendMessage request to the Supporting Service to validate the request

- Issue the request to the transport adapter (in this case the Broker service) to send the payload from the Originator to the target AE.

- Issue the complete sendMessage request to the Supporting Service

Figure 6.4.2.4.3-1 Data Exchange Service –sendMessage capability

##### 6.4.2.4.4	Post-Conditions

Not Applicable

##### 6.4.2.4.5	Exceptions

Not Applicable

##### 6.4.2.4.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.4.2.4.7	oneM2M Resource Interworking

Not Applicable

## 6.2	Service Subscription

### 6.2.2	Service Capabilities

#### 6.2.2.6	associateAEWithServiceSubscription

This service capability provides the ability to associate an AE with a M2M Service Subscription. This service capability shall be restricted to the Msc Reference Point.

##### 6.2.2.6.1	Pre-conditions

One of the following combinations has to be unique within the M2M System for the AE to be associated with an M2M Service Subscription:

Identifier of Application Entity (AE-ID) or

Identifier of the M2M Application (App-ID) and the credential identifier for the M2M Application.

The M2M System is pre-provisioned with the Application Rule (clause 6.9.1.3) that includes one of the above combinations in order for a M2M Service Subscription to the returned.

##### 6.2.2.6.2	Signature – associateAEWithServiceSubscription

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| aeId | IN | NO | The Application Entity Identifier (AE-ID). |
| credentialId | IN | YES | The Application Credential Identifier |
| applicationId | IN | YES | The Application Identifier (App-ID) |
| serviceSubscriptionId | OUT | NO | The M2M Service Subscription Identifier (M2M-Service-Profile-ID) |
| responseType | OUT | YES | Unique response types for this service. M2M Service Subscription does not exist. Application Entity Identifier is not unique within the context of the M2M System. |

Table 6.2.2.6.2-1 Service Subscription – associateAEWithServiceSubscription capability

##### 6.2.2.6.3	Service Interactions

The interactions of service capabilities required for this service capability:

- Issue this capability

Figure 6.2.2.6.3-1 Service Subscription – associateAEWithServiceSubscription Diagram

##### 6.2.2.6.4	Post-Conditions

The Application Entity Identifier (AE-ID) provided as the input parameter is associated with the M2M Service Subscription.

##### 6.2.2.6.5	Exceptions

Not Applicable

##### 6.2.2.6.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.2.2.6.7	oneM2M Resource Interworking

This service capability associates the AE-ID with the M2M Service Subscription Profile. Currently TS-0001 [2] does not define how an AE is associated with a M2M Service Subscription Profile as part of a registration flow.

#### 6.2.2.7	disassociateAEFromServiceSubscription

This service capability provides the ability to remove the association of  an AE from a M2M Service Subscription. This service capability shall be restricted to the Msc Reference Point.

##### 6.2.2.7.1	Pre-conditions

An AE has successfylly registered with the M2M system

##### 6.2.2.7.2	Signature – disassociateAEFromServiceSubscription

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| aeId | IN | NO | The Application Entity Identifier (AE-ID). |
| serviceSubscriptionId | IN | NO | The M2M Service Subscription Identifier (M2M-Service-Profile-ID) |
| responseType | OUT | YES | Unique response types for this service. M2M Service Subscription does not exist. Application Entity Identifier is not associated with the M2M Service Subscription. |

Table 6.2.2.7.2-1 Service Subscription – disassociateAEFromServiceSubscription capability

##### 6.2.2.7.3	Service Interactions

The interactions of service capabilities required for this service capability:

- Issue this capability

Figure 6.2.2.7.3-1 Service Subscription – disassociateAEFromServiceSubscription Diagram

##### 6.2.2.7.4	Post-Conditions

The Application Entity registration association is removed from the M2M Service Subscription.

##### 6.2.2.7.5	Exceptions

Not Applicable

##### 6.2.2.7.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.2.2.7.7	oneM2M Resource Interworking

This service capability removes the association of the AE-ID from the M2M Service Subscription Profile. Currently TS-0001 [2] does not define how an AE is disassociated from a M2M Service Subscription Profile as part of a AE lifecycle flow.

#### 6.2.2.8	refreshAEAssociationWithServiceSubscription

This service capability provides the ability to refresh an existing registration association between an Application Entity and  a M2M Service Subscription. This service capability shall be restricted to the Mca and Msc Reference Points.

##### 6.2.2.8.1	Pre-conditions

An AE has successfully registered with the M2M system

##### 6.2.2.8.2	Signature – refreshAEAssociationWithServiceSubscription

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| aeId | IN | NO | The Application Entity Identifier (AE-ID). |
| serviceSubscriptionId | IN | NO | The M2M Service Subscription Identifier (M2M-Service-Profile-ID) |
| responseType | OUT | YES | Unique response types for this service. M2M Service Subscription does not exist. Application Entity Identifier is not associated with the M2M Service Subscription. |

Table 6.2.2.8.2-1 Service Subscription – refreshAEAssociationFWithServiceSubscription capability

##### 6.2.2.8.3	Service Interactions

The interactions of service capabilities required for this service capability:

- Issue this capability

Figure 6.2.2.8.3-1 Service Subscription – refreshAEAssociationWithServiceSubscription Diagram

##### 6.2.2.8.4	Post-Conditions

Not Applicable

##### 6.2.2.8.5	Exceptions

Not Applicable

##### 6.2.2.8.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.2.2.8.7	oneM2M Resource Interworking

This service capability refreshes the association of the Application Entity (AE-ID) with the M2M Service Subscription Profile. Currently TS-0001 [2] does not define how an AE registration association is refreshed with a M2M Service Subscription Profile as part of a AE lifecycle flow.

## 6.9	Service Subscription Administration

### 6.9.1	Overview

The Service Subscription Administration service provides the capability to administer the following across the Mca and Msc Reference Points:

Maintenance of M2M Services Subscriptions

Association of M2M Nodes and Application Rules to the M2M Service Subscription

The M2M Service Subscription defines the technical part of the contract between a M2M Subscriber (typically an M2M Application Service Provider) and a M2M Service Provider. Each M2M Service Subscription has a unique identifier (M2M-Service-Profile-ID).

A M2M Service Subscription establishes an association between one or more M2M Application Rules and one or more M2M Nodes. In addition, the M2M Service Subscription is associated with one or more Service Roles.

A M2M Service Subscription shall be used for the following purposes:

Serve as a basis for authorization for service capabilities

Serve as the basis for charging

Identify which devices and M2M Applications are part of this M2M Service Subscription

#### 6.9.1.1	Service Subscription Entity

| Attribute name | Description |
| --- | --- |
| serviceSubscriptionId | The M2M Service Subscription Identifier (M2M-Service-Profile-ID). |
| serviceRoleIds | List of Service Role Identifiers (SRole-ID) associated with the M2M Service Subscription. |

Table 6.9.1.1-1 Service Subscription Entity

##### 6.9.1.1.1	Service Subscription Filter Criteria

| Criterion name | Description |
| --- | --- |
| serviceSubscriptionIds | List of the M2M Service Subscription Identifiers (M2M-Service-Profile-ID). |
| serviceRoleIds | List of Service Role Identifiers (SRole-ID) associated with the M2M Service Subscription entity. |

Table 6.9.1.1.1-1 Service Subscription Filter Criteria

#### 6.9.1.2	M2M Node Entity for Service Subscription

| Attribute name | Description |
| --- | --- |
| serviceSubscriptionId | The M2M Service Subscription Identifier (M2M-Service-Profile-ID) for the Device. |
| nodeId | The unique M2M Node identifier in the context of the M2M Service Subscription. |
| externalIds | List of URNs that represent the external identifiers associated with this M2M Node. |
| applicationRuleIds | List of Application Rules Indentifiers associated with the M2M Node. |

Table 6.9.1.2-1 M2M Node Entity for Service Subscription

#### 6.9.1.2.1	M2M Node Filter Criteria

| Criterion name | Description |
| --- | --- |
| serviceSubscriptionIds | List of the M2M Service Subscription Identifier (M2M-Service-Profile-ID) for the Device. |
| nodeIds | List of the unique M2M Node identifier in the context of the M2M Service Subscription. |
| externalIds | List of URNs that represent the external identifiers associated with this M2M Node. |
| applicationRuleIds | List of Application Rule identifiers associated with the M2M Node. |

Table 6.9.1.2.1-1 M2M Node Filter Criteria

#### 6.9.1.3	Application Rule

| Criterion name | Description |
| --- | --- |
| applicationRuleId | The unique Application Rule identifier in the context of the M2M Service Subscription. |
| credentialIds | List of credential identifiers for which this Application Rule is applicable, i.e. for registration requests coming into a CSE via a Security Association Endpoint (SEA) [i.4], that was authenticated using credentials that match with any of these credential identifiers, the current Application Rule applies. This can contain a ‘*’ for any credential identifier or ‘None’ for not authenticated case. Also Wildcards within an element of this list are possible (e.g. ‘C123*X’ for any credential identifier that starts with ‘C123’ and ends with ‘X’) to define sets or ranges of credential identifiers. |
| allowedApplicationIds | List of M2M Application Identifiers (App-ID) that shall be considered to be allowed for AE registration requests received via Security Association Endpoint (SEA) [i.4]. This can contain ‘*’ for any App-ID. Also Wildcards within an element of this list are possible (e.g. ‘C123*X’ for any App-ID that starts with ‘C123’ and ends with ‘X’) to define sets or ranges of App-IDs. |
| allowedAEIds | List of M2M Application Entity Identifiers (AE-ID) that shall be considered to be allowed for AE registration requests. This can contain zero or more specific AE identifier values, ‘S*’ for any Service Provider AE-ID, ‘C*’ for any system assigned AE-ID, or ‘*’ for any AE-ID. Also Wildcards within an element of this list are possible (e.g. ‘C123*X’ for any AE-ID that starts with ‘C123’ and ends with ‘X’) to define sets or ranges of AE-ID. |

Table 6.9.1.3-1 Application Rule Entity

#### 6.9.1.3.1	Application Rule Filter Criteria

| Criterion name | Description |
| --- | --- |
| applicationRuleIds | List of the unique Application Rule identifier in the context of the M2M Service Subscription. |
| credentialIds | List of credential identifiers for which this Application Rule is applicable, i.e. for registration requests coming into the M2M System via a Security Association Endpoint (SEA) [i.1], that was authenticated using credentials that match with any of these credential identifiers, the current Application Rule applies. This can contain a ‘*’ for any credential identifier or ‘None’ for not authenticated case. Also Wildcards within an element of this list are possible (e.g. ‘C123*X’ for any credential identifier that starts with ‘C123’ and ends with ‘X’) to define sets or ranges of credential identifiers. |
| allowedApplicationIds | List of M2M Application Identifiers (App-ID) that shall be considered to be allowed for AE registration requests received via Security Association Endpoint (SEA) [i.2]. This can contain ‘*’ for any App-ID. Also Wildcards within an element of this list are possible (e.g. ‘C123*X’ for any App-ID that starts with ‘C123’ and ends with ‘X’) to define sets or ranges of App-IDs. |
| allowedAEIds | List of M2M Application Entity Identifiers (AE-ID) that shall be considered to be allowed for AE registration requests. This can contain zero or more specific AE identifier values, ‘S*’ for any Service Provider AE-ID, ‘C*’ for any system assigned AE-ID, or ‘*’ for any AE-ID. Also Wildcards within an element of this list are possible (e.g. ‘C123*X’ for any AE-ID that starts with ‘C123’ and ends with ‘X’) to define sets or ranges of AE-ID. |

Table 6.9.1.3.1-1 Application Rule Filter Criteria

### 6.9.2	Service Capabilities

#### 6.9.2.1	createServiceSubscription

This service capability provides the ability to create a M2M Service Subscription. This service capability shall be restricted to the Msc Reference Point.

##### 6.9.2.1.1	Pre-conditions

Not Applicable

##### 6.9.2.1.2	Signature – createServiceSubscription

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| serviceSubscriptionId | IN-OUT | YES | The M2M Service Subscription Identifier (M2M-Service-Profile-ID). If the attribute is not provided on input, the oneM2M System shall assign the M2M-Service-Profile-ID. The M2M-Service-Profile-ID is unique for the oneM2M System. |
| serviceRoleIds | IN | NO | List of Service Role Identifiers (SRole-ID) to be associated with the M2M Service Subscription. |
| responseType | OUT | YES | Unique response types for this service. M2M Service Subscription exists Service Role does not exist |

Table 6.9.2.1.2-1 Service Subscription Administration – createServiceSubscription capability

##### 6.9.2.1.3	Service Interactions

The interactions of service capabilities required for this service capability:

- Issue the createServiceSubscription capability

Figure 6.9.2.1.3-1 Service Subscription Administration – createServiceSubscription Diagram

##### 6.9.2.1.4	Post-Conditions

The M2M Service Subscription is created and any Service Roles are associated with the M2M Service Subscription.

##### 6.9.2.1.5	Exceptions

Not Applicable

##### 6.9.2.1.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.9.2.1.7	oneM2M Resource Interworking

This service capability creates the M2M Service Subscription with the identifier (M2M-Service-Profile-ID) and maps to the CREATE procedure for the <m2mServiceSubscriptionProfile> resource.

This service capability utilizes the access management services with the privileges associated with the associated Service Role. As such the accessControlPolicyIDs attribute of the <m2mServiceSubscriptionProfile> resource is not used within this service capability.

#### 6.9.2.2	deleteServiceSubscription

This service capability provides the ability to delete a M2M Service Subscription. This service capability shall be restricted to the Msc Reference Point.

##### 6.9.2.2.1	Pre-conditions

Not Applicable

##### 6.9.2.2.2	Signature – deleteServiceSubscription

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| serviceSubscriptionId | IN | NO | The M2M Service Subscription Identifier (M2M-Service-Profile-ID). |
| responseType | OUT | YES | Unique response types for this service. M2M Service Subscription does not exist |

Table 6.9.2.2.2-1 Service Subscription Administration – deleteServiceSubscription capability

##### 6.9.2.2.3	Service Interactions

The interactions of service capabilities required for this service capability:

- Issue the deleteServiceSubscription capability

Figure 6.9.2.2.3-1 Service Subscription Administration – deleteServiceSubscription Diagram

##### 6.9.2.2.4	Post-Conditions

The M2M Service Subscription is deleted along with any associations of the M2M Service Subscription has to the Service Roles. The Node information (e.g., devices, M2M Applications) associated with the M2M Service Subscription is also deleted.

##### 6.9.2.2.5	Exceptions

Not Applicable

##### 6.9.2.2.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.9.2.2.7	oneM2M Resource Interworking

This service capability deletes the M2M Service Subscription with the identifier (M2M-Service-Profile-ID) and maps to the DELETE procedure for the <m2mServiceSubscriptionProfile> resource.

#### 6.9.2.3	updateServiceSubscription

This service capability provides the ability to update a M2M Service Subscription. This service capability shall be restricted to the Msc Reference Point.

##### 6.9.2.3.1	Pre-conditions

Not Applicable

##### 6.9.2.3.2	Signature – updateServiceSubscription

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| serviceSubscriptionId | IN | NO | The M2M Service Subscription Identifier (M2M-Service-Profile-ID). |
| serviceRoleIds | IN | YES | List of Service Role Identifiers (SRole-ID) to be associated with the M2M Service Subscription. If supplied, SRole-IDs in the list that are not already associated with the M2M Service Subscription are added. SRole-IDs that are associated with the M2M Service Subscription but not in the list are deleted. |
| roleIdResult | OUT | YES | If the parameter serviceRoleIds is present, this parameter provides the results (added, deleted) for each affected Service Roles. |
| responseType | OUT | YES | Unique response types for this service. M2M Service Subscription does not exist Service Role does not exist for a Supporting Service |

Table 6.9.2.3.2-1 Service Subscription Administration – updateServiceSubscription capability

##### 6.9.2.3.3	Service Interactions

- The interactions of service capabilities required for this service capability:

- Issue the updateServiceSubscription capability

Figure 6.9.2.3.3-1 Service Subscription Administration – updateServiceSubscription Diagram

##### 6.9.2.3.4	Post-Conditions

The M2M Service Subscription is updated along with any associations of the M2M Service Subscription has to the Service Roles.

##### 6.9.2.3.5	Exceptions

Not Applicable

##### 6.9.2.3.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.9.2.3.7	oneM2M Resource Interworking

This service capability updates the M2M Service Subscription with the identifier (M2M-Service-Profile-ID) and maps to the UPDATE procedure for the <m2mServiceSubscriptionProfile> resource.

#### 6.9.2.4	addRoleToServiceSubscription

This service capability provides the ability to add new Service Roles to a M2M Service Subscription. This service capability shall be restricted to the Msc Reference Point.

##### 6.9.2.4.1	Pre-conditions

Not Applicable

##### 6.9.2.4.2	Signature – addRoleToServiceSubscription

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| serviceSubscriptionId | IN | NO | The M2M Service Subscription Identifier (M2M-Service-Profile-ID). |
| serviceRoleIds | IN | NO | List of Service Role Identifiers (SRole-ID) to be associated with the M2M Service Subscription. If a SRole-ID in the parameter is already associated with the M2M Service Subscription, nothing is done for the SRole-ID as it already is associated. |
| responseType | OUT | YES | Unique response types for this service. M2M Service Subscription does not exist Service Role does not exist for a Supporting Service |

Table 6.9.2.4.2-1 Service Subscription Administration – addRoleToServiceSubscription capability

##### 6.9.2.4.3	Service Interactions

The interactions of service capabilities required for this service capability:

- Issue the addRoleToServiceSubscription capability

Figure 6.9.2.4.3-1 Service Subscription Administration – addRoleToServiceSubscription Diagram

##### 6.9.2.4.4	Post-Conditions

The M2M Service Subscription is updated with any associations of the M2M Service Subscription has to the Service Roles.

##### 6.9.2.4.5	Exceptions

Not Applicable

##### 6.9.2.4.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.9.2.4.7	oneM2M Resource Interworking

This service capability updates the M2M Service Subscription with the identifier (M2M-Service-Profile-ID) and maps to the UPDATE procedure for the <m2mServiceSubscriptionProfile> resource for the serviceRoles attribute.

#### 6.9.2.5	deleteRoleFromServiceSubscription

This service capability provides the ability to delete existing Service Roles from a M2M Service Subscription. This service capability shall be restricted to the Msc Reference Point.

##### 6.9.2.5.1	Pre-conditions

Not Applicable

##### 6.9.2.5.2	Signature – deleteRoleFromServiceSubscription

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| serviceSubscriptionId | IN | NO | The M2M Service Subscription Identifier (M2M-Service-Profile-ID). |
| serviceRoleIds | IN | NO | List of Service Role Identifiers (SRole-ID) to be deleted from the association with the M2M Service Subscription. |
| responseType | OUT | YES | Unique response types for this service. M2M Service Subscription does not exist Service Role does not exist for a Supporting Service |

Table 6.9.2.5.2-1 Service Subscription Administration – deleteRoleFromServiceSubscription capability

##### 6.9.2.5.3	Service Interactions

The interactions of service capabilities required for this service capability:

- Issue the deleteRoleFromServiceSubscription capability

Figure 6.9.2.5.3-1 Service Subscription Administration – deleteRoleFromServiceSubscription Diagram

##### 6.9.2.5.4	Post-Conditions

The M2M Service Subscription is updated with associations of the identified Service Roles deleted.

##### 6.9.2.5.5	Exceptions

Not Applicable

##### 6.9.2.5.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.9.2.5.7	oneM2M Resource Interworking

This service capability updates the M2M Service Subscription with the identifier (M2M-Service-Profile-ID) and maps to the UPDATE procedure for the <m2mServiceSubscriptionProfile> resource for the serviceRoles attribute.

#### 6.9.2.6	getServiceSubscription

This service capability provides the ability to retrieve the existing M2M Service Subscription. This service capability shall be restricted to the Msc and Mca Reference Points.

##### 6.9.2.6.1	Pre-conditions

Not Applicable

##### 6.9.2.6.2	Signature – getServiceSubscription

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| filterCriteria | IN | NO | See Table 6.9.1.1.1-1 |
| serviceSubscriptions | OUT | NO | The resulting M2M Service Subscription entities in Table 6.9.1.2-1. |
| responseType | OUT | YES | Unique response types for this service. None |

Table 6.9.2.6.2-1 Service Subscription Administration – getServiceSubscription capability

##### 6.9.2.6.3	Service Interactions

The interactions of service capabilities required for this service capability:

- Issue the getServiceSubscription capability

Figure 6.9.2.6.3-1 Service Subscription Administration – getServiceSubscription Diagram

##### 6.9.2.6.4	Post-Conditions

Not Applicable

##### 6.9.2.6.5	Exceptions

Not Applicable

##### 6.9.2.6.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.9.2.6.7	oneM2M Resource Interworking

This service capability retrieves the M2M Service Subscription for the specified filter criteria and maps to the RETRIEVE procedure for the <m2mServiceSubscription> resource.

#### 6.9.2.7	addNodeToServiceSubscription

This service capability provides the ability to add a M2M Node to the existing M2M Service Subscription. This service capability shall be restricted to the Msc and Mca Reference Points.

##### 6.9.2.7.1	Pre-conditions

Not Applicable

##### 6.9.2.7.2	Signature – addNodeToServiceSubscription

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| serviceSubscriptionId | IN | NO | The M2M Service Subscription (M2M-Service-Profile-ID) to add the Device |
| externalIds | IN | YES | A List of URNs that represent the external identifiers associated with this M2M Node. |
| applicationRuleIds | IN | YES | A list of Application Rules associated with this Node. |
| nodeId | OUT | NO | The unique M2M Node identifer for this entity. |
| responseType | OUT | YES | Unique response types for this service. M2M Service Subscription does not exist. |

Table 6.9.2.7.2-1 Service Subscription Administration – addNodeToServiceSubscription capability

##### 6.9.2.7.3	Service Interactions

The interactions of service capabilities required for this service capability:

- Issue the addNodeToServiceSubscription capability

Figure 6.9.2.7.3-1 Service Subscription Administration – addNodeToServiceSubscription Diagram

##### 6.9.2.7.4	Post-Conditions

Not Applicable

##### 6.9.2.7.5	Exceptions

Not Applicable

##### 6.9.2.7.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.9.2.7.7	oneM2M Resource Interworking

This service capability adds the M2M Node information for the M2M Service Subscription. This capability maps to the CREATE procedure of the <serviceSubscribedNode> resource.

#### 6.9.2.8	deleteNodesFromServiceSubscription

This service capability provides the ability to delete M2M Nodes from the existing M2M Service Subscription. This service capability shall be restricted to the Msc and Mca Reference Points.

##### 6.9.2.8.1	Pre-conditions

Not Applicable

##### 6.9.2.8.2	Signature – deleteNodesFromServiceSubscription

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| serviceSubscriptionId | IN | NO | The M2M Service Subscription (M2M-Service-Profile-ID) for the Devices |
| nodeIds | IN | NO | List of M2M Node identifiers to be deleted from the M2M Service Subscription. |
| responseType | OUT | YES | Unique response types for this service. M2M Service Subscription does not exist. M2M Node does not exist for this M2M Service Subscription |

Table 6.9.2.8.2-1 Service Subscription Administration – deleteNodesFromServiceSubscription capability

##### 6.9.2.8.3	Service Interactions

The interactions of service capabilities required for this service capability:

- Issue the deleteNodesFromServiceSubscription capability

Figure 6.9.2.8.3-1 Service Subscription Administration – deleteNodesFromServiceSubscription Diagram

##### 6.9.2.8.4	Post-Conditions

Not Applicable

##### 6.9.2.8.5	Exceptions

Not Applicable

##### 6.9.2.8.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.9.2.8.7	oneM2M Resource Interworking

This service capability removes the M2M Node from the M2M Service Subscription. This capability maps to the DELETE procedure of the <serviceSubscribedNode> resource.

#### 6.9.2.9	getNodesForServiceSubscription

This service capability provides the ability to retrieve M2M Nodes for an existing M2M Service Subscription. This service capability shall be restricted to the Msc and Mca Reference Points.

##### 6.9.2.9.1	Pre-conditions

Not Applicable

##### 6.9.2.9.2	Signature – getNodesForServiceSubscription

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| filterCriteria | IN | NO | See Table 6.9.1.2.1-1 |
| nodes | OUT | NO | The resulting M2M Node entities in Table 6.9.1.2-1. |
| responseType | OUT | YES | Unique response types for this service. None |

Table 6.9.2.9.2-1 Service Subscription Administration – getNodesForServiceSubscription capability

##### 6.9.2.9.3	Service Interactions

The interactions of service capabilities required for this service capability:

- Issue the getNodesForServiceSubscription capability

Figure 6.9.2.9.3-1 Service Subscription Administration – getNodesForServiceSubscription Diagram

##### 6.9.2.9.4	Post-Conditions

Not Applicable

##### 6.9.2.9.5	Exceptions

Not Applicable

##### 6.9.2.9.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.9.2.9.7	oneM2M Resource Interworking

This service capability retrieves the devices for a M2M Service Subscription for the specified filter criteria and maps to the RETRIEVE procedure for the <serviceSubscribedNode> resource.

#### 6.9.2.10	createApplicationRule

This service capability provides the ability to create a M2M Application Rule to to be associated with one or more M2M Nodes. This service capability shall be restricted to the Msc and Mca Reference Points.

##### 6.9.2.10.1	Pre-conditions

Not Applicable

##### 6.9.2.10.2	Signature – createApplicationRule

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| credentialIds | IN | YES | List of credential identifiers for which this Application Rule is applicable, i.e. for registration requests coming into the M2M System via a Security Association Endpoint (SEA) [i.3], that was authenticated using credentials that match with any of these credential identifiers, the current Application Rule applies. |
| allowedApplicationIds | IN | YES | List of M2M Application Identifiers (App-ID) that shall be considered to be allowed for AE registration requests received via Security Association Endpoint (SEA) [i.4]. |
| allowedAEIds | IN | YES | List of M2M Application Entity Identifiers (AE-ID) that shall be considered to be allowed for AE registration requests. |
| applicationRuleId | OUT | NO | The unique Application Rule identifier in the context of the M2M Service Subscription. |
| responseType | OUT | YES | Unique response types for this service. None |

Table 6.9.2.10.2-1 Service Subscription Administration – createApplicationRule capability

##### 6.9.2.10.3	Service Interactions

The interactions of service capabilities required for this service capability:

- Issue the createApplicationRule capability

Figure 6.9.2.10.3-1 Service Subscription Administration – createApplicationRule Diagram

##### 6.9.2.10.4	Post-Conditions

Not Applicable

##### 6.9.2.10.5	Exceptions

Not Applicable

##### 6.9.2.10.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.9.2.10.7	oneM2M Resource Interworking

This service capability adds an Application Rule. This capability maps to the CREATE procedure of the <serviceSubscribedAppRule> resource..

#### 6.9.2.11	deleteApplicationRules

This service capability provides the ability to delete Application Rules and any references to the Application Rule made by M2M Nodes to the Application Rules. This service capability shall be restricted to the Msc and Mca Reference Points.

##### 6.9.2.11.1	Pre-conditions

Not Applicable

##### 6.9.2.11.2	Signature – deleteApplicationRules

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| applicationRuleIds | IN | NO | A list of Application Rule identifiers. |
| responseType | OUT | YES | Unique response types for this service. Application Rule does not exist |

Table 6.9.2.11.2-1 Service Subscription Administration – deleteApplicationRules capability

##### 6.9.2.11.3	Service Interactions

The interactions of service capabilities required for this service capability:

- Issue the deleteApplicationRules capability

Figure 6.9.2.11.3-1 Service Subscription Administration – deleteApplicationRules Diagram

##### 6.9.2.11.4	Post-Conditions

Not Applicable

##### 6.9.2.11.5	Exceptions

Not Applicable

##### 6.9.2.11.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.9.2.11.7	oneM2M Resource Interworking

This service capability adds Application Rules. This capability maps to the DELETE procedure of the <serviceSubscribedAppRule> resource.

.

#### 6.9.2.12	getApplicationRules

This service capability provides the ability to retrieve the Application Rules. This service capability shall be restricted to the Msc and Mca Reference Points.

##### 6.9.2.12.1	Pre-conditions

Not Applicable

##### 6.9.2.12.2	Signature – getApplicationRules

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| filterCriteria | IN | NO | See Table 6.9.1.3.1-1 |
| applicationRules | OUT | NO | The resulting M2M Node entities in Table 6.9.1.3-1. |
| responseType | OUT | YES | Unique response types for this service. None |

Table 6.9.2.12.2-1 Service Subscription Administration – getApplicationRules capability

##### 6.9.2.12.3	Service Interactions

The interactions of service capabilities required for this service capability:

- Issue the getApplicationRules capability

Figure 6.9.2.12.3-1 Service Subscription Administration – getApplicationRules Diagram

##### 6.9.2.12.4	Post-Conditions

Not Applicable

##### 6.9.2.12.5	Exceptions

Not Applicable

##### 6.9.2.12.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.9.2.12.7	oneM2M Resource Interworking

This service capability retrieves Application Rules. This capability maps to the RETRIEVE procedure of the <serviceSubscribedAppRule> resource..

#### 6.9.2.13	updateNodeForServiceSubscription

This service capability provides the ability to update the Application Rules and External Identifiers to be associated to a Node within the context of a M2M Service Subscription. This service capability shall be restricted to the Msc and Mca Reference Points.

##### 6.9.2.13.1	Pre-conditions

Not Applicable

##### 6.9.2.13.2	updateNodeForServiceSubscription

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| serviceSubscriptionId | IN | NO | The M2M Service Subscription (M2M-Service-Profile-ID) for the device |
| nodeId | IN | NO | The unique M2M Node identifier in the context of the M2M Service Subscription. |
| applicationRuleIds | IN | YES | A list of Application Rule Identifier. When present this list will overlay the list of Applications associated with the Node. |
| externalIds | IN | YES | List of URNs that represent the external identifiers associated with this device. When present this list will overlay the list of external identifiers associated with the Node. |
| responseType | OUT | YES | Unique response types for this service. M2M Service Subscription does not exist M2M Node does not exist for the M2M Service Subscription |

Table 6.9.2.13.2-1 Service Subscription Administration – updateNodeForServiceSubscription capability

##### 6.9.2.13.3	Service Interactions

The interactions of service capabilities required for this service capability:

- Issue the updateNodeForServiceSubscription capability

Figure 6.9.2.13.3-1 Service Subscription Administration – updateNodeForServiceSubscription Diagram

##### 6.9.2.13.4	Post-Conditions

When parameters are present, the M2M Applications and External Identifiers are replaced for the M2M Node.

##### 6.9.2.13.5	Exceptions

Not Applicable

##### 6.9.2.13.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.9.2.13.7	oneM2M Resource Interworking

This service capability updates the M2M Application and/or External Identifier list(s) for the Node in the context of the M2M Service Subscription Profile. This capability maps to the UPDATE procedure of the <serviceSubscribedNode> resource.

#### 6.9.2.14	updateApplicationRule

This service capability provides the ability to update an Application Rule. This service capability shall be restricted to the Msc and Mca Reference Points.

##### 6.9.2.14.1	Pre-conditions

Not Applicable

##### 6.9.2.14.2	Signature – updateApplicationRule

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| applicationRuleId | IN | NO | The unique Application Rule identifier in the context of the M2M Service Subscription. |
| credentialIds | IN | YES | List of credential identifiers for which this Application Rule is applicable, i.e. for registration requests coming into the M2M System via a Security Association Endpoint (SEA) [i.5], that was authenticated using credentials that match with any of these credential identifiers, the current Application Rule applies. When present this list will overlay the list of credential identifiers. |
| allowedApplicationIds | IN | YES | List of M2M Application Identifiers (App-ID) that shall be considered to be allowed for AE registration requests received via Security Association Endpoint (SEA) [i.6]. When present this list will overlay the list of allowed App-IDs. |
| allowedAEIds | IN | YES | List of M2M Application Entity Identifiers (AE-ID) that shall be considered to be allowed for AE registration requests. When present this list will overlay the list of allowed AE-IDs. |
| responseType | OUT | YES | Unique response types for this service. Application Rule does not exist. |

Table 6.9.2.14.2-1 Service Subscription Administration – updateApplicationRule capability

##### 6.9.2.14.3	Service Interactions

The interactions of service capabilities required for this service capability:

- Issue the updateApplicationRule capability

Figure 6.9.2.14.3-1 Service Subscription Administration – updateApplicationRule Diagram

##### 6.9.2.14.4	Post-Conditions

When parameters are present, the Allowed Application, AEs and Credentials are replaced for the Application Rule.

##### 6.9.2.14.5	Exceptions

Not Applicable

##### 6.9.2.14.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.9.2.14.7	oneM2M Resource Interworking

This service capability updates an Application Rule. This capability maps to the UPDATE procedure of the <serviceSubscribedAppRule> resource.

## 6.11	Registration

### 6.11.1	Overview

The Registration service provides the ability for:

- Initial Registration of an AE

- Refresh an existing Registration of an AE

- AE initiated termination of an existing Registration

### 6.11.2	Service Capabilities

#### 6.11.2.1	registerAE

This service capability enables an AE with the proper authorization to register with the M2M System. This service capability shall be restricted across the Mca Reference Point.

##### 6.11.2.1.1	Pre-conditions

The AE has not registered with the M2M System. An AE identifier may have been already allocated to the registering AE and acquired by the AE by means outside the scope of this specification.

##### 6.11.2.1.2	Signature – registerAE

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| pointOf Access | IN | NO | The point of Access of the registered AE. |
| applicationId | IN | NO | The Application Identifier (App-ID). |
| credentialId | IN | YES | Application Credential-ID used to identify the Application Entity for the Application. It is used to retrieve the corresponding M2M Service Subscription. |
| expirationTime | IN | NO | The expiration time of the registration as requested by the Originator. |
| aeId | IN-OUT | Optional for IN only-Not Optional for OUT | Application Entity (AE-ID) is provided back in the response. |
| responseType | OUT | NO | Unique response types for this service: AE successfully registered AE not successfully registered M2M Service Subscription does not exist Invalid Application Credential Identifier. |

Table 6.11.2.1.2-1 Registration – registerAE capability

##### 6.11.2.1.3	Services Interaction

The interactions of service capabilities required for this service capability:

- Associate the AE with the M2M Service Subscription

- Issue the request to the Supporting Service.

- Send a notification to the Device Onboarding Supporting Service for a first-time application registration  in the event there is a subscription of the first contact event by the Supporting Service.

Figure 6.11.2.1.3-1 Registration – registerAE Diagram

##### 6.11.2.1.4	Post-Conditions

AE is registered and can start using service capabilities

The returned AE-ID shall be used in any subsequent operation related to that application

##### 6.11.2.1.5	Exceptions

Not Applicable

##### 6.11.2.1.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.11.2.1.7	oneM2M Resource Interworking

This service capability maps to the CREATE procedure of the <AE> resource.

#### 6.11.2.2	refreshAERegistration

This service capability enables an AE to refresh an existing AE registration with the M2M System. This service capability shall be restricted to the Mca Reference Points.

##### 6.11.2.2.1	Pre-conditions

The AE has successfully registered with the M2M System.

##### 6.11.2.2.2	Signature – refreshAERegistration

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| aeId | IN | NO | The Application Entity Identifier (AE-ID) of the request originator. |
| pointOfAccess | IN | YES | The point of Access of the registered AE. POA is optional only if identical to the one in the refreshed registration |
| expirationTime | IN | NO | The expiration time of the registration as requested by the Originator. |
| responseType | OUT | NO | Unique response types for this service: AE successfully refreshed Registration does not exist |

Table 6.11.2.2.2-1 Registration – refreshAERegistration capability

##### 6.11.2.2.3	Service Interactions

The interactions of service capabilities required for this service capability:

- Issue a request to regresh the AE association with the M2M Service Profile

- Issue the request to the Supporting Service

Figure 6.11.2.2.3-1 Registration – refreshAERegistration Diagram

##### 6.11.2.2.4	Post-Conditions

The Application Entity registration is refereshed and can continue using service capabilities.

##### 6.11.2.2.5	Exceptions

Not Applicable

##### 6.11.2.2.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.11.2.2.7	oneM2M Resource Interworking

This service capability maps to the UPDATE procedure of the <AE> resource.

#### 6.11.2.3	deregisterAE

This service capability enables an AE to deregister from the M2M System. This service capability shall be restricted to the Mca Reference Points.

##### 6.11.2.3.1	Pre-conditions

The AE successfully registered with the M2M System.

##### 6.11.2.3.2	Signature – deregisterAE

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| aeId | IN | NO | The Application Identifier (AE-ID) |
| responseType | OUT | NO | Unique response types for this service: AE successfully De-registered Registration does not exist |

Table 6.11.2.3.2-1 Registration – deregisterAE capability

##### 6.11.2.3.3	Service Interactions

The interactions of service capabilities required for this service capability:

- Disassociate the AE with Service Subscription

- Issue the request to Supporting Services.

- Send a notification  to device onboarding service supporting service for application de-registration in the event there is a subscription

Figure 6.11.2.3.3-1 Registration – deregisterAE Diagram

##### 6.11.2.3.4	Post-Conditions

AE is no longer registered and cannot use any services.

##### 6.11.2.3.5	Exceptions

Not Applicable

Transaction Pattern: Participation allowed

##### 6.11.2.3.6	oneM2M Resource Interworking

This service capability maps to the DELETE procedure of the <AE> resource.

## 6.12	Registration Administration

### 6.12.1	Overview

The Registration administration service provides the ability for:

- Retrieve the AE’s Registration status

- Revoke an AE existing Registration

- Permit subscriptions to AE Registration events

- Removal of subscriptions to AE Registration events

### 6.12.2	Service Capabilities

#### 6.12.2.1	getRegistrationStatus

This service capability enables a Supporting Service authorized for this operation, to retrieve the registration status for an AE. This service capability is restricted to the Msc Reference Point.

##### 6.12.2.1.1	Pre-conditions

Not Applicable

##### 6.12.2.1.2	Signature – getRegistrationStatus

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| aeId | IN | NO | The Application Entity Identifier (AE-ID) |
| responseType | OUT | NO | Unique response types for this service: AE is registered AE registration does not exist |

Table 6.12.2.1.2-1 Registration Administration – getRegistrationStatus capability

##### 6.12.2.1.3	Service Interaction

The interactions of service capabilities required for this service capability:

- Retrieve the Application Entity information

Figure 6.12.2.1.3-1 Registration Administration – getRegistrationStatus Diagram

##### 6.12.2.1.4	Post-Conditions

Not Applicable

##### 6.12.2.1.5	Exceptions

Not Applicable

##### 6.12.2.1.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.12.2.1.7	oneM2M Resource Interworking

This service capability maps to the RETRIEVE procedure of the <AE> resource.

#### 6.12.2.2	revokeAERegistration

This service capability enables a Supporting Service authorized for this operation to revoke an existing AE registration. This service capability shall be restricted to the Msc Reference Points

##### 6.12.2.2.1	Pre-conditions

The AE is successfully registered with the M2M System.

##### 6.12.2.2.2	Signature – revokeAERegistration

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| aeId | IN | NO | Application Entity Identifier (AE-ID) |
| responseType | OUT | NO | Unique response types for this service: AE successfully De-registered Registration does not exist |

Table 6.12.2.2.2-1 Registration Administration – revokeAERegistration capability

##### 6.12.2.2.3	Service Interaction

The interactions of service capabilities required for this service capability:

- Issue a request to the Service Subscription Administration to fetch the service profile.

- Disassociate the AE from the M2M Service Subscription

Figure 6.12.2.2.3-1 Registration Administration – revokeAERegistration Diagram

##### 6.12.2.2.4	Post-Conditions

The Application Entity is no longer registered and cannot use any services

##### 6.12.2.2.5	Exceptions

Not Applicable

##### 6.12.2.2.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.12.2.2.7	oneM2M Resource Interworking

This service capability maps to the DELETE procedure of the <AE> resource.

#### 6.12.2.3	subscribeInitialAERegistrationEvent

This service capability enables subscription to the initial (first time only) registration of an AE. This capability shall be restricted to the Msc Reference Point.

##### 6.12.2.3.1	Pre-conditions

Not Applicable

##### 6.12.2.3.2	Signature – subscribeInitialAERegistrationEvent

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| subscriptionId | OUT | NO | Return subscriptionId in case of a success. |
| responseType | OUT | NO | Unique response types for this service: Successfully subscribed Not successfully subscribed |

6.12.2.3.2-1 Registration Administration – subscribeInitialAERegistrationEvent capability

##### 6.12.2.3.3	Service Interaction

The interactions of service capabilities required for this service capability:

- Subscribe the requesting AE for the initial registration event.

Figure 6.12.2.3.3-1 Registration Administration– subscribeInitialAERegistrationEvent Diagram

##### 6.12.2.3.4	Post-Conditions

A Subscription is created for the Originator to receive initial contact events.

##### 6.12.2.3.5	Exceptions

Not Applicable

##### 6.12.2.3.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.12.2.3.7	oneM2M Resource Interworking

Not Applicable

#### 6.12.2.4	unsubscribeInitialAERegistrationEvent

This service capability enables a Supoorting Service for this operation to remove an existing subscription against an AE initial registration. This capability shall be restricted to the Msc Reference Point.

##### 6.12.2.4.1	Pre-conditions

Not Applicable

##### 6.12.2.4.2	Signature – unsubcribeInitialAERegistrationEvent

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| subscriptionId | IN | NO | The subscriptionId for the AE initial registration event. |
| responseType | OUT | NO | Unique response types for this service: Successfully unsubscribed Subscription does not exist |

Table 6.12.2.4.2-1 unsubscribeInitialAERegistrationEvent capability

##### 6.12.2.4.3	Service Interaction

The interactions of service capabilities required for this service capability:

- Remove the subscription

Figure 6.12.2.4.3-1 Registration Administration – unsubscribeInitialAERegistrationEvent Diagram

##### 6.12.2.4.4	Post-Conditions

Subscription to initial registration event is removed.

##### 6.12.2.4.5	Exceptions

Not Applicable

##### 6.12.2.4.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.12.2.4.7	oneM2M Resource Interworking

Not Applicable

# Annex F (Informative): Registration Services

## F.1	Overview

This annex illustrates the usage of the services for requests to register AEs across the Mca Reference Point and between M2M Service Components across the Msc Reference Point.

### F.2	Mca Registration Service Processing and Supporting Services

AEs communicate with the M2M System over the Mca Reference Point through the SE component. The SE component accepts the request from the AE and provides the request to the Supporting Service in order allow the M2M Service Provider to ensure the request is properly authorized and recorded. In addition, the M2M Service Provider is able to orchestrate other capabilities that have not been specified.

### F.2.1	Message Exchanges

#### F.2.1.2	Service Capabilities

##### F.2.1.2.1	registerAE

This service capability enables an AE to register with the M2M System. This service capability shall be restricted across the Mca Reference Point

###### F.2.1.2.1.1	Pre-conditions

The AE has not registered with the M2M System.

The pre-conditions for Mca Received Requests are met.

###### F.2.1.2.1.2	Signature – registerAE

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| Mca Common request input parameters | - | - | See Table A.2.1-1 |
| pointOf Access | IN | NO | The point of Access of the registered AE. |
| applicationId | IN | NO | The Application Identifer (App-ID). |
| credentialId | IN | YES | Application Credentials. It is used to retrieve the corresponding Service Subscription |
| expirationTime | IN | NO | The expiration time of the registration as requested by the Originator |
| aeId | IN-OUT | Option for IN only-Not an Option for OUT | The Application Entity Identiifer (AE-ID) is provided back in the response |
| responseType | OUT | NO | Unique response types for this service: AE successfully registered AE not successfully registered |

Table  F.2.1.2.1.2-1  Registration Services – registerAE capability

###### F.2.1.2.1.3	Service Interactions

The interactions of service capabilities required for this service capability:

- Perform the Common Request Services for requests across the Mca Reference Point

- Record the event

Figure F.2.1.2.1.3-1 Registration Services – registerAE Diagram

###### F.2.1.2.1.4	Post-Conditions

Event is recorded

###### F.2.1.2.1.5	Exceptions

No unique exceptions for this service capability.

Consumed services may throw exceptions which are forwarded by this service capability.

###### F.2.1.2.1.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

Maximum Response: 250ms

##### F.2.1.2.2	refreshAERegistration

This service capability enables an AE to refresh an existing registration with the M2M System

###### Y2.1.2.2.1	Pre-conditions

The pre-conditions for Mca Received Requests are met.

The AE is registered and allocated an aeId by the M2M System.

###### F.2.1.2.2.2	Signature – refreshAERegsitration

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| Mca Common request input parameters | - | - | See Table A.2.1-1 |
| aeId | IN | NO | The Application Entity Identifier (AE-ID) to be refreshed. |
| pointOfAccess | IN | YES | The point of Access of the registered AE. POA is optional only if identical to the one in the refreshed registration |
| expirationTime | IN | NO | The expiration time of the registration as requested by the Originator. |
| responseType | OUT | NO | Unique response types for this service: AE successfully refreshed Registration does not exist |

Table F.2.1.2.2.2-1 Registration Services – refreshAERegistration capability

###### F.2.1.2.2.3	Service Interactions

The interactions of service capabilities required for this service capability:

- Perform the Common Request Services for requests across the Msc Reference Point

- Record the event

Figure F.2.1.2.2.3-1 Registration Services – refreshAERegistration Diagram

###### F.2.1.2.2.4	Post-Conditions

Success case: The request is permitted.

Failure case: The request is not permitted and a response type is transmitted to the AE

###### F.2.1.2.2.5	Exceptions

No unique exceptions for this service capability.

Consumed services may throw exceptions which are forwarded by this service capability.

###### F.2.1.2.2.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

Maximum Response: 50ms

##### F.2.1.2.3	deregisterAE

This service capability enables an AE to deregister from the M2M System.

###### F.2.1.2.3.1	Pre-conditions

The pre-conditions for Mca Received Requests are met.

The Application Entity is registered.

###### F.2.1.2.3.2	Signature – deregisterAE

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| Mca Common request input parameters | - | - | See Table A.2.1-1 |
| aeId | IN | NO | The Application Entity Identifier (AE-ID) to be deregistered. |
| responseType | OUT | NO | Unique response types for this service: AE successfully De-registsred Registration does not exist |

Table F.2.1.2.3.2-1 RegistrationServcies – deregisterAE capability

###### F.2.1.2.3.3	Service Interactions

The interactions of service capabilities required for this service capability:

- Perform the Common Request Services for requests across the Msc Reference Point

- Record the event

Figure F.2.1.2.3.3-1 Registration Services – deregisterAE Diagram

###### F.2.1.2.3.4	Post-Conditions

Success case: The request is permitted.

Failure case: The request is not permitted and a response type is transmitted back to the AE

###### F.2.1.2.3.5	Exceptions

No unique exceptions for this service capability.

Consumed services may throw exceptions which are forwarded by this service capability.

###### F.2.1.2.3.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

Maximum Response: 300ms

NotifyDeregContact –This isnt defined in the Onboarding Service.

Why wouldnt refresh go through common processing (e.g., authorization?)