| CHANGE REQUEST |
| --- |
| Meeting:* | WG2 Architecture – ARC 16 |
| Source:* | Ericsson |
| Date:* | ARC16 |
| Contact:* | 2015-03-15 |
| Reason for Change/s:* | George Foti |
| CR against: Release* | V1.0.1 |
| CR against: WI* |  |
| CR against: TS/TR* | TS-0001 |
| Clauses/Sub Clauses* | Discussion Paper |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The current SUBSCRIBE/NOTIFY procedure has some limitations since it does not allow an entity that is the target of a notification, and that is not the subscription originator, to express its desire not to receive such a notification. There are cases where unsolicited notifications due to such subscriptions may not be desired by the target of such a notification.

Consumer related applications typically represent those cases where these unsolicited notifications may not be desirable and mechanisms to stop these notifications should be supported in a controlled fashion.

On the other hand, requests initiated by targets of notification to stop receiving them in industrial applications which use the subscription notifications for critical applications, have to be handled differently and may require authorization or be completely denied depending on the scenario.

This paper proposes an alternative to address these limitations in a comprehensive manner to support both types of applications

## Requirements

We start by examining the requirements that need to be fulfilled to provide a comprehensive and flexible framework to support both types of applications

These requirements are considered essential for supporting a framework that can be tailored to different applications:

The event subscription originator may indicate at subscription origination and/or subscription refresh the handling for requests originating from targets of notifications, in regard their requests for cessation of  receiving notifications related to the event

The event subscription origination at subscription creation and/or subscription refresh may support a different action per recipient of a notification regarding handling of requests for cessation of receiving notifications related to that event.

The framework for handling requests for cessation of receiving notifications related to an event shall support a default action that applies to a recipient (s) in case no specific action is defined for a recipient related to that event by subscription originator

The framework for handling of requests for cessation of receiving notifications related to an event shall result in a single action as an outcome that may be conditional upon certain criteria. For example the action may depend on the time of the day; and/or geographical location of the target, etc...

Actions defined for a recipient of a notification for an event can be applied  across subscriptions related to different events and different targets of notifications without needing to redefine them.

## Proposal

The following elements are essential to support the above requirements:

### Support for Policy Definitions

The solution must support the definition of any number of policies, where each policy can be referenced through an identifier labelled policy-ID. Each policy shall result in only a single action as an outcome. However a policy outcome can be made conditional on a number of factors such as time of the day, geographic location of notification target recipient, etc.  as long a single action results from applying the policy. The factors can be combined as well to support multiple conditions for an outcome in an AND/OR fashion.

One of the actions that have to be supported as an outcome is to seek authorization from the subscription originator prior to responding to a notification target request to stop receiving notifications. A response is returned to the notification target once a response is received from the subscription originator

In addition there shall be support to define a default policy that shall be applied when no policy is allocated to a recipient of a notification at event subscription creation. The definition of such a policy is identical to any other policy; the only exception being that no policy-ID is allocated to it.

Policies defined can be reused  by  refencing the policy-ID

Policy definition can be inspired, but not restricted to IETF RFC 4745.

### Policy Allocation to Recipients of Notification

During the creation of a subscription for a specific event, for each recipient targeted to receive a notification other than the subscription creator, a policy-ID should be allocated to the recipient by subscription originator.  If no policy is explicitly allocated to a recipient, then the default policy shall apply. The policy allocated by the subscription creator shall be consulted if a notification recipient made a request not to receive any more notifications.

Policies can be updated through a subscription refresh just like any other attribute for the subscription.

The call flow below illustrates an example to illustrate the abiev concepts:

## Solution Evaluation

The above framework provides flexible and simple way to handle, through provisioned policies,  notification recipient requests.  The flexibility for defining the policies, as well as the simple referencing to them through a policy-ID, combined with the ability to update the policies real time provide all what is need to support a large number of consumer and industrial related applications. In addition, references to policy-IDs allow policies to be reused acorss different subscriptiuon events.

If this solution is agreed upon, then normative text shall follow in accordance with that.

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?