ARC-2015-1797SecurityAlignment

Change Request

| CHANGE REQUEST |
| --- |
| Meeting:* | ARC16 |
| Source:* | Gemalto (ETSI) |
| Date:* | 2015-03-19 |
| Contact:* | francois.ennesser@gemalto.com |
| Reason for Change/s:* | Clause 11 of TS-0001, providing references to the TS-0003 security specifications, does not reflect the latest status of TS-0003 Release 1 following its finalization at TP 14 and TP 15. |
| CR against: Release* | Release 1 |
| CR against: WI* | Active MNT Maintenance STE Small Technical Enhancements Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0001 v 1.6.1 |
| Clauses/Sub Clauses* | Subclauses of Clause 11 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

### Following finalization of the initial release of TS-0003 at TP14, some alignments must be made in the Security clause of TS-0001to reflect the latest status. The intention of the present CR is to propose applicable corrections to Section 11 of TS-0001.

### This CR is based on previous contributions which were discussed but could not be finalized during TP15, especially latest revisions of ARC-1703 and ARC-1726 which were drafted  by Qualcomm.

### -----------------------Start of change 1 -------------------------------------------

## 11.1	Enrolling M2M Nodes and M2M Applications for oneM2M Services

Though M2M Nodes in the field domain are assumed to communicate without human involvement, individuals or organizations remain responsible for setting the access control policies used to authorize their M2M Nodes to access M2M services. In the following text, M2M Nodes refers to M2M field nodes.

In particular, individuals or organizations acquiring M2M Nodes can subscribe to a contract with an M2M Service provider (M2M Service Subscription) under which they enrol their M2M Nodes (e.g. using identifiers pre-provisioned on the nodes, such as Node-ID). This in turn may require an M2M Service provisioning step (including Security provisioning) that takes place on the target M2M Nodes themselves, for which interoperable procedures are specified by oneM2M (see clause 11.2.1). Following M2M service provisioning, the nodes can be identified and authenticated for association with an M2M Service Subscription, whose properties reflect the contractual agreement established between their owner and the M2M Service Provider.

Similarly, it shall be possible for an M2M Service Provider to mandate that applications accessing M2M services be provisioned with security credentials used to authorize specific operations to instantiated applications (see clause 11.2.2). This step facilitates the deployment and management of applications that are instantiated in great numbers, as it enables all instances of an application to be managed through common security policies that are set once for all. It also enables keeping control over applications issued by untrusted sources.

The above steps may be delegated to an M2M trust enabler, when this role is not assumed by the M2M Service Provider.

## 11.2	M2M Initial Provisioning Procedures

### 11.2.1	M2M Node Enrolment and Service Provisioning

M2M service provisioning is the process by which M2M Nodes are loaded with the specific information needed to seamlessly access the M2M Services offered by an M2M Service Provider. This is an initial step performed only when an M2M Node is enrolled for using the M2M services of an M2M Service Provider. Though this process can be performed during device manufacturing, there is a need to enable this process to take place during field deployment in an interoperable way. M2M service provisioning assumes the existence of an M2M service subscription contracted with the target M2M Service Provider for the target M2M Node. Remote provisioning scenarios require the M2M Node to be mutually authenticated using pre-existing credentials (e.g. Node-ID and associated credential) with an M2M enrolment function, to securely exchange the provisioning information with the contracted M2M Service Provider. The M2M Service Provisioning takes place between an M2M Node (without provisioned CSE) and an M2M Service Provider via an M2M enrolment function. As a result of provisioning, M2M Nodes are provided with necessary credentials and possibly other M2M service related parameters (e.g. CSE-ID, M2M-Sub-ID).

The first step of M2M service provisioning is the security provisioning procedure, by which M2M service provider specific credentials are either shared between two M2M Nodes, or shared between the M2M Node in the field domain and an M2M authentication function in the infrastructure. Authenticated M2M Nodes can then be associated with an M2M Service Subscription used to determine their specific authorizations.

The following security provisioning scenarios are supported by the oneM2M architecture:

- Pre-provisioning:

Pre-provisioning includes all forms of out-of-band provisioning, e.g. provisioning M2M Nodes with M2M subscription information during the manufacturing stage.

Remote provisioning:

Remote provisioning relies on pre-existing credentials in M2M Nodes (e.g. digital certificates or network access credentials) to provision subscription related parameters through a secure session with an M2M Enrolment Function. This form of provisioning enables M2M Nodes already in the field (e.g. operational M2M Nodes) to be provisioned with M2M Service subscription.

When supported, remote provisioning procedure shall be implemented as described in the oneM2M security specification [1].

Following M2M service provisioning, the provisioned entity securely stores credentials used for authentication, with an associated lifetime (e.g. corresponding to the duration of the contractual agreement embodied by the M2M service subscription).

### 11.2.2	M2M Application Enrolment

This procedure is an optional step that enables the M2M SP and/or M2M application provider to control which applications are allowed to use the M2M services. It assumes that M2M applications obtains or registers credentials to be used for controlling authorization with an M2M application registration authority (see clause 7.1.3).. Each application identified by an App-ID is then associated with a security credential which can be used to grant specific authorization to application instances to access an approved list of M2M services, or revoke access to all instances of undesirable applications. Such authorization takes place between a CSE and an AE as specified in the present document and the oneM2M security specification [1].

## 11.3	M2M Operational Security Procedures

This clause introduces the high level procedures, following M2M Enrolment, that shall be performed before any other procedure on Mcc and Mca can take place. These procedures shall be implemented as specified in the oneM2M security specification [1].

Figure 11.3-1. High Level Procedures on Mcc or Mca

### 11.3.1	Identification of CSE and AE

Once a CSE or AE is provisioned with its security credentials, there is no need to configure long-term secret information to the CSE or AE. However, additional non-secret information may need to be configured.

Prior to a CSE or AE initiating security association establishment, the Registree CSE or AE is configured with the Registrar CSE-ID so that the Registree knows who to establish the security association with. This process is called “Association Configuration” in TS-0003 [1]. Some authentication methods also require additional non-secret information be configured to the Registree and/or Registree – the details are specific to the authentication mechanism.

### 11.3.2	Authentication and Security Association of CSE and AE

The association security handshake (See TS-0003 [1]) provides dual purposes of

(a) mutual authentication of CSE and AE and

(b) session key derivation.

Prior to granting access to M2M services, the credentials resulting from the M2M Node and M2M application enrolment procedures shall be used, together with the information supplied in the identification step (clause 11.1), to perform mutual authentication of the Registree CSE or AE with the Registrar CSE. Upon mutual authentication:

- Registree CSE or AE associates, with the Registrar CSE, the CSE-ID supplied in the identification step (clause 11.1).

- If the Registree CSE or AE has previously registered successfully with the Registrar CSE and the Registrar CSE has cached the applicable M2M service subscription and CSE-ID or AE-ID, then the Registrar CSE can use this information.

- In other cases, the Registrar CSE determines the applicable M2M service subscription and CSE-ID or AE-ID as described in clause 10.1.1.2 “Registration related CREATE procedure” in the present document.

The Registree receives authorization to access the M2M services defined in the M2M Service Subscription.

Session keys are then derived for providing desired security services to the communicating entities, such as confidentiality and/or integrity of information exchange (these security services may be provided through establishment of a secure channel between the communicating entities or through object based security where only relevant information is encrypted prior to being shared). The lifetime of a security association shall be shorter than the lifetime of the credential used for authentication from which it is derived: It may be valid for the duration of a communication session, or be determined according to the validity period of the protected data. In case of a security association between two AEs, the lifetime of the security association can result from a contractual agreement between the subscribers of the communicating AEs.

### -----------------------End of change 3---------------------------------------------

# Comments

BUG: Not all authentication is through an M2M Authentication Function. Delete this.

BUG: credentials can be shared by two M2M Nodes, as well as by an M2M Node and M2M Authentication Function..

BUG: An ADN on an AE can be remotely provisioned. Easier to just ae “the M2M Node”

BUG: the credential can be associated with another M2M Node or an M2M Authentication function – easiest to just not dictate which.

REGISTRATION ALIGNMENT

REGISTRATION ALIGNMENT

BUG: The description of Identification no longer aligns with the SEC and ARC specifications. DELETE

EDITORIAL: The reference to [1] is moved to the beginning of clause 11.3

EDITORIAL: The reference to [1] is moved to the beginning of clause 11.3

This term is not used elsewhere. In fact, the opposite is true: security context establishment occurs as a result of Security Association Establishment Framework.

REGISTRATION ALIGNMENT

EDITORIAL: Clarification

EDITORIAL: The reference to [1] is moved to the beginning of clause 11.3