| CHANGE REQUEST |
| --- |
| Meeting:* | ARC17 |
| Source:* | Omar Elloumi, Alcatel-Lucent (ATIS), omar.elloumi@alcatel-lucent.com Martin Bauer, NEC Europe Ltd. (ETSI), martin.bauer@neclab.eu Joerg Swetina, NEC Europe Ltd. (ETSI), joerg.swetina@neclab.eu Ataru Kobayashi, NEC Corporation (TTC), a-kobayashi@df.jp.nec.com Mahdi Ben Alaya, LAAS-CNRS (ETSI), ben.alaya@laas.fr Khalil Drira, LAAS-CNRS (ETSI), khalil@laas.fr |
| Date:* | 2015-05-06 |
| Contact:* | Omar Elloumi, Alcatel-Lucent (ATIS), omar.elloumi@alcatel-lucent.com Martin Bauer, NEC Europe Ltd. (ETSI), martin.bauer@neclab.eu Joerg Swetina, NEC Europe Ltd. (ETSI), joerg.swetina@neclab.eu Ataru Kobayashi, NEC Corporation (TTC), a-kobayashi@df.jp.nec.com Mahdi Ben Alaya, LAAS-CNRS (ETSI), ben.alaya@laas.fr Khalil Drira, LAAS-CNRS (ETSI), khalil@laas.fr |
| Reason for Change/s:* | Introduce semantic description of AE, container and contentInstance resources |
| CR against: Release* | oneM2M R2 |
| CR against: WI* | X Active WI-0005 MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0001 and 2.1.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality X New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO X This CR is a mirror CR? YES NO X if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution adds a <semanticDescriptor> resource that can be a child resource of AE, container and contentInstance resources. The idea is that the semanticDescriptor contains the semantic description of the resource and possibly including common aspects of child resource. The semantic description can also contain further links to other resources to which there is a semantic relation.

For example, the semantic description of an AE may semantically describe the application functionalities, e.g. how to start and stop a washing machine, the semantic description of a container instance may describe the general purpose of the container, e.g. that it stores the current water temperature of a boiler,  and common aspects about the contentInstances, e.g.  that the unit of the temperature values is celsius, whereas the semantic description of a content instance may store aspects relevant to the specific instance, e.g. the accuracy of the contained GPS measurement (depends on the currently visible satellites, i.e. may be different for each instance).

The motivation to bring this contribution is related to the following requirements:

| ANN-003 | The oneM2M System shall support semantic annotation of oneM2M resources for example application related data contained in containers. |  |
| --- | --- | --- |
| QRY-001 | The oneM2M System shall provide capabilities to discover oneM2M resources based on semantic descriptions. |  |
| ANN-001 | The oneM2M System shall provide capabilities to manage semantic information about the oneM2M resources, e.g, create, retrieve, update, delete, associate/link. |  |
| ANN-002 | The oneM2M System shall support a common language for semantic description, e.g. RDF. |  |
| ANN-004 | The oneM2M System shall support semantic annotation based on related ontologies. |  |
| ANN-005 | The oneM2M System shall provide the capability for making semantic descriptions available in the oneM2M System, e.g. announcement. |  |

We propose to add semantic descriptors to AE, container and contentInstance resources for which we provide examples below. In the future, we may add it to additional resources given there is a clear motivation.

- AE: AEs implement an M2M application service logic, e.g. there may be an AE that represents the service logic  of a washing machine. The semantic descriptor would describe the functionalities offered by the washing machine and how you can interact with it, e.g. which containers are used to provide the current state or how the creation of a contentInstance can be used to start or stop the washing machine.

- Container: containers contain contentInstances. This can be data provided by appliactions, e.g.sensor data. In this case, the semantic descriptor would describe information related to the sensor information, e.g. that the contentInstances contain temperature information, the unit is Celsius, the accuracy is +/-1°C, etc.

- contentInstance: while some semantic information applies to all contentInstances and should be added to the semantic descriptor of the container, other information may be specific to the contentInstance, e.g. in the case of GPS sensor information, the accuracy of the measurement depends on the visibility of satellites, which could be different for each measurement.

Beyond making semantic information accessible to applications, the semantic information will be used for providing semantically enhanced functionalities of the platform. In a first step, this will be semantic discovery, further  semantic functionalities will be semantic mash-ups and supporting data analytics based on semantic information.

### -----------------------Start of change 1-------------------------------------------

#### 9.6.1.1	Resource Type Summary

Table 9.6.1.1-1 introduces the normal and virtual resource types and their related child or parent resource types. Details of each resource type follow in the remainder of this clause.

Table 9.6.1.1-1 lists each specified <resourceType>. An addition of suffix "Annc" to such <resourceTypes> indicates the associated announced resource type.

Table 9.6.1.1-1 Resource Types

| Resource Type | Short Description | Child Resource Types | Parent Resource Types | Clause |
| --- | --- | --- | --- | --- |
| accessControlPolicy | Stores a representation of privileges. It is associated with resources that shall be accessible to entities external to the Hosting CSE. It controls "who" is allowed to do "what" and the context in which it can be used for accessing resources | subscription | AE, AEAnnc, remoteCSE, remoteCSEAnnc, CSEBase | 9.6.2 |
| AE | Stores information about the AE. It is created as a result of successful registration of an AE with the Registrar CSE | subscription, container, group, accessControlPolicy, schedule, pollingChannel, semanticDescriptor | remoteCSE, remoteCSEAnnc, CSEBase | 9.6.5 |
| container | Shares data instances among entities. Used as a mediator that buffers data exchanged between AEs and/or CSEs. The exchange of data between AEs (e.g. an AE on a Node in a field domain and the peer-AE on the infrastructure domain) is abstracted from the need to set up direct connections and allows for scenarios where both entities in the exchange do not have the same reachability schedule | container, contentInstance, subscription, latest, oldest, semanticDescriptor | AE, AEAnnc, container, containerAnnc, remoteCSE, remoteCESAnnc, CSEBase | 9.6.6 |
| contentInstance | Represents a data instance in the <container> resource | semanticDescriptor | Container, containerAnnc | 9.6.7 |
| CSEBase | The structural root for all the resources that are residing on a CSE. Stores information about the CSE itself | remoteCSE, remoteCSEAnnc, node, AE, container, group, accessControlPolicy, subscription,, mgmtCmd, locationPolicy, statsConfig, statsCollect, request, delivery, schedule | None specified | 9.6.3 |
| delivery | Forwards requests from CSE to CSE | subscription | CSEBase | 9.6.11 |
| eventConfig | Defines events that trigger statistics collection | subscription | statsConfig | 9.6.24 |
| execInstance | Contains all execution instances of the same Management Command | subscription | mgmtCmd | 9.6.17 |
| fanOutPoint (V) | Virtual resource containing target for group request It is used for addressing bulk operations to all the resources that belong to a group | None specified | group | 9.6.14 |
| group | Stores information about resources of the same type that need to be addressed as a Group. Operations addressed to a Group resource shall be executed in a bulk mode for all members belonging to the Group | fanOutPoint, subscription | AE, AEAnnc, remoteCSE, remoteCSEAnnc, CSEBase | 9.6.13 |
| latest (V) | Virtual resource that points to most recently created <contentInstance> child resource within a <container> resource | None specified | container | 9.6.27 |
| locationPolicy | Includes information to obtain and manage geographical location. It is only referenced within a container, the contentInstances of the container provide location information | subscription | CSEBase | 9.6.10 |
| mgmtCmd | Management Command resource represents a method to execute management procedures required by existing management protocols | execInstance, subscription | CSEBase | 9.6.16 |
| mgmtObj | Management Object resource represents management functions that provides an abstraction to be mapped to external management technology. It represents the node and the software installed in the node (see note) | subscription, mgmtObj, schedule | node, mgmtObj, mgmtObjAnnc | 9.6.15 Annex D |
| m2mServiceSubscriptionProfile | Data pertaining to the M2M Service Subscription | serviceSubscribedNode, subscription | CSEBase | 9.6.19 |
| node | Represents specific Node information | mgmtObj, subscription | CSEBase, remoteCSE | 9.6.18 |
| oldest (V) | Virtual resource that points to first created <contentInstance> child resource within a <container> resource | None specified | container | 9.6.28 |
| pollingChannel | Represent a channel that can be used for a request-unreachable entity | pollingChannelURI | remoteCSE, AE | 9.6.21 |
| pollingChannelURI (V) | Virtual resource used to perform service layer long polling of a resource Hosting CSE by a request-unreachable entity | None specified | pollingChannel | 9.6.22 |
| remoteCSE | Represents a remote CSE for which there has been a registration procedure with the registrar CSE identified by the CSEBase resource | AE, container, group, accessControlPolicy, subscription, pollingChannel, schedule, node | CSEBase | 9.6.4 |
| request | Expresses/access context of an issued Request | subscription | CSEBase | 9.6.12 |
| schedule | Contains scheduling information for delivery of messages | subscription | subscription, CSEBase, remoteCSE,AE | 9.6.9 |
| serviceSubscribedNode | Node information | subscription | m2mServiceSubscriptionProfile | 9.6.20 |
| statsCollect | Defines triggers for the IN-CSE to collect statistics for applications | subscription | CSEBase (in IN-CSE) | 9.6.25 |
| statsConfig | Stores configuration of statistics for applications | eventConfig, subscription | CSEBase (in IN-CSE) | 9.6.23 |
| Subscription | Subscription resource represents the subscription information related to a resource. Such a resource shall be a child resource for the subscribe-to resource | schedule | accessControlPolicy,accessControlPolicyAnnc, AE, AEAnnc, container, CSEBase, delivery, eventConfig, execInstance, group, groupAcce, locationPolicy, mgmtCmd, mgmtObj, mgmtObjAnnc, m2mServiceSubscriptionProfile, node, nodeAnnc, serviceSubscribedNode, remoteCSE, remoteCSEAnnc, request, schedule, statsCollect, statsConfig | 9.6.8 |
| serviceSubscribedAppRule | Represents a rule that defines allowed App-ID and AE-ID combinations that are acceptable for registering an AE on a Registrar CSE | subscription | CSEBase | 9.6.29 |
| semanticDescriptor | Stores semantic description pertaining to a resource and potentially sub-resources. | subscription | AE, container, contentInstance | 9.6.30 |
| NOTE: See clause 9.6.12 for a summary of specializations of <mgmtObj>. |

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

### 9.6.5	Resource Type AE

An <AE> resource shall represent information about an Application Entity registered to a CSE.

Figure 9.6.5-1: Structure of <AE> resource

The <AE> resource shall contain the child resources specified in table 9.6.5-1.

# Table 9.6.5-1: Child resources of <AE> resource

| Child Resources of <AE> | Child Resource Type | Multiplicity | Description | <AEAnnc> Child Resource Types |
| --- | --- | --- | --- | --- |
| semanticDescriptor | <semanticDescriptor> | 0..n | See clause 9.6.30 | <semanticDescriptor>, <semanticDescriptorAnnc> |
| [variable] | <subscription> | 0..n | See clause 9.6.8 | <subscription> |
| [variable] | <container> | 0..n | See clause 9.6.6 | <container> <containerAnnc> |
| [variable] | <group> | 0..n | See clause 9.6.13 | <group> <groupAnnc> |
| [variable] | <accessControlPolicy> | 0..n | See clause 9.6.2 | <accessControlPolicy> <accessControlPolicyAnnc> |
| [variable] | <schedule> | 0..1 | See clause 9.6.9 | <scheduleAnnc> |
| [variable] | <pollingChannel> | 0..n | See clause 9.6.21. When the AE is request-unreachable, the AE should create this <pollingChannel> resource and perform long polling. | None |

The <AE> resource shall contain the attributes specified in table 9.6.5-2.

# Table 9.6.5-2: Attributes of <AE> resource

| Attributes of <AE> | Multiplicity | RW/ RO/ WO | Description | <AEAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | NA |
| resourceID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | MA |
| resourceName | 1 | WO | See clause 9.6.1.3 where this common attribute is described. | MA |
| parentID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | NA |
| expirationTime | 1 | RW | See clause 9.6.1.3 where this common attribute is described. | MA |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3 where this common attribute is described. | MA |
| creationTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | NA |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | NA |
| labels | 0..1 (L) | RW | See clause 9.6.1.3 where this common attribute is described. | MA |
| announceTo | 0..1 (L) | RW | See clause 9.6.1.3 where this common attribute is described. | NA |
| announcedAttribute | 0..1 (L) | RW | See clause 9.6.1.3 where this common attribute is described. | NA |
| appName | 0..1 | RW | The name of the application, as declared by the application developer(e.g. "HeatingMonitoring"). Several sibling resources may share the appName. | OA |
| App-ID | 1 | WO | The identifier of the Application (see clause 7.1.2). | OA |
| AE-ID | 1 | RO | The identifier of the Application Entity (see clause 7.1.2). | OA |
| pointOfAccess | 0..1 (L) | RW | The list of addresses for communicating with the registered Application Entity over Mca reference point via the transport services provided by Underlying Network (e.g. IP address, FQDN, URI). This attribute shall be accessible only by the AE and the Hosting CSE. If this information is not provided, the AE should use <pollingChannel> resource. Then the Hosting CSE can forward a request to the AE without using the PoA. | OA |
| ontologyRef | 0..1 | RW | A URI of the ontology used to represent the information that is managed and understood by the AE. | OA |
| requestReachability | 1 | RW | If the AE that created this <AE> resource can receive a request, this attribute is set to "TRUE" otherwise "FALSE" | OA |
| nodeLink | 0..1 | RO | The resourceID of a <node> resource that stores the node specific information where the AE resides. | OA |

### 9.6.6	Resource Type container

The <container> resource represents a container for data instances. It is used to share information with other entities and potentially to track the data. A <container> resource has no associated content. It has only attributes and child resources.

Figure 9.6.6-1: Structure of <container> resource

The <container> resource shall contain the child resources specified in table 9.6.6-1.

# Table 9.6.6-1: Child resources of <container> resource

| Child Resources of <container> | Child Resource Type | Multiplicity | Description | <containerAnnc> Child Resource Types |
| --- | --- | --- | --- | --- |
| semanticDescriptor | <semanticDescriptor> | 0..n | See clause 9.6.30 | <semanticDescriptor>, <semanticDescriptorAnnc> |
| [variable] | <contentInstance> | 0..n | See clause 9.6.7 | <contentInstance>, <contentInstanceAnnc> |
| [variable] | <subscription> | 0..n | See clause 9.6.8 | <subscription> |
| [variable] | <container> | 0..n | See clause 9.6.6 | <container> <containerAnnc> |
| latest | <latest> | 1 | See clause 9.6.27 | None |
| oldest | <oldest> | 1 | See clause 9.6.28 | None |

The <container> resource shall contain the attributes specified in table 9.6.6-2.

# Table 9.6.6-2: Attribute of <container> resource

| Attributes of <container> | Multiplicity | RW/ RO/ WO | Description | <containerAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | NA |
| resourceID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | MA |
| resourceName | 1 | WO | See clause 9.6.1.3 where this common attribute is described. | MA |
| parentID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | NA |
| expirationTime | 1 | RW | See clause 9.6.1.3 where this common attribute is described. | MA |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3 where this common attribute is described. If no accessControlPolicyIDs are provided at the time of creation, the accessControlPolicyIDs of the parent resource is linked to this attribute | MA |
| Labels | 0..1 (L) | RW | See clause 9.6.1 where this common attribute is described. | MA |
| creationTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | NA |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | NA |
| stateTag | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | OA |
| announceTo | 0..1 (L) | RW | See clause 9.6.1.3 where this common attribute is described. | NA |
| announcedAttribute | 0..1 (L) | RW | See clause 9.6.1.3 where this common attribute is described. | NA |
| Creator | 0..1 | RO | The AE-ID or CSE-ID of the entity which created the resource. | NA |
| maxNrOfInstances | 0..1 | RW | Maximum number of instances of <contentInstance> child resources. | OA |
| maxByteSize | 0..1 | RW | Maximum number of bytes that are allocated for a <container> resource for all instances in the <container> resource. | OA |
| maxInstanceAge | 0..1 | RW | Maximum age of the instances of <contentInstance> resources within the <container>. The value is expressed in seconds. | OA |
| currentNrOfInstances | 1 | RO | Current number of instances in a <container> resource. It is limited by the maxNrOfInstances. | OA |
| currentByteSize | 1 | RO | Current size in bytes of data stored in total using child <contentInstance> resources of a <container> resource. It is limited by the maxNrOfBytes. | OA |
| locationID | 0..1 | RW | An ID of the resource where the attributes/policies that define how location information are obtained and managed. This attribute is defined only when the <container> resource is used for containing location information. | OA |
| ontologyRef | 0..1 | RW | A reference (URI) of the ontology used to represent the information that is stored in the child <contentInstance> resources of the present <container> resource (see note). | OA |
| NOTE: The access to this URI is out of scope of oneM2M. |

### 9.6.7	Resource Type contentInstance

The <contentInstance> resource represents a data instance in the <container> resource. The content of the contentInstance can be encrypted.

Unlike other resources, the <contentInstance> resource shall not be modified once created. An AE shall be able to delete a contentInstance resource explicitly or it may be deleted by the platform based on policies. If the platform has policies for contentInstance retention, these shall be represented by the attributes maxByteSize, maxNrOfInstances and/or maxInstanceAge attributes in the <container> resource. If multiple policies are in effect, the strictest policy shall apply.

The <contentInstance> resource inherits the same access control policies of the parent <container> resource, and does not have its own accessControlPolicyIDs attribute.

Figure 9.6.7-1: Structure of <contentInstance> resource

The <contentInstance> resource shall contain the child resources specified in table 9.6.7-1.

# Table 9.6.7-1: Child resources of <container> resource

| Child Resources of <contentInstance> | Child Resource Type | Multiplicity | Description | <contentInstanceAnnc> Child Resource Types |
| --- | --- | --- | --- | --- |
| semanticDescriptor | <semanticDescriptor> | 0..n | See clause 9.6.30 | <semanticDescriptor>, <semanticDescriptorAnnc> |

The <contentInstance> resource shall contain the attributes specified in table 9.6.7-2.

# Table 9.6.7-2: Attributes of <contentInstance> resource

| Attributes of <contentInstance> | Multiplicity | RW/ RO/ WO | Description | <contentInstanceAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | NA |
| resourceID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | MA |
| resourceName | 1 | WO | See clause 9.6.1.3 where this common attribute is described. | MA |
| parentID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | NA |
| labels | 0..1 (L) | WO | See clause 9.6.1.3 where this common attribute is described. | MA |
| expirationTime | 1 | RW | See clause 9.6.1.3 where this common attribute is described. | NA |
| creationTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | NA |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | NA |
| stateTag | 1 | RO | See clause 9.6.1.3 where this common attribute is described. The stateTag attribute of the parent resource should be incremented first and copied into this stateTag attribute when a new instance is added to the parent resource. | OA |
| announceTo | 0..1 (L) | RW | See clause 9.6.1.3 where this common attribute is described. | NA |
| announcedAttribute | 0..1 (L) | RW | See clause 9.6.1.3 where this common attribute is described. | NA |
| creator | 0..1 | RO | The AE-ID or CSE-ID of the entity which created the resource. | NA |
| contentInfo | 0..1 | WO | Information on the content that is needed to understand the content. This attribute is a composite attribute. It is composed first of an Internet Media Type (as defined in the IETF RFC 6838) describing the type of the data, and second of an encoding information that specifies how to first decode the received content. Both elements of information are separated by a separator defined in oneM2M TS-0004 [i.2]. | OA |
| contentSize | 1 | RO | Size in bytes of the content attribute. | OA |
| ontologyRef | 0..1 | WO | A reference (URI) of the ontology used to represent the information that is stored in the contentInstances resources of the <container> resource. If this attribute is not present, the contentInstance resource inherits the ontologyRef from the parent <container> resource if present NOTE: Access to this URI is out of scope of oneM2M. | OA |
| content | 1 | WO | Actual content of a contentInstance. This content may be opaque data for understandable with the help of the contentInfo. This may, for example, be an image taken by a security camera, or a temperature measurement taken by a temperature sensor. | OA |

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3-------------------------------------------

### 9.6.26	Resource Announcement

#### 9.6.26.1	Overview

A resource can be announced to one or more remote CSEs to inform the remote CSEs of the existence of the original resource.  An announced resource can have a limited set of attributes and a limited set of child resources from the original resource.  The announced resource includes a link to the original resource hosted by the original resource-Hosting CSE.

In case that the original resource is deleted, all announced resources for the original resource shall be deleted, except for <AEAnnc> resources that were created during the registration of an AE with AE-ID-Stem starting with "S", which shall not be deleted. If the announced resource is not deleted promptly (e.g. the announced resource is not reachable), the announced resource can be deleted later either by the original resource Hosting CSE or by the expiration of the announced resource itself. The original resource shall store the list of links for the announced resources for those purposes.

Synchronization between the attributes announced by the original resource and the announced resource is the responsibility of the original resource Hosting CSE. The access control policy for the announced resource shall synchronize with the one from the original resource. In case that the attribute accessControlPolicyIDs is not present in the original resource it is the responsibility of the original resource Hosting CSE to choose the appropriate value depending on the policy for the original resource (e.g. take the parent accessControlPolicyIDs value).

The original resource shall have at least announceTo attribute present if the resource itself has been announced. If any of the Optional Announced (OA) attributes are also announced, then announcedAttribute attribute shall also be present. An AE or other CSE can request the original resource Hosting CSE for announcing the original resource to the list of CSE-IDs or the address(es) listed in the announceTo attribute in the announcing request. An Update to the announceTo attribute will trigger new resource announcement(s) or the de-announcement(s) of the announced resource. After a successful announcement procedure the attribute announceTo contains only the list of address(es) of the announced resources.

In order to announce an attribute marked as OA (see clause 9.5.1.1), the attribute shall be included in the announcedAttribute attribute list at the original resource. The attributes included in the announcedAttribute attribute are announced to the announced resource. On successful announcement of the resource, such attributes shall be created at the announced resource; otherwise they shall not be present in the announced resource. Update to the announcedAttribute attribute in the original resource will trigger new attribute announcement or the de-announcement of the announced attribute(s). The announced attributes shall have the same value as the original resource, and synchronization between the value of the announced attributes at the original resource and the announced resource is the responsibility of the original resource Hosting CSE.

An announced resource may have child resources. The child resource shall be of the same type as the original child resource or its associated Announce type.

Child resources of the original resource can be announced independently as needed. In this case, the child resources at the announced resource shall be of the child resource "Announced" type. When a child resource at the announced resource is created locally at the remote CSE, the child resource shall be of normal child resource type.

When a Hosting CSE of an original resource is initiating an announcement, it shall first check if the parent resource of the original resource has a representation at the announcement target CSE. If that is the case, the announced resource shall be created as a child resource of that representation of the parent resource. If that is not the case, the announced resource shall be created as a child of the <CSEBase> resource of the announcement target CSE.

Table 9.6.26.1-1: Announced Resource Types

| Announced Resource Type | Short Description | Child Resource Types | Clause |
| --- | --- | --- | --- |
| accessControlPolicyAnnc | Announced variant of accessControlPolicy | subscription | 9.6.2 |
| AEAnnc | Announced variant of AE | subscription, container, containerAnnc, group, groupAnnc, accessControlPolicy, accessControlPolicyAnnc, semanticDescriptor, semanticDescriptorAnnc | 9.6.5 |
| containerAnnc | Announced variant of container | container, containerAnnc, contentInstance, contentInstanceAnnc, subscription, semanticDescriptor, semanticDescriptorAnnc | 9.6.6 |
| contentInstanceAnnc | Announced variant of contentInstance | semanticDescriptor, semanticDescriptorAnnc | 9.6.7 |
| groupAnnc | Announced variant of group | subscription | 9.6.13 |
| locationPolicyAnnc | Announced variant of locationPolicy | None specified | 9.6.10 |
| mgmtObjAnnc | Announced variant of mgmtObj | subscription, mgmtObj, mgmtObjAnnc, scheduleAnnc | 9.6.15 |
| nodeAnnc | Announced variant of node | mgmtObjAnnc, subscription | 9.6.18 |
| remoteCSEAnnc | Announced variant of remoteCSE | AE, AEAnnc, container, containerAnnc, group, groupAnnc, accessControlPolicy, accessControlPolicyAnnc, subscription, scheduleAnnc, nodeAnnc, locationPolicyAnnc | 9.6.4 |
| scheduleAnnc | Announced variant of schedule | None specified | 9.6.39 Annex D |

### -----------------------End of change 3---------------------------------------------

### -----------------------Start of change 4-------------------------------------------

### 9.6.30	Resource semanticDescriptor

The <semanticDescriptor> resource is used to store a semantic description pertaining to a resource and potentially sub-resources. Such a description may be provided according to ontologies. The semantic information is used  by the semantic functionalities of the oneM2M system and is also available to applications or CSEs.  [i.30] provides an informative example of a descriptor attribute.

Editor’s note: There might be a need to make a normative reference to a stage 3 TS, depending how far PRO goes in standardizing semantic descriptors using RDF or OWL formats.

Figure 9.6.30-1: Structure of <semanticDescriptor> resource

The <semanticDescriptor> resource shall contain the child resources specified in table 9.6.30-1.

Table 9.6.23-1: Child resources of <semanticDescriptor> resource

| Child Resources of <semanticDescriptor> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 where the type of this resource is described. |

The <semanticDescriptor> resource shall contain the attributes specified in table 9.6.23-2.

Table 9.6.23-2: Attributes of <semanticDescriptor> resource

| Attributes of <semanticDescriptor> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 where this common attribute is described |
| resourceID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| resourceName | 1 | WO | See clause 9.6.1.3 where this common attribute is described. |
| parentID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3 where this common attribute is described |
| creationTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described |
| expirationTime | 1 | RW | See clause 9.6.1.3 where this common attribute is described |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described |
| labels | 0..1 (L) | RW | See clause 9.6.1.3 where this common attribute is described |
| creator | 0..1 | RO | The AE-ID of the entity which created the resource. This can also be the CSE-ID of the IN-CSE if the IN-CSE created the resource. |
| descriptor | 1 | RW | store a semantic description pertaining to a resource and potentially sub-resources. Such a description may be provided according to ontologies |
| ontologyRef | 0..1 | WO | A reference (URI) of the ontology used to represent the information that is stored in the descriptor attribute. If this attribute is not present, the ontologyRef from the parent resource is used if present. |

Editor’s note: the possibility for  semantic descriptor attribute t link to other descriptor attributes is not excluded to optimize storage but it needs further study.

### -----------------------End of change 4 ---------------------------------------------

### -----------------------Start of Changes to References Section -------------

## 2.2	Informative references

References are either specific (identified by date of publication and/or edition number or version number) or non-specific. For specific references, only the cited version applies. For non-specific references, the latest version of the reference document (including any amendments) applies.

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

[i.1]	oneM2M TS-0002: " Requirements".

[i.2]	oneM2M TS-0004: "Service Layer Core Protocol Specification".

[i.3]	oneM2M TS-0003: " Security Solutions".

[i.4]	TR-069: "CPE WAN Management Protocol Issue": 1 Amendment 5, November 2013, Broadband Forum.

[i.5]	OMA-DM: "OMA Device Management Protocol", Version 1.3, Open Mobile Alliance.

[i.6]	LWM2M: "OMA LightweightM2M", Version 1.0, Open Mobile Alliance.

[i.7]	OMA-TS-MLP-V3-4-20130226-C: "Mobile Location Protocol", Version 3.4.

[i.8]	OMA-TS-REST-NetAPI_TerminalLocation-V1_0-20130924-A: "RESTful Network API for Terminal Location", Version 1.0.

[i.9]	IETF RFC 1035: "Domain names - Implementation and specification".

[i.10]	IETF RFC 3588: "Diameter Base Protocol".

[i.11]	IETF RFC 3596: "DNS Extensions to Support IP Version 6".

[i.12]	IETF RFC 3986: "Uniform Resource Identifier (URI): General Syntax".

[i.13]	IETF RFC 4006: "Diameter Credit-Control Application".

[i.14]	IETF RFC 6895: "Domain Name System (DNS) IANA Considerations".

[i.15]	GSMA-IR.67: "DNS/ENU Guidelines for Service Providers & GRX/IPX Providers".

[i.16]	3GPP TS 23.682: "Architecture enhancements to facilitate communications with packet data networks and applications (Release 11)".

[i.17]	ETSI TS 132 240: "Digital cellular telecommunications system (Phase 2+); Universal Mobile Telecommunications System (UMTS); LTE; Telecommunication management; Charging management; Charging architecture and principles (3GPP TS 32.240)".

[i.18]	ETSI TS 132 299: "Digital cellular telecommunications system (Phase 2+); Universal Mobile Telecommunications System (UMTS); LTE; Telecommunication management; Charging management; Diameter charging applications (3GPP TS 32.299)".

[i.19]	3GPP2 .S0068: "Network Enhancements for Machine to Machine (M2M)".

[i.20]	JNI 6.0 API Specification: "Java Native Interface 6.0 Specification".

[i.21]	3GPP TS 23.401: "General Packet Radio Service (GPRS) enhancements for Evolved Universal Terrestrial Radio Access Network (E-UTRAN) access".

[i.22]	3GPP TS 23.402: "Architecture enhancements for non-3GPP accesses".

[i.23]	3GPP TS 23.060: "General Packet Radio Service (GPRS); Service description; Stage 2".

[i.24]	3GPP TS 22.368: "Service requirements for Machine Type Communications (MTC); Stage 1".

[i.25]	3GPP TS 23.003: "Numbering, addressing and identification".

[i.26]	Recommendation ITU-T X.660 | ISO/IEC 9834-1: "Information technology - Procedures for the operation of object identifier registration authorities: General procedures and top arcs of the international object identifier tree".

[i.27]	oneM2M TR-0008: "Analysis of Security Solutions for oneM2M System".

[i.28]	IETF RFC 4122: "A Universally Unique IDentifier (UUID) URN Namespace".

[i.29]	oneM2M Drafting Rules.

[i.30]	oneM2M TR-0007: "Study of Abstraction and Semantics Enablement".

NOTE:	Available at http://member.onem2m.org/Static_pages/Others/Rules_Pages/oneM2M-Drafting-Rules-V1_0.doc.

### -----------------------End of Changes to References  -------------

### -Start of changes to Definitions Symbols Abbreviations Acronyms -

# 3	Definitions, symbols, abbreviations  and acronyms

## 3.1	Definitions

<defined term>: <definition>

<defined term>[N]: <definition>

## 3.2	Symbols

<symbol>	<Explanation>

## 3.3	Abbreviations and Acronyms

<ABBREVIATION/ACRONYM>	<Explanation>

### ---End of changes to Definitions, Symbols, Abbreviations, Acronyms ---

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?