| CHANGE REQUEST |
| --- |
| Meeting:* | ARC 17.0 |
| Source:* | KT Corp. (TTA) |
| Date:* | 2015-MM-DD |
| Contact:* | Francisco Sang-Eon Kim (kim.sangeon@kt.com) |
| Reason for Change/s:* | Some mandatory parameters for Request message and Response message are missed. This is not consistent with between Request/Response Message at 8.1.2/8.1.3 and Section 10.1.5 for NOTIFY. |
| CR against: Release* | Release 1 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0001-V1.8.0 |
| Clauses/Sub Clauses* | 10.1.5. NOTIFY(N) |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Parameters of Request Message are specified with mandatory, conditional and optional at 8.1.2.

The mandatory parameters for Request Message are To, From, Operation and Request Identifier.

The conditional parameters for Request Message are Content and Resource Type. Content parameter is mandatory for NOTIFY operation. Resource Type parameter is not applicable for NOTIFY operation.

The optional parameters for Request Message are Role, Name, Originating Timestamp, Request Expiration Timestamp, Result Expiration Timestamp, Response Type, Result Content, Result Persistence, Operation Execution Time, Event Category, Delivery Aggregation, Group Request Identifier, Filter Criteria and Discovery Result Type.

Request Identifier parameter, mandatory parameter, is missed at Step 002 for Figure 10.1.5-1.

Parameters of Response Message are specified with mandatory, conditional and optional at 8.1.3.

The mandatory parameters for Response Message are Response Code and Request Identifier.

The conditional parameters for Response Message are Content.

The optional parameters for Response Message are To, From, Originating Timestamp, Result Expiration Timestamp, Event Category and Status Code.

Request Identifier parameter, mandatory parameter, is missed at Step 004 for 10.1.5-1.

### -----------------------Start of change 1-------------------------------------------

### 10.1.5	NOTIFY (N)

The NOTIFY operation shall be used for notifying information.

Originator: The Originator requests to notify an entity by using NOTIFY method. See clause 8.1.2 for the information to be included in a Request message.

Receiver: The Receiver responds to the Originator with the operation results as specified in clause 8.1.3.

Figure 10.1.5-1: Procedure for NOTIFYing Information

Step 001: A notification to be sent to the Receiver is triggered in the Originator.

Step 002: The Originator shall send the following parameters in the NOTIFY Request message:

Mandatory Parameters:

- Operation: N (Notify).

- To: URI/Address where the notification should be sent to.

# From: ID of the Originator (only a CSE).

# Request Identifier: Request Identifier provided by the Originator.

- Content: Notification data and/or Notification reference.

Step 003: Local Processing.

Step 004: The Receiver responds with a Response message that shall contain the following information:

Mandatory Parameters:

- Response Code: Operation result.

- Request Identifier: Request Identifier provided by the Originator.

General Exceptions:

See oneM2M TS-0003 [i.3].

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?