| CHANGE REQUEST |
| --- |
| Meeting:* | ARC#19.0 |
| Source:* | ZTE Corporation (CCSA) |
| Date:* | 2015-08-28 |
| Contact:* | Weixiang Shao, ZTE Corporation, shao.weixiang@zte.com.cn |
| Reason for Change/s:* | Add introduction about 3GPP MTC feature: MONTE |
| CR against: Release* | Rel-2.0 |
| CR against: WI* | Active / WI-0037 MNT Maintenance / < Work Item number (optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | oneM2M-TR-0024-v0.0.1 |
| Clauses/Sub Clauses* | 2.2, 5 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The CR Proposes to add introduction about 3GPP MTC feature: Monitoring Enhancements (MONTE).

### -----------------------Start of change 1-------------------------------------------

# 2	References

## 2.2	Informative references

Clause 2.2 shall only contain informative references which are cited in the document itself.

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

[i.1]	oneM2M Drafting Rules  (http://member.onem2m.org/Static_pages/Others/Rules_Pages/oneM2M-Drafting-Rules-V1_0.doc)

[i.3] 	3GPP TR 23.789: "Monitoring Enhancements"

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2---------------------------------------------

# 5	Introduction and analysis to 3GPP Service Capability Exposure

## 5.1	3GPP MTC features

## 5.1.2	Monitoring Enhancements

3GPP TR 23.789 [i.3] studies and evaluates architectural enhancements required for 3GPP systems to provide monitoring service capability. Monitoring feature is intended to use applicable architecture enhancements determined as part of AESE work item.

Monitoring is intended for monitoring of configured events. This comprises of means that allow for activating monitoring of specific events, the event detection and the reporting to authorised users, e.g. for use by applications or logging. For MTC Devices, it is desirable that the network detects and reports events (including location) caused by those. If such an event is detected, the network might be configured to perform special actions, e.g. limit the access or reduce the allocated resource.

- The following architectural requirements need to be met:Configuration of Monitoring Events and actions by 3rd party application provider

- Detection of Monitoring Events

- Reporting of Monitoring Events to 3rd party application provider

The set of capabilities required for monitoring may be accessible via different 3GPP interfaces/nodes (e.g. HSS via Sh (with enhancements), or PCRF via Rx (with enhancements), or MME/SGSN via a new interface). Reporting of the same event via different interfaces might be envisaged, to satisfy different usage scenarios (e.g.: different frequency of location reporting or different location accuracy requirements).

The combined MME/SGSN and HSS solution should be used as a basis for developing generic event monitoring flows. In this solution, configuration of event(s) is done by the SCEF on HSS, and if required, depending on the event type, on the serving node(s) via HSS. The reporting of event(s), depending on the event type, is done either via HSS or the serving node(s) to the SCEF. The monitoring via HSS path is intended for infrequent events reporting or when MME/SGSN based monitoring is not available (i.e. when a MME/SGSN does not support a requested monitoring feature).

Based on operator preferences, (Policy Control and Charging) PCC-based solution may be used for event(s) with the exception that existing 3GPP specifications for PCC will be used as-is. The main idea is that the SCEF receives the monitoring event subscription request or status queries from SCS or Application Server via API and distributes those to PCRF in HPLMN. PCC based monitoring functionality provides monitoring event reports via SCEF to SCS/AS. The SCEF plays the role of an AF in PCC reference architecture.

Table 5.1.2-1	Solution for specific Monitoring Events

| Event | Event type | Solution |
| --- | --- | --- |
| Roaming status, and Serving Network of the UE | One-time Roaming status or Serving Network of UE | Recommend combined MME/SGSN + HSS solution |
|  | Change in Roaming status or Serving Network of UE | Recommend combined MME/SGSN + HSS solution |
| Location of the UE | One-time current location of UE | Recommend combined MME/SGSN + HSS solution PCC-based solution for dynamic PCC |
|  | One-time last known location of UE | Recommend combined MME/SGSN + HSS solution PCC-based solution for dynamic PCC |
|  | Reporting upon change of location area | Recommend combined MME/SGSN + HSS solution |
|  | Continuous reporting of Location | Recommend combined MME/SGSN + HSS solution |
| Change in association of the MTC Device and UICC |  | Recommend combined MME/SGSN + HSS solution |
| Loss of connectivity |  | Recommend combined MME/SGSN + HSS solution |
| UE Reachability |  | Recommend combined MME/SGSN + HSS solution |
| Communication Failure | Limited to reporting of RAN/NAS failure cause code values | Recommend combined MME/SGSN + HSS solution PCC-based solution for dynamic PCC |
| Reporting the number of UEs present in a certain area | Limited to one time reporting | Recommend combined MME/SGSN + HSS solution, the event directly between in serving node(s) and SCEF |

### -----------------------End of change 2---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?