| CHANGE REQUEST |
| --- |
| Meeting:* | ARC#19.0 |
| Source:* | ZTE Corporation (CCSA) |
| Date:* | 2015-08-28 |
| Contact:* | Weixiang Shao, ZTE Corporation, shao.weixiang@zte.com.cn |
| Reason for Change/s:* | Add introduction about 3GPP MTC feature: HLCom |
| CR against: Release* | Rel-2.0 |
| CR against: WI* | Active / WI-0037 MNT Maintenance / < Work Item number (optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | oneM2M-TR-0024-v0.0.1 |
| Clauses/Sub Clauses* | 2.2, 5 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The CR Proposes to add introduction about 3GPP MTC feature: Support High Latency Communications (HLCom).

### -----------------------Start of change 1-------------------------------------------

# 2	References

## 2.2	Informative references

Clause 2.2 shall only contain informative references which are cited in the document itself.

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

[i.1]	oneM2M Drafting Rules  (http://member.onem2m.org/Static_pages/Others/Rules_Pages/oneM2M-Drafting-Rules-V1_0.doc)

[i.4] 	3GPP TR 23.709: "Study on Optimizations to Support High Latency Communications"

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2---------------------------------------------

# 5	Introduction and analysis to 3GPP Service Capability Exposure

## 5.1	3GPP MTC features

## 5.1.3	Support High Latency Communications

3GPP TR 23.709 [i.4] studies to support applications that communicate with devices that are not reachable for a long period over the 3GPP IP connectivity and being able to support large number of such devices in the system without negatively affecting the system performance.

It studies the following problem : Downlink access for devices that are not reachable for a long period and the problems associated with such devices (e.g. packet discard when the UE sleeps, frequent retransmissions, load on the CN network, waste of radio resources and UE power when the network unnecessarily conveys retransmit packets, etc.).

Which with two scenarios:

- Scenario A : Downlink packet transmission to UE applying power saving function

- Scenario B : Coordination of maximum latency between the application and the network

Study conclusions:

- Extended buffering in the SGW of downlink data buffering in S-GW or Gn-SGSN solution is used to handle high latency communication to devices using power saving functions e.g. eDRX and PSM.

- This solution addresses Scenario A by providing a mechanism to buffer data in S-GW or Gn-SGSN for later delivery to UEs that are unreachable for some time. The solution works regardless if the AS/SCS uses a SCEF interface or not. It also works regardless which power saving method is used, given that considerations in the eDRX work are taken. The solution has only minor impact on signalling protocols, i.e. the DDN and DDN Ack messages on S11 and S4. The solution has impact on S-GW buffer size, potentially a significant impact, but implementations may mitigate the impact. With regards to the impact on buffer resources the solution should preferably be used when the buffer time (power saving interval) has short and medium lengths. For long power saving intervals, it is recommended that instead a solution is applied where the AS/SCS only sends DL data when the UE is reachable to reduce required buffer resources.

- MONTE event notifications to notify an AS/SCS when downlink data can be sent to a UE that uses power saving functions e.g. PSM or eDRX, based on:

- Solution of Using Monitoring Event "UE Reachability", which is for Scenario A and Scenario B mainly for a UE which is adopting Power Saving Mode or other features that cause high latencies for downlink data e.g. eDRX (depending on eDRX study results). The Monitoring event "UE reachability" for MONTE in 3GPP TR 23.789 [i.3] is reused to inform about UE reachability to SCS/AS. If a SCS/AS wants to send downlink data to a sleeping UE (e.g. to a UE that is adopting Power Saving Mode), the SCS/AS registers a new Onetime Request 'UE reachability' monitoring event via the SCEF-interface/API in order to detect delivery availability. Then the SCS/AS sends MT data only when the UE is reachable i.e. when the SCS/AS receives a 'UE reachability' notification. This solution ensures the safe delivery of MT data if the SCS/AS sends MT data after the SCS/AS is informed the UE reachability.

- Solution of sending notifications triggered by DDN provides the ability to notify an application of the availability of a UE that may be a high latency UE, with minimized signalling load. The AS subscribes "network application triggering when the UE is available after a DDN failure" once and then gets notification only when there has been some Data delivery failure followed by the UE becoming reachable. This is a different MONTE event from the MONTE event "UE is reachable". The MME is informed about the subscription to the event by the HSS as part of the normal registration process. The application registers with the HSS, e.g., via an interface defined as part of AESE, to be notified of DDN failure. This method effectively provides an alternative to the use of SMS for triggering, along with the associated core network signalling necessary to deliver the SMS message. This solution also provides additional battery saving to the UE that awakes and does not receive a downlink packet.

- The Extended buffering in the SGW/SGSN and the MONTE based notifications shall apply to E-UTRAN, UTRAN and GERAN.

- Coordination of maximum latency between the application and the network

- Either by interaction between the application in the UE with the UE NAS layer according to solution of Coordination using the UE application. This solution relates to Scenario B. The UE should set parameters related to power saving functions e.g. PSM and eDRX. Application Servers which need to initiate data transmissions to devices that are applying power saving functions, may control the maximum latency for downlink data to the device. The solution makes it possible for applications set the maximum acceptable response time it will experience when the 3GPP system applies power saving functions such as PSM and potentially eDRX.

- Or through the parameter on Maximum latency in monitoring event configuration from SCS/AS to SCEF according to 3GPP TR 23.789[i.3] specific parameters for the UE Reachability event.

### -----------------------End of change 2---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?