| CHANGE REQUEST |
| --- |
| Meeting:* | ARC 19.0 |
| Source:* | InterDigital |
| Date:* | 2015-08-28 |
| Contact:* | Catalina Mladin, InterDigital, Catalina.Mladin@InterDigital.com Qing Li, InterDigital, Qing.Li@InterDigital.com |
| Reason for Change/s:* | Correcting error introduced with multiplicity notation change, R01 cover page correction R02 adds editorials agreed in joint ARC/PRO session at TP#19 |
| CR against: Release* | Release-2 |
| CR against: WI* | Active <Work Item number> MNT maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0001 V2.3.0 |
| Clauses/Sub Clauses* | 9.6.16 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

When changing notations for lists of sub-resources, an error has been introduced and the <execInstances> list has been changed to <execInstance> resource with no multiplicity.

In TS-0001 V. 0.3.2 contained <execInstances> as a child of mgmtCmd, with the following description (see text in green)

### 9.6.13	Resource Type execInstances

The <execInstances> resource contains all execution instances of the same management command <mgmtCmd>. Each <execInstance> is a sub-resource of <execInstances>. When <mgmtCmd> is successfully triggered by an M2M network application using UPDATE method, a corresponding <execInstance> sub-resource shall be generated.

Figure 9.6.13-1: Structure of <execInstances> resource 
(only resource specific attributes are shown)

The clean up in the following version (V0.4.2) removed lists of resources such as <execInstances>, but the multiplicity was carried incorrectly in this instance, with only on <execInstance> child being specified for the <mgmtCmd> resources. Note that both TS-0001 and TS-0004 clearly indicate the multiplicity in functional descriptions

“For multiple requests of the same management command, <mgmtCmd> may use the child-resource (i.e. <execInstance>) to contain all execution instances.” (TS-0001 V0.4.2)

“The Receiver shall automatically create an <execInstance> based on the <mgmtCmd> resource. If the execTarget attribute addresses a <group> resource, the Receiver shall create multiple <execInstance> sub-resources based on the value of currentNrOfMembers attribute.” (TS-0004 V.1.3.0)

This CR restores the correct multiplicity for <execInstance> child of <mgmtCmd>.

### -----------------------Start of change 1-------------------------------------------

### 9.6.16	Resource Type mgmtCmd

The <mgmtCmd> resource represents a method to execute management procedures or to model commands and remote procedure calls (RPC) required by existing management protocols (e.g. BBF TR-069 [i.4]), and enables AEs to request management procedures to be executed on a remote entity. It also enables cancellation of cancellable and initiated but unfinished management procedures or commands.

Figure 9.6.16-1: Structure of <mgmtCmd> resource

Each <mgmtCmd> corresponds to a specific type of management command, as defined by its attribute cmdType. For multiple requests of the same management command, <mgmtCmd> shalluse separate child-resources (i.e. <execInstance>) to contain each  execution instance. The execution of the management procedure represented by <mgmtCmd> shall be triggered using the UPDATE method to its attribute execEnable.

The <mgmtCmd> resource shall contain the child resources specified in table 9.6.16-1.

Table 9.6.16-1: Child resources of <mgmtCmd> resource

| Child Resources of <mgmtCmd> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 |
| [variable] | <execInstance> | 0..n | See clause 9.6.17 |

The <mgmtCmd> resource shall contain the attributes specified in table 9.6.16-2.

Table 9.6.16-2: Attributes of <mgmtCmd> resource

| Attributes of <mgmtCmd> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 where this common attribute is described |
| resourceID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| resourceName | 1 | WO | See clause 9.6.1.3 where this common attribute is described. |
| parentID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| expirationTime | 1 | RW | See clause 9.6.1.3 where this common attribute is described |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3 where this common attribute is described |
| labels | 0..1 (L) | RW | See clause 9.6.1.3 where this common attribute is described |
| creationTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described |
| description | 0..1 | RW | The text-format description of this resource. |
| cmdType | 1 | WO | The type to identify the management operation (e.g. download). |
| execReqArgs | 0..1 | RW | Structured attribute (e.g. abstract type) to contain any command-specific arguments of the request. |
| execEnable | 1 | RO | The attribute can be blank without any value or it can contain an address that can be used to trigger execution of <mgmtCmd> using UPDATE method. |
| execTarget | 1 | RW | ID of the <node> resource of the target on which this <mgmtCmd> will be executed. It may be the URI of a <group> resource in which case the <mgmtCmd> will be executed on all members in the memberList attribute of the addressed <group> resource. |
| execMode | 0..1 | RW | The mode used to specify how the command will be executed (e.g. Immediate Once, Immediate and Repeatedly, Random Once, Random and Repeatedly). May be used together with execFrequency, execDelay and execNumber to provide the scheduling information. |
| execFrequency | 0..1 | RW | The minimum interval between two executions, to be used in conjunction with execMode. Modes involving random execution can be used to add random values between individual executions. |
| execDelay | 0..1 | RW | The minimum delay before the instance should be executed. Modes involving random execution can be used to increase this delay randomly. |
| execNumber | 0..1 | RW | The number of times the instance should be executed, to be used when execMode indicates a repetition pattern. |

### -----------------------End of change 1 ---------------------------------------------