| Input Contribution |
| --- |
| Meeting ID* | ARC 19.0 |
| Title:* | Technical comparison of oneM2M and OIC in Clause5.2 |
| Source:* | Sung-Chan Choi, Jaeho Kim, Minu Ryu KETI (TTA), csc@keti.re.kr Jieun Keum, Samsung Electronics, je.keum@samsung.com Seonhyang Kim, DT&C, shkim@dtnc.net Bahareh Sadeghi, Intel, bahareh.sadeghi@intel.com Lionel Florit, Cisco, lflorit@cisco.com |
| Uploaded Date:* | 2015-09-09 |
| Document(s) Impacted* | WI-0044 OIC-Interworking TR-0023 v0.0.1 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Include the proposed text into TR-0023 |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

This contribution is based on ARC-2015-2138-oneM2M-OIC_Interworking_Technical_Comparison. The proposed text will be included in Clause5.2 in TR0024 for the technical comparison between oneM2M and OIC from the perspective of Resource representation and Communication model.

================ Start or Text Proposal 1 =======================

# 5	Technical Comparison of oneM2M and OIC

This clause will include the introduction of OIC technology and  the comparison between oneM2M and OIC technology.

## 5.2        Technical Comparison

This clause describes the technical comparison of oneM2M and OIC. Both oneM2M and OIC adopt ROA(Resource Oriented Architecture) design principles which expose their functionalities by means of  resoruces and manipulated with RESTful APIs. However, There are some points of comparison between oneM2M and OIC from the perspective of discovery model, communication model, and resource representation.

### 5.2.1	Discovery Model

The table 5.2.1-1 demonstrates the comparison between oneM2M and OIC with respect to discovery model.

Table 5.2.1-1 The Comparison of Discovery Model of oneM2M and OIC System

|  | oneM2M | OIC |
| --- | --- | --- |
| Resource Discovery | Resource discovery supported, which allows discovering of resources residing on a CSE. Using the Filter Criteria parameter for discovery allows limiting the scope of the results. (e.g. resource types, creation time, maximum size and matching string) The discovery message is sent over unicast for a target CSE. oneM2M supports resource announcement which means original resource can be announced to one or more remote CSEs, which facilitate resource discovery. | Resource discovery supported, which allows discovering of resources residing on OIC device. OIC core resource, /oic/res maintains the list of its referenced resources that are discoverable on OIC device. The discovery message may be sent multicast for multiple OIC devices (default) or unicast for a single OIC device. |
| Peer Discovery | Peer discovery not supported. oneM2M basically needs to be pre-provisioned which means AE/CSE must know the peer IP address it will register to. | Peer discovery supported. OIC device sends CoAP multicast message over the IP network to discover peers. For HTTP, it use Multicast DNS(mDNS). |

### 5.2.2	Communication Model

The table 5.2.2-1 demonstrates the comparison between oneM2M and OIC with respect to communication model.

Table 5.2.2-1 The Comparison of Communication Model of oneM2M and OIC System

|  | oneM2M | OIC |
| --- | --- | --- |
| Registration Need | Each entity in oneM2M must perform registration procedure which establishes a relationship between CSEs/AE allowing them to exchange information. Registree-Registrar relationship produces routing path when transferring messages. | OIC does not have the concept of registration between OIC devices. |
| Communication Flow | Based on RESTful stateless request-response paradigm Request message flow occurs from the Originator CSE to the Hosting CSE which generates Hop-by-Hop data delivery. Blocking and non-Blocking mode supported | Based on RESTful stateless request-response paradigm OIC client and OIC server directly communicate without involvement of any other OIC entity. OIC supports remote access (RA) which enables communication between OIC client and OIC server where each device is in a different network via connection broker server. |

The figure 5.2.2-1 and figure 5.2.2-2 illustrate message delivery in each oneM2M and OIC system and show comparison between oneM2M and OIC system communication model.

Figure 5.2.2-1	oneM2M Reqeust-Response communication model (Multi-Hop)

Figure 5.2.2-2 OIC Peer-to-Peer communication model

### 5.2.3	Resource Representation

The table 5.2.3-1 demonstrates the comparison between oneM2M and OIC with respect to resource representation.

Table 5.2.3-1	The Comparison of Resource Representation of oneM2M and OIC System

|  | oneM2M | OIC |
| --- | --- | --- |
| Functionality exposed by Resources | oneM2M defines common M2M services which can be used for any vertical application service domains. oneM2M common services are exposed via oneM2M defined resource types which comprises of <container>, <group>, <locationPolicy>, <subscription>, <request>, <delivery> etc. Based on the device capability, oneM2M entity can be represented as CSE or AE. oneM2M resource model provides common service layer level interoperability. | OIC represents an entity of the physical world as a OIC device (e.g. temperature, an electric light or a home applicance) using resource model. OIC device includes the base/core functionality and device specific functionality which is represented by OIC defined resource types. OIC resource model provides application profile level interoperability among OIC Devices. |
| Resource Structure | Hierarchical resource structure <CSEBase> represents the oneM2M CSE and is the the root for all the resources. oneM2M resources have a parent-child relationships. Each resource in oneM2M entity can be accessed via both structured (hierarchical) URI as well as un-structured (flat) URI. | Flat resource structure OIC device consists of core resource and device specific resource. Core resource has pre-defined resource name which can be accessed via fixed URI Device specific resource has variable resource name and represents device specific functionality (e.g. binary switch, brightness etc.) |

Assuming a light bulb is modelled as oneM2M device or OIC device in each domain, the table 5.2.1-2 and 5.2.1-3 show examples about oneM2M and OIC resource representation respectively.

Table 5.2.3-2 oneM2M <AE> resource (XSD example)

<xs:schema xmlns=http://www.w3.org/2001/XMLSchema targetNamespace="http://www.onem2m.org/xml/protocols" xmlns:m2m=http://www.onem2m.org/xml/protocols xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance" elementFormDefault="unqualified" xmlns:xs="http://www.w3.org/2001/XMLSchema"> <xs:element name="AE"> <xs:complexType> <xs:complexContent> <!-- Inherit common attributes for announceable Resources --> <xs:extension base="m2m:announceableResource"> <xs:sequence> <!-- Resource Specific Attributes --> <xs:element name="appName" type="xs:string" minOccurs="0" /> <xs:element name="App-ID" type="xs:string" /> <xs:element name="AE-ID" type="m2m:ID" /> <xs:element name="pointOfAccess" type="m2m:poaList" minOccurs="0" /> <xs:element name="ontologyRef" type="xs:anyURI" minOccurs="0" /> <xs:element name="nodeLink" type="xs:anyURI" minOccurs="0" /> <xs:element name="requestReachability" type="xs:boolean" /> <!-- Child Resources --> <xs:choice minOccurs="0" maxOccurs="1"> <xs:element name="childResource" type="m2m:childResourceRef" minOccurs="1" maxOccurs="unbounded" /> <xs:choice minOccurs="1" maxOccurs="unbounded"> <xs:element ref="m2m:container" /> <xs:element ref="m2m:group" /> <xs:element ref="m2m:accessControlPolicy" /> <xs:element ref="m2m:subscription" /> <xs:element ref="m2m:pollingChannel" /> <xs:element ref="m2m:schedule" /> </xs:choice> </xs:choice> </xs:sequence> </xs:extension> </xs:complexContent> </xs:complexType> </xs:element> </xs:schema>

Table 5.2.3-3	OIC light device resource (JSON example)

[{ "di": "example_device_id", "links": [ { "href": "/oic/d", "rt": "oic.d.light", "if": "oic.if.r", "rel": "hosts"}, { "href": "/myLightSwitch", "rt": "oic.r.switch.binary", "if": "oic.if.a", "rel": "hosts"}, { "href": "/myLightBrigtness", "rt": "oic.r.light.brightness", "if": "oic.if.a", "rel": "hosts"} ] }] { "n": "myRoomLightDevice", "rt": “oic.d.light", "if": "oic.if.r", “di": "example_device_id“, "icv": "oic.1.5" } { "n": MyRoomLightSwitch", "rt": "oic.r.switch.binary", "if": "oic.if.a", "id": "b.switch_TF38_3", "value": "true" } { "n": MyRoomLightBrightness", "rt": "oic.r.light.brightness", "if": "oic.if.a", "id": “light_brightenss_TF38_3", "value": 30 }

================ End or Text Proposal 1 =====================