| CHANGE REQUEST |
| --- |
| Meeting:* | ARC#19.0 |
| Source:* | Darold Hemphill, iconectiv, dhemphill@iconectiv.com |
| Date:* | 2015-08-31 |
| Contact:* | Darold Hemphill, iconectiv, dhemphill@iconectiv.com |
| Reason for Change/s:* | App-ID Format |
| CR against: Release* | 2.0 |
| CR against: WI* | Active WI-0029 MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0001 ver 2.2.0 |
| Clauses/Sub Clauses* | Clause 7.2, Table 7.2-1 and Clause 7.1.3 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

We propose elaborating the App-ID [registered-App-ID] with two components: a namespace and the application name.

# Proposing a new App-ID Format

Release One defined the registered App-ID in Table 7.2-1 as:

R[authority-ID]/[registered-App-ID]

We propose the following format for App-ID for Release Two:

r[Authority-ID].[namespace].[appName] e.g., ra01.com.ibm.smartcity

The period is proposed as a separator between components to avoid escaping the forward slash character. The namespace component may include embedded periods.

The App-ID format would be composed of the following components:

[Authority-ID]: Steering Committee Ad Hoc group suggested A01, A02 etc. to identify the Registration Authority

[namespace]: the application developer namespace e.g., reverse DNS or value provided by application developer

[appName]: application name

### Example: ra01.com.ibm.smartcity

### -----------------------Start of change 1-------------------------------------------

| Identifier Name | Absolute & Format-Designator or Relative & Format-Designator & Context | Format | Rule of use |
| --- | --- | --- | --- |
| APP-ID | App-ID | Either "R[authority-ID].[namespace].[appName] " or "N[non-registered-App-ID]" If the first letter is "R", then the App-ID is managed and assigned by the Registration Authority. If the first letter is "N", then non-registered-App-ID is not registered by the Registration Authority. | AE Registration Procedure described in clause 10.1.1.2.2. |

### -----------------------End of change 1---------------------------------------------

# Capitalizing Defined Terms

The term Registration Authority has been defined in TS-0002 and TS-0011 and should be capitalized.

### -----------------------Start of change 2-------------------------------------------

### 7.1.3	Application Identifier (App-ID)

An Application Identifier (App-ID) uniquely identifies an M2M Application in a given context. More precisely, there are two types of App-ID: Registration Authority defined App-ID (registered App-ID) and non-registered App-ID. The establishment of the registered App-ID is guaranteed to be globally unique; the non-registered App-ID is not guaranteed to be globally unique. The detail format is described in clause 7.2.

### -----------------------End of change 2---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?