## Slide 1: Fuctional Procedure for oiC interworking
Group Name: Architecture WG
Source: Jinhyeock Choi,Samsung Electronics, jinchoe@samsung.com
Jieun Keum, Samsung Electronics, je.keum@samsung.com
Sung Chan Choi, KETI, csc@keti.re.kr
Meeting Date: <2015-09-23>
Agenda Item: <WI 44: oneM2M-OIC interworking >
Notes: Other suggested titles:
“Benefits of oneM2M Standardization”

## Slide 2: Basic Sketch
IPE in between
  which plays the role of both oneM2M & OIC entities.
Separation of OIC & oneM2M operation
  The intermediary interact with OIC (& oneM2M) devices with OIC (& oneM2M) procedures respectively.
oneM2M device
(controller)
① oneM2M REQ
OIC device
(sensor & actuator)
IPE
② OIC REQ
③ OIC RES
④ oneM2M RES
(virtual)
oneM2M device
(virtual)
OIC device
oneM2M & OIC resource translation

## Slide 3: Main operations
(virtual) OIC device representation
  replicating OIC device in IPE as (virtual) OIC device
    With OIC discovery procedures.
(virtual) oneM2M device representation
  translating OIC device into (virtual) oneM2M device.
    With virtual CSE (?)
oneM2M discovery
  oneM2M controller finds (virtual) oneM2M devices
oneM2M monitoring & controlling
  oneM2M controller interacts with (virtual) oneM2M devices
on2M2M & OIC resource translation
  Translating oneM2M & OIC resources to synchronize virtual devices state
OIC synchronization
  Synchronizing virtual OIC device & OIC device
    With OIC Request & response via BINDING (?).

## Slide 4: Main operations
(virtual) OIC device representation
  replicating OIC device in IPE as (virtual) OIC device
    With OIC discovery procedures.
(virtual) oneM2M device representation
  translating OIC device into (virtual) oneM2M device.
    With virtual CSE (?)
oneM2M discovery
  oneM2M controller finds (virtual) oneM2M devices
oneM2M monitoring & controlling
  oneM2M controller interacts with (virtual) oneM2M devices
on2M2M & OIC resource translation
  Translating oneM2M & OIC resources to synchronize virtual devices state
OIC synchronization
  Synchronizing virtual OIC device & OIC device
    With OIC Request & response via BINDING (?).
Initial preparation
Actual monitoring & controlling

## Slide 5: Main operations
(virtual) OIC device representation
  replicating OIC device in IPE as (virtual) OIC device
    With OIC discovery procedures.
(virtual) oneM2M device representation
  translating OIC device into (virtual) oneM2M device.
    With virtual CSE (?)
oneM2M discovery
  oneM2M controller finds (virtual) oneM2M devices
oneM2M monitoring & controlling
  oneM2M controller interacts with (virtual) oneM2M devices
on2M2M & OIC resource translation
  Translating oneM2M & OIC resources to synchronize virtual devices state
OIC synchronization
  Synchronizing virtual OIC device & OIC device
    With OIC Request & response via BINDING (?).
OIC operation
OIC operation
oneM2M operation
oneM2M operation
oneM2M & OIC
translation
oneM2M & OIC
translation

## Slide 6: (virtual) OIC device representation
Overview (What)
  replicating OIC device in IPE as (virtual) OIC device, (IPE as OIC server (?) )
  ensuring two OIC devices to be synchronized, i.e. having the same resource representation
Methods (How)
  Using OIC discovery to acquire the OIC device information
    GET to /oic/res (from IPE)
    POST to /factoryResource (from OIC device)
  Establishing the relationship between two OIC devices .
    Link with “binding” relationship
This is OIC specific procedure, outside of oenM2M scope. Also some ideas still unspecified in OIC.
/oic/res
/oic/d
/lightSwitch
GET /oic/res
Response
OIC Client
GET /oic/d
Response
GET /lightSwitch
Response
/oic/res
/oic/d
/lightSwitch
Bind
Bind
Bind
OIC device
IPE
Bind
Bind
Bind

## Slide 7: (virtual) oneM2M device representation
Overview (What)
  translating OIC device into (virtual) oneM2M device.
Methods (How)
  Virtual CSE
OIC Client
/oic/res
/oic/d
/lightSwitch
Bind
Bind
Bind
/oic/res
/oic/d
/lightSwitch
/myLight
/lightSwitch
value
IPE

## Slide 8: oneM2M discovery
Overview (What)
  oneM2M controller finds (virtual) oneM2M devices
Methods (How)
  Usual oneM2M procedures
OIC Client
/oic/res
/oic/d
/lightSwitch
Bind
Bind
Bind
/oic/res
/oic/d
/lightSwitch
/myLight
/lightSwitch
value
IPE
AE or CSE
oneM2M device
oneM2M REQ
oneM2M RES

## Slide 9: oneM2M monitoring & controlling
Overview (What)
  oneM2M controller interacts with (virtual) oneM2M devices
Methods (How)
  Usual oneM2M procedures
  Need consideration regarding OIC REQ/ RES procedures
    Blocking or Non-blocking procedure
OIC Client
/oic/res
/oic/d
/lightSwitch
Bind
Bind
Bind
/oic/res
/oic/d
/lightSwitch
/myLight
/lightSwitch
value
IPE
AE or CSE
oneM2M device
oneM2M REQ
oneM2M RES

## Slide 10: on2M2M & OIC resource translation
Overview (What)
  Translating oneM2M & OIC resources to reflect oneM2M resource change into OIC resource & vice versa.
Methods (How)
  More structural approach would help.
OIC Client
/oic/res
/oic/d
/lightSwitch
Bind
Bind
Bind
/oic/res
/oic/d
/lightSwitch
/myLight
/lightSwitch
value
IPE
value

## Slide 11: OIC synchronization
Overview (What)
  Synchronizing virtual OIC device & OIC device i.e. all of their resources have the same representation.
Methods (How)
  Binding to establish the relationship between (virtual) OIC device & the original device (similar to CoAP Observe binding)
  Usual CoAP procedure for resource UPDATE. UPDATE procedure can be initiated by both.
OIC Client
/oic/res
/oic/d
/lightSwitch
Bind
Bind
Bind
/oic/res
/oic/d
/lightSwitch
/myLight
/lightSwitch
value
IPE
value
/oic/res
/oic/d
/lightSwitch
Bind
Bind
Bind
value
POST /lightSwitch
"value": False
Response
Response
POST /lightSwitch
"value": False

## Slide 12: Appendix

## Slide 13: Functional Architecture
Interworking with IPE
  IPE, as an intermediary, facilitates oneM2M & OIC interworking in between.
Functional Entities
  IPE: a specialized AE which maps OIC devices to oneM2M resources & exposes those via Mca (or Mcc) reference point.
  oneM2M CSE: an usual oneM2M common service entity (CSE)
  OIC device: a logical entity which plays either OIC client or OIC server roles or both. OIC server hosts OIC resources and expose those for IoT service. OIC client accesses OIC server to manipulate OIC resources, i.e. monitoring & controlling
OIC device
oneM2M CSE
IPE
oneM2M AE
virtual OIC device
Mca (or Mcc)
Reference Point
OIC
Interface

## Slide 14: oneM2M interworking with OIC via IPE
OIC device
MN-CSE
OIC device
IPE
IPE
Gateway
IN-CSE
IN-AE
ASN-AE
ASN-CSE
ADN-AE
OIC
Interface
OIC
Interface
Mca
Mcc
Mca
Mcc
Mca
Mca
Deployment model based on Functional Architecture
  Main entities and their interworking via reference points.

## Slide 15: Interworking with OIC via virtual devices
virtual OIC devices in IPE
  Replicating virtual OIC device in IPE with OIC procedures.
  Binding two devices such that they are synchronized, i.e. the same resource representations
virtual oneM2M devices in IPE
  Mirroring virtual OIC device to virtual oneM2M device by resource mapping.
  oneM2M service by manipulating virtual oneM2M device, which will reflected in the virtual & original OIC devices.
vOIC device
/oic/res
/oic/d
/lightSwitch
vCSE (AE)
IPE
/oic/res
/oic/d
/myLight
/lightSwitch
value
vCSE (AE)
/oic/res
/oic/d
/myLight
/lightSwitch
value
Mirroring oneM2M & OIC devices
OIC device
/oic/res
/oic/d
/lightSwitch
Sync OIC devices via OIC interfaces
oneM2M services with oneM2M interfaces