| CHANGE REQUEST |
| --- |
| Meeting:* | ARC 19.0 |
| Source:* | FUJITSU |
| Date:* | 2015-08-31 |
| Contact:* | Shingo Fujimoto, FUJITSU, shingo_fujimoto@jp.fujitsu.com |
| Reason for Change/s:* | <exact change/s to be provided below> |
| CR against: Release* | Release-2 |
| CR against: WI* | Active <Work Item number> MNT maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0001 V2.3.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Since connectivity between a CSE and other entities may not be available all time, CSE will spool the incoming requests.

However, how the spooling requests is enabled or disabled was not specified.

Further more, place to store spooled request on CSE is not defined.

This CR proposed to add new resource type <requestSpool>, to resolved isssues described above.

<requestSpool> resource can be created as child resource of <remoteCSE> or <AE> resource.

### -----------------------Start of change 1-------------------------------------------

### 9.6.x	Resource Type requestSpool

The <requstSpooler> resource represents a spooler for incoming request while bidirectional communication channel to the peered oneM2M entities is temporaly closed.

When the spooling request feature is enabled with setting TRUE on enabled attribute, incoming messages targeted to a request-unreachable entity (i.e. an AE or a CSE which is behind NAT so it cannot receive a request from other Nodes) shall be stored on the registrar CSE. Otherwise, incoming messages are re-targeted to the actual registree entity.

Figure 9.5.21-1: Structure of <requestSpool> resource

The <requestSpool> resource shall contain the child resource specified in table 9.6.21-1.

Table 9.6.21-1: Child resources of <requestSpool> resource

| Child Resources of <requestSpool> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| None |

The <requestSpool> resource shall contain the attributes specified in table 9.6.21-2.

Table 9.6.21-2: Attributes of <requestSpool> resource

| Attributes of <pollingChannel> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| resourceID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| resourceName | 1 | WO | See clause 9.6.1.3 where this common attribute is described. |
| parentID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| creationTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| expirationTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3 where this common attribute is described. |
| labels | 0..1 (L) | RW | See clause 9.6.1.3 where this common attribute is described. |
| enabled | 1 | RW | The indication of whether spooling request feature is enabled or not. When this value is ‘TRUE’, incoming requests targeted to oneM2M entity associated with the parent resource shall be stored at hosting CSE. Otherwise, CSE shall not spool incoming request. |
| spoolingLifeTime | 0..1 | RW | When this attribute is present, hosting CSE may delete request which aged than specified seconds. Otherwise, hosting CSE may regard any value which is implementation dependent. |

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

### -----------------------End of change 2---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?