| Input Contribution |
| --- |
| Meeting ID* | ARC19.4 |
| Title:* | OIC Interworking Procedure Addressing and Discovery |
| Source:* | Kiran Vedula, Samsung Electronics, kiran.vedula@samsung.com Jieun Keum, Samsung Electronics, je.keum@samsung.com Jinhyeock Choi, Samsung Electronics, jinchoe@samsung.com Sungchan Choi, KETI, sungchan.keti@gmail.com SeonHyang Kim, DT&C, shkim@dtnc.net Bahar Sadeghi, Intel, bahareh@intel.com |
| Uploaded Date:* | 2015-11-05 |
| Document(s) Impacted* | WI-0044 OIC-Interworking TR-0023 v0.1.0 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Include the proposed text into TR-0023 |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# ================ Start of Text Proposal 1 =======================

## 7.4.	Possible Operational Procedures

### 7.4.1 Addressing

To perform operations on entities/ resources they have to be addressed. OIC and oneM2M have their own addressing mechanisms. The addressing mechanisms as defined are reused with some mapping for OIC resources represented in oneM2M.

In oneM2M the “To” parameter in a request/ notification is used as a target for the request/ notification. To address a resource first the CSE is to be addressed and then the resource under the CSE. The CSE-ID is used to address the CSE. The originator of the request is recommended to use “Absolute” or “SP-relative” format of addressing when sending requests. This is just to ensure that the MN-CSE hosting OIC AE resources always receives the request without any scoping issues.

The details of addressing in case of Request/ Response and Notification scenarios is described below.

- Request Target

  - Requests are targeted to AEs but via CSE which hosts them

  - The MN CSE-PoA is used by IN to reach the CSE which is hosting the OIC AE resource

  - Specific AE under the MN-CSE is addressed using the AE-ID attribute of the <AE>

- Notification Target

  - Notifications are usually targeted to AEs

  - A hosting CSE which receives notification request, can retarget the request to AE-PoA

IPE needs to retarget the requests and notifications on the OIC side. This could be done based on some implementation specific mapping on the IPE or storing the URI information in some attribute of mapped resource, for example, for resourceName.

### 7.4.2 Initialization of Entities

In order for the OIC and oneM2M interworking to work there is a need to initialize this functionality. 	In the figure below a possible initialization procedure is depicted. The MN (Gateway) acts as a logical entity which is having this functionality. Discovery procedures described below are based on this initialization. The procedures described are for scenario shown in figure 6-2.

Figure 7.4.2-1 Intialization of Entities

Below are the possible steps for initialization as depicted in the figure:

- MN is installed with an IPE based on an out of band mechanism

  - Triggered by a user action e.g. user subscribing to some service or

  - Based on business logic of service provider

  - IPE registers with MN-CSE

  - Subsequently an AE can communicate with OIC Device by

- Registering itself with IN-CSE

- And IN-CSE registering with MN-CSE

### 7.4.3 Discovery

Once the initialization is finished, the next step is discovery wherein oneM2M entities try to discover OIC entities. There could be 2 modes of discovery

  - Request-response Mode

  - Notification Mode

  - The modes described here are not for lazy discovery.

#### 7.4.3.1 Request-response Mode

In request-response mode, AE’s explicitly request a CSE to provide details about any newly registered AE’s. In the figure below a possible request-response mode procedure is depicted.

Figure 7.4.3.1-1 Request-response Mode

Below are the possible steps for request-response mode of discovery:

- The IPE discovers OIC devices using its OIC Client functionality as soon as it is installed on MN. It uses OIC mechanisms for the discovery

- After the discovery, IPE uses its IWK (Interworking) function to map the discovered OIC devices and resources into oneM2M resources and creates them on MN

- For each discovered OIC Device an OIC AE is created and registered with MN-CSE

- (4.0/ 4.1) After that an AE through an IN-CSE can anytime discover OIC AE resources by sending a RETRIEVE REQ with appropriate filter criteria to the MN-CSE where they are registered

- (5.0/ 5.1) The MN-CSE sends a RETRIEVE RES to IN-CSE with the OIC AE’s information which in turn is sent to the AE

#### 7.4.3.2 Notification Mode

In notification mode, AE’s subscribe to any changes in registration details of a CSE and gets notified whenever new OIC AE’s are registered to CSE. In the figure below a possible notification mode preocedure is depicted.

Figure 7.4.3.2-1 Notification Mode

Below are the possible steps for notification mode of discovery:

- (1.0/ 1.1) AE creates subscription resource on IN-CSE to get notification for any changes in registered AE’s on MN-CSE. This request is forwarded to MN-CSE

- The IPE discovers OIC devices using its OIC Client functionality as soon as it is installed on MN. It uses OIC mechanisms for the discovery

- After the discovery, IPE uses its IWK (Interworking) function to map the discovered OIC devices and resources into oneM2M resources and creates them on MN

- For each discovered OIC Device an OIC AE is created and registered with MN-CSE

- (5.0/5.1) IN-CSE and in-turn AE is notified of the newly registered AE’s based on the earlier subscription

For efficiency purposes IPE could perform lazy discovery i.e. discover OIC resources only after getting a request from any oneM2M entity. Such options could be added in the TS.

================ End of Text Proposal 1 =====================