| Input Contribution |
| --- |
| Meeting ID* | ARC 20 |
| Title:* | TS-0014-LWM2M_Object_Transport and Interworking |
| Source:* | Thierry GARNIER, Gemalto N.V, Thierry.garnier@gemalto.com |
| Uploaded Date:* | 2015-10-29 |
| Document(s) Impacted* | TS-0014 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Add to next TS-0014 Baseline |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## 6.4  LWM2M Object Transport and Interworking

### 6.4.1	Introduction

The LWM2M Client uses the Device Management & Service Enablement interface to  provide the capabilities for the LWM2M Server of the IPE to access LWM2M Objects, Objects Instances and Resources available from the LWM2M Client.

An hosting CSE maintains a representation of the LWM2M Data Model  of  LWM2M Object, Object Instance or Resources as instances of oneM2M resource types. These oneM2M resources are instantiated and registered as described in clause 6.3 allowing oneM2M AEs and CSEs to exchange data with LWM2M Clients.

In reference to clause 6.3, at the end of the registration phase all declared LWM2M Object Instances and  LWM2M Objects are associated  to a <container>  resource created with  the resourceName attribute set accordingly to the proper LWM2M Object Instance path (e.g. /9/1) or to the LWM2M Object  path (e.g /9).

When a oneM2M request is addressed from a registrar CSE to a  hosting CSE containing the representation of  a  LWM2M Client, the oneM2M response to the Originator of the request is returned through the  cooperation of the hosting CSE and the IPE..

### 6.4.2	LWM2M Interworking mechanisms

- A cooperation between IPE and the oneM2M hosting CSE, requires efficient  mechanisms to maintain the latest state of the targeted LWM2M Objects, Object Instances and Resources. These mechanisms include data synchronization between the IPE and hosting CSE.

- Data synchronization  relies on the oneM2M Subscription/Notification and LWM2M Observation/Notification mechanisms. For automated data synchronization between the IPE and hosting CSE to be achieved , the solution shall be granular enough to allow data synchronization for each LWM2M Object  Instance.

- Access Control mechanisms relies on an interworking between oneM2M and LWM2M Access Control Policies .

LWM2M and oneM2M  mechanisms  used to achieve Data Synchronisation and Access Control are specified in more details in clauses 6.5 and  6.6. In particular these mechanisms require,  the <container> resource’ subscribtion shall have use eventNotificationCritera attribute with eventType  ‘B’ ,‘C’ and ’E’ set (clause 6.4.2.2, 6.4.2.3, 6.4.2.4) .

| eventType | 0..n | B. Deletion of the subscribed-to resource , Creation of a direct child of the subscribed-to resource Retrieval attempt of obsolete or non existing information for the subscribed-to resource |
| --- | --- | --- |

These following sub-clauses specify the sequences of operations involved for each type of  supported oneM2M requests following the general procedures specified  in clause 10 (RETRIEVE, CREATE, DELETE) as used within the context of the interworking for this present document

6.4.2.2  oneM2M RETRIEVE Procedure

This procedure describes the retrieval of a resource using the oneM2M RETRIEVE request.The information contained within the resource is related to the LWM2M Objects Instances that are interworked  through the IPE. This clause shall  be treated in conformance with the RETRIEVE Procedure specified in TS-0001 clause 10.1.2.

The Receiver performs local processing to verify the existence of requested Resource and checks privileges for retrieving the information related to the resource. After successful verification, the Receiver shall return the requested information according to the procedures for the type of interworking (e.g Transparent, Semanticaly Enabled) as described in clause 7 and 8, otherwise an error response shall be returned to the Originator

Figure 6.4-3: Procedure for Retrieving a Resource (TS-0001 Clause 10)

Specific  steps of the Receiver Processing according to the interworking process are defined   as follows:

Step 001:  Find and verify the targeted <container> resource  : the  resourceName corresponds to clause 6.3.2

Step 002 : Using the hosting CSE Access Control mechanisms,  check for Access Control Policy for retrieving information related to the resource

Step 003  On successful validation  of  the Access Control Policy, check the lastest information contained within the targeted resource has expired or does not exist. This is known as an obsolete resource

Step 003.1 : When the resource Information is obsolete or not existing   an event for Information Retrieval  (eventType ‘E’) is triggered to the entities that subscribed to the event (i.e.  IPE)

Step 003.1.1 : On receiving the event  ‘Retrieval attempt of obsolete or non existing information’ (eventType ‘E’) the IPE performs a LWM2M READ request on the Object Instance of  the targeted  LWM2M Client .

Step 003.1.2 : Once the targeted Object Instance is available to IPE, the IPE  creates and populates a <contentInstance> resource in the  requested  <container>  resource.

Step 004 :   The hosting CSE returns the appropriate response  back to the Originator (e.g. Acknowlegment, Errors, Data)

NB : as an OBSERVATION has been set up on the targeted LWM2M Object Instance, the automatic synchronisation between the Object Instance and its representation in the hosting CSE is performed. Further oneM2M accesses to the resource should be simplified in minimizing  impact of Step003  (up-to-date data already present from the hosting CSE resources).

General Exceptions:

- The targeted resource/attribute in To parameter does not exist. The Receiver responds with an error.

- The Originator does not have privileges to retrieve information stored in the resource on the Receiver. The Receiver responds with an error.

6.4.2.3  oneM2M CREATEProcedure

<to be completed>

6.4.2.4  oneM2M DELETE Procedure

This procedure describes the deletion of resource using the oneM2M DELETE request for a  resource  related to a LWM2M Object Instance that is interworked through the IPE. This clause shall be treated in conformance with the DELETE Procedure specified in TS-0001 clause 10.1.2.

The DELETE procedure deletes  all related information of the target resource,resulting in a request by the IPE to delete the LWM2M Object Instance in the LWM2M Client.

Figure 6.4-5: Procedure for Deleting a Resource (TS-0001 Clause 10)

Specific  steps of the Receiver Processing according to the LWM2M Interworking process are defined as follows:

Step 001:   Find  and verify the targeted  <container> resource  : the resourceName corresponds to clause 6.3.2

Step 002 : Using the hosting CSE Access Control mechanisms, check if the privileges of the Access Control Policy permit the resource to be deleted

Step 003 : On successful validation  of  Access Control Policy :

Step 003.1:  The subscribed-to <container> resource and associated resource(s) are deleted.

Step 003.2:  (from previous step) According to the <subscribed>-to resource parameters  notification  (eventType ‘B’  Deletion of the subscribed-to resource),  a notification  is sent from the hosting CSE to the IPE in order to advise IPE a LWM2M Object Instance has to be deleted in the LWM2M Client.

    - The LWM2M Object Instance is deleted in the LWM2M Client

    - A LWM2M  Update Registration is performed by the LWM2M Client to the IPE

Step 004 :   The hosting CSE returns the appropriate response to the Originator (e.g. Acknowlegment, Errors) as specified in TS-0001 clause 8.1.3.

General Exceptions:

- The targeted resource in To information does not exist. The Receiver responds with an error.

- The Originator does not have the privileges to delete the resource on the Receiver. The Receiver responds with an error.

### 6.4.3  oneM2M Resource Operation Responses

| LWM2M Client Response Codes on Device Management & Service Enablement interface | oneM2M Resource Operation Response |
| --- | --- |
| Create 2.01 Created: 4.00 Bad Request 4.01 Unauthorized 4.04 Not Found | 2001 Created 4000 4103 4004 |
| Read 2.05 Content: 4.01 Unauthorized 4.04 Not Found 4.05 Method Not Allowed | 2000 OK 4103 4004 4005 |
| Write 2.04 Changed 4.00 Bad Request 4.01 Unauthorized 4.04 Not Found 4.05 Method Not Allowed | 2004 Changed 4000 4103 4004 4005 4102 |
| Delete 2.02 Deleted 4.00 Bad Request 4.01 Unauthorized 4.04 Not Found 4.05 Method Not Allowed | 2002 deleted 4103 4103 4004 4005 |

Table 6.4.3-1 LWM2M Response Codes  to oneM2M Resource Operation Response Codes