| CHANGE REQUEST |
| --- |
| Meeting:* | ARC#20.2 |
| Source:* | SeungMyeong JEONG, LG Electronics |
| Date:* | 2015-12-08 |
| Contact:* | seungmyeong.jeong@lge.com |
| Reason for Change/s:* | resource type name cleanup |
| CR against: Release* | Rel-2 |
| CR against: WI* | Active WI-0041 Subscription/Notification Enhancements MNT maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0001 |
| Clauses/Sub Clauses* | 10.2.12.2.1 Notification Target removal handling procedure |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution provides the missing cleanup for Notification Target deletion scheme from “ARC-2015-2235R02-cleanup_for_notification_target_deletion”.

Note that the CR 2235R02 missed clause 10.2.12.2.1 Notification Target removal handling procedure. In that CR, notificationTargetDisposition resource type name was replaced by notificationTargetMgmtPolicyRef. It was simply missing clause 10.2.12.2.1 to use the new name.

This also includes editorial corrections, removal of spaces between pointy brackets, and the delete procedurs reference.

### -----------------------Start of change 1-------------------------------------------

##### 10.2.12.2.1	Notification Target removal handling procedure

The Notifier(i.e., the Originator of the Notify request) shall handle the notification target removal based on a <notificationTargetPolicy> resource. Selecting the applicable  <notificationTargetPolicy> resource shall be performed as follows:

- Check if there’s a <notificationTargetMgmtPolicyRefs> resource as a child of the <subscription> resource which includes the Notification Target in the notificationTargetURI attribute. If one is located, the Notifier shall apply the <notificationTargetPolicy> resource specified in the notificationPolicyID attribute in the matching <notificationTargetMgmtPolicyRefs> resource.

- Otherwise, the Notifier shall check if there is a <notificationTargetMgmtPolicyRefs> resource which has the creator attribute set in the corresponding <subscription> resource and there is a <notificationTargetPolicy> resource which has the policyLabel attribute set as “default” and the creator attribute is equal to the creator of the <subscription> resource.

- Otherwise, the Notifier shall fetch the <notificationTargetPolicy> resource which has the policyLabel attribute set as “default”.

With the selected <notificationTargetPolicy> resource, the Notifier shall handle the target removal as specified in the action attribute of the <notificationTargetPolicy> resource. If there’s <policyDeletionRules> resource(s) then the action shall be applied when the rule(s) is satisfied.

The action shall be performed as follows:

- If the action is “accept”, then the Notifier shall remove the address which is corresponding to the Notification Target and returns a successful response if applicable.

- If the action is “reject” and if the target removal was requested with Delete request (clause 10.2.25.1), then the Notifier shall return an unsuccessfull response if applicable.

- If the action is “seek authorization from the subscription creator”, then the Notifier shall return a successful response to the Notification Target if applicable and shall send a Notify request including the ID of the <subscription> resource, the Notification Target, and the ‘removalAuthorization’ indicator which is set as TRUE, to the subscription creator. When the Notifier gets successful response from the creator, then the Notifier shall remove the address which is corresponding to the Notification Target.

If the action is “inform the subscription creator”, then the Notifier shall return a successful response to the Notification Target if applicable and shall send a Notify request including the ID of the <subscription> resource, the Notification Target, and the ‘targetRemoval’ indicator which is set as TRUE to the subscription creator.

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?