| CHANGE REQUEST |
| --- |
| Meeting:* | ARC#21 |
| Source:* | InterDigital, NEC |
| Date:* | 2016-01-07 |
| Contact:* | Catalina Mladin, Catalina.Mladin@InterDigital.com Qing Li, Qing.Li@InterDigital.com Martin Bauer, Martin.Bauer@neclab.eu |
| Reason for Change/s:* | Implementing TR-0007 V.2.8.0. section 8.5.5 |
| CR against: Release* | Rel-2 |
| CR against: WI* | Active WI-5 MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0001 V.2.5.1 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR introduces the resources and attributes necessary for implementing  semantic discovery, given that an overall semantic description (logical tree) may be distributed across the <semanticDescriptor> resources. These proposals correspond to the solutions agreed in TR-0007 V.2.8.0. section 8.5.5

Change 1 reflects the update of the resource type summary table based on the proposals later in the document, as well as a couple of corrections to the table, mainly related to the semanticDescriptor resource.

Change 2 provides the addition of the attribute relatedSemantics to the semanticDescriptor resource. The use of this attribute is detailed later in the document, in the semantic discovery procedures.

Change 3 introduces new clauses corresponding to two new resources, namely semanticGroup and its virtual child semanticFanOutPoint. The corresponding flows for semantic group management are described in the new clauses introduced by Change 4.

Change 5 details the semantic discovery procedures in order to provide a detailed overview of the various methods which may be employed. Finally, a new reference is introduced in the section on changes to the Reference Section.

### -----------------------Start of change 1-------------------------------------------

### 9.6.1	Overview

#### 9.6.1.1	Resource Type Summary

Table 9.6.1.1-1 introduces the normal and virtual resource types and their related child or parent resource types. Details of each resource type follow in the remainder of this clause.

Table 9.6.1.1-1 lists each specified <resourceType>. An addition of suffix "Annc" to such <resourceTypes> indicates the associated announced resource type.

Among the resource types listed in Table 9.6.1.1-1, the following are termed “Content Sharing Resources” in oneM2M Specifications for the purpose of referring to any of those resource types:

- container

- contentInstance

- flexContainer

Table 9.6.1.1-1 Resource Types

| Resource Type | Short Description | Child Resource Types | Parent Resource Types | Clause |
| --- | --- | --- | --- | --- |
| accessControlPolicy | Stores a representation of privileges. It is associated with resources that shall be accessible to entities external to the Hosting CSE. It controls "who" is allowed to do "what" and the context in which it can be used for accessing resources | subscription | AE, AEAnnc, remoteCSE, remoteCSEAnnc, CSEBase | 9.6.2 |
| AE | Stores information about the AE. It is created as a result of successful registration of an AE with the Registrar CSE | subscription, container, group, accessControlPolicy, schedule, pollingChannel，semanticDescriptor, semanticGroup | remoteCSE, remoteCSEAnnc, CSEBase | 9.6.5 |
| container | Shares data instances among entities. Used as a mediator that buffers data exchanged between AEs and/or CSEs. The exchange of data between AEs (e.g. an AE on a Node in a field domain and the peer-AE on the infrastructure domain) is abstracted from the need to set up direct connections and allows for scenarios where both entities in the exchange do not have the same reachability schedule | container, flexContainer, contentInstance, subscription, latest, oldest，semanticDescriptor | AE, AEAnnc, container, containerAnnc, remoteCSE, remoteCESAnnc, CSEBase, flexContainer, flexContainerAnnc | 9.6.6 |
| contentInstance | Represents a data instance in the <container> resource | semanticDescriptor | Container, containerAnnc | 9.6.7 |
| flexContainer | A template which allows to define specialized (customizable) versions of containers with a flexible and lightweight structure | container, flexContainer, subscription, semanticDescriptor, | AE, AEAnnc, container, containerAnnc, flexContainer, flexContainerAnnc, remoteCSE, remoteCESAnnc, CSEBase | 9.6.35 |
| CSEBase | The structural root for all the resources that are residing on a CSE. Stores information about the CSE itself | remoteCSE, remoteCSEAnnc, node, AE, container, group, accessControlPolicy, subscription,, mgmtCmd, locationPolicy, statsConfig, statsCollect, request, delivery, schedule, notificationTargetPolicy, flexContainer, semanticGroup | None specified | 9.6.3 |
| delivery | Forwards requests from CSE to CSE | subscription | CSEBase | 9.6.11 |
| eventConfig | Defines events that trigger statistics collection | subscription | statsConfig | 9.6.24 |
| execInstance | Contains all execution instances of the same Management Command | subscription | mgmtCmd | 9.6.17 |
| fanOutPoint (V) | Virtual resource containing target for group request It is used for addressing bulk operations to all the resources that belong to a group | None specified | group | 9.6.14 |
| group | Stores information about resources of the same type that need to be addressed as a Group. Operations addressed to a Group resource shall be executed in a bulk mode for all members belonging to the Group | fanOutPoint, subscription | AE, AEAnnc, remoteCSE, remoteCSEAnnc, CSEBase | 9.6.13 |
| latest (V) | Virtual resource that points to most recently created <contentInstance> child resource within a <container> resource | None specified | container | 9.6.27 |
| locationPolicy | Includes information to obtain and manage geographical location. It is only referenced within a container, the contentInstances of the container provide location information | subscription | CSEBase | 9.6.10 |
| mgmtCmd | Management Command resource represents a method to execute management procedures required by existing management protocols | execInstance, subscription | CSEBase | 9.6.16 |
| mgmtObj | Management Object resource represents management functions that provides an abstraction to be mapped to external management technology. It represents the node and the software installed in the node (see note) | subscription, mgmtObj, schedule | node, mgmtObj, mgmtObjAnnc | 9.6.15 Annex D |
| m2mServiceSubscriptionProfile | Data pertaining to the M2M Service Subscription | serviceSubscribedNode, subscription | CSEBase | 9.6.19 |
| node | Represents specific Node information | mgmtObj, subscription | CSEBase, remoteCSE | 9.6.18 |
| notificationTargetMgtPolicyRefs | Represents a list of notification targets and the deletion policy | subscription | subscription | 9.6.31 |
| notificationTargetPolicy | Represents a notification target deletion policy with pre-defined action and deletion rules | subscription, policyDeletionRules | CSEBase | 9.6.32 |
| notificationTargetSelfReference (V) | Virtual resource used to remove the Notification Target | None specified | subscription | 9.6.34 |
| oldest (V) | Virtual resource that points to first created <contentInstance> child resource within a <container> resource | None specified | container | 9.6.28 |
| pollingChannel | Represent a channel that can be used for a request-unreachable entity | pollingChannelURI | remoteCSE, AE | 9.6.21 |
| pollingChannelURI (V) | Virtual resource used to perform service layer long polling of a resource Hosting CSE by a request-unreachable entity | None specified | pollingChannel | 9.6.22 |
| policyDeletionRules | Represents a set of rules which is associated with notification target removal policy | subscription | notificationTargetPolicy | 9.6.33 |
| remoteCSE | Represents a remote CSE for which there has been a registration procedure with the registrar CSE identified by the CSEBase resource | AE, container, group, accessControlPolicy, subscription, pollingChannel, schedule, node, semanticGroup | CSEBase | 9.6.4 |
| request | Expresses/access context of an issued Request | subscription | CSEBase | 9.6.12 |
| schedule | Contains scheduling information for delivery of messages | subscription | subscription, CSEBase, remoteCSE,AE | 9.6.9 |
| serviceSubscribedNode | Node information | subscription | m2mServiceSubscriptionProfile | 9.6.20 |
| statsCollect | Defines triggers for the IN-CSE to collect statistics for applications | subscription | CSEBase (in IN-CSE) | 9.6.25 |
| statsConfig | Stores configuration of statistics for applications | eventConfig, subscription | CSEBase (in IN-CSE) | 9.6.23 |
| subscription | Subscription resource represents the subscription information related to a resource. Such a resource shall be a child resource for the subscribe-to resource | schedule, notificationTargetSelfReference, notificationTargetMgtPolicyRefs | accessControlPolicy,accessControlPolicyAnnc, AE, AEAnnc, container, CSEBase, delivery, eventConfig, execInstance, group, groupAcce, locationPolicy, mgmtCmd, mgmtObj, mgmtObjAnnc, m2mServiceSubscriptionProfile, node, nodeAnnc, serviceSubscribedNode, remoteCSE, remoteCSEAnnc, request, schedule, semanticDescriptor, semanticGroup, statsCollect, statsConfig, flexContainer, flexContainerAnnc, | 9.6.8 |
| serviceSubscribedAppRule | Represents a rule that defines allowed App-ID and AE-ID combinations that are acceptable for registering an AE on a Registrar CSE | subscription | CSEBase | 9.6.29 |
| semanticDescriptor | Stores semantic description pertaining to a resource and potentially sub-resources. | subscription | AE, container, contentInstance | 9.6.30 |
| semanticFanOutPoint | Virtual resource used as target for semantic discovery aimed at a logical graph distributed over multiple semanticDescriptor resources, which belong to the corresponding semanticGroup parent resource | None specified | semanticGroup | 9.6.y |
| semanticGroup | Stores information about semanticDescriptor resources with related content that need to be used together for the purposes of semantic discovery. Operations addressed to a semanticGroup resource shall be executed in a bulk mode for all members belonging to the Group | semanticFanOutPoint , subscription | AE, AEAnnc CSEBase, remoteCSE, remoteCSEAnnc | 9.6.x |
| NOTE: See clause 9.6.12 for a summary of specializations of <mgmtObj>. |

### -----------------------End of change 1-------------------------------------------

### -----------------------Start of change 2-------------------------------------------

### 9.6.30	Resource Type semanticDescriptor

The <semanticDescriptor> resource is used to store a semantic description pertaining to a resource and potentially sub-resources. Such a description may be provided according to ontologies. The semantic information is used by the semantic functionalities of the oneM2M system and is also available to applications or CSEs.  [i.28] provides an informative example of a descriptor attribute.

Editor’s note: There might be a need to make a normative reference to a stage 3 TS, depending how far PRO goes in standardizing semantic descriptors using RDF or OWL formats.

Figure 9.6.30-1: Structure of <semanticDescriptor> resource

The <semanticDescriptor> resource shall contain the child resources specified in table 9.6.30-1.

Table 9.6.30-1: Child resources of <semanticDescriptor> resource

| Child Resources of <semanticDescriptor> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 where the type of this resource is described. |

The <semanticDescriptor> resource shall contain the attributes specified in table 9.6.23-2.

Table 9.6.30-2: Attributes of <semanticDescriptor> resource

| Attributes of <semanticDescriptor> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 |
| resourceID | 1 | RO | See clause 9.6.1.3 |
| resourceName | 1 | WO | See clause 9.6.1.3 |
| parentID | 1 | RO | See clause 9.6.1.3 |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3 |
| creationTime | 1 | RO | See clause 9.6.1.3 |
| expirationTime | 1 | RW | See clause 9.6.1.3 |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 |
| Labels | 0..1 (L) | RW | See clause 9.6.1.3 |
| Creator | 0..1 | RO | The AE-ID of the entity which created the resource. This can also be the CSE-ID of the IN-CSE if the IN-CSE created the resource. |
| Descriptor | 1 | RW | Stores a semantic description pertaining to a resource and potentially sub-resources. Such a description shall be according to subject-predicate-object triples as defined in the RDF graph-based data model [4].The elements of such triples may be provided according to ontologies. |
| ontologyRef | 0..1 | WO | A reference (URI) of the ontology used to represent the information that is stored in the descriptor attribute. If this attribute is not present, the ontologyRef from the parent resource is used if present. |
| relatedSemantics | 0..1(L) | WO | List of URIs for resources containing related semantic information to be used in processing semantic queries. The URI(s) may reference either a <semanticGroup> resource or other <semanticDescriptor> resources. |

Editor’s note: the possibility for the semantic descriptor attribute to link to other descriptor attributes is not excluded to optimize storage but it needs further study.

### ----------------------- End of change 2-------------------------------------------

### --------------------Start of change 3 (new clause) ---------------------------

### 9.6.x	Resource Type semanticGroup

The <semanticGroup> resource represents a group of <semanticDescriptor> resources with have related descriptor content which should be used as a whole when executing semantic queries. The <semanticGroup> resource contains an attribute that provides links to the members of the group and a virtual resource (the <semanticFanOutPoint>) that allows semantic queries operations addressing the group to be distributed to the members.

Figure 9.6.x-1: Structure of <semanticGroup> resource

The <semanticGroup> resource shall contain the child resources specified in table 9.6.x-1.

Table 9.6.x-1: Child resources of <semanticGroup> resource

| Child Resources of <semanticGroup> | Child Resource Type | Multiplicity | Description | <semanticGroupAnnc> Child Resource Types |
| --- | --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 | <subscription> |
| semanticFanOutPoint | <semanticFanOutPoint> | 0..1 | See clause 9.6.y | none |

The <semanticGroup> resource shall contain the attributes specified in table 9.6.x-2

Table 9.6.x-2: Attributes of <semanticGroup> resource

| Attributes of <semanticGroup> | Multiplicity | RW/ RO/ WO | Description | <semanticGroupAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 | NA |
| resourceID | 1 | RO | See clause 9.6.1.3 | NA |
| resourceName | 1 | WO | See clause 9.6.1.3 | NA |
| parentID | 1 | RO | See clause 9.6.1.3 | NA |
| expirationTime | 1 | RW | See clause 9.6.1.3 | MA |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3 | MA |
| Labels | 0..1 (L) | RW | See clause 9.6.1.3 | MA |
| creationTime | 1 | RO | See clause 9.6.1.3 | NA |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 | NA |
| announceTo | 0..1 (L) | RW | See clause 9.6.1.3 | NA |
| announcedAttribute | 0..1 (L) | RW | See clause 9.6.1.3 | NA |
| Creator | 0..1 | RO | The AE-ID or CSE-ID of the entity which created the resource. | NA |
| semanticGroupID | 0..1 | RW | Optional ID of the <semanticGroup>. | OA |
| currentNrOfMembers | 1 | RO | Current number of members in the semantic group. It shall not be larger than maxNrOfMembers. | OA |
| maxNrOfMembers | 1 | RW | Maximum number of members in the semantic group | OA |
| fanOutAccessControlPolicyIDs | 0..1 (L) | RW | List of IDs of <accessControlPolicy> resources defining who is allowed to access the <semanticFanOutPoint> child resource, if present. | OA |
| semanticDescriptorLinks | 1 (L) | RW | List of URIs referencing the <semanticDescriptor>members of the semantic group | OA |
| ontologyRef | 0..1 | WO | A reference (URI) of the ontology used to represent the information that is stored in the descriptor attribute. If this attribute is not present, the ontologyRef from the parent resource is used if present. | OA |

### 9.6.y	Resource Type semanticFanOutPoint

The <semanticFanOutPoint> resource is a virtual resource because it does not have a representation. It is the child resource of a <semanticGroup> resource.

Whenever a semantic discovery request is sent to the <semanticFanOutPoint> resource the host uses the semanticGroupLinks attribute of the parent <semanticGroup> resource to retrieve all the related descriptors. If there are descriptors stored on a different CSEs, individual RETRIEVE requests are sent to each CSE for retrieving the external descriptors. All semantic descriptors are accessed based on the respective access control policies.

Once all of the related <semanticDescriptor>(s) have been retrieved, the content of each of the descriptor attributes is added to the content on which the SPARQL request is being executed.The full/enlarged content subject to the SPARQL request is provided to the SPARQL engine for processing

The <semanticFanOutPoint> resource uses fanOutAccessControlPolicyIDs attribute in the parent <semanticGroup> resource.for access control policy validation.

### -----------------------End of change 3---------------------------------------------

### -------------------Start of change 4 (new clause)------------------------------------------

### 10.2.x	Semantic Group Management Procedures

#### 10.2.x.1	Introduction

This clause describes semantic group management procedures using a <semanticGroup> resource. It also details the use of the virtual resource <semanticFanOutPoint>.

#### 10.2.x.2	Create <semanticGroup>

This procedure shall be used for creating a <semanticGroup> resource.

Table 10.2.x.2-1: <semanticGroup> CREATE

| <semanticGroup> CREATE |
| --- |
| Associated Reference Point | Mcc, Mca and Mcc' |
| Information in Request message | According to clause 10.1.1.1 |
| Processing at Originator before sending Request | According to clause 10.1.1.1 |
| Processing at Receiver | According to clause 10.1.1.1. In addition, the Receiver shall: Validate that there are no duplicate members present in the semanticDecriptorLinks attribute and that the targets of all the links are of type <semanticDescriptor>. If the validation is not successful the CREATE operation is considered un-sucessful. Upon successful validation, create a new <semanticGroup> resource including the <semanticFanOutPoint> child-resource. |
| Information in Response message | According to clause 10.1.1.1 |
| Processing at Originator after receiving Response | According to clause 10.1.1.1 |
| Exceptions | According to clause 10.1.1.1 |

#### 10.2.x.3	Retrieve <semanticGroup>

This procedure shall be used for retrieving <semanticGroup> resource.

Table 10.2.x.3-1: <semanticGroup> RETRIEVE

| <semanticGroup> RETRIEVE |
| --- |
| Associated Reference Point | Mcc, Mca and Mcc' |
| Information in Request message | According to clause 10.1.2 |
| Processing at Originator before sending Request | According to clause 10.1.2 |
| Processing at Receiver | According to clause 10.1.2 |
| Information in Response message | According to clause 10.1.2 |
| Processing at Originator after receiving Response | According to clause 10.1.2 |
| Exceptions | According to clause 10.1.2 |

#### 10.2.x.4	Update <semanticGroup>

This procedure shall be used for updating an existing <semanticGroup> resource.

Table 10.2.x.4-1: <semanticGroup> UPDATE

| <semanticGroup> UPDATE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | According to clause 10.1.3 |
| Processing at Originator before sending Request | According to clause 10.1.3 |
| Processing at Receiver | According to clause 10.1.3. In addition the Receiver shall: Validate that no duplication of members in the semanticDecriptorLinks attribute would occur based on the update and that the targets of all the links are of type <semanticDescriptor>. If the validation is not successful the UPDATE operation is considered un-sucessful. Note: the operation shall not have any effect on the <semanticFanOutPoint> child-resource. |
| Information in Response message | According to clause 10.1.3 |
| Processing at Originator after receiving Response | According to clause 10.1.3 |
| Exceptions | According to clause 10.1.3 |

#### 10.2.x.5	Delete <semanticGroup>

This procedure shall be used for deleting an existing <semanticGroup> resource.

Table 10.2.x.5-1: <semanticGroup> DELETE

| <semanticGroup> DELETE |
| --- |
| Associated Reference Point | Mcc, Mca and Mcc' |
| Information in Request message | According to clause 10.1.4.1 |
| Processing at Originator before sending Request | According to clause 10.1.4.1 |
| Processing at Receiver | According to clause 10.1.4.1. Note that the <semanticFanOutPoint> child-resource is deleted at the same time with the <semanticGroup> resource target of the operation |
| Information in Response message | According to clause 10.1.4.1 |
| Processing at Originator after receiving Response | According to clause 10.1.4.1 |
| Exceptions | According to clause 10.1.4.1 |

#### 10.2.x.6	<semanticFanOutPoint> Procedures

The virtual resource <semanticFanOutPoint> is used for processing semantic discovery requests. As such, this virtual resource can be the target of RETRIEVE operations only. The <semanticFanOutPoint> resource is created and deleted at the same time with the <semanticGroup> resource, see clauses 10.2.x.2. and 10.2.x.4 respectively.

#### 10.2.x.7	Retrieve <semanticFanOutPoint>

This procedure shall be used for retrieving the content of all member resources belonging to an existing <semanticGroup> resource.

Table 10.2.x.7-1: <semanticFanOutPoint> RETRIEVE

| <semanticFanOutPoint> RETRIEVE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | According to clause 10.1.2 |
| Processing at Originator before sending Request | The Originator shall request a semantic discovery to be performed using the content of the semantic descriptors of all member resources belonging to an existing <semanticGroup> resource, by using a RETRIEVE operation. The request addresses the virtual child resource <semanticFanOutPoint> of the specific <semanticGroup> resource of a Hosting CSE. The Originator may be an AE or CSE |
| Processing at Receiver | The Receiver shall: Check if the Originator has RETRIEVE permission in the <accessControlPolicy> resource referenced by the fanoutAccessControlPolicyIDs in the addressed <semanticGroup> resource. In the case fanoutAccessControlPolicyIDs is not provided, the access control policy defined for the <semanticGroup> resource shall be used Upon successful validation, obtain the URIs of all the member <semanticDescriptor> resources from the semanticDescriptorLinks attribute of the addressed <semanticGroup> resource. If there are <semanticDescriptor> resources stored on different CSEs, individual RETRIEVE requests are sent to each CSE for retrieving the descriptors, otherwise the descriptor attributes are simply retrieved for all the <semanticDescriptor> resources hosted locally. All semantic descriptors are accessed based on the respective access control policies. Once all of the related descriptor attributes have been retrieved, the SPARQL request is being executed on the combined content. |
| Information in Response message | The result of the SPARQL request executed on the combined content of the members’ descriptors. |
| Processing at Originator after receiving Response | According to clause 10.1.2 |
| Exceptions | According to clause 10.1.2 |

### -----------------------End of change 4---------------------------------------------------------

### ---------------------Start of change 5 (new clause)---------------------------------------

### 10.2.z	Semantic Discovery Procedures

#### 10.2.z.1	Introduction

This clause describes semantic discovery procedures on semantic descriptions represented as RDF triples, given that an overall semantic description (logical tree) may be distributed across the <semanticDescriptor> resources.

Semantic discovery procedures may be performed using RETRIEVE operations as follows:

Targeting any resource other than <semanticFanOutPoint>:

- The receiver begins processing the request by retrieving the <semanticDescriptor> resource of the request target and its descriptor attribute. Related descriptors are discovered and accessed according to clause 10.2.z.2. The content of related descriptor attributes are added to the content on which the SPARQL request is being executed. Depending on which of the options described in 10.2.z.2.1 or 10.2.z.2.2 is chosen, all potentially relevant descriptor attributes are added before executing the SPARQL request or they are added when needed during the execution of the SPARQL request.

- The resulting content subject to the SPARQL request is provided to the SPARQL engine for processing

Targeting a <semanticFanOutPoint> resource (see also clauses 10.2.x.6 and 10.2.x.7):

- Based on the semanticGroupLinks attribute targeted all the related Descriptors are discovered, and those on the <semanticGroup> hosting CSE are retrieved together

- If there are descriptors stored on a different CSE, individual RETRIEVE requests are sent to each CSE for retrieving the external descriptors.

- All semantic descriptors are accessed based on the respective access control policies.

- Once all of the related <semanticDescriptor>(s) have been accessed, the content of each of the descriptor attributes is added to the content on which the SPARQL request is being executed.

- The full/enlarged content subject to the SPARQL request is provided to the SPARQL engine for processing

#### 10.2.z.2	Discovering and establishing the logical tree in the semantic discovery scope without the use of <semanticFanOutPoint>

Given that an overall semantic description (logical tree) may be distributed across the <semanticDescriptor> resources, there are two methods of constructing the logical tree in the scope of a semantic discovery targeting any resource other than <semanticFanOutPoint>.

- If the attribute relatedSemantics is empty or does not exist, the “Annotation-based method” (using resourceDescriptorLink) detailed in clause 10.2.z.2.1 shall be used

- If the attribute relatedSemantics is not empty the “Resource link-based method” (using relatedSemantics) detailed in clause 10.2.z.2.2 shall be used

##### 10.2.z.2.1	Annotation-based method

In this option, the links to related semanticDescriptor resources are encoded in the semantic description itself, which is encoded as RDF triples [4] logically structured as <subject> <predicate> <object>. For this purpose, an annotation property called onem2m:resourceDescriptorLink is introduced. It is formally specified as part of the oneM2M Base Ontology defined in [6] and can be used as a predicate in any RDF triple with any subject and without further relation to the oneM2M Base Ontology. Only the use of the onem2m namespace is required to uniquely identify the annotation property.

Whenever further information about a semantic instance <X> is stored in another semanticDescriptor resource. a new RDF triple <X> onem2m:resourceDescriptorLink <SemanticDescriptorURL> may be added to this semantic description, where <SemanticDescriptorURL> is the URL of the other semanticDescriptor resource containing additional information related to <X>.

Editor's Note: The RDF triple syntax in this paragraph is only used for illustration purposes. The actual encoding of the RDF triples will be defined in stage 3 documents. Once this is there, this editor's note should be replaced by a note including the actual reference to the stage 3 document.

To make use of the onem2m:resourceDescriptorLink property, the evaluation of semantic queries formulated as SPARQL requests by the SPARQL engine has to be adapted in the following way:

- The SPARQL request is executed on the content of the semantic description in the descriptor attribute of the semanticDescriptor resource.

- For each semantic instance matched in the SPARQL request, it is checked whether one or more onem2m:resourceDescriptorLink annotations exist.

- If this is the case, the execution of the SPARQL request is halted.

- The content of the descriptor attribute of each of the semanticDescriptor resources the onem2m:semanticDescriptorLink annotations reference is added to the content on which the SPARQL request is being executed

- The execution of the SPARQL request is continued on the enlarged content

##### 10.2.z.2.2	 Resource link-based method

In this option, the links to related <semanticDescriptor> resources are specified in the relatedSemantics attribute. The attribute contains a list of URIs referencing either other <semanticDescriptor> resources, to a <semanticGroup> resource or to a <group> resource.

Processing of the SPARQL engine procedures at the receiver :

- The receiver retrieves the  <semanticDescriptor> resource of the request target

- Based on the relatedSemantics attribute of the <semanticDescriptor> resource targeted, all the related descriptors are discovered, as follows:

  - If the relatedSemantics attribute includes a list of links, each of the linked Descriptors are accessed based on the respective access control policies.

  - If the relatedSemantics points to a <semanticGroup> resource, the semantic group members from the semanticGroupLinks attribute are used and each of their <semanticDescriptor>(s) are accessed based on the respective access control policies.

  - If the relatedSemantics points to a <group> resource, the group members from the memberID attribute are used and each of their <semanticDescriptor>(s) are accessed based on the respective access control policies.

- Once all of the related <semanticDescriptor>(s) have been accessed, the content of each of the descriptor attributes is added to the content on which the SPARQL request is being executed.

- The full/enlarged content subject to the SPARQL request is provided to the SPARQL engine for processing

### -----------------------End of change 5----------------------------------------------------------

### ------------------- Start of changes to  References Section------------------------------

# 2	References

## 2.1	Normative references

References are either specific (identified by date of publication and/or edition number or version number) or non-specific. For specific references, only the cited version applies. For non-specific references, the latest version of the reference document (including any amendments) applies.

The following referenced documents are necessary for the application of the present document.

[1]		oneM2M TS-0011: “Common Terminology”

[2]	oneM2M TS-0003: " Security Solutions".

[3]	oneM2M TS-0004: "Service Layer Core Protocol Specification".

[4]	W3C RDF 1.1 Concepts and Abstract Syntax

[5]	W3C SPARQL 1.1 Query Language

[6]	oneM2M TS-0012: "oneM2M Base Ontology"

### --------------------End of changes to Reference Section --------------------------------