| CHANGE REQUEST |
| --- |
| Meeting:* | ARC#21 |
| Source:* | NEC |
| Date:* | 2015-01-08 |
| Contact:* | Tetsuo Inoue, NEC (TTC), t-inoue@fp.jp.nec.com Ataru Kobayashi, NEC (TTC), a-kobayashi@df.jp.nec.com Joerg Swetina, NEC Europe Ltd. (ETSI), JoergSwetina@neclab.eu |
| Reason for Change/s:* | Provide a feature of the configuration of device communication patterns as one of 3GPP Rel-13 IWK features. |
| CR against: Release* | oneM2M R2 |
| CR against: WI* | Active WI-0037 MNT maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0001 v2.5.0 |
| Clauses/Sub Clauses* | 8.8 (new) |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

As described in the TR-0024 3GPP Rel13 IWK (WI-0037), an interworking feature for Configuration of Device Communication Patterns is proposed as summarized below contents.

- Describe  general concept of the Configuration of Device Communication Patterns feature.

- Describe Communication Pattern parameters.

- Describe general procedure for Configuration of Device Communication Patterns.

There is no impact to the oneM2M Release1.

### -----------------------Start of change 1-------------------------------------------

## 8.8 Functions for interaction with Underlying Networks

### 8.8.1  Introduction

Functions for interaction with Underlying Networks are used to provide information about the M2M service layer (e.g. communication patterns of oneM2M devices) to the Unterlying Network or receive information from the Unterlying Network (e.g. reports on issues of the Unterlying Network).

Such information enables the Unterlying Network to provide means for optimization of M2M traffic and also allows M2M service layer to optimize its services.

### 8.8.2  Configuration of Device Communication Patterns

The purpose of the Configuration of Device Communication Patterns feature is to provide a means to the oneM2M System  to inform the Underlying Network on parameters that can be used for optimizing the processing at the Underlying Network for a specific Field Domain Node. The feature includes following functionalities:

- An Application Entity (AE) or a Common Service Entity (CSE) shall be able to provide information on the communication behavior (i.e. Device Communication Patterns) of a Field Domain Node (ASN or MN).

- To that purpose the AE or CSE shall be able to set Device Communication Patterns of a particular Field Domain Node via the Mca or Mcc reference point of a IN-CSE,

  - The Field Domain Node is addressed using the (NodeID, AE-IDs) of the Node

- The NSSE CSF of the IN-CSE shall in turn use the Mcn interface towards the Underlying Network to provide information on Device Communication Patterns of a the Field Domain Node.

  - The NSSE CSF of the IN-CSE uses the M2M-Ext-ID to identify the Node towards the Underlying Network.

### 8.8.2.1  Communication Pattern parameters

Communication Pattern (CP) parameters can be associated with one or multiple field domain nodes and are defined in the table below.

A Field Domain Node can be associated with one or multiple sets of CP parameters. At any time only a single set of CP parameters can be associated with a Field Domain Node.

The IN-CSE shall assure that different CP parameter sets for a Node are not overlapping at any point in time.

A combination of the following parameters can be set

Table 8.8.2-1: CP parameter set

| CP parameter set | Description |
| --- | --- |
| Periodic communication indicator | Identifies whether the Node communicates periodically or not, e.g. only on demand. |
| Communication duration time | Duration interval time of periodic communication [may be used together with 1)] Example: 5 minutes |
| Time period | Interval Time of periodic communication [may be used together with 1)] Example: every hour |
| Scheduled communication time | Time zone and Day of the week when the Node is available for communication Example: Time: 13:00-20:00, Day: Monday |
| Stationary indication | Identifies whether the UE is stationary or mobile |
| Data size indication | indicates the expected data size for the pattern |
| Validity time | The time after which a CP parameter becomes invalid once it had been set |

### 8.8.2.2  General procedure for Configuration of Device Communication Patterns

Figure 8.8-1 below depicts a general procedure for configuration of device communication patterns.

Figure 8.8.2-1  General procedure for configuration of device communication patterns

Step-1: Provide information onthe behavior of a field domain node

An AE (IN-AE or an AE of the Field Domain Node that reports its communication behaviour) provides the IN-CSE with information on the behavior of the Field Domain Node (i.e. CP parameter sets) and requests the IN-CSE to provide them to the Underlying Network over the appropriate Mcn protocol.

The AE may provide CP parameter sets for a group of field domain nodes .

The request includes

- the originator AE-ID of the requesting AE,

- a target identifier for example a NodeID or an AE-ID of the field domain node or a group identifier of multiple field domain nodes for which the communication behaviour is provided, and

- a CP parameter set  as indicated in table 8.8.2-1.

The request may include multiple of CP parameter set(s) and validity time(s).

If the IN-CSE has received a request from an AE to provide device communication patterns to the Underlying Network, the IN-CSE checks if the request from the AE is valid with the pre-configured information which may be m2mServiceSubscriptionProfile (with serviceRoles attribute), serviceSubscribedNode, and serviceSubscribedAppRule (with allowedAEs attribute) resources.

Step-2(Optional): Configuration of the CMDH policy for the field domain node

If the communication behavior of the field domain node can be configured and the infrastructure domain node (IN-CSE or IN-AE) wants to modify the behavior of the filed domain node, the IN-CSE may issue a request for configuration of the CMDH policy of the field domain node by means of device management features.

Step-3: Select the server NSE to request for the configuration of the CP parameter sets

For the configuration of the CP parameter sets for a specific field domain node, the IN-CSE selects the server NSE by using the identifier of the field domain node (i.e. the M2M-Ext-ID) by which the node can be identified in the NSE.

Note: The selection of the server NSE can be performed by means of a chain of links of multiple resources in the IN-CSE, i.e. the nodeLink in the AEAnnc resource of a target AE of field domain node linking to the nodeAnnc resource having the hostedCSELink linking to the remoteCSE resource having  the M2M-Ext-ID linking to the UNetwork-ID of the server NSE. (See sections 7.1.8 and 7.1.9)

Step-4: Request for the configuration of the CP parameter sets

For each field domain node received in the AE request the IN-CSE sends a request to provide CP parameter sets for the field domain node to the NSE, using the appropriate Mcn protocol. The request includes an identifier of the filed domain node and one or more CP parameter set(s) as defined at section 8.8.1.

The actual parameters of the request depend on the specification of the selected server NSE.

Example: In the  case that the selected server NSE is a 3GPP HSS, the protocol of the S6t reference point defined by 3GPP is used for the request. The S6t uses one of Diameter Application protocols defined by 3GPP. The request on the S6t reference point for the configuration of the CP parameter sets (a CIR command) must include a User-Identifier AVP (either an External Identifeir or a MSISDN of the UE), may include one or more AESE-Communication-Pattern AVP. An AESE-Communication-Pattern AVP must include a SCEF-ID AVP (represent the ID of the IN-CSE or M2M-SP-ID), may include a SCEF-Reference-ID AVP (assigned by the IN-CSE or M2M-SP to identify the configuration of CP parameter sets uniquely) , may include one or more Communication-Pattern-Set AVP. A Communication-Pattern-Set AVP may include AVPs for Periodic-Communication-Indicator, Communication-Duration-Time, Periodic-Time, one or more Scheduled-Communication-Time, Stationary-Indication, and Validity-Time. Refer to the 3GPP TS29.336 for the detailed protocol description.

Step-5: Response for the configuration of the CP parameter sets

The IN-CSE receives the response for the configuration of the CP parameter sets from the NSE. The response includes the result of the request.

The actual parameters of the response depend on the specification of the selected server NSE.

Example); In the  case that  the selected server NSE is a 3GPP HSS, the protocol of the S6t reference point defined by 3GPP is used for the response. The response on the S6t reference point for the configuration of the CP parameter sets (a CIA command) must include either Result-Code AVP or Experimental-Result AVP, may include a User-Identifier AVP if successful case, may include one or more AESE-Communication-Pattern-Config-Status AVP. An AESE-Communication-Pattern-Config-Status AVP must include the SCEF-Reference-ID AVP (same value in the request), may include the SCEF-ID (same value in the request) and an AESE-Error-Report AVP. Refer to the 3GPP TS29.336 for the detailed protocol description.

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?

# Text boxes

Infrastructure Domain

Field Domain

1. provide information onthe behavior of a field domain node

2. Configuration of the CMDH policy for the field domain node (optional)

- Request for providing 
the CP parameter set sets

- Response

3. Select the server NSE to request for the configuration of the CP parameter sets

Mca

Mcn

IN-CSE

Mcc

NSE

ASN/MN-CSE

AE