| CHANGE REQUEST |
| --- |
| Meeting:* | <ARC 21> |
| Source:* | NEC |
| Date:* | 2015-01-08 |
| Contact:* | Tetsuo Inoue, NEC (TTC), t-inoue@fp.jp.nec.com Ataru Kobayashi, NEC (TTC), a-kobayashi@df.jp.nec.com Joerg Swetina, NEC Europe Ltd. (ETSI), JoergSwetina@neclab.eu |
| Reason for Change/s:* | Provide new resource types for the feature of the configuration of device communication patterns as one of 3GPP Rel-13 IWK features. |
| CR against: Release* | 2 |
| CR against: WI* | Active WI-0037 MNT maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0001 v2.5.0 |
| Clauses/Sub Clauses* | 9.6.38 (new), 9.6.39 (new), 9.6.40 (new) |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

As described in the TR-0024 3GPP Rel13 IWK (WI-0037), new resource types for the Configuration of Device Communication Patterns feature are proposed as summarized below contents.

- 9.6.38 (new): Resource Type <trafficCharacteristics>

- 9.6.39 (new): Resource Type <trafficPatternSet>

- 9.6.40 (new): Resource Type <scheduledCommunicationTime>

There is no impact to the oneM2M Release1.

### -----------------------Start of change 1-------------------------------------------

9.6.38 Resource Type <trafficCharacteristics>

The <trafficCharacteristics> resource represents the characteristic information (e.g. communication pattern, mobility pattern, etc..) of a field domain node. These information may be detected or scheduled by an application level processing. This resource type is used to share information with other entities such as the underlying network entity (server NSE) of the field domain node which may optimize the processing of the underlying network for the specific field domain node.

Figure 9.6.38-1: Structure of <trafficCharacteristics> resource

The <trafficCharacteristics> resource shall contain the child resources specified in table 9.6.38-1.

Table 9.6.38-1: Child resources of <trafficCharacteristics> resource

| Child Resources of <trafficCharacteristics> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 |
| [variable] | <trafficPatternSet> | 0..n | See clause 9.6.39. A source AE can create multiple number of <trafficPatternSet> resources for a single target AE of field domain node. In this case the source AE assures that different communication patterns are not overlapped in a point of time. |

The <trafficCharacteristics> resource shall contain the attributes specified in table 9.6.38-2.

Table 9.6.38-2: Attributes of <trafficCharacteristics> resource

| Attributes of <deviceCharacteristics> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3. |
| resourceID | 1 | RO | See clause 9.6.1.3. |
| resourceName | 1 | WO | See clause 9.6.1.3. |
| parentID | 1 | RO | See clause 9.6.1.3. |
| creationTime | 1 | RO | See clause 9.6.1.3. |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3. |
| expirationTime | 1 | RW | See clause 9.6.1.3. |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3. |
| Labels | 0..1 (L) | RW | See clause 9.6.1.3. |
| creator | 1 | WO | The AE-ID of the entity which created the resource. |

    - Resource Type <trafficPatternSet>

The <trafficPatternSet> resource represents the communication pattern and the mobility pattern of a field domain node to be shared with other entities such as the underlying network entity (server NSE) of the field domain node which may optimize the processing of the underlying network for the specific field domain node by using this information.

Figure 9.6.39-1: Structure of <trafficPatternSet> resource

The <trafficPatternSet> resource shall contain the child resources specified in table 9.6.39-1.

Table 9.6.39-1: Child resources of <trafficPatternSet> resource

| Child Resources of <trafficPatternSet> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8. |
| [variable] | <schedule> | 0..1 | See clause 9.6.9. It provides the mask for the day of week, the starting time and end time for communication. If it is not provided this shall be interpreted as ‘anytime’ at the server NSE. |

The <trafficPatternSet> resource shall contain the attributes specified in table 9.6.39-2.

Table 9.6.39-2: Attributes of <trafficPatternSet> resource

| Attributes of <trafficPatternSet> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3. |
| resourceID | 1 | RO | See clause 9.6.1.3. |
| resourceName | 1 | WO | See clause 9.6.1.3. |
| parentID | 1 | RO | See clause 9.6.1.3. |
| creationTime | 1 | RO | See clause 9.6.1.3. |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3. |
| expirationTime | 1 | RW | See clause 9.6.1.3. |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3. |
| Labels | 0..1 (L) | RW | See clause 9.6.1.3. |
| periodicIndicator | 0..1 | RW | It indicates as ‘Periodical’ or ‘On demand’. |
| periodicDurationTime | 0..1 | RW | It provides the time in seconds of the duration of the periodic communication. |
| periodicIntervalTime | 0..1 | RW | It provides the time in seconds of the interval for periodic communication. |
| stationaryIndication | 0..1 | RW | It indicates as ‘Stationary (Stopping)’ or ‘Mobile (Moving)’. |
| dataSizeIndicator | 0..1 | RW | It indicates the expected data size for the pattern |
| validityTime | 0..1 | RW | It contains the point of time when the informed <trafficPatternSet> information to the server NSE becoming invalid and shall be deleted at the server NSE. |

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?