| CHANGE REQUEST |
| --- |
| Meeting:* | WG2 Architecture - ARC 21 |
| Source:* | Ericsson |
| Date:* | 2016-01-07 |
| Contact:* | George Foti |
| Reason for Change/s:* | Renaming Streaming Session to MM session |
| CR against: Release* | Release 2 |
| CR against: WI* | Active MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0020-V-0.2.0 |
| Clauses/Sub Clauses* | 8.2 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Section 8.3 applies to any Multi media session and not  just  multi-media session. Steraming session  is just an example of a multi media session. Hence this CR replaces the term stremming session with multi media session.

### -----------------------Start of change 1-------------------------------------------

## 8.3        Support for Realtime Multi-media Sessions

Multi-media sessions refer to a session where two peers communicating with the oneM2M system, typically, two AEs, exchange media that has to be streamed between them and that requires specific Quality of Service (QoS). The streamed media will not traverse the oneM2M control nodes but will go directly between the two peers. The oneM2M system role is to ensure that the underlying network nodes that the streamed media traverse shall be provisioned with the proper QoS for the session. The required QoS for the streamed media shall be negotiated between the two AEs through the oneM2M system.

Negotiation between AEs requiring a multi-media session shall be based on SDP as defined in [i.31]. Two modes for negotiation shall be supported by oneM2M:

- In the first mode, the originating AE provides only one offer that the target AE can reject or accept as is.

- In the second mode, the originating AE provides multiple offers and the target AE can reject all offers or accept one and return the accepted offer in the response.

A multi-media session has typically 3 states: session initialization; session modification, and session termination.

To modify (UPDATE) an ongoing session, the session shall be put on hold first, and after successful updating, it shall be resumed. Note that SDP as defined [i.31] specifies all these aspects.

### 8.3.1 Roles of M2M Nodes to support multi-media sessions

There are two main scenarios involving multi-media sessions. They are as follows:

- Scenario 1 where two MN-CSEs or ASNs or one of each is involved.

- Scenario 2 where one MN-CSE or ASN is involved and an IN-CSE is involved

For scenario 1, the IN-CSE has to be involved to ensure that the proper QoS shall be set in the core network nodes connecting the two M2M nodes.  It is the responsibility of the target M2M Node to create the multi-media session resources in the IN-CSE before an offer can be accepted by the target AE and before responding to the originating M2M node.

Should a multi-media session be updated in scenario 1, regardless of which AE initiated the update of the multi-media session the target M2M node, in relation to session initiation, shall ensure the IN-CSE is updated . This implies that the target M2M node shall update the IN-CSE before sending a response to the originating AE if the originating AE initiated the session modification or before sending the request to the originating AE if the target AE initaed the session modification.

The figures below depict the above concepts using 3GPP as an underlying network

Figure 8.3.1-1: 2 peers in a real time multi-media session communicating via an MN-CSE and an IN-CSE

Figure 8.3.1-2: 2 peers in a real time multi-media session communicating via an IN-CSE

Figure 8.3.1-3: 2 peers in a real time multi-media session communicating via 2  MN-CSEs

More generically the architecture looks as follows.

Figure 8.3.1-4: Generic Architecture to Suport Real time multi-media

### 8.3.2  Real time Multi-media Session examples

This section  provides some examples for the establishment/update of a multi-media session to clarify the usage of applicable resources and the service description decpicted above

#### 8.3.2.1 Example 1 - Establishing Multi-media Session (ADN-ADN)

This example below shows the scenario where an AE registered with an MN-CSE desires to establish a multi-media session with a target AE that is registered to another MN-CSE.  In this scenario the IN-CSE has to be involved as described before to ensure that the wide area network resources are configured with the proper QoS for the negotiated session.

The following is a brief description of the steps in the call flow:

- In steps 1a and 1b, the originating and target AE are registered with the corresponding MN-CSE

- In Step 2 the originating AE creates the proper resources for a multi-media session in the MN-CSE with whom it is registered. This is shown as one step in the call flow but there are multiple steps that are not shown for brevity. All necessary resources have to be created in the proper order for the SS resource to be properly created. All requests have to be non-blocking

- In step 3, the MN-CSE creates temporary resources that will be confirmed when the final response is received.

- In step 4, the MN-CSE sends the request to the target MN-CSE. Again here this is shown as one step in the call flow but there are multiple steps that are not shown for brevity. All necessary resources have to be created in the proper order for the SS resource to be properly created in the target MN-CSE. Note that the originating MN-CSE has to maintain the necssary information for the resources it created in the target CSE so it can update/delete/retrieve information later.

- In step 5, the target MN-CSE shall also create the necessary temporary multi-media session resources based on the incoming requests.

- In step 6, the MN-CSE sends a NOTIFY request to the target AE including the originator AE offer for the multi-media session, as well as the needed multi-media session resource IDs information so the AE can update the created resources in the target MN-CSE.

- In step 7, the AE acknowledges the NOTIFY request

- In step 8, the target AE updates the necessary multi-media session resources based on the incoming offer and what it desires to accept.

- In Step 9, the target MN-CSE needs to invoke the IN-CSE since the original request came from another MN-CSE. Hence it sends a CREATE Request based on the accepted offer to the IN-CSE to create the iNMulti-media Session resource

- In steps 10a and 10b, and in this example of a 3GPP underlying LTE network, the IN-CSE interfaces with the PCRF to configure the proper QoS for the session using the Rx reference point. The IN-CSE updates the resources if needed.

- In step 11, the IN-CSE returns the response to MN-CSE.

- In step 12, the MN-CSE updates the resources if needed

- In step 13a, the target MN-CSE forwards the accepted offer to the originating MN-CSE.

- In step 13b the MN-CSE sends the response to the target AE.

- In step 14, the originating MN-CSE updates its resources based on received response in step 13a

- In step 15, the originating MN-CSE returns the response to the originating AE

- In step 16, the originating AE many needs to reserve access bearers. This is optional

Following that multi-media can start between the two ADNs

Figure 8.3.2.1-1: Establishing Real time multi-media session (ADN-ADN)

#### 8.3.2.2 Example 2 - Establishing Multi-media Session (ADN-NA)

This example below shows the scenario where an AE registered win an MN-CSE desires to establish a multi-media session with a target NA that is registered with the IN-CSE.

The following is a brief description of the steps in the call flow:

- In steps 1a and 1b, the originating AE and target NA are registered with the corresponding MN-CSE and IN-CSE respectively

- In Step 2 the originating AE creates the proper resources for a multi-media session in the MN-CSE with whom it is registered. This is shown as one step in the call flow but there are multiple steps that are not shown for brevity. All necsseary resources have to be created in the proper order for the SS resource to be properly created. All requests have to be non-blocking

- In step 3, the MN-CSE creates temporary resources that will be confirmed when the final response is received.

- In step 4, the MN-CSE sends the request to the target IN-CSE. Again here this is shown as one step in the call flow but there are multiple steps that are not shown for brevity. All necsseary resources have to be created in the proper order for the SS resource to be properly created in the IN-CSE. Note that the originating MN-CSE has to maintain the necessary information for the resources it created in the IN-CSE so it can update/delete/retrieve information later.

- In step 5, the target IN-CSE shall also create the necessary temporary multi-media session resources based on the incoming requests.

- In step 6, the IN-CSE sends a NOTIFY request to the target AE including the originator AE offer for the multi-media session, as well as the needed multi-media session resource IDs so the AE can update the created resources in the target IN-CSE.

- In step 7, the AE acknowledges the NOTIFY request

- In step 8, the target AE updates the necessary multi-media session resources based on the incoming offer and what it desires to accept.

- In steps 9a and 9b, and in this example of a 3GPP underlying LTE network,  the IN-CSE interacts with the PCRF to configure the proper OoS using the Rx reference point. The IN-CSE update the resources if needed.

- In step 10, the target IN-CSE forwards the accepted offer to the originating MN-CSE.

- In step 11, the target IN-CSE forwards the response to the target AE..

- In step 12, the originating MN-CSE updates its resources based on received response in step 10

- In step 13, the orioginating MN-CSE retunrs the response to the originating AE

- In step 14,  the originating AE many needs to reserve access bearers. This is optional

Following  that multi-media can start between the two AEs

Figure 8.3.2.2-1: Establishing Real time multi-media session (ADN-NA)

#### 8.3.2.3 Example 3 – Updating an Established Multi-media Session

This example below shows the scenario where an established session between two ADNs have to be updated.  Multi-media has to stop or be put on hold first to enable the session to be updated.

The following is a brief description of the steps in the call flow:

- In step 1 ,a multi-media session is already been established between two ADNs. The session has to be put on hold by updating the session. This is not shown explicitly, but the steps below can be used for that purpose as well. The SDP enables a session to be put hold for updating the QoS, then be resumed once the update is successfully done.

- In Step 2 the originating AE sends an UPDATE request for the resources of the established session. This is shown as one step in the call flow but there are multiple steps that are not shown for brevity. All necessary resources have to be updated in the proper order for the SS resource to be properly updated. All requests have to be non-blocking

- In step 3, the MN-CSE updates the corresponding target MN-CSE for the updated multi-media session and sends the request to the target MN-CSE. Again this is shown as one step in the call flow but there are multiple steps that are not shown for brevity. All necessary resources have to be updated in the proper order for the SS resource to be properly updated. All requests have to be non-blocking.

- In step 4, the MN-CSE sends a NOTIFY request to the target AE including the originator AE updated offer for the multi-media session.

- In step 5, the AE acknowledges the NOTIFY request

- In step 6, the target AE updates the necessary multi-media session resources based on the incoming offer and what it desires to accept.  Again this is shown as one step in the call flow but there are multiple steps that are not shown for brevity. All necessary resources have to be updated in the proper order for the SS resource to be properly updated

- In step 7, the target MN-CSE updates the IN-CSE multi-media session resource

- In steps 8a and 8b, and in this example of a 3GPP underlying LTE network, the IN-CSE interfaces with the PCRF to set the proper QoS using the Rx reference point. The IN-CSE updates the resources if needed.

- In step 9, the IN-CSE updates is resources accordingly .

- In step 10, the IN-CSE sends the response to the target MN-CSE.

- In step 11, the MN-CSE updates the resources if needed

- In step 12a, the target MN-CSE forwards the accepted offer to the originating MN-CSE.

- In step 12b the MN-CSE sends the response to the target AE.

- In step 13, the originating MN-CSE updates its resources based on received response in step 13a

- In step 14, the originating MN-CSE returns the response to the originating AE

- In step 15, the originating AE may need to update the reserved access bearers. This is optional

Following that multi-media can start between the two ADNs

Figure 8.3.2.3-1: Updating a Real  time multi-media session

### 8.3.3 Resource Types To Support Real Time Multi-media Sessions

Note that references to clauses within the attribute and children Resource Tables for existing resources not new for real time multi-media sessions  are for TS-0001.

#### 8.3.3.1Resource Type (SS)

An <SS> resource shall represent information about a multi-media session involving two AEs.

Figure 8.3.3.1-1: Structure of <SS> resource

The <SS> resource shall contain the child resources specified in table 8.3.3.1-1.

# Table 8.3.3.11: Child resources of <SS> resource

| Child Resources of <SS> | Child Resource Type | Multiplicity | Description | <SSAnnc> Child Resource Types |
| --- | --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 | <subscription> |
| [variable] | <accessControlPolicy> | 0..n | See clause 9.6.2 | <accessControlPolicy> <accessControlPolicyAnnc> |

The <SS> resource shall contain the attributes specified in table 8.3.3.1-2.

# Table 8.3.3.1-2: Attributes of <SS> resource

| Attributes of <SS> | Multiplicity | RW/ RO/ WO | Description | <SSAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | NA |
| resourceID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | MA |
| resourceName | 1 | WO | See clause 9.6.1.3 where this common attribute is described. | MA |
| parentID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | NA |
| expirationTime | 1 | RW | See clause 9.6.1.3 where this common attribute is described. | MA |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3 where this common attribute is described. | MA |
| creationTime | 1 | RW | See clause 9.6.1.3 where this common attribute is described. | NA |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | NA |
| labels | 0..1 (L) | RO | See clause 9.6.1.3 where this common attribute is described. | MA |
| sessionID | 1 | RO | The sessionID shall be the same as the resourceID | NA |
| sessionOriginator ID | 1 | WO | The M2M identifier of the originator of the multi-media session. | NA |
| SessionTargetID | 1 | WO | The M2M identifier of the target of the multi-media session. | NA |
| sessionDescription | 1 | RW | Session description, including charateristics of the session that is the subject of multi-media. The sessionDescription attribute is compliant to [i.31]. This is the the final agreed upon session description based on the received response from the target of the multi-media session. | NA |
| initialSDOfferID | 1 | RW | The attribute contains the identifier of an <initialSDOffer> resource. See 8.3.3.2 | NA |

#### 8.3.3.2 Resource Type initialSDOffer

An <initialSDOffer> resource shall represent information about an initial offer for a multi-media session.

Figure 8.3.3.2-1: Structure of <initialSDOffer> resource

The <initialSDOffer> resource shall contain the child resources specified in table 8.3.3.2-1

# Table 8.3.3.2-1: Child Resources of <initialSDOffer> resource

| Child Resources of <initialSDOffer> | Child Resource Type | Multiplicity | Description | <SSAnnc> Child Resource Types |
| --- | --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 | <subscription> |
| [variable] | <accessControlPolicy> | 0..n | See clause 9.6.2 | <accessControlPolicy> <accessControlPolicyAnnc> |
| [variable] | <originatorOffer> | 1 (L) | See clause 8.3.3.3 | NA |

The <initialSDOffer> resource shall contain the attributes specified in table 8.3.3.2-2.

# Table 8.3.3.2-2: Attributes of <initialSDOffer> resource

| Attributes of <originatorOffer> | Multiplicity | RW/ RO/ WO | Description | <AEAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | NA |
| resourceID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | MA |
| resourceName | 1 | WO | See clause 9.6.1.3 where this common attribute is described. | MA |
| parentID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | NA |
| expirationTime | 1 | RW | See clause 9.6.1.3 where this common attribute is described. | MA |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3 where this common attribute is described. | MA |
| creationTime | 1 | RW | See clause 9.6.1.3 where this common attribute is described. | NA |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | NA |
| labels | 0..1 (L) | RO | See clause 9.6.1.3 where this common attribute is described. | MA |

#### 8.3.3.3Resource Type originatorOffer

An <originatorOffer> resource shall represent session description information about an initial offer from an originating AE.

Figure 8.3.3.3-1: Structure of <originatorOffer> resource

The <originatorOffer> resource shall contain the child resources specified in table 8.3.3.3-1 .

# Table 8.3.3.3-1: Vhild Resources of <originatorOffer> resource

| Child Resources of <originatorOffer> | Child Resource Type | Multiplicity | Description | <SSAnnc> Child Resource Types |
| --- | --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 | <subscription> |
| [variable] | <accessControlPolicy> | 0..n | See clause 9.6.2 | <accessControlPolicy> <accessControlPolicyAnnc> |

The <originatorOffer> resource shall contain the attributes specified in table 8.3.3.3-2.

# Table 8.3.3.3-2: Attributes of <originatorOffer> resource

| Attributes of <originatorOffer> | Multiplicity | RW/ RO/ WO | Description | <AEAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | NA |
| resourceID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | MA |
| resourceName | 1 | WO | See clause 9.6.1.3 where this common attribute is described. | MA |
| parentID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | NA |
| expirationTime | 1 | RW | See clause 9.6.1.3 where this common attribute is described. | MA |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3 where this common attribute is described. | MA |
| creationTime | 1 | RW | See clause 9.6.1.3 where this common attribute is described. | NA |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | NA |
| labels | 0..1 (L) | RO | See clause 9.6.1.3 where this common attribute is described. | MA |
| priroity | 1 | RW | The prioriy alliocated to the offer | NA |
| sessionOfferName | 1 | WO | The name allocated to the offer | NA |
| sesssionDescription | 1 | RW | The session Desciption information shall be compliant to [i.31] | NA |

#### 8.3.3.4Resource Type (iNMulti-mediaSession)

An <iNMulti-mediaSession> resource shall represent information about a multi-media session involving two AEs. This resource shall be created only in an IN-CSE node.

Figure 8.3.3.4-1: Structure of <iNMulti-mediaSession> resource

The <iNMulti-mediaSession> resource shall contain the child resources specified in table 8.3.3.4-1

# Table 8.3.3.4-1 : Child resources of <iNMulti-mediaSession> resource

| Child Resources of <SS> | Child Resource Type | Multiplicity | Description | <SSAnnc> Child Resource Types |
| --- | --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 | <subscription> |
| [variable] | <accessControlPolicy> | 0..n | See clause 9.6.2 | <accessControlPolicy> <accessControlPolicyAnnc> |

The <iNMulti-mediaSession> resource shall contain the attributes specified in table 8.3.3.4-2.

# Table 8.3.3.4-2: Attributes of <iNMulti-mediaSession> resource

| Attributes of <SS> | Multiplicity | RW/ RO/ WO | Description | <SSAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | NA |
| resourceID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | MA |
| resourceName | 1 | WO | See clause 9.6.1.3 where this common attribute is described. | MA |
| parentID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | NA |
| expirationTime | 1 | RW | See clause 9.6.1.3 where this common attribute is described. | MA |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3 where this common attribute is described. | MA |
| creationTime | 1 | RW | See clause 9.6.1.3 where this common attribute is described. | NA |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | NA |
| labels | 0..1 (L) | RO | See clause 9.6.1.3 where this common attribute is described. | MA |
| sessionID | 1 | RO | The sessionID shall be the same as the resourceID | NA |
| sessionOriginator ID | 1 | WO | The M2M identifier of the originator of the multi-media session. | NA |
| SessionTargetID | 1 | WO | The M2M identifier of the originator of the multi-media session. | NA |
| sessionDescription | 1 | RW | The description, including charateristics of the session that is the subject of multi-media. The sessionDescription attribute is compliant to [i.31] | OA |

### 8.3.4 Procedures

Note that references to clauses within theses tables are for existing prcoedures in TS-0001 and that are applicable here as well.

#### 8.3.4.1 <SS> Resource Procedures

#### 8.3.4.1.1  Create <SS>

This procedure shall be used for creating an <SS> resource.

Table 8.3.4.1.1-1: <SS> CREATE

| <SS> CREATE |
| --- |
| Associated Reference Point | Mca, and Mcc |
| Information in Request message | All parameters defined in table 8.1.2-2 apply with the specific details for: To: Address of <AE>. Only an originating AE can create an originatorOffer resource over Mca. For Mcc, the To address shall be set to the Address of <remote CSE> of the originating CSE . Only a registered CSE can create an originatorOffer resource over Mcc. Content: The resource content shall provide the information as defined in clause 9.6.35 Only blocking request shall be allowed. All intermediate M2M nodes shall comply to this. |
| Processing at Originator before sending Request | According to clause 10.1.1.1 |
| Processing at Receiver | According to clause 10.1.1.1 with the replacement for sub-step 1) of Step 002 as follows: For a request over Mca, the Hosting CSE shall check if the Originator ID is the same as the AE-ID of the parent resource which is the <AE> resource and If the check fails, the request shall be rejected. For a request over Mcc, the Hosting CSE shall check if the Originator ID is the same as the CSE-ID of the parent resource which is the <remoteCSE> resource and If the check fails, the request shall be rejected |
| Information in Response message | According to clause 10.1.1.1 |
| Processing at Originator after receiving Response | According to clause 10.1.1.1 |
| Exceptions | According to clause 10.1.1.1 |

#### 8.3.4.1.2  Retrieve <SS>

This procedure shall be used for retrieving the attributes of an <SS> resource.

Table 8.3.4.1.2-1: <SS> RETRIEVE

| <SS> RETRIEVE |
| --- |
| Associated Reference Point | Mca, and Mcc |
| Information in Request message | All parameters defined in table 8.1.2-2 apply. |
| Processing at Originator before sending Request | According to clause 10.1.2 |
| Processing at Receiver | According to clause 10.1.2 |
| Information in Response message | All parameters defined in table 8.1.3-1 apply. |
| Processing at Originator after receiving Response | According to clause 10.1.2 |
| Exceptions | According to clause 10.1.2 |

#### 8.3.4.1.3  Update <SS>

This procedure shall be used for updating attributes of an <SS> resource.

Table 8.3.4.1.3-1: <SS> UPDATE

| <SS> UPDATE |
| --- |
| Associated Reference Point | Mca, and Mcc |
| Information in Request message | All parameters defined in table 8.1.2-2 apply. To modify (UPDATE) an ongoing session, the session shall be put on hold first, and after successful updating, it shall be resumed. Note that SDP as defined [i.31] specifies all these aspects. |
| Processing at Originator before sending Request | According to clause 10.1.3 |
| Processing at Receiver | According to clause 10.1.3 The Hosting CSE shall enforce the session state (hold, modify) principles for UPDATES as defined in as defined [i.31] |
| Information in Response message | According to clause 10.1.3 |
| Processing at Originator after receiving Response | According to clause 10.1.3 |
| Exceptions | According to clause 10.1.3 |

#### 8.3.4.1.4  Delete <SS>

This procedure shall be used for deleting an <SS> resource .

Table 8.3.4.1.4-1: <SS> DELETE

| <SS> DELETE |
| --- |
| Associated Reference Point | Mca, and Mcc |
| Information in Request message | All parameters defined in table 8.1.2-2 apply |
| Processing at Originator before sending Request | According to clause 10.1.4.1 |
| Processing at Receiver | According to clause 10.1.4.1 |
| Information in Response message | According to clause 10.1.4.1 |
| Processing at Originator after receiving Response | According to clause 10.1.4.1 |
| Exceptions | According to clause 10.1.4.1 |

### 8.3.4.2 <initialSDOffer> Resource Procedures

#### 8.3.4.2.1 Create <initialSDOffer>

This procedure shall be used for creating an <initialSDOffer> resource.

Table 8.3.4.2.1-1: <initialSDOffer> CREATE

| <initialSDOffer> CREATE |
| --- |
| Associated Reference Point | Mca, and Mcc |
| Information in Request message | All parameters defined in table 8.1.2-2 apply with the specific details for: To: Address of <AE>. Only an originating AE can create an originatorOffer resource over Mca For Mcc, the To: address shall be set to the Address of <remote CSE> of the originating CSE . Only a registered CSE can create an originatorOffer resource over Mcc. Content: The resource content shall provide the information as defined in clause 9.6.36 Only blocking request shall be allowed. All intermediate M2M nodes shall comply to this. |
| Processing at Originator before sending Request | According to clause 10.1.1.1 |
| Processing at Receiver | According to clause 10.1.1.1 with the replacement for sub-step 1) of Step 002 as follows: For a request over Mca, the Hosting CSE shall check if the Originator ID is the same as the AE-ID of the parent resource which is the <AE> resource and If the check fails, the request shall be rejected For a request over Mcc, the Hosting CSE shall check if the Originator ID is the same as the CSE-ID of the parent resource which is the <remoteCSE> resource and If the check fails, the request shall be rejected. |
| Information in Response message | According to clause 10.1.1.1 |
| Processing at Originator after receiving Response | According to clause 10.1.1.1 |
| Exceptions | According to clause 10.1.1.1 |

#### 8.3.4.2.2 Retrieve <initialSDOffer>

This procedure shall be used for retrieving the attributes of an <initialSDOffer> resource.

Table 8.3.4.2.2-1: <initialSDOffer> RETRIEVE

| <initialSDOffer> RETRIEVE |
| --- |
| Associated Reference Point | Mca, and Mcc |
| Information in Request message | All parameters defined in table 8.1.2-2 apply. |
| Processing at Originator before sending Request | According to clause 10.1.2 |
| Processing at Receiver | According to clause 10.1.2 |
| Information in Response message | All parameters defined in table 8.1.3-1 apply. |
| Processing at Originator after receiving Response | According to clause 10.1.2 |
| Exceptions | According to clause 10.1.2 |

#### 8.3.4.2.3 Update <initialSDOffer>

This procedure shall be used for updating attributes of an  <initialSDOffer> resource.

Table 8.3.4.2.3-1: <initialSDOffer> UPDATE

| <initialSDOffer> UPDATE |
| --- |
| Associated Reference Point | Mca, and Mcc |
| Information in Request message | All parameters defined in table 8.1.2-2 apply. To modify (UPDATE) an ongoing session, the session shall be put on hold first, and after successful updating, it shall be resumed. Note that SDP as defined [i.31] specifies all these aspects. |
| Processing at Originator before sending Request | According to clause 10.1.3 |
| Processing at Receiver | According to clause 10.1.3 The Hosting CSE shall enforce the session state (hold, modify) principles for UPDATES as defined in as defined [i.31] |
| Information in Response message | According to clause 10.1.3 |
| Processing at Originator after receiving Response | According to clause 10.1.3 |
| Exceptions | According to clause 10.1.3 |

#### 8.3.4.2.4 Delete <initialSDOffer>

This procedure shall be used for deleting an <initialSDOffer> resource .

Table 8.3.4.2.4-1: <initialSDOffer> DELETE

| <initialSDOffer> DELETE |
| --- |
| Associated Reference Point | Mca, and Mcc |
| Information in Request message | All parameters defined in table 8.1.2-2 apply |
| Processing at Originator before sending Request | According to clause 10.1.4.1 |
| Processing at Receiver | According to clause 10.1.4.1 |
| Information in Response message | According to clause 10.1.4.1 |
| Processing at Originator after receiving Response | According to clause 10.1.4.1 |
| Exceptions | According to clause 10.1.4.1 |

### 8.3.4.3  <originatorOffer> Resource Procedures

#### 8.3.4.3.1  Create <originatorOffer>

This procedure shall be used for creating an <originatorOffer> resource. Only a registered AE can create such a resource

Table 8.3.4.3.3-1: <originatorOffer> CREATE

| <originatorOffer> CREATE |
| --- |
| Associated Reference Point | Mca, and Mcc |
| Information in Request message | All parameters defined in table 8.1.2-2 apply with the specific details for: To: Address of <AE>. Only an originating AE can create an originatorOffer resource over Mca. For Mcc, the To: address shall be set to the Address of <remote CSE> of the originating CSE . Only a registered CSE can create an originatorOffer resource over Mcc. Content: The resource content shall provide the information as defined in clause 9.6.37 Only blocking request shall be allowed. All intermediate M2M nodes shall comply to this. |
| Processing at Originator before sending Request | According to clause 10.1.1.1. Since AE is the Originator, it shall address the <AE> resource that it already created. |
| Processing at Receiver | According to clause 10.1.1.1 |
| Information in Response message | According to clause 10.1.1.1 with the replacement for sub-step 1) of Step 002 as follows: For a request over Mca,the Hosting CSE shall check if the Originator ID is the same as the AE-ID of the parent resource which is the <AE> resource and If the check fails, the request shall be rejected For a request over Mcc, the Hosting CSE shall check if the Originator ID is the same as the CSE-ID of the parent resource which is the <remoteCSE> resource and If the check fails, the request shall be rejected |
| Processing at Originator after receiving Response | According to clause 10.1.1.1 |
| Exceptions | According to clause 10.1.1.1 |

#### 8.3.4.3.2  Retrieve <originatorOffer>

This procedure is used for retrieving the attributes of a <originatorOffer> resource.

Table 8.3.4.3.2-1: <originatorOffer> RETRIEVE

| <originatorOffer> RETRIEVE |
| --- |
| Associated Reference Point | Mca, and Mcc |
| Information in Request message | All parameters defined in table 8.1.2-2 apply. |
| Processing at Originator before sending Request | According to clause 10.1.2 |
| Processing at Receiver | According to clause 10.1.2 |
| Information in Response message | All parameters defined in table 8.1.3-1 apply. |
| Processing at Originator after receiving Response | According to clause 10.1.2 |
| Exceptions | According to clause 10.1.2 |

#### 8.3.4.3.3  Update <originatorOffer>

This procedure shall be used for updating attributes of a <originatorOffer> resource.

Table 8.3.4.3.3-1:  originatorOffer> UPDATE

| <originatorOffer> UPDATE |
| --- |
| Associated Reference Point | Mca, and Mcc |
| Information in Request message | All parameters defined in table 8.1.2-2 apply. |
| Processing at Originator before sending Request | According to clause 10.1.3 To modify (UPDATE) an ongoing session, the session shall be put on hold first, and after successful updating, it shall be resumed. Note that SDP as defined [i.31] specifies all these aspects. |
| Processing at Receiver | According to clause 10.1.3 The Hosting CSE shall enforce the session state (hold, modify) principles for UPDATES as defined in as defined [i.31] |
| Information in Response message | According to clause 10.1.3 |
| Processing at Originator after receiving Response | According to clause 10.1.3 |
| Exceptions | According to clause 10.1.3 |

#### 8.3.4.3.4   Delete <originatorOffer>

This procedure shall be used for deleting a <originatorOffer> resource .

Table 8.3.4.3.4-1: <originatorOffer> DELETE

| <originatorOffer> DELETE |
| --- |
| Associated Reference Point | Mca,and Mcc |
| Information in Request message | All parameters defined in table 8.1.2-2 apply |
| Processing at Originator before sending Request | According to clause 10.1.4.1 |
| Processing at Receiver | According to clause 10.1.4.1 |
| Information in Response message | According to clause 10.1.4.1 |
| Processing at Originator after receiving Response | According to clause 10.1.4.1 |
| Exceptions | According to clause 10.1.4.1 |

### 8.3.4.4  < iNMulti-mediaSession > Resource Procedures

#### 8.3.4.4.1  Create <iNMulti-mediaSession>

This procedure shall be used for creating an <iNMulti-mediaSession> resource. Only a registered CSE can create such a resource in an IN-CSE on behalf of an AE

Table 8.3.4.4.1-1: <iNMulti-mediaSession> CREATE

| <iNMulti-mediaSession> CREATE |
| --- |
| Associated Reference Point | Mcc |
| Information in Request message | All parameters defined in table 8.1.2-2 apply with the specific details for: To: Address of <remoteCSE> of originating CSE. Only an originating CSE can create an originatorOffer resource Content: The resource content shall provide the information as defined in clause 9.6.37 Only blocking request shall be allowed |
| Processing at Originator before sending Request | According to clause 10.1.1.1. Since CSE is the Originator, it shall address the <remoteCSE> resource that it already created. |
| Processing at Receiver | According to clause 10.1.1.1 The IN-CSE shall check if the Originating CSE is the same as the of the parent resource which is the <remoteCES> resource and If the check fails, the request shall be rejected |
| Information in Response message | According to clause 10.1.1.1 with the replacement for sub-step 1) of Step 002 as follows: |
| Processing at Originator after receiving Response | According to clause 10.1.1.1 |
| Exceptions | According to clause 10.1.1.1 |

#### 8.3.4.4.2  Retrieve  <iNMulti-mediaSession>

This procedure is used for retrieving the attributes of a <iNMulti-mediaSession> resource.

Table 8.3.4.4.2-1 <iNMulti-mediaSession> RETRIEVE

| <iNMulti-mediaSession> RETRIEVE |
| --- |
| Associated Reference Point | Mcc |
| Information in Request message | All parameters defined in table 8.1.2-2 apply. |
| Processing at Originator before sending Request | According to clause 10.1.2 |
| Processing at Receiver | According to clause 10.1.2 |
| Information in Response message | All parameters defined in table 8.1.3-1 apply. |
| Processing at Originator after receiving Response | According to clause 10.1.2 |
| Exceptions | According to clause 10.1.2 |

#### 8.3.4.4.3  Update <iNMulti-mediaSession>

This procedure shall be used for updating attributes of a <iNMulti-mediaSession> resource.

Table 8.3.4.4.3-1:  <iNMulti-mediaSession> UPDATE

| <iNMulti-mediaSession> UPDATE |
| --- |
| Associated Reference Point | Mcc |
| Information in Request message | All parameters defined in table 8.1.2-2 apply. |
| Processing at Originator before sending Request | According to clause 10.1.3. To modify (UPDATE) an ongoing session, the session shall be put on hold first, and after successful updating, it shall be resumed. Note that SDP as defined [i.31] specifies all these aspects. |
| Processing at Receiver | According to clause 10.1.3 The Hosting CSE shall enforce the session state (hold, modify) principles for UPDATES as defined in as defined [i.31] |
| Information in Response message | According to clause 10.1.3 |
| Processing at Originator after receiving Response | According to clause 10.1.3 |
| Exceptions | According to clause 10.1.3 |

#### 8.3.4.4.4  Delete <iNMulti-mediaSession>

This procedure shall be used for deleting a <iNMulti-mediaSession> resource.

Table 8.3.4.4.4-1: <iNMulti-mediaSession> DELETE

| <iNMulti-mediaSession> DELETE |
| --- |
| Associated Reference Point | Mcc |
| Information in Request message | All parameters defined in table 8.1.2-2 apply |
| Processing at Originator before sending Request | According to clause 10.1.4.1 |
| Processing at Receiver | According to clause 10.1.4.1 |
| Information in Response message | According to clause 10.1.4.1 |
| Processing at Originator after receiving Response | According to clause 10.1.4.1 |

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?