| Input Contribution |
| --- |
| Meeting ID* | ARC#21 |
| Title:* | OIC Interworking Architectural Aspects (Clause 6) and Transparent Interworking (Clause 7) |
| Source:* | Kiran Vedula, Samsung Electronics, kiran.vedula@samsung.com |
| Uploaded Date:* | 2016-01-06 |
| Document(s) Impacted* | WI-0044 OIC-Interworking TS-0024 v0.0.1 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Include the proposed text into TS-0024 |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# ================ Start of Text Proposal 1 =======================

# 6	Architectural Aspects

## 6.1	Introduction

The OIC IPE participation in the OIC Protocol as described in clause 5 does so in the role of a OIC Client to which OIC Applications (OIC Servers) interact. As a OIC Client, the IPE provides the following Architecture Aspects based on the OIC Protocol Aspects:

- OIC Device Lifecycle

- OIC Resource Discovery

- OIC Interworking Procedure

- OIC Subscription Notification

- OIC Device Management

- OIC Provisioning and Security

## 6.2	OIC Device Lifecycle

### 6.2.1	Introduction

As the OIC IPE discovers OIC Devices when the OIC IPE interacts with the OIC Server over the OIC protocol, the OIC IPE shall maintain the associated resources in the CSE that represents the OIC Device.

### 6.2.2	OIC Device Representation

#### 6.2.2.1	Introduction

OIC Device provides the management and control functions for any M2M application. As such, the CSE that hosts the M2M Applications shall represent the OIC Device as a <AE> resource (OIC Device <AE> resource).  The OIC physical Device that hosts the logical OIC Device shall be represented as a <node> resource.

The properties carried by OIC Device (i.e. device type) shall be translated into the labels attribute of the <AE> Resource as separate entries with the following format:

- OICDT: Device Type (e.g. oic.d.light)

#### 6.2.2.2	OIC Device Identification

OIC Devices are identified by their “di” property as described in OIC Core Specification [3]. The “di” property is used as the AE-ID of the associated <AE> resource that represents the OIC Device.

In most deployment scenarios, OIC physical Devices host one (1) OIC Device. In this scenario the OIC physical Device’s <node> resource’s M2M-Node-ID should be the same as the “di” property. When a OIC physical Device host’s more than one (>1) OIC Device, the determination of the <node> resource’s M2M-Node-ID is implementation specific. In all deployment scenarios, the <AE> resource is linked with the <node> resource as described in TS-001 [2].

As the OIC Device is represented as an <AE>  resource and a OIC Resource is represented as a Content Sharing Resource in the M2M Service Layer, a reference shall be made between the <AE> resource that represents the OIC Device and the Content Sharing Resources which represents the list of OIC Resources available in that OIC Server.

In addition the <AE> resource uses the Hierarchical and Non-Hierarchical mechanisms for Resource Addressing as defined in clause 9.3.1 of TS-001 [2] where the resourceName attribute of the <AE> shall be same as “di” property.

#### 6.2.2.3	OIC Device Discovery and Forget

The OIC Client can periodically get the OIC Server details by requesting them using procedures defined in OIC specifications [2]. The details that the OIC Client gets becomes stale or invalid once the time to live expires.

The OIC operations and events map to the following operations on the <AE> and <node> resources:

| OIC Operation (Discovery) | oneM2M Resource and Operation |
| --- | --- |
| GET | create <AE>, create <Node> |

Table 6.2.2.3-1 OIC Device Discovery Translation - Operations

| OIC Client Events | oneM2M Resource and Operation |
| --- | --- |
| <ttl> expires | delete <AE>, delete <Node>, delete <container> and <flexContainer> resources associated with the <AE> resource. |

Table 6.2.2.3-2 OIC Device Discovery Translation – OIC Client Events

| OIC Properties (Discovery) | oneM2M Resource Attribute |
| --- | --- |
| di | <AE>: AE-ID, resourceName <Node>: M2M-Node-ID when the Device only supports one Endpoint; resourceName |
| ttl | <AE>, <Node>: expirationTime |
| OIC version | <AE>, <Node>: labels. Value is “OIC Server:”appended with the value of the OIC Version. |

Table 6.2.2.3-3 OIC Device Discovery Attribute Translation

| OIC Errors (Discovery) | oneM2M Resource Operation Response |
| --- | --- |
| GET 2.01 Success: Created 4.00 Bad Request 4.03 Forbidden | create <AE>, create <Node> 2001 Created All other codes 4105 Conflict |

Table 6.2.2.3-4 OIC Device Discovery Response Code Translation

##### 6.2.2.4	Configuration of CMDH Policies

In the present document, the CMDH Policies associated with the <Node> resource for the AE is implementation specific.

## 6.3	OIC Resource Discovery

### 6.3.1	Introduction

OIC Server provides the information of supported OIC Resources to an OIC Client. The OIC IPE uses its OIC Client function to synchronize which OIC Resources are supported by the OIC Device and what is stored in the hosting CSE for the M2M Application representing the OIC Device. This clause specifies how discovered OIC Resources are translated to discoverable Content Sharing Resources along with the associated linkages to other resources.

### 6.3.2	OIC Resource Representation

#### 6.3.2.1	Introduction

OIC Server provides the list of supported OIC Resources, where information of each resource is specified in a oic-link format as specified in OIC Core specification [2]. The oic-link format contains information like the resource type, uri and interface.

Optionally other information can be carried by that list as the capability for all the OIC Resources in the OIC Server:

- a specific Content-Format (e.g. OIC JSON/ OIC CBOR Content-Format)

- time to live

For discovery of OIC Resources by M2M Applications, the properties carried by OIC Resources list (i.e. resource type, uri, interface, optional content format, time to live) shall be translated into the labels attribute of the Content Sharing Resource as separate entries with the following format:

- OICRT: Resource Type

- OICURI: Resource URI (href)

- OICIF: Resource Interfaces

- OICCT: Supported Content Format (OIC default supported ContentFormat is CBOR. Others could be JSON, XML)

- OICTTL: Time to Live

For each OIC Resource discovered there will be a separate Content Sharing resource represented.

#### 6.3.2.2	OIC Resource Identification

OIC Resources are identified by their URI within the context of the OIC Device as described in OIC Core specification [3].

As the OIC Device is represented as an <AE>  resource and a OIC Resource is represented as a Content Sharing Resource in the M2M Service Layer, a reference shall be made between the <AE> resource that represents the OIC Device and the Content Sharing Resources which represent the list of OIC Resources available in the OIC Server.

In addition, Content Sharing Resources that represents the OIC Resources use the Hierarchical and Non-Hierarchical mechanisms for Resource Addressing as defined in clause 9.3.1 of TS-001 [2] where the resourceName attribute of the Content Sharing Resource shall be the value of the OICURI.

#### 6.3.2.3	OIC Resource Discovery and Forget

The OIC Client can periodically get the OIC Server details by requesting them using procedures defined in OIC specifications [2]. The details that the OIC Client gets becomes stale or invalid once the time to live expires.

The OIC operations and events map to the following operations on the Content Sharing resource:

| OIC Operation (Discovery) | oneM2M Resource and Operation |
| --- | --- |
| GET | create <container> or <flexContainer> |

Table 6.3.2.3-1 OIC Resource Discovery Translation – Operations

| OIC Client Events | oneM2M Resource and Operation |
| --- | --- |
| <ttl> expires | delete <container> or <flexContainer> |

Table 6.3.2.3-2 OIC Resource Discovery Translation – OIC Client Events

| OIC Attributes (Discovery) | oneM2M Resource Attribute |
| --- | --- |
| di | Not Applicable |
| Resource URI | <container> or <flexContainer> resourceName |
| ttl | <container> or <flexContainer> expirationTime |

Table 6.3.2.3-3 OIC Resource Discovery Attribute Translation

| OIC Errors (Discovery) | oneM2M Resource Operation Response |
| --- | --- |
| GET 2.01 Success: Created 4.00 Bad Request 4.03 Forbidden | create <container> or <flexContainer> 2001 Created All other codes 4105 Conflict |

Table 6.3.2.3-4 OIC Resource Discovery Response Code Translation

## 6.4	OIC Interworking Procedure

### 6.4.1	Introduction

When an oneM2M request is addressed from a CSE/AE to a hosting CSE containing the representation of an OIC Server, the oneM2M response to the Originator of the request is returned through the cooperation of the hosting CSE and the IPE.

The OIC Server provides the capabilities for the OIC Client of the IPE to access available OIC Resources from the OIC Server.

A hosting CSE maintains a representation of OIC Resources as instances of oneM2M resource types. These oneM2M resources are instantiated and discovered as described in clause 6.3 allowing oneM2M AEs and CSEs to exchange data with OIC Servers.

In reference to clause 6.3, at the end of the discovery phase all declared OIC Resources are associated  to a Content Sharing Resource created with  the resourceName attribute set to OICURI.

### 6.4.2	Interworked Resource Settings

An OIC Resource is represented in oneM2M as a Content Sharing Resource with 2 direct children resource types:  a <subscription> resource and a <contentInstance> resource when used with a <container> resource.

For supporting the OIC interworking process, a few attributes for the Content Sharing Resource and the <notification> resource shall have a specified set of parameters.

- Attributes of Content Sharing Resource

| Attributes of <container> or <flexContainer> resource | Value |
| --- | --- |
| accessControlPolicyIDs | ACP set (see Clause 6.7) |
| maxNrOfInstances | 1 |

Table 6.4.2-1 <container> resource – Relevant Interworked Attributes

- Child  resource types of <container> resource

Child resources of <container> resource

<contentInstance> resource

<subscription> resource

Table 6.4.2-2 <container> resource – Relavent Child resource types

- Child  resource types of <flexContainerr> resource

Child resources of <flexContainer> resource

<subscription> resource

Table 6.4.2-3 <flexContainer> resource – Relavent Child resource types

- Attributes of <subscription> resource

| Attributes of <subscription> | Description / Value |
| --- | --- |
| notificationURI | IPE URI |
| eventType | Retrieval attempt of obsolete or non existing direct child resource for the subscribed-to resource |

Table 6.4.2-4 <subscription> resource – Relevant Interworked Attributes

### 6.4.3	Further Considerations for Interworking

Cooperation between IPE and the oneM2M hosting CSE requires efficient mechanisms to maintain the latest state of the targeted OIC Resources. These mechanisms include data synchronization between the IPE and hosting CSE.

Data synchronization relies on the oneM2M Subscription/Notification and OIC Observation/Notification mechanisms. For automated data synchronization between the IPE and hosting CSE to be achieved, the solution shall be granular enough to allow data synchronization for each OIC Resource.

Access Control mechanisms relies on an interworking between oneM2M and OIC Access Control Policies.

OIC and oneM2M mechanisms used to achieve Data Synchronization and Access Control is specified in more details in clauses 6.5 and 6.7.

These following sub-clauses specify the sequences of operations involved for each type of  supported oneM2M requests following the general procedures specified  in clause 10 of TS-001 [2] (CREATE,RETRIEVE, UPDATE, DELETE) as used within the context of the interworking for this present document.

### 6.4.4	Retrieve Procedure

This procedure describes the retrieval of a resource using the oneM2M RETRIEVE request. The information contained within the resource is related to the OIC Resources that are interworked through the IPE. This clause shall be treated in conformance with the RETRIEVE Procedure specified in TS-0001 clause 10.1.2.

The Receiver performs local processing to verify the existence of requested Resource and checks privileges for retrieving the information related to the resource. After successful verification, the Receiver shall return the requested information according to the procedures for interworking as described in clause 7, otherwise an error response shall be returned to the Originator.

Figure 6.4.4-1: Procedure for Retrieving a Resource (TS-0001 Clause 10)

Specific steps of the Receiver Processing according to the interworking process are defined as follows:

Step 001:  Find and verify the targeted Content Sharing Resource: the resourceName corresponds to clause 6.3.2

Step 002: Using the hosting CSE Access Control mechanisms, check for Access Control Policy for retrieving the <contentInstance> resource related to the <container> resource or the <flexContainer> resource.

Step 002a: On successful validation of the Access Control Policy, check if the latest <contentInstance> resource contained within the targeted <container> resource or the <flexContainer> resource has expired or does not exist.

Step 002a.1: When the <contentInstance> resource for the <container> resource or <flexContainer> resource is obsolete or not existing an event for Retrieval attempt (eventType ‘E’) is triggered to the Entity that subscribed to the event (i.e., IPE); as a Blocking Procedure, the hosting CSE shall monitor the arrival of the new data or decide to report a timeout error in jumping to Step 003.

Step 002a.1.1: On receiving the event ‘Retrieval attempt of obsolete or non existing direct child resource (eventType ‘E’) the IPE performs a OIC GET request on the OIC Resource of the targeted OIC Server.

Step 002a.1.2: Once the targeted OIC Resource is available to IPE, the IPE creates and populates a <contentInstance> resource in the requested <container> resource or the <flexContainer> resource.

Step 003: The hosting CSE returns the appropriate response back to the Originator (e.g. Acknowledgment, Errors, and Data)

Note: as an OBSERVATION has been set up on the targeted OIC Resource, the automatic synchronization between the OIC Resource and its representation in the hosting CSE is performed. Further oneM2M accesses to the resource should be simplified in minimizing impact of Step002a (up-to-date data already present from the hosting CSE resources).

General Exceptions:

- The targeted resource/attribute in To parameter does not exist. The Receiver responds with an error.

- The Originator does not have privileges to retrieve information stored in the resource on the Receiver. The Receiver responds with an error.

| OIC Server Response Codes | oneM2M Resource Operation Response |
| --- | --- |
| Read 2.05 Content: 4.01 Unauthorized 4.04 Not Found 4.05 Method Not Allowed | 2000 OK 4103 4004 4005 |

Table 6.4.4-1 OIC Response Codes to oneM2M Resource Operation Response Codes

## 6.5	OIC Resource Subscription and Notification

<TBD>

## 6.6		OIC Device Management

<TBD>

## 6.7	OIC Provisioning and Security

<TBD>

## 6.8	IPE Management

### 6.8.1	IPE Administration

The OIC IPE provides the functionality that plays the role of the OIC Client in order to communicate with OIC Servers.

In order for communication to be established information must be provisioned into the OIC Client where the following artifacts are necessary to be established for the OIC Client:

- OIC Client Credentials

- OIC Access control lists

The mechanisms used to administer and maintain the OIC Client functionality within the OIC IPE is out of scope of this present document.

### 6.8.2	Maintaining IPE Context

The OIC IPE maintains information related to its operational context. Specifically the following elements are maintained for the OIC IPE:

- List of currently discovered OIC Devices.

- List of OIC Resources supported.

Whenever an OIC Endpoint <AE> resource is created, updated or deleted as described in clause 6.2, the OIC IPE also manages the list of OIC Endpoint <AE> resources using a oneM2M  <group> resource.

The oneM2M <group> resource’s lifecycle is linked to the OIC IPE <AE> resource’s lifecycle:

| OIC IPE <AE> resource Operation | oneM2M Resource and Operation |
| --- | --- |
| create | create <group>. The group resourceName is the AE-ID of the OIC IPE <AE>.resource |
| update | update <group> |
| delete | delete <group> |

Table 6.8.2-1 OIC IPE <AE> resource – Group Lifecycle

The OIC Device <AE> resources lifecycle operation maps to the following operations on the oneM2M <group> resource:

| OIC Device <AE> resource Operation | oneM2M Resource and Operation |
| --- | --- |
| Create | update <group> (add member) |
| Delete | update <group> (delete member) |

Table 6.8.2-2 OIC Device <AE> resource – Group member Lifecycle

# 7	Transparent Interworking Function

## 7.1	Introduction

Clause 5.4 introduced the Transparent Interworking function as depicted in Figure 5.4-1. This clause specifies the mappings of the attributes of the <contentInstance> resource for a <container> resource or updating the <flexContainer> resource in order to allow an AE that uses the Content Sharing Resource to understand that the Content Sharing Resource has an encapsulated OIC Resource.

## 7.2	Attribute Mapping for the Content Sharing Resources

When an AE accesses a <contentInstance> resource or <flexContainer> resource, the AE needs to know that the <contentInstance> resource or <flexContainer> resource encapsulates an OIC Resource as well as how the OIC Resource is encoded.

| Interworking Function Mapping | oneM2M Resource Attribute |
| --- | --- |
| Indication that a OIC Resource is encapsulated in the <contentInstance> or <flexContainer> resource with the content type and encoding of the OIC Resource. | <contentInstance> or <flexContainer> resource: labels. Value is “OIC Resource Encapsulation e.g. oic.r.switch.binary” |
| The content type of the OIC Resource based on the Content-Type option | <contentInstance>: contentInfo. Possible contentInfo values are translated from the OIC Content-Type option. Note: The OIC Core Specification [3] defines the value to be used for the [encoding] if the Content-Type option is not present. <flexContainer>: contentInfo |
| The encoding of the OIC Resource | <flexContainer>: containerDefinition: OIC Core Specification:OIC Resource URN. <flexContainer>: customAttribute: The name of the customAttribute shall be the resourceName of the OIC Resource. The data type shall be the OIC Resource's data type as defined in OIC Core Specification [3]. |

Table 7.2-1 Transparent Interworking Function Mapping

================ End of Text Proposal 1 =====================