| Input Contribution |
| --- |
| Meeting ID* | ARC#21 |
| Title:* | oneM2M resource mapping structure |
| Source:* | LG Electronics, SeungMyeong JEONG (seungmyeong.jeong@lge.com) |
| Uploaded Date:* | 2016-01-11 |
| Document(s) Impacted* | TS-0021 oneM2M-AllJoyn interworking |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the text into the TS. |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

This contribution proposes a new clause 6.3 to specify the oneM2M resource mapping tree for AllJoyn services.

The tree structure would help reader’s understanding of the rest part of this TS and be the reference to implementations. Hence, this is added before other architecture aspects.

## ----------------------- Start of text 1 -----------------------

# 6	Architecture Aspect

## 6.1	Introduction

oneM2M and AllJoyn have different architecture aspects (Annex A oneM2M and AllJoyn technical comparison). The present document specifies the interworking functions for those differences in the following aspects:

- oneM2M resource mapping structure

- AllJoyn IPE registration

- AllJoyn service discovery

- AllJoyn service mapping

- AllJoyn access control mapping

## 6.2	oneM2M resource mapping structure

Figure 6.2-1	Resource mapping structure

The figure above illustrates the tree structure of oneM2M resource types that mapps AllJoyn services components. There shall be a single <AE> resource on a CSE that is AllJoyn IPE.

## 6.3	AllJoyn IPE registration

To start oneM2M-AllJoyn interworking, the IPE shall perform AE registration procedure to the MN-CSE specified in [1]. When the IPE creates an <AE> resource, the resource shall include the label attribute set as “IPE:AllJoyn” value.

After the registration, the IPE may perform AllJoyn service discovery.

To stop using the interworking function, IPE shall perform AE de-registration procedure.

## ----------------------- End of text 1 -----------------------

# Text boxes

member value

0..n

0..n

<CSEBase>

<AE>

AllJoyn IPE

<container>

AllJoyn object

<container>

<container>

AllJoyn interface

<flexContainer>

<flexContainer>

AllJoyn interface

0..1

0..n

0..n

<contentInstance>

interface member

interface member

0..n

0..n