²

| CHANGE REQUEST |
| --- |
| Meeting:* | ARC TP21 |
| Source:* | GEMALTO N.V |
| Date:* | 2016-01-11 |
| Contact:* | Thierry Garnier , GEMALTO N.V, Thierry.garnier@gemalto.com |
| Reason for Change/s:* | For improving Interworking efficiency, (see Input Contribution “ARC-2016-2064- IW - ARC improvement - LWM2M/IW Procedures” for the detailed rational) the <latest> resource procedures should support minor modification |
| CR against: Release* | Release 2 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0001 V2.5.0 |
| Clauses/Sub Clauses* | Clause 10.2.22 <latest> Resource Procedures |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

### -----------------------Start of change 1 ---------------------------------------------10.2.22	<latest> Resource Procedures

Only Retrieve, Create and Delete operations shall be allowed for the <latest> resource.

.

.

#### 10.2.22.2	Create <latest>

This procedure shall apply to the latest <contentInstance> resource among all existing <contentInstance> resources in the parent <container> resource.

If creating the latest <contentInstance> resource violates the policy defined in the parent <container> resource regarding the  maxNrOfInstances, then the oldest <contentInstance> resources shall be removed from the <container> to enable the creation of the new <contentInstance> resource and this procedure then is the same as the procedures in clause 10.2.19.2 <contentInstance> CREATE.

If there is no existing <contentInstance> resource, a new <contentInstance>  resource is created according to the clause  10.2.19.2 <contentInstance> .

In both case,  the  <latest> resource shall point to the newly created <contentInstance> child resource within the parent <container> resource.

-----------------------End of change 1 --------------------------------------------------