²

| CHANGE REQUEST |
| --- |
| Meeting:* | ARC TP21 |
| Source:* | GEMALTO N.V |
| Date:* | 2016-01-11 |
| Contact:* | Thierry Garnier , GEMALTO N.V, Thierry.garnier@gemalto.com |
| Reason for Change/s:* |  |
| CR against: Release* | Release 2 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0014 V0.7 |
| Clauses/Sub Clauses* | Clause 6.4 LWM2M Object Transport and Interworking |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

### -----------------------Start of change 1 -------------------------------------------------

### 6.4.2	LWM2M Interworking Mechanisms

#### 6.4.2.1	Introduction

.

These following sub-clauses specify the sequences of operations involved for each type of  supported oneM2M requests following the general procedures specified  in clause 10 (CREATE,RETRIEVE, DELETE) as used within the context of the interworking for this present document

According to clause 10.2.4 (<container> resource procedures) and 10.2.19  (<contentInstance> resource procedures), the effective request result is depending of the targeted resource type.

For each oneM2M general procedures supported by LWM2M Interworking, the following sub-clauses specify the operations and  expected behaviour according to the type of the targeted resource type.

When the <contentInstance> resource of a <container> resource is targeted in a request, it shall be targeted in using the <latest> resource only.

Table xxxxx : Correlation between oneM2M procedures and  effects in the Interworked LWM2M context according to the type of targeted resource

| oneM2M Request | CREATE | RETRIEVE | DELETE |
| --- | --- | --- | --- |
| <container> resource | FFS (LWM2M Object Instantiation) | Retrieval of partial or complet <container> resource data according to request parameters | LWM2M Object Instance Deletion and de-registration |
| <latest> resource | LWM2M Object Instance Update | LWM2M Object Instance data Retrieval | Make <latest> resource obsolete |

### -----------------------End of change 1 --------------------------------------------------

### ---------------------- Start of change 2 --------------------------------------------------

#### 6.4.2.2	Relevant Interworked Resource Settings

A LWM2M Object Instance is represented in oneM2M as a <container> resource with 2 direct children resource types:  a <subscription> resource and a <contentInstance> resource.

For supporting the LWM2M interworking process, a few attributes for the <container> resource and the <notification> resource shall have a specified set of parameters

- Attributes of <container> resource

| Attributes of <container> resource | Value |
| --- | --- |
| accessControlPolicyIDs | ACP set (see Clause 6.6) |
| maxNrOfInstances | 1 |

Table 6.4.2.2-1 <container> resource – Relevant Interworked Attributes

- Child  resource types of <container> resource

Child resources of <container> resource

<contentInstance> resource

<subscription> resource

Table 6.4.2.2-2 <container> resource – Relevent Child resource types

- Attributes of <subscription> resource

| Attributes of <subscription> resource | Description / Value |
| --- | --- |
| notificationURI | IPE URI |
| eventType | Deletion of the subscribed-to resource , Creation of a direct child of the subscribed-to resource , Deletion of a direct child of the subscribed-to resource E. Retrieval attempt of obsolete or non existing direct child resource for the subscribed-to resource |

Table 6.4.2.2-3 <subscription> resource – Relevant Interworked Attributes

### -----------------------End of change 2 --------------------------------------------------

#### 6.4.2.3	oneM2M RETRIEVE Procedure

This procedure describes the retrieval of a resource using the oneM2M RETRIEVE request. The information contained within the resource is related to the LWM2M Objects Instances that are interworked through the IPE. This clause shall be treated in conformance with the RETRIEVE Procedure specified in TS-0001 clause 10.1.2.

The Receiver performs local processing to verify the existence of requested Resource and checks privileges for retrieving the information related to the resource. After successful verification, the Receiver shall return the requested information according to the procedures for the type of interworking (e.g. Transparent, Semantically Enabled) as described in clause 7 and 8, otherwise an error response shall be returned to the Originator

Figure 6.4.2.3-1: Procedure for Retrieving a Resource (TS-0001 Clause 10)

##### Whatever the target <container> resource or <latest> resource of the request, the operations for the RETRIEVE are the same, only the content of the returned message can be different.

Specific steps of the Receiver Processing according to the interworking process shall be   as followed:

Step 001:  Find and verify the <container> resource of the request : the resourceName corresponds to clause 6.3.2

Step 002: Using the Hosting CSE Access Control mechanisms, check for Access Control Policy attached to the <container> resource of the request

Step 003: On successful validation of the Access Control Policy, check if the <latest>  resource of the <container> resource is involved in the request: if not jump to step 4.

Step 003.1: When the <contentInstance> resource is obsolete or not existing   an event for Retrieval attempt (eventType ‘E’) is triggered to the Entity that subscribed to the event (i.e. IPE); as a Blocking Procedure, the Hosting CSE shall monitor the arrival of the new data or decide to report a timeout error in jumping to Step 004

Step 003.1.1: On receiving the event ‘Retrieval attempt of obsolete or non existing direct child resource’ (eventType ‘E’) the IPE performs a LWM2M READ request on the Object Instance of the targeted LWM2M Client.

Step 003.1.2: Once the targeted Object Instance is available to IPE, the IPE creates and populates the  <latest> resource in the  <container> resource of the request.

Step 004: The Hosting CSE returns the appropriate response back to the Originator (e.g. Acknowledgment, Errors, and Data)

Note: as an OBSERVATION has been set up on the targeted LWM2M Object Instance, the automatic synchronization between the Object Instance and its representation in the Hosting CSE is performed. Further oneM2M accesses to the resource should be simplified in minimizing impact of Step003 (up-to-date data already present from the Hosting CSE resources).

General Exceptions:

When the targeted resource/attribute in To parameter does not exist, and no notification with eventType ‘E’ is triggered (“Retrieval attempt of obsolete or non existing direct child resource for the subscribed-to resource”), then ,. the Receiver responds with an error.

The Originator does not have privileges to retrieve information stored in the resource on the Receiver. The Receiver responds with an error.

### ----------------------- Start of change 2 -------------------------------------------------

#### 6.4.2.4	oneM2M CREATE Procedure

##### 6.4.2.4.1 <container> resource as a target

<FFS : should be used to create Instance of registered LWM2M Object>

##### 6.4.2.4.2 <latest> resource as a target

This procedure describes the update of  LWM2M Object Instance within a LWM2M Client using the oneM2M CREATE <latest> request . The information contained within the request  is related to the LWM2M Objects Instances that are interworked through the IPE. This clause shall be treated in conformance with the CREATE Procedures specified in TS-0001 clause 10.1.2 and 10.2.22.2.

If there is no existing <contentInstance> resource, a new <contentInstance> resource is created with the <latest> resource pointing to it.

In LWM2M Interworking context, if there is already an existing <contentInstance> resource, creating the latest <contentInstance> resource shall violates the policy defined in the parent <container> resource regarding the  maxNrOfInstances which shall be set to 1.Then the oldest <contentInstance> resources shall be removed from the <container> to enable the  creation of the new <contentInstance> resource upon which the <latest> resource

shall point.

In both cases, a notification is sent to the IPE, which subscribed to the parent <container> resource with the eventType ‘C’ (Creation of a direct child of the subscribed-to resource ), for updating the LWM2M resource model with the new data received.

Figure 6.4.2.3-2: Procedure for Creating a Resource (TS-0001 Clause 10)

Specific steps of the Receiver Processing according to the interworking process shall be as followed:

Step 001:  Find and verify the <container> resource of the request : the resourceName corresponds to clause 6.3.2

Step 002: Using the Hosting CSE Access Control mechanisms, check for Access Control Policy attached to the <container> resource of the request

Step 003: On unsuccessful validation of the Access Control Policy, jump to step 4

Step 003.1: When the <latest> resource is created  an event (eventType ‘C’)  for  Child Creation (eventType ‘C’)   is triggered to the Entity that subscribed to that event (i.e. IPE).

Step 003.2: On receiving the event ‘Creation of a direct child of the subscribed-to resource’, the IPE get - via the Mca reference point - the data from the created  <latest> resource and propagates the updated data of the related Object Instance into the LWM2M Client.

Step 004: The Hosting CSE returns the appropriate response back to the Originator (e.g. Acknowledgment, Errors)

General Exceptions:

- The Originator does not have the privileges to create a resource on the Receiver. The Receiver responds with an error.

- The resource with the specified name (if provided) already exists at the Receiver. The Receiver responds with an error.

- The provided information in Content is not accepted by the Receiver (e.g. missing mandatory parameter). The Receiver responds with an error.

### ---------------------- End of change 2 -------------------------------------------------

### ----------------------- Start of change 4 -------------------------------------------------

#### 6.4.2.5	oneM2M DELETE Procedure

This procedure describes the delete of a resource using the oneM2M DELETE request.

##### 6.4.2.5.1 <container> resource as a target

This procedure describes the delete of a LWM2M Object Instance within a LWM2M Client using the oneM2M DELETE request

This clause shall be treated in corformance with the DELETE Procedure specified in TS-0001 clause 10.1.4.

##### 6.4.2.5.2 <latest> resource as a target

This procedure describes the delete of an resource in the Hosting CSE using the oneM2M DELETE request

The information contained within the resource is related to LWM2M Objects Instance that is interworked through the IPE.

### ----------------------- End of change 4 -------------------------------------------------