| CHANGE REQUEST |
| --- |
| Meeting:* | ARC 21 |
| Source:* | Datang |
| Date:* | 2016-01-18 |
| Contact:* | Wei Zhou, Datang, zhouwei@catt.cn |
| Reason for Change/s:* | Proposing role based access control architecture and procedures. |
| CR against: Release* | Release 2 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0001 V2.5.0 |
| Clauses/Sub Clauses* | 11.x Role Based Access Control |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This contribution proposes role based access control architecture and procedures.

### -----------------------Start of change 1---------------------------------------------

## 11.x	Role Based Access Control

### 11.x.1	Role Based Access Control Architecture

Figure 11.x-1 provides a high level overview of the role based access control architecture in the oneM2M System. The entities related to role issuance are described as follows:

Role Authority: It is responsible for assigning roles to Originators through creating <role> resources in Role Repositories.

Role Repository: It is a CSE that is responsible for storing <role> resources created by Role Authorities.

Figure 11.x-1. Role based access control architecture

The generic procedure of this architecture is described as follows:

Step 001:	An Originator applies for a privilege from a Role Authority.

Step 002:	The Role Authority checks if the applied privilege can be assigned to the Originator. If it is permitted, the Role Authority issues a role to the Originator.

Step 003:	The Originator creates a <role> resource in a Role Repository from which the role consumers can retrieve the roles assigned to an AE or CSE.

Step 004:	The Originator retrieves the assigned role from its registration resource.

Step 005:	The Originator sends a resource access request in which role ids are included to the Hosting CSE.

Step 006:	The Hosting CSE sends an access decision request to a PDP.

Step 007:	The PDP need to retrieve the Originator’s role assignment information according to the role ids from a Role Repository.

Step 008:	The PDP verifies the Originator’s roles and then makes an access control decision according to the access control policies and roles.

NOTE 1:	Some steps described here may not need in some applications, e.g. a Role Authority may directly issue roles to an Originator without step 1, or the Originator already have the role information from the Role Authority, and does not need to do the step 4.

### 11.x.2	Role Issuing Procedure

The general procedure of issuing a role to an Originator is shown in the Figure 11.x.2-1 and described as follows:

# Figure 11.x.2-1: Procedure of issuing a role

Procedure of role issuance is:

- The Originator sends privilege application request to the Role Authority.

- The Role Authority checks if the applied privilege can be assigned to the Originator. After passing the privilege authorization check the Role Authority issues a role to the Originator.

- The Role Authority sends a <role> resource creation request to the Role Repository.

- The Role Repository creates a <role> resource according to the creation request.

- The Registrar CSE returns the result of <role> resource creation back to the Role Authority.

- The Role Authority returns the result of role issuance back to the Originator. The response may or may not contain the role information.

- The Originator may send <role> resource retrieve request to the Role Repository in order to get the role assignment information.

- The Role Repository returns retrieved <role> resources back to the Originator.

### 11.x.3	Role Based Access Control Procedure

The general procedure of using a role in an authorization process is shown in the Figure 11.x.3-1 and described as follows:

# Figure 11.x.3-1: Role based access control procedure

Procedure of using role and/or token is:

- The Originator selects applicable role IDs according to the App-IDs attribute of <role> resources, and includes them into the request sent to the Hosting CSE.

- The PEP [2] in the Hosting CSE generates access decision request according to the request of the Originator, and sends the request to a PDP [2]. The role IDs received from the Originator should be included in the request.

- The PDP send role attribute requests to a PIP [2] in order to get the role information using the role IDs, and the PIP further sends <role> resource retrieve requests to the Role Repository. The PDP may directly send <role> resource retrieve requests to the Role Repository instead of via a PIP.

- The Role Repository retrieves the <role> resource and returns the information of <role> resources back to the PIP or directly back to the PDP.

- The PDP verifies the received roles, the verification includes: roles are issued by a valid Role Authority and are still valid. Only valid roles can be used for access control.

- The PDP evaluates the access request of the Originator using access control policies and privileges assigned to the Originator for making an access control decision.

- The PDP returns the access control decision back to the PEP.

- The Hosting CSE enforces the access control decision, i.e. either performs the resource access on behalf the Originator or denies the resource access.

- The Hosting CSE returns the result of resource access back to the Originator.

### -----------------------End of change 1 ---------------------------------------------