| CHANGE REQUEST |
| --- |
| Meeting:* | <ARC 21.2> |
| Source:* | Tetsuo Inoue, NEC (TTC), t-inoue@fp.jp.nec.com Ataru Kobayashi, NEC (TTC), a-kobayashi@df.jp.nec.com Joerg Swetina, NEC Europe Ltd. (ETSI), JoergSwetina@neclab.eu |
| Date:* | 2015-02-18 |
| Contact:* | Tetsuo Inoue, NEC (TTC), t-inoue@fp.jp.nec.com Ataru Kobayashi, NEC (TTC), a-kobayashi@df.jp.nec.com Joerg Swetina, NEC Europe Ltd. (ETSI), JoergSwetina@neclab.eu |
| Reason for Change/s:* | Provide a feature of the configuration of device communication patterns as one of 3GPP Rel-13 IWK features. |
| CR against: Release* | oneM2M R2 |
| CR against: WI* | Active WI-0037 MNT maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0024 v0.2.0 |
| Clauses/Sub Clauses* | 8.3 (new), 1, 5.3, 2.2 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR proposes to add new section 8.3 of TR-0024 3GPP Rel13 IWK (WI-0037) for Configuration of Device Communication Patterns feature. The contents are summarized as below.

- General concept for Configuration of Device Communication Pattern feature

- What are the Communication Pattern parameters

- General procedure for Configuration of Device Communication Patterns

- Relationshp between resources (existing and new)

There is no impact to the oneM2M Release1.

Note):

Number of discussions for this topics have been done at ARC20.1, ARC20.2 and e-mails by another contributions ARC-2015-2290(-R01,R02,R03). This contribution is resolving comments on these discussions.

R03: To be corrected TR-0024 based on the agreed CRs of TS-0001 and some editorial correction of TR-0024.

R04/R05: To be fixed TR-0024 based on the e-mail comments at ARC 21.1 conference for shynchronization aspects and others.

R06: To be fixed TR-0024 based on the e-mail comments at ARC 21.2.

### -----------------------Start of change 1-------------------------------------------

### 8.3  Configuration of Node Traffic Patterns

#### 8.3.1  Purpose of Configuration of Node Traffic Patterns

Cellular M2M devices that have predicable communication patterns can profit in terms of reduction of signalling, energy saving, fewer sleep/awake transitions, etc., when these patterns are communicated to the underlying network. Especially devices that will  use new 3GPP power savings features such as eDRX (extended discontinuous reception) and PSM (Power Saving Mode) on LTE devices.  Benefits will also be seen in the underlying network.  For example, if the IN-CSE knows the device’s communication pattern and transmits it via a 3GPP SCEF to an underlying 3GPP network, then this information can be used by a 3GPP network to set the device’s “Maximum Response Time” (3GPP Term) to tune the UE’s DRX and PSM parameters.  If these parameters are tuned properly, the network will benefit because the UE will have fewer sleep/awake transitions and unnecessary signalling in the network can be avoided.  Also, if the IN-CSE knows when the device is awake, it can send data exactly at the time when the device is listening, thus requiring the network to buffer less data for unavailable devices.

The purpose of the Configuration of Node traffic patterns feature is to provide a means to the oneM2M System  to inform the Underlying Network on parameters that can be used for optimizing the processing at the Underlying Network for a specific Field Domain Node. The feature includes following functionalities:

- An Application Entity (AE) or a Common Service Entity (CSE) shall be able to provide information on the communication behavior (i.e. Device Communication Patterns) of a Field Domain Node (ASN or MN).

- To that purpose the AE or CSE shall be able to set Node traffic patterns of a particular Field Domain Node via the Mca or Mcc reference point of a IN-CSE,

  - The Field Domain Node is addressed using the (NodeID, AE-IDs) of the Node

- The IN-CSE shall in turn use the Mcn interface towards the Underlying Network to provide information on Node traffic patterns of a the Field Domain Node.

  - The IN-CSE uses the M2M-Ext-ID to identify the Node towards the Underlying Network.

#### 8.3.2  Traffic pattern parameters

A set of Traffic pattern (TP) parameters can be associated with a Traffic Pattern of one or multiple field domain nodes and are defined in the table below.

A Field Domain Node can be associated with one or multiple Traffic Patterns. At any time only a single Traffic Pattern can be associated with a Field Domain Node.

The IN-CSE shall assure that different Traffic Patterns for a Node are not overlapping at any point in time.

A combination of the following TP parameters can be set for a Traffic Pattern

Table 8.3.2-1: Traffic pattern parameters

| TP parameter | Description |
| --- | --- |
| TP Periodic communication indicator | Identifies whether the Node communicates periodically or not, e.g. only on demand. |
| TP Communication duration time | Duration interval time of periodic communication [may be used together with TP periodic communication indicator] Example: 5 minutes |
| TP Time period | Interval Time of periodic communication [may be used together with TP periodic communication indicator] Example: every hour |
| TP Scheduled communication time | Time zone and Day of the week when the Node is available for communication Example: Time: 13:00-20:00, Day: Monday |
| TP Stationary indication | Identifies whether the Node is stationary or mobile |
| TP Data size indication | indicates the expected data size for the pattern |
| TP Validity time | The time after which aTP parameter becomes invalid once it had been set |

#### 8.3.3  General procedure for Configuration of Traffic Patterns

Figure 8.3.3-1 below depicts a general procedure for configuration of AE and Node traffic patterns.

Figure 8.3.3-1  General procedure for configuration of Node traffic patterns

Step-1: AE Request to Provide information on the Traffic Patterns of a field domain node

An AE (IN-AE or an AE of the Field Domain Node) provides the IN-CSE with information on the Traffic Patterns of the Field Domain Node

1a) An AE of the Field Domain Node may provide its own, application specific, Traffic Patterns in its <AE> resource and announce them as a child resource of the <AEAnnc> resource on the IN-CSE.
Subject to access rights the AE may also provide Traffic Patterns of its Node in the <node> resource and announce them as a child resource of the <nodeAnnc> resource on the IN-CSE.

1b) An AE in the Infrastructure Domain may provide the Traffic Patterns of a field domain Node or a group of multiple field domain Nodes.

The request for providing the IN-CSE with Traffic Patterns includes

- the creator AE-ID of the requesting AE,

- a target identifier:  i.e. a <node> resource or an <AE> resource of the field domain node, its announced <nodeAnnc> or <AEAnnc> resource on the IN-CSE or a group identifier of multiple announced resources on the IN-CSE for field domain nodes for which the Traffic Patterns  is provided, and

- a set of TP parameters as indicated in table 8.3.2-1.

The request may include multiple of TP parameter set(s) and validity time(s).

If the IN-CSE has received a request from an AE to provide Node traffic patterns, the IN-CSE checks if the request from the AE is valid, using pre-configured information which may be found in m2mServiceSubscriptionProfile (with serviceRoles attribute), serviceSubscribedNode, and serviceSubscribedAppRule (with allowed AEs attribute) resources.

- In case of a target field domain node that has multiple AEs with different application specific traffic patterns, the IN-CSE shall perform the following steps:

  - If the new request to provide Node traffic patterns  includes the same traffic patterns as the existing traffic patterns for the Node the IN-CSE accepts the request. But the IN-CSE does not provide the Node traffic pattern to the Underlying Network, i.e. it is not performing steps 3 to 5.

  - If the new request to provide Node traffic patterns includes a traffic pattern different to the previous one the IN-CSE checks consistency of the new traffic pattern for the Node with the existing traffic patterns for the Node and with traffic patterns for AEs of the Node. If  no inconsistency is detected (e.g. if different traffic pattern sets have different time frames), the new request is accepted and the new traffic pattern is created in the <trafficCharacteristics> resource of the Node (or an existing traffic pattern is updated). Otherwise, the request is rejected.

  - Editor's note; If multiple AEs on several ADNs tied to an MN-CSE or an ASN report different TPs to the IN-CSE, then coordination for no inconsistency between multiple AEs on an ADN by the IN-CSE is assumed and it is out of scope.

  - Note: The creator AE of the Traffic Patterns has to assure as no inconsistency between <schedule> resource of the Node and the Traffic Patterns. Thus the creator AE may update the <schedule> resource of the Node in advance to request for providing the IN-CSE with the Traffic Patterns.

Step-3: Select the server NSE of the Underlying Network to request configuration of the Traffic Pattern

For the configuration of the Traffic Pattern for a specific field domain node în the Underlying Network, the IN-CSE selects the NSE by using the identifier of the Field Domain Node (i.e. the M2M-Ext-ID) by which the Node can be identified in the NSE.

Note: The correct server NSE can be found by following of a chain of links of multiple resources in the IN-CSE, e.g. the nodeLink in the AEAnnc resource of a target AE of field domain node linking to the nodeAnnc resource having the hostedCSELink linking to the remoteCSE resource having  the M2M-Ext-ID linking to the UNetwork-ID of the server NSE. (See sections 7.1.8 and 7.1.9)

Step-4: Request for configuration of the Traffic Pattern in the Underlying Network

For each field domain node received in the AE request the IN-CSE sends a request to provide Traffic Patterns (i.e. a  set of TP parameters) for the field domain node to the NSE, using the appropriate Mcn protocol. The request includes an identifier of the filed domain node and one or more TP parameter set(s) as defined at section 8.3.2.

Note 1: oneM2M Traffic pattern parameters,  as in Table 8.3.2-1, may need to be translated into the corresponding Traffic pattern parameters that are supported by the Mcn reference point of the Underlying network

Note 2: For an example in 3GPP see section 8.3.5.

Step-5: Response for the configuration of the TP parameter sets

The IN-CSE receives the response for the configuration of the TP parameter sets from the NSE. The response includes the result of the request.

Note: For an example in 3GPP see section 8.3.5.

Step-6: Forward Response to requesting AE

The IN-CSE may inform the requesting AE if the TP parameter sets were accepted in the Underlying Network or not. In particular the IN-CSE may provide information to the AE if some provided TP parameters could not be transmitted via the Mcn interface (e.g. because the Underlying Network does not support them).

#### 8.3.4  New resource types and attributes

This section provides information of new resource types and new attributes including relationship with existing resource types and attributes.

Proposed new resources are as below.

- Resource Type <trafficCharacteristics>

  - Note: It is child resource of existing Resource Type <AE> or <node>.

- Resource Type <trafficPattern>

  - Note: It is child resource of new Resource Type <trafficCharacteristics>.

Detailed information of new resource types are described in subclauses below.

8.3.4.1 Resource Type <trafficCharacteristics>

The <trafficCharacteristics> resource represents the characteristic information (e.g. communication pattern, mobility pattern, etc..) of a field domain node. These information may be detected or scheduled by an application level processing. This resource type is used to share information with other entities such as the underlying network entity (server NSE) of the field domain node which may optimize the processing of the underlying network for the specific field domain node.

Figure 8.3.4.1-1: Structure of <trafficCharacteristics> resource

The <trafficCharacteristics> resource shall contain the child resources specified in table 8.3.4.1-1.

Table 8.3.4.1-1: Child resources of <trafficCharacteristics> resource

| Child Resources of <trafficCharacteristics> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <subscription> | 0..n |  |
| [variable] | <trafficPattern> | 0..n | See clause 8.3.4.2. A source AE can create multiple number of <trafficPattern> resources for a single target AE of field domain node. In this case the source AE assures that different communication patterns are not overlapped in a point of time. |

The <trafficCharacteristics> resource shall contain the attributes specified in table 8.3.4.1-2.

Table 8.3.4.1-2: Attributes of <trafficCharacteristics> resource

| Attributes of <deviceCharacteristics> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO |  |
| resourceID | 1 | RO |  |
| resourceName | 1 | WO |  |
| parentID | 1 | RO |  |
| creationTime | 1 | RO |  |
| lastModifiedTime | 1 | RO |  |
| expirationTime | 1 | RW |  |
| accessControlPolicyIDs | 0..1 (L) | RW |  |
| Labels | 0..1 (L) | RW |  |
| creator | 1 | WO | The AE-ID of the entity which created the resource. |

8.3.4.2 Resource Type <trafficPattern>

The <trafficPattern> resource represents the communication pattern and the mobility pattern of a field domain node to be shared with other entities such as the underlying network entity (server NSE) of the field domain node which may optimize the processing of the underlying network for the specific field domain node by using this information.

Figure 8.3.4.2-1: Structure of <trafficPattern> resource

The <trafficPattern> resource shall contain the child resources specified in table 8.3.4.2-1.

Table 8.3.4.2-1: Child resources of <trafficPattern> resource

| Child Resources of <trafficPattern> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <subscription> | 0..n |  |
| [variable] | <schedule> | 0..1 | It provides the mask for the day of week, the starting time and end time for communication. If it is not provided this shall be interpreted as ‘anytime’ at the server NSE. |

The <trafficPattern> resource shall contain the attributes specified in table 8.3.4.2-2.

Table 8.3.4.2-2: Attributes of <trafficPattern> resource

| Attributes of <trafficPattern> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO |  |
| resourceID | 1 | RO |  |
| resourceName | 1 | WO |  |
| parentID | 1 | RO |  |
| creationTime | 1 | RO |  |
| lastModifiedTime | 1 | RO |  |
| expirationTime | 1 | RW |  |
| accessControlPolicyIDs | 0..1 (L) | RW |  |
| Labels | 0..1 (L) | RW |  |
| periodicIndicator | 0..1 | RW | It indicates as ‘Periodical’ or ‘On demand’. |
| periodicDurationTime | 0..1 | RW | It provides the time in seconds of the duration of the periodic communication. |
| periodicIntervalTime | 0..1 | RW | It provides the time in seconds of the interval for periodic communication. |
| stationaryIndication | 0..1 | RW | It indicates as ‘Stationary (Stopping)’ or ‘Mobile (Moving)’. |
| dataSizeIndicator | 0..1 | RW | It indicates the expected data size for the pattern |
| validityTime | 0..1 | RW | It contains the point of time when the informed <trafficPattern> information to the server NSE becoming invalid and shall be deleted at the server NSE. |

#### 8.3.5	3GPP Release-13 MTC feature for Configuration of Device Communication Patterns

oneM2M uses the 3GPP Release-13 MTC feature for Configuration of Device Communication Patterns to  configure Node Traffic Patterns in the Underlying Network (see section 8.3  Configuration of Node Traffic Patterns). 
To that purpose the IN-CSE translates the oneM2M Node Traffic Pattern (TP) into a 3GPP Device Communication Pattern.

A signalling sequence for provisioning of CP parameters is described in the sub-clause 5.10.2 of 3GPP TS 23.682 [i.5]. Following figure 8.3.5-1 provides the signalling sequence derived from the 3GPP specification with oneM2M terminologies mapping.

Figure 8.3.5-1:  Signalling sequence for provisioning of CP Parameters

3GPP TS 23.682 [i.5] defines the request message of step 3 as below.

The SCEF sends Update CP Parameter Request (External Identifier or MSISDN, SCEF Reference ID(s), SCEF Address, CP parameter set(s), validity time(s), SCEF Reference ID(s) for Deletion) messages to the HSS for delivering the selected CP parameter set(s) per UE. There may be multiple CP parameter sets included in this message where each CP parameter set for addition or modification has been determined to be non-overlapping with other CP parameter sets either included in the message or already provisioned for a given UE. The SCEF derives the SCEF Reference (IDs) for CP parameter sets to be sent to the HSS based on the SCS/AS Reference ID(s) from the SCS/AS.

NOTE 3:	A request for deletion of a CP parameter set from the SCS/AS may result in a request for modification of the non-overlapping CP parameter set by the SCEF.

Example: In the  case that the selected server NSE is a 3GPP HSS, the protocol of the S6t reference point defined by 3GPP is used for the request. The S6t uses one of Diameter Application protocols defined by 3GPP. The request on the S6t reference point for the configuration of the CP parameter sets (a CIR command) must include a User-Identifier AVP (either an External Identifeir or a MSISDN of the UE), may include one or more AESE-Communication-Pattern AVP. An AESE-Communication-Pattern AVP must include a SCEF-ID AVP (represent the ID of the IN-CSE or M2M-SP-ID), may include a SCEF-Reference-ID AVP (assigned by the IN-CSE or M2M-SP to identify the configuration of CP parameter sets uniquely) , may include one or more Communication-Pattern-Set AVP. A Communication-Pattern-Set AVP may include AVPs for Periodic-Communication-Indicator, Communication-Duration-Time, Periodic-Time, one or more Scheduled-Communication-Time, Stationary-Indication, and Validity-Time.

3GPP TS 23.682 [i.5] defines the response message of step 5 as below.

The HSS sends Update CP Parameter Response (SCEF Reference ID, Cause) message to the SCEF. The cause value indicates successful subscription update or the reason of failed subscription update.

Example); In the  case that  the selected server NSE is a 3GPP HSS, the protocol of the S6t reference point defined by 3GPP is used for the response. The response on the S6t reference point for the configuration of the CP parameter sets (a CIA command) must include either Result-Code AVP or Experimental-Result AVP, may include a User-Identifier AVP if successful case, may include one or more AESE-Communication-Pattern-Config-Status AVP. An AESE-Communication-Pattern-Config-Status AVP must include the SCEF-Reference-ID AVP (same value in the request), may include the SCEF-ID (same value in the request) and an AESE-Error-Report AVP. Refer to the 3GPP TS29.336 for the detailed protocol description.

The actual parameters for the request and response messages in above steps 3 and 5 are defined by 3GPP TS 29.336 [i.10] section 7 and 8 for S6t reference point.

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

# 1	Scope

The present document is a study of interworking between oneM2M Architecture and 3GPP Rel-13 architecture for Service Capability Exposure as defined in the release 13 version of TS 23.682. The key objective and value is analyzed and described. The document also investigates the potential solution in oneM2M by evaluating the existing technical solutions.

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3-------------------------------------------

## 5.3	3GPP architecture for Service Capability Exposure

The 3GPP architecture for the Service Capability Exposure Function (SCEF) is defined in 3GPP TS 23.682 [i.5]. The specification includes two different architectures. One is for the “MTC Device triggering” feature and was specified in 3GPP release 11. The other one is for 3GPP Service exposure with 3rd party service providers features newly provided in Release 13 which is the focus of the present document. Refer to the following figure 5.3-1, taken from the release 13 version of 3GPP TS 23.682 [i.5].

### -----------------------End of change 3---------------------------------------------

### -----------------------Start of Changes to References Section -------------

## 2.2	Informative references

Clause 2.2 shall only contain informative references which are cited in the document itself.

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

[i.1]	oneM2M Drafting Rules  (http://member.onem2m.org/Static_pages/Others/Rules_Pages/oneM2M-Drafting-Rules-V1_0.doc)

[i.2]	oneM2M TS-0002: " Requirements".

[i.3]	3GPP TS 22.101 Service aspects; Service principles (Release 13).

[i.4]	3GPP TS 22.115 Service aspects; Charging and billing (Release 13).

[i.5]	3GPP TS 23.682 Architecture enhancements to facilitate communications with packet data networks and applications (Release 13).

[i.6]	OMA API Inventory (http://technical.openmobilealliance.org/Technical/technical-information/oma-api-program)

[i.7]	OMA Service Exposure Framework (http://member.openmobilealliance.org/ftp/Public_documents/ARCH/ServiceExposure)

[i.8]	OMA Exposing Network Capabilities to M2M (http://member.openmobilealliance.org/ftp/Public_documents/ARCH/ENCap-M2M)

[i.9]	oneM2M TS-0001: " Functional Architecture ".

[i.10]	3GPP TS 29.336: Home Subscriber Server (HSS) diameter interfaces for interworking with packet data networks and applications (Release 13)

### -----------------------End of Changes to References  -------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?

# Text boxes

Infrastructure Domain

Field Domain

1b. An IN-AE provides information on Traffic Patterns of a field domain Node to  the IN-CSE

- Request for providing 
TP parameter set

- Response

3. Select the server NSE to request for the configuration of the TP parameter sets

Mca

Mcn

IN-CSE

Mcc

NSE

ASN/MN-CSE

IN-AE

1a. An ASN-AE provides information on the Traffic Patterns of an AE and/or Node of the field domain Node, announced to IN-CSE

ASN-AE

Mca

- Response