| CHANGE REQUEST |
| --- |
| Meeting:* | ARC#22 |
| Source:* | ZTE |
| Date:* | 2016-03-04 |
| Contact:* | Wu Hao, ZTE, wu.hao18@zte.com.cn Weixiang Shao, ZTE Corporation, shao.weixiang@zte.com.cn Yingjie Hong, ZTE, hong.yingjie@zte.com.cn |
| Reason for Change/s:* | Add description for section 8 |
| CR against: Release* | Rel-0.2 |
| CR against: WI* | Active / WI-0037 MNT Maintenance / < Work Item number (optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | oneM2M-TR-0024-v0.2.0 |
| Clauses/Sub Clauses* | 8 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The CR Proposes to add description for section 8.

### -----------------------Start of change 1-------------------------------------------

#### 8.3.x2	Support for Monitoring procedure

Figure 8.3.x2-1 shows a generic procedure to support monitoring service between oneM2M and 3GPP network.

Figure 8.3.x2-1: General monitoring procedure between oneM2M and 3GPP network

Step-1: Request for monitoring

The AE sends the Request message for monitoring to the IN-CSE with related monitoring parameters.

Step-2: IN-CSE handling

The IN-CSE stores or updates monitoring parameters, and assigns an IN-CSE Reference ID. Based on operator policies, if either the AE is not authorized to perform this request or the Request is malformed or the AE has exceeded its quota or rate of submitting monitoring requests, the IN-CSE performs Step 5 and provides a Cause value appropriately indicating the error. If the IN-CSE received a Deletion request, the IN-CSE derives the related IN-CSE Reference ID for Deletion for Step 3.

Step-3: Monitoring Request

The IN-CSE sends Monitoring Request message to request NSE to configure or delete the given Monitoring Event on the NSE.

Step-4: Monitoring Response.

The NSE sends a Monitoring Response message to the IN-CSE to acknowledge acceptance of the Monitoring Request and the deletion of the identified monitoring event configuration, if it was requested.

Step-5: Response for monitoring.

The IN-CSE sends Monitoring Response message to the AE to acknowledge acceptance of the Monitoring Request or the deletion of the identified monitoring event configuration, if it was requested.

Step-6: Monitoring Event Detecting.

A Monitoring Event is detected by the NSE.

Step-7: Monitoring Indication.

The NSE sends a Monitoring Indication message to the IN-CSE. If the Monitoring Event is configured as a One-time Monitoring, then the Monitoring Event configuration is deleted by the NSE upon completion of this step. If the NSE has a Maximum Number of Reports stored for this monitoring task, the NSE shall decrease its value by one.

Step-8: Notification.

If related resource is subscribed, the IN-CSE sends notification to the AE.

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?