| CHANGE REQUEST |
| --- |
| Meeting:* | ARC#22 |
| Source:* | Joerg Swetina, NEC, Joerg.swetina@neclab.eu |
| Date:* | 2016-03-14 |
| Contact:* | Joerg Swetina, NEC, Joerg.swetina@neclab.eu |
| Reason for Change/s:* | Generic Interworking will make use of two specializations of the <flexContainer> resource type. |
| CR against: Release* | 2 |
| CR against: WI* | Active WI-0025 – Generic Interworking MNT maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0001 V2.6.0 |
| Clauses/Sub Clauses* | 9.6.1.2.2, |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

<Provide an introduction containing the problem(s) being solved, and a summary list of proposals.  Discuss any risk of breaking backwards compatibility with last published version of the impacted TS.>

### -----------------------Start of change 1-------------------------------------------

##### 9.6.1.2.2	Specializations of <flexContainer>

Editor’s note: Standardized specializations of <flexContainer> resources shall be listed in this section, e.g. those required for standardized interworking procedures.

9.6.1.2.2.x	Specializations of <flexContainer> for Generic Interworking

Generic Interworking (specified in TS-0012 [6]) provides interworking with many types of non- oneM2M Area Networks and their devices. It supports the interworking variant “ full mapping of the semantic of the non-oneM2M data model to Mca” as indicated in Annex F.2. 
For Generic Interworking the non-oneM2M data model of the non- oneM2M Area Network needs to be described in the form of a oneM2M compliant ontology which is derived from the oneM2M Base Ontology (specified in TS-0012 [6]) and that may be available in a formal description language (e.g. OWL).

Note 1: While in general the semantic information contained in the ontology can be made available (in semanticDescriptor child-resources of the utilized resources) the mechanisms used for Generic Interworking as described in [6] for data exchange with an AE do not rely on the existence of semanticDescriptors. This allows e.g. very simple devices to exchange their data in “raw” form (e.g. as byte-fields that need to be interpreted by the communicating entity as integer numbers or text strings).

Note 2: Generic Interworking is aiming at a maximum of flexibility regarding the types of interworked Area Networks / Devices (e.g. RESTful or RPC based) while at the same time requiring a minimum of specialized resource types. Generic Interworking can make use of <container> / <contentInstance> resource types and/or <flexContainer> resource types for communication with the Generic Interworking IPE.

Table 9.6.1.2.2.x-1 lists specializations of the <flexContainer> resource type for Generic Interworking in which the containerDefinition attribute provides further definition of the resource.

Table 9.6.1.2.2.x-1 <flexContainer> Specializations for Generic Interworking

| Resource specialization | Short Description | Child Resource Types | Parent Resource Types | Clause |
| --- | --- | --- | --- | --- |
| genericInterworkingService | This resource type is used to link to a set of input- and outputDataPoints of the service and to provide the parent resource for operationInstance resourcesof the service | genericInterworkingService, genericInterworkingOperationInstance, semanticDescriptor, subscription | AE, container, flexContainer, genericInterworkingService, | 9 in [6] |
| genericInterworkingOperationInstance | This resource type is used to link to a set of input- and outputDataPoints and a set of operationInputs and operationOutputs of the operationInstance | semanticDescriptor, subscription | genericInterworkingService, | 9 in [6] |

### -----------------------End of change 1---------------------------------------------