| CHANGE REQUEST |
| --- |
| Meeting:* | ARC#22 |
| Source:* | LG Electronics |
| Date:* | 2016-03-17 |
| Contact:* | SeungMyeong JEONG, seungmyeong.jeong@lge.com |
| Reason for Change/s:* |  |
| CR against: Release* | Rel-2 |
| CR against: WI* | Active WI-0018 oneM2M and AllJoyn Interworking MNT maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0021 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR modifies editorial error (reference, numbering…) and update the <locationPolicy> resource type XSD as the latest version.

### -----------------------Start of change 1-------------------------------------------

# Annex A (Informative) oneM2M and AllJoyn technical comparison

## A.1	API styles

The table A.1-1 describes how API styles of oneM2M and AllJoyn system are different to expose its services that can provide some functionalities.

Table A.1-1	The Comparison of API Styles of oneM2M and AllJoyn System

|  | oneM2M | AllJoyn |
| --- | --- | --- |
| API Style | Resource based API (RESTful Architecture). It assigns all procedures, instances of data a resource identified by a URI and leverage web-based protocol’s operations (CRUD) to define service behaviors. | D-Bus [i.4] based API. It defines a protocol for exposing a typical object-oriented language-based service to other applications that consume the service. |
| Representation of a Service | An oneM2M Service is defined by one or more resources specified in [1]. An oneM2M resource defines a set of representations of data. Each resource has attributes that stores information regarding the resource itself, procedures or data. | An AllJoyn Service is defined by one or more AllJoyn Interfaces. An AllJoyn interface can include one or more of following types of members: Methods: a function call that typically takes a set of inputs, performs and returns. Properties: a variable that holds values. Signals: an asynchronous notification that is generated by a service to notify remote peers of an event or change. |

Following, the table A.1-2 and A.1-3 give examples how an oneM2M and AllJoyn service is described respectively. Both examples demonstrate a schema or introspection that describes location service to acquire the location information of a target information.

Table A. 1-2	Resource Schema of <locationPolicy> (v2.4.0)

<xs:schema xmlns="http://www.w3.org/2001/XMLSchema" targetNamespace="http://www.onem2m.org/xml/protocols" xmlns:m2m="http://www.onem2m.org/xml/protocols" xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance" elementFormDefault="unqualified" xmlns:xs="http://www.w3.org/2001/XMLSchema"> <xs:include schemaLocation="CDT-commonTypes-v2_4_0.xsd" /> <xs:include schemaLocation="CDT-subscription-v2_4_0.xsd" /> <xs:element name="locationPolicy"> <xs:complexType> <xs:complexContent> <!-- Inherit common attributes for announceable Resources --> <xs:extension base="m2m:announceableResource"> <xs:sequence> <!-- Resource Specific Attributes --> <xs:element name="locationSource" type="m2m:locationSource" /> <xs:element name="locationUpdatePeriod" type="m2m:listOfDuration" minOccurs="0" /> <xs:element name="locationTargetID" type="m2m:nodeID" minOccurs="0" /> <xs:element name="locationServer" type="xs:anyURI" minOccurs="0" /> <xs:element name="locationContainerID" type="xs:anyURI" minOccurs="0" /> <xs:element name="locationContainerName" type="xs:string" minOccurs="0" /> <xs:element name="locationStatus" type="xs:string" /> <!-- Child Resources --> <xs:choice minOccurs="0" maxOccurs="1"> <xs:element name="childResource" type="m2m:childResourceRef" minOccurs="1" maxOccurs="unbounded" /> <xs:choice minOccurs="1" maxOccurs="unbounded"> <xs:element ref="m2m:subscription"></xs:element> </xs:choice> </xs:choice> </xs:sequence> </xs:extension> </xs:complexContent> </xs:complexType> </xs:element> <xs:element name="locationPolicyAnnc"> <xs:complexType> <xs:complexContent> <!-- Inherit common attributes for announced Resources --> <xs:extension base="m2m:announcedResource"> <xs:sequence> <!-- Resource Specific Attributes --> <xs:element name="locationSource" type="m2m:locationSource" minOccurs="0" /> <xs:element name="locationUpdatePeriod" type="m2m:listOfDuration" minOccurs="0" /> <xs:element name="locationTargetID" type="m2m:nodeID" minOccurs="0" /> <xs:element name="locationServer" type="xs:anyURI" minOccurs="0" /> <xs:element name="locationContainerID" type="xs:anyURI" minOccurs="0" /> <xs:element name="locationContainerName" type="xs:string" minOccurs="0" /> <xs:element name="locationStatus" type="xs:string" minOccurs="0" /> <!-- No Child Resources --> </xs:sequence> </xs:extension> </xs:complexContent> </xs:complexType> </xs:element> </xs:schema>

Furthermore, the resource schema described in table above can be also graphically represented as the figure below.

Figure A.1-1	Structure of <locationPolicy> resource

Table A.1-3	Introspection XML of an AllJoyn Location Service (example)

<node name="/com/alljoyn/LocationService"> <interface name="com.alljoyn.LocationService"> <method name="getLocation"> <arg name="locationSource" type="s" direction="in"> </arg> <arg name="targetID" type="s" direction="in"> </arg> </method> <signal name="locationPoint" sessionless="true> </signal> <property name="locationStatus" type="y" access="read"> </property> </interface> </node>

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?