| CHANGE REQUEST |
| --- |
| Meeting:* | ARC#22 |
| Source:* | InterDigital |
| Date:* | 2016-03-16 |
| Contact:* | Dale Seed (dale.seed@InterDigital.com ) |
| Reason for Change/s:* | Introducing functionality to enable re-targeting different NOTIFY requests with different notificationURIs to the same AE. |
| CR against: Release* | Release-3 |
| CR against: WI* | Active WI MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0001-V2.6.0 |
| Clauses/Sub Clauses* | 9.6.6, 9.6.27, 9.6.2.3, 10.2.22.1 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

For the case, where an AE needs to create multiple subscriptions, there is a limitation currently in oneM2M where the AE must configure the notification URI with the same Resource-ID (i.e. the Resource-ID of its <AE> resource) in order to allow its registrar CSE to properly send it notifications.

This is problematic since an AE would prefer to receive notifications from different subscriptions via different URIs such that it can differentiate the notifications based on the targeted URI of the received notification rather than having to parse each notification to inspect the subscriptionReference element in the notification payload.

Proposed Solution:

Enhance the <AE> resource with an optional retargetPaths attribute.  The attribute consists of a list of paths relative to an AE.  The retargetPaths attribute is used by a Hosting CSE to determine whether or not a request shall be re-targeted to an AE.

For example, a retargetPaths attribute is configured with sensors/temp, sensors/pressure and sensors/humidity.

A CSE receives a request having a To parameter consisting of an identifier of the <AE> resource (e.g. AE01) concatenated with a relative path (e.g. sensors/temp) which matches a path configured in the retargetPaths attribute.

As a result, the registrar CSE re-targets the request to the AE’s pointOfAccess concatenated with the relative path defined in the original request and that matches a path configured in this attribute (i.e. sensors/temp). For example,   https://172.25.30.25:7000/sensors/temp.

This allows an AE with the ability to receive requests having different target URIs from a CSE (e.g. notifications from different subscriptions that target the same AE).

### -----------------------Start of change 1-------------------------------------------

### 9.6.5 Resource Type AE

An <AE> resource shall represent information about an Application Entity registered to a CSE.

Figure 9.6.5-1: Structure of <AE> resource

The <AE> resource shall contain the attributes specified in table 9.6.5-2.

Table 9.6.5-2: Attributes of <AE> resource

| Attributes of <AE> | Multiplicity | RW/ RO/ WO | Description | <AEAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3. | NA |
| resourceID | 1 | RO | See clause 9.6.1.3. Contains the AE-ID-Stem of the AE (see clause 7.2 on identifier formats and clause 10.1.1.2.2 for AE registration procedure). | NA |
| resourceName | 1 | WO | See clause 9.6.1.3. | NA |
| parentID | 1 | RO | See clause 9.6.1.3. | NA |
| expirationTime | 1 | RW | See clause 9.6.1.3. | MA |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3. | MA |
| creationTime | 1 | RO | See clause 9.6.1.3. | NA |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3. | NA |
| labels | 0..1 (L) | RW | See clause 9.6.1.3. | MA |
| announceTo | 0..1 (L) | RW | See clause 9.6.1.3. | NA |
| announcedAttribute | 0..1 (L) | RW | See clause 9.6.1.3. | NA |
| dynamicAuthorizationConsultationIDs | 0..1 (L) | RW | See clause 9.6.1.3. | OA |
| appName | 0..1 | RW | The name of the application, as declared by the application developer(e.g. "HeatingMonitoring"). Several sibling resources may share the appName. | OA |
| App-ID | 1 | WO | The identifier of the Application (see clause 7.1.2). | OA |
| AE-ID | 1 | RO | The identifier of the Application Entity (see clause 7.1.2). | OA |
| pointOfAccess | 0..1 (L) | RW | The list of addresses for communicating with the registered Application Entity over Mca reference point via the transport services provided by Underlying Network (e.g. IP address, FQDN, URI). This attribute shall be accessible only by the AE and the Hosting CSE. If this information is not provided and the <pollingChannel> resource does exist, the AE should use <pollingChannel> resource. Then the Hosting CSE can forward a request to the AE without using the PoA. | OA |
| ontologyRef | 0..1 | RW | A URI of the ontology used to represent the information that is managed and understood by the AE. | OA |
| requestReachability | 1 | RW | If the AE that created this <AE> resource can receive a request, this attribute is set to "TRUE" otherwise "FALSE" | OA |
| nodeLink | 0..1 | RW | The resourceID of a <node> resource that stores the node specific information where this AE resides. | OA |
| contentSerialization | 0..1 (L) | RW | The list of supported serializations of the Content primitive parameter for receiving a request from its registrar CSE. (e.g. XML, JSON). The list shall be ordered so that the most preferred format comes first. | OA |
| e2ESecurityCapabilities | 0..1 | RW | See clause 9.6.1.3. | MA |
| retargetPaths | 0..1 (L) | RW | A list of tuples. Each tuple consists of a path element and an accessControlPolicyID element. The path element shall be configured with an AE relative path (e.g. sensors/temp). The accessControlPolicyID element shall be configured with an identifier of an <accessControlPolicy> resource. See clause 10.2.XX. |  |

### -----------------------End of change 1-------------------------------------------

### -----------------------Start of change 2-------------------------------------------

### 10.2.XX 	Procedure for Re-Targeting Requests to AE

For the case when a retargetPaths attribute of an <AE> resource is configured, its Registrar CSE shall enable AE re-targeting functionality for the AE.

When a Registrar CSE receives a request having a To parameter consisting of an identifier of the <AE> resource (e.g. AE01) concatenated with a relative path (e.g. sensors/temp) and that matches a path configured in the retargetPaths attribute, the Registrar CSE shall attempt to re-target the request to the AE. Before re-targeting, the Registrar shall first verify that the Originator of the request has the proper privileges to perform the request.  This verification shall be done by checking the <accessControlPolicy> resource referenced by the corresponding accessControlPolicyID specified in the matching the retargetPaths tuple, to verify that the Originator has the proper privileges (e.g. NOTIFY) to allow the Registrar to re-target the request to the AE.

When re-targeting a request to an AE, the Registrar CSE shall re-target the request to the AE’s pointOfAccess concatenated with the relative path defined in the original request and that matches a path configured in retargetPaths attribute (e.g. sensors/temp).  For example, https://172.25.30.25:7000/sensors/temp.

When re-targeting a request to an AE, the Registrar CSE shall include the following request parameter rules.  All other oneM2M request parameters shall not be present in a re-targeted request to an AE.

- To – The AE’s pointOfAccess concatenated with the AE’s relative path from the original request and matching the retargetPaths attribute

- From – The ID of the request Originator

- Operation - the operation used for re-targeting matches the operation in the original request

- Request Identifier – Identifier generated by Registrar CSE

- Content - The content included in the original request

- Resource Type (Create Only) – Resource Type of the original request

When a response to a re-targeted request is returned by an AE, the following oneM2M response parameters shall be included.

- Response Status Code – Configured by the AE based on the status of processing the re-targeted request

- Request Identifier – Matching the Request Identifier in the re-targeted request

- Content (when applicable to operation)

### -----------------------End of change 2-------------------------------------------