| CHANGE REQUEST |
| --- |
| Meeting:* | ARC 23 |
| Source:* | ZTE |
| Date:* | 2016-05-06 |
| Contact:* | Wu Hao, ZTE, wu.hao18@zte.com.cn Weixiang Shao, ZTE Corporation, shao.weixiang@zte.com.cn Yingjie Hong, ZTE, hong.yingjie@zte.com.cn |
| Reason for Change/s:* | Provide context for network issue report features for 3GPP Rel-13 IWK. |
| CR against: Release* | oneM2M R2 |
| CR against: WI* | Active WI-0037 MNT maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0024 v0.3.0 |
| Clauses/Sub Clauses* | New clause 8.x |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR proposes to add new section 8.3 of TR-0024 3GPP Rel13 IWK (WI-0037) for the Network issue report feature.

### -----------------------Start of change 1-------------------------------------------

### 8.x  Support for Network status report

### 8.x.1 Description

The IN-CSE needs to know the NSE available in the operator network,for example, Congestion level or an indication of the "no congestion" state for NSE.

An IN-CSE may request for being notified about the network status. The following methods are supported:

-	The IN-CSE requests to be informed, one-time, about the network status by providing a geographical area. This procedure is referred to as one-time network status request;

-	The IN-CSE requests to be informed, continuously, about the network status by providing a geographical area. This procedure is referred to as continuous network status request.

### 8.x.2	3GPP Release-13 MTC procedure

8.x.2.1	Request procedure for one-time or continuous reporting of network status

This procedure is used by an SCS/AS to retrieve Network Status Indication from the network. This procedure can be used to request a one-time or continuous reporting of network status. Figure 8.x.2.1-1 illustrates the procedure.

Figure 8.x.2.1-1: Request procedure for one-time or continuous reporting of network status

NOTE 1:	Step 1 and 6 are outside of 3GPP scope, but are shown for informative purposes only.

1.	When the SCS/AS needs to retrieve NSI, the SCS/AS sends a Network Status Request (Geographical area, SCS/AS Identifier, SCS/AS Reference ID, Duration, Threshold) message to the SCEF. Duration indicates the time for which a continuous reporting is requested. The absence of Duration indicates a one-time reporting. Threshold indicates a range at which the SCS/AS wishes to be informed of the network status. Multiple Threshold values may be included.

NOTE 2:	Geographical area specified by SCS/AS could be at cell level (CGI/ECGI), TA/RA level or other formats e.g. shapes (e.g. polygons, circles etc.) or civic addresses (e.g. streets, districts etc.) as referenced by OMA Presence API.

2.	The SCEF authorizes the SCS/AS request for notifications about potential network issues. The SCEF stores SCS/AS Address, SCS/AS Reference ID, Duration, if present and Threshold if present. The SCEF assigns an SCEF Reference ID.

NOTE 3:	Based on operator policies, if either the SCS/AS is not authorized to perform this request (e.g. if the SLA does not allow for it) or the SCS/AS has exceeded its quota or rate of submitting requests, the SCEF sends a Network Status Response (Cause) message with a Cause value appropriately indicating the error.

3.	The SCEF assigns an SCEF Reference ID and identifies, based on local configuration, the RCAF(s) responsible for the provided Geographical Area. For every identified RCAF, the SCEF derives a Location Area from the Geographical Area provided by the SCS/AS. The Location Area is according to operator configuration either a 3GPP location area (e.g. list of TA/RAs, list of cell(s), list of eNodeBs etc) or a sub-area of the Geographical Area provided by the SCS/AS. The SCEF sends an Aggregated Congestion Request (SCEF Reference ID, Location Area, Duration, Threshold) message to the identified RCAF(s). Duration indicates the time for which a continuous reporting is requested. The absence of Duration indicates a one-time reporting. The SCEF, based on operator policies, may chose a different Threshold value than the one indicated by the SCS/AS in step 1.

4.	The RCAF examines the Aggregated Congestion Request message. If the SCEF provided a Duration, the RCAF stores the SCEF instructions and starts to monitor the set of cells or eNodeBs belonging to the Location Area for a change in the congestion status that is crossing a Threshold (if provided by the SCEF). The RCAF sends an Aggregated Congestion Report to the SCEF including the SCEF Reference ID and, depending on the operator configuration and current RCAF knowledge, the congestion status for every cell or eNodeB belonging to the Location Area requested by the SCEF.

5.	The SCEF verifies whether the Network Status Request identified via the SCEF Reference ID is valid and active and stores the report. After receiving reports from all the involved RCAF(s) to which step 3 was executed, the SCEF derives the NSI for the requested Geographical Area by combining all reports with the same SCEF Reference ID in an operator configurable way (governed by SLAs, network topology, usage etc).

NOTE 4:	Either exact values for congestion status, as reported by RCAF(s) to SCEF or abstracted values e.g. (High, Medium, Low) can be reported by the SCEF to the SCS/AS. The calculation and the reporting of the NSI to the SCS/AS depends on operator configuration (SLAs, network topology, usage etc), and is outside the scope of this specification.

6.	The SCEF send a Network Status Report (SCS/AS Reference ID, NSI) message to the SCS/AS.

8.x.2.2 	Report procedure for continuous reporting of network status

This procedure is used by the SCEF to report a change of Network Status Information (NSI) to the SCS/AS which requested a continuous reporting of network status. Figure 8.x.2.2-1 illustrates the procedure.

Figure 8.x.2.2-1: Report procedure for continuous reporting of network status

NOTE 1:	Step 4 and 5 are outside of 3GPP scope, but are shown for informative purposes only.

1.	The RCAF detects a change in the congestion status that is crossing a Threshold (if provided by the SCEF) for the set of cells or eNodeBs belonging to the Location Area requested by the SCEF. An Aggregated Congestion Report message is sent to this SCEF including the SCEF reference ID and, depending on the operator configuration, the congestion status for every cell or eNodeB belonging to the Location Area requested by the SCEF.

2.	The SCEF acknowledges the report to the RCAF.

NOTE  2:	Step 1 and 2 can happen multiple times and the Aggregated Congestion Report message can be sent by any of the involved RCAFs.

3.	Whenever a new Aggregated Congestion Report message arrives, the SCEF stores the report and derives a new NSI for the requested geographical area by combining this report with all other reports having the same SCEF reference ID in an operator configurable way (governed by SLAs, network topology, usage etc.).

NOTE 3:	Either exact values for congestion status, as reported by RCAF(s) to SCEF or abstracted values e.g. (High, Medium, Low) can be reported by the SCEF to the SCS/AS. The calculation and the reporting of the NSI to the SCS/AS depends on operator configuration (SLAs, network topology, usage etc), and is outside the scope of this specification.

4.	Triggered by a NSI change (derived in step 3) that is crossing a Threshold (if provided by the SCS/AS), the SCEF sends a Network Status Report (SCS/AS Reference ID, NSI) message to the SCS/AS.

5.	The SCS/AS acknowledges the report to the SCEF.

8.x.2.3 	Removal procedure for continuous reporting of network status

This procedure is used for termination of the continuous reporting of network status. It can be triggered by the SCS/AS at any time before the Duration is over or if no Duration was provided. The SCEF will trigger this procedure when the Duration is over. Figure 8.x.2.3-1 illustrates the procedure.

Figure 8.x.2.3-1: Removal procedure for continuous reporting of network status

NOTE 1:	Step 1b and 3b are outside of 3GPP scope, but are shown for informative purposes only.

1a.	The SCEF detects that the requested Duration for an ongoing continuous reporting of network status to an SCS/AS is over and indentifies the corresponding SCEF Reference ID.

1b.	When the SCS/AS needs to terminate an ongoing continuous reporting of network status, the SCS/AS sends a Cancel Network Status Request (SCS/AS Identifier, SCS/AS Reference ID) message to the SCEF.

2b.	The SCEF authorizes the SCS/AS request and indentifies the corresponding SCEF Reference ID.

3b.	If the SCS/AS requested to terminate an ongoing continuous reporting of network status in step 1b, the SCEF sends a Cancel Network Status Response (SCS/AS Reference ID) message to the SCS/AS.

4.	The SCEF identifies the RCAF(s) involved in the continuous reporting represented by the SCEF Reference ID. The SCEF sends a Cancel Aggregated Congestion Request (SCEF Reference ID) message to the identified RCAF(s).

5.	The RCAF removes the related SCEF instructions and stops monitoring the set of cells or eNodeBs belonging to the Location Area for a change in the congestion status. Afterwards, a Cancel Aggregated Congestion Response is sent to the SCEF including the SCEF Reference ID.

6.	The SCEF removes all state information related to this continuous reporting represented by the SCEF Reference ID.

### 8.x.3 3GPP Parameters

A set of Network issue report parameters can be associated with a newwork stauts request, as defined in the tables below.

Table 8.x.3-1: Network issue report parameters

| Parameter | Description |
| --- | --- |
| Reference ID | A reference ID that is passed from the requester to SCEF and to the NSE in each request. The reference ID will be included in each response to associate it with the original request. |
| Location Area | Location Area is according to operator configuration either a 3GPP location area or a sub-area of the Geographical Area provided by the SCS/AS. |
| Threshold | Threshold indicates a range at which the SCS/AS wishes to be informed of the network status. Multiple Threshold values may be included. |
| Duration | Duration indicates the time for which a continuous reporting is requested. The absence of Duration indicates a one-time reporting. |
| Network status information | Congestion level or an indication of the "no congestion" state for NSE. |

### 8.x.4 Solution(s)

#### 8.x.4.1 Solution1

##### 8.x.4.1.1 Proposed resource types and attributes

Proposed new resources are as below.

- Resource Type <networkStatus>

  - Note: It is child resource of existing Resource Types <CSEBase>.

Detailed information of new resource types are described in subclauses below.

#### 8.x.4.1.1 Resource Type <networkStatus>

The <networkStatus> resource represents the characteristics of a request for network issue report using Underlying Network information.

Figure 8.x.4.1.1: Structure of <networkStatus> resource

The <networkStatus> resource shall contain the child resources specified in table 8.x.4.1.1-2.

Table 8.x.4.1.1-1: Child resources of <networkStatus> resource

| Child Resources of <locationPolicy> | Child Resource Type | Multiplicity | Description | <networkStatusAnnc> Child Resource Types |
| --- | --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 of TS-0001 | None |

The <networkStatus> resource shall contain the attributes specified in table 8.x.4.1.1-2.

Table 8.x.4.1.1-2: Attributes of <networkStatus> resource

| Attributes of <networkStatus> | Multiplicity | RW/ RO/ WO | Description | <networkStatusAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 of TS-0001. | NA |
| resourceID | 1 | RO | See clause 9.6.1.3 of TS-0001. | NA |
| resourceName | 1 | WO | See clause 9.6.1.3 of TS-0001. | NA |
| parentID | 1 | RO | See clause 9.6.1.3 of TS-0001. | NA |
| creationTime | 1 | RO | See clause 9.6.1.3 of TS-0001. | NA |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 of TS-0001. | NA |
| expirationTime | 1 | RW | See clause 9.6.1.3 of TS-0001. | MA |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3 of TS-0001. | MA |
| labels | 0..1 (L) | RW | See clause 9.6.1.3 of TS-0001. | MA |
| announceTo | 0..1(L) | RW | See clause 9.6.1.3 of TS-0001. | NA |
| announcedAttribute | 0..1(L) | RW | See clause 9.6.1.3 of TS-0001. | NA |
| creator | 1 | WO | The AE-ID of the entity which created the resource. | OA |
| referenceID | 1 | WO | A reference ID that is passed from the requester to IN-CSE and to the NSE in each request. The reference ID will be included in each response to associate it with the original request. | OA |
| locationArea | 1 | RW | Geographical area where AE needs to obtain the network status. It could be shapes (e.g. polygons, circles etc.) or civic addresses (e.g. streets, districts etc.) | OA |
| threshold | 0..1(L) | RW | A range at which the AE wishes to be informed of the network status of NSE. Multiple threshold values may be included. | OA |
| duration | 0..1 | RW | The time for which a continuous reporting is requested. The absence of duration indicates a one-time reporting. | OA |
| networkStatus | 0..1 | RO | Congestion level for NSE. It could be defined as High, Medium, Low, and No congestion. | OA |

##### 8.x.4.1.2 Proposed Flow(s)

This section describes the general procedure for network issue report service between oneM2M and 3GPP network.

8.x.4.1.2.1 Request procedure for one-time or continuous reporting of network status

This procedure is used by an oneM2M system to retrieve network status from the NSE. This procedure can be used to request a one-time or continuous reporting of network status. Figure 8.x.4.1.2-1 illustrates the procedure.

Figure 8.x.4.1.2-1: General procedure to support network status report between oneM2M and 3GPP network

Step-1: CRUD Request

AE can send CRUD Request to retrieve network status with providing Location Area, Duration, Threshold.

Step-2: CRUD Response

The IN-CSE sends a Response to the AE to acknowledge acceptance of the Request.

Step-3: Request for network status

The IN-CSE sends an Request  message to the NSE including Location Area, Duration, Threshold. Duration indicates the time for which a continuous reporting is requested. The absence of Duration indicates a one-time reporting. The IN-CSE, based on operator policies, may chose a different Threshold value than the one indicated by the AE in step 1.

Step-4: Report network status.

The NSE sends an one-time or continuous Report to the IN-CSE including depending on the operator configuration and current NSE knowledge, the congestion status for radio access network belonging to the Location Area requested by the IN-CSE.

8.x.4.1.2.2 Removal procedure for continuous reporting of network status

This procedure is used for termination of the continuous reporting of network status. It can be triggered by the AE at any time before the Duration is over. The IN-CSE will trigger this procedure when the Duration is over. Figure 8.x.4.1.2-2 illustrates the procedure.

Figure 8.x.4.1.2-1: General procedure to support network status report between oneM2M and 3GPP network

Step-1a: Detect end of duration.

The IN-CSE detects that the requested Duration for an ongoing continuous reporting of network status is over.

Step-1b: CRUD Request.

When the AE needs to terminate an ongoing continuous reporting of network status, the AE sends a Request message to the IN-CSE.

Step-2b: CRUD Response.

If the AE requested to terminate an ongoing continuous reporting of network status in step 1b, the IN-CSE sends a Response message to the AE.

Step-3: Request for termination.

The IN-CSE sends a Request message to the NSE to an ongoing continuous reporting of network status.

Step-4: Response.

The NSE removes the related instructions and stops monitoring the radio access network belonging to the Location Area for a change in the congestion status. Afterwards, the Response is sent to the IN-CSE.

Step-5: Remove status information.

The IN-CSE removes all network status information related to this continuous reporting.

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?