| CHANGE REQUEST |
| --- |
| Meeting:* | ARC 23 |
| Source:* | Tetsuo Inoue, NEC (TTC), t-inoue@fp.jp.nec.com Norio Uchida, NEC (TTC), n-uchida@fp.jp.nec.com Ataru Kobayashi, NEC (TTC), a-kobayashi@df.jp.nec.com Joerg Swetina, NEC Europe Ltd. (ETSI), JoergSwetina@neclab.eu |
| Date:* | 2016-05-16 |
| Contact:* | Tetsuo Inoue, NEC (TTC), t-inoue@fp.jp.nec.com Norio Uchida, NEC (TTC), n-uchida@fp.jp.nec.com Ataru Kobayashi, NEC (TTC), a-kobayashi@df.jp.nec.com Joerg Swetina, NEC Europe Ltd. (ETSI), JoergSwetina@neclab.eu |
| Reason for Change/s:* | Correction of Traffic Pattern section: 1.) In the flow it is not sufficiently clear that an IN-AE may modify the communication patterns of a field domain node on behalf of that node. 2.) The text on consistency check, that was part of Note 1, had been wrongly formatted and could be misunderstood as normative text (outside of the Note). 3.) Corrected formatting of heading for Step 2. |
| CR against: Release* | oneM2M R2 |
| CR against: WI* | Active WI-0037 MNT maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0001 v2.8.1 |
| Clauses/Sub Clauses* | 8.3.5.3 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR corrects the clause on Traffic Pattern:

- In the flow it is not sufficiently clear that an IN-AE may modify the communication patterns of a field domain node on behalf of that node.

- The text on consistency check, that was part of Note 1, had been wrongly formatted and could be misunderstood as normative text (outside of the Note).

- Corrected formatting of heading for Step 2.

### -----------------------Start of change 1-------------------------------------------

#### 8.3.5.3	General procedure for Configuration of Traffic Patterns

Figure 8.3.5.3-1 depicts a general procedure for configuration of Traffic Patterns.

Figure 8.3.5.3-1: General procedure for configuration of Traffic Patterns

Step-1: Provide information on the behavior of a field domain AE or field domain Node

An AE (AE of the Field Domain Node that reports its communication behaviour or an IN-AE that reports communication behaviour of a Field Domain Node on behalf of that Field Domain Node) provides the hosting CSE (i.e. ASN/MN-CSE of the field domain AE/Node or IN-CSE) with information on the communication behavior of the AE/Node (i.e. TP parameter sets) by creating, updating or deleting its Traffic Patterns(TP).

The AE may provide TP parameter sets for a group of field domain nodes.

The request shall include:

the originator AE-ID of the requesting AE;

a target identifier: i.e. the <trafficCharacteristics> child resource of a <node> resource or an <AE> resource of the field domain node or a group identifier of multiple field domain AEs/Nodes for which the Traffic Patterns is provided; and

a set of TP parameters as indicated in table 8.3.5.2-1.

The request may include multiple of TP parameter set(s) and validity time(s).

If the hosting CSE has received a request from an AE to create, update or delete Traffic Patterns, it shall check if the request from the AE is valid (note 1).

NOTE 1: Apart from checking access rights of the AE the validation of the request from the AE could include:
 - Consistency with <schedule> resources supported by an M2M SP in various M2M entities (MN-CSE, ASN)  hosting this AE/Node.
 - If there are several TP parameter sets active for one Field Domain Node, then the original resource hosting CSE needs to ensure that the different TP parameter sets are not overlapping.

Step-2 :  Announce the Traffic Patterns to the IN-CSE that has an interface to the NSE

If the hosting CSE recognizes an announcement procedure is needed, it shall announce the Traffic Patterns received from the AE to the IN-CSE that has an interface to the NSE contained in the “AnnounceTo” attribute of the Traffic Patterns resources based on the existing announcement procedures.

Step-3: Select the server NSE to request for the configuration of the TP parameter sets

If the IN-CSE receives announced Traffic Patterns and the IN-CSE recognizes that the configuration of the Traffic Patterns at the NSE is needed by checking the “provideToNSE” attribute, the IN-CSE shall perform the subsequent steps.

For the configuration of the TP parameter sets for a specific field domain node, the IN-CSE selects the NSE by using the identifier of the Field Domain Node (i.e. the M2M-Ext-ID) by which the Node can be identified in the NSE.

NOTE 2:	The correct server NSE can be found by following of a chain of links of multiple resources in the IN-CSE, e.g. the nodeLink in the AEAnnc resource of a target AE of field domain node linking to the nodeAnnc resource having the hostedCSELink linking to the remoteCSE resource having  the M2M-Ext-ID linking to the UNetwork-ID of the server NSE (see clauses 7.1.8 and 7.1.9).

Step-4: Request for the configuration of the TP parameter sets

For each field domain node received in the AE request the IN-CSE sends a request to provide TP parameter sets for the field domain node to the NSE, using the appropriate Mcn protocol. The request includes an identifier of the filed domain node and one or more TP parameter set(s) as defined at clause 8.3.5.2.

NOTE 3:	If the Underlying Network is 3GPP-compliant, see Annex B for more details.

Step-5: Response for the configuration of the TP parameter sets

The IN-CSE receives the response for the configuration of the TP parameter sets from the NSE. The response includes the result of the request.

NOTE 4:	If the Underlying Network is 3GPP-compliant, see Annex B for more details.

### -----------------------End of change 1---------------------------------------------

# Text boxes

Mca

Infrastructure Domain

Field Domain

1. provide information on the behavior of a field domain AE or field domain Node

2. Announce the Traffic Patterns to the IN-CSE that has an interface to the NSE

- Request for providing 
the TP parameter sets

- Response

3. Select the server NSE to request for the configuration of the TP parameter sets

Mca

Mcn

IN-CSE

Mcc

NSE

ASN/MN-CSE

AE

Any Domain