| CHANGE REQUEST |
| --- |
| Meeting:* | ARC #24 |
| Source:* | Catalina Mladin, InterDigital Quang Ly, InterDigital Jason Yin, Huawei |
| Date:* | 2016-07-15 |
| Contact:* | Catalina.Mladin@InterDigital.com yinjiaxin@huawei.com |
| Reason for Change/s:* | Action resource use clarifications and improvementss |
| CR against: Release* | Rel-3 |
| CR against: WI* | Active WI-0035 MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0021 |
| Clauses/Sub Clauses* | 7.2 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution addresses several questions regarding the use of the resources proposed for action triggering and proposes that text for clarification and new attributes to complement existing functionality are included.

- Regarding the priority attribute in the <action> resource, see section 7.2.1:  “The attribute indicate the priority of the action when compared with the other actions.” A discussion / text regarding how different <actions> resources should be linked so that their priorities are evaluated in relationship to each other may be helpful.

- filterCriteria in <action> is 0..1: we should clarify how the action triggering is performed when this attribute is absent or change multiplicity.

- The use of filterCriteria in this context makes the triggering of the actions relatively limited. Based on previously discussed use cases, should the use of logical constructs (e.g. “greater than”, etc.) be included?

- Two new <action> attributes are proposed to allow for repeated/periodic evaluation of the triggering condition: evalMode and evalControlParam, see section 7.2.1

- One new <action> attribute (evalPriority) is proposed to indicate the priority between the dependency resources/criteria to be evaluated, see section 7.2.1

- One new <action> attribute (actionSubjectResource) is proposed to enable the filterCriteria to be evaluated on resources other than the parent resource, if needed.

- To clarify the use of the logic attribute of the <dependency> resource: “The operate of the related parent <action> resource need to match”? Is an AND needed between the conditions? The description on step 4 of 7.2.3 does not match the table description, to be clarified.

R01 introduces text agreed to clarify the use of the priority and logic attributes and further editorial corrections.

### ----------------------Start of change 1-------------------------------------------

## 7.2	New resource types

### 7.2.1	Action resource type

An <action> resource represents information about an action that is to be operated on a certain resource depending on certain conditions.

Figure 7.2.1-1: Structure of <action> resource

The <action> resource contains the child resources specified in table 7.2.1-1.

Table 7.2.1-1: Child resources of <action> resource

| Child Resources of <action> | Child Resource Type | Multiplicity | Description | <actionAnnc> Child Resource Types |
| --- | --- | --- | --- | --- |
| [variable] | <dependency> | 0..n | See clause 7.2.2 | <dependencyAnnc> |

The <action> resource contains the attributes specified in table 7.2.1-2.

Table 7.2.1-2: Attribute of <action> resource

| Attributes of <action> | Multiplicity | RW/ RO/ WO | Description | <actionAnnc> Attributes |
| --- | --- | --- | --- | --- |
| actionSubjectResource | 0..1 | RW | The resource that is the subject for triggering the evaluation of the filterCriteria attribute. The subject can be any the resource in the system. If the attribute is missing the subject is the parent resource. | OA |
| priority | 0..1 | RW | The attribute indicates the priority of the action when compared with the other actions with the same actionSubjectResource, with highest priority indicated by the lowest value. | OA |
| filterCriteria | 0,,1 | RW | The filterCriteria to decide if the action is going to be triggered. | OA |
| evalMode | 1 | RW | Attribute provides the macro control mode of the evaluation of the <action> resource. Some values are: 0 = off 1 = once 2 = periodic 3 = continuous | OA |
| evalControlParam | 0..1 | RW | When evalMode= periodic, evalControlParam represents the periodicity. When evalMode= continuous the evaluation is restarted as soon as an action has been triggered. In this case, if evalControlParam is specified, it indicates the number of times to repeat an evaluation in continuous mode, otherwise it is repeated indefinitely. When evalMode is off or once this attribute is irrelevant. | OA |
| evalPriority | 0..1 | RW | Prioritized list of the dependencies for evaluation. This is an ordered list of The resourceIDs of the child <dependency> resources. | OA |
| objectResource | 1 | RW | The object resource that the operation is going to operate on. The resource could be any of the resource in the system. | MA |
| operation | 1 | RW | The operation that is going to be performed. The operation could be Create, Update, Retrieve, Delete or Notify. | MA |
| input | 0..1 | RW | Input parameter for the operation. The attribute could be the value of the input parameter or could be the reference to the resource which is the input. | OA |
| outputResource | 0..1 | RO | The reference to the resource where the result of the action can be retrieved. | OA |
| actionResult | 1 | RO | The result of the action. If outputResource is set, the actionResult is the retrieved resource representation of the outputResource. Otherwise, it’s the result of the request. | OA |

### 7.2.2	Dependency resource type

An <dependency> resource represents the condition that determines if the related parent <action> resource can be operated.

Figure 7.2.2-1: Structure of <dependency> resource

The <dependency> resource contains the attributes specified in table 7.2.2-1.

Table 7.2.2-1: Attribute of <dependency> resource

| Attributes of <dependency> | Multiplicity | RW/ RO/ WO | Description | <dependencyAnnc> Attributes |
| --- | --- | --- | --- | --- |
| logic | 0..1 | RW | Indicates if the dependency is SUFFICIENT or NECESSARY. The operand of the related parent <action> resource needs to match: Either of the sufficient dependency OR All of the necessary dependency | OA |
| filterCriteria | 0,,1 | RW | The filterCriteria to decide if the dependency matches the criteria. | OA |
| dependentResource | 1 | RW | The resourceID of the resource that the filterCriteria applies on. | MA |

### 7.2.3	Action triggering Procedure

The Hosting CSE of the <action> resource follows the steps below to perform an action triggering.

Step 1:	<action> resource is created either as the child resource of subject resource or elsewhere in the resource tree. Thesubject resource can be any of the resources defined in oneM2M and is indicated by the actionSubjectResource attribute. A change on the subject resource triggers the evaluation of the filterCriteria. The <dependency> resources are created as the child resources of the <action> resource.

Step 2:	Subject resource is updated.

Step 3:	Check if the updated subject resource matches the criteria defined in the filterCriteria attribute in the <action> resource

Step 4:	Upon successful check in step 3, retrieve <dependency>  child resources in the order provided in the evalPriority attribute, or based on local policy if the attribute is missing. For each of the <dependency> child resource, retrieve dependent resource according to the dependentResource attribute. If the dependent resource matches the criteria defined in the filterCriteria attribute and the logic attribute is of value SUFFICIENT, go to step 5. Otherwise if the dependent resource matches the criteria defined in the filterCriteria attribute and the logic attribute is of value NECESSARY, the hosting CSE checks if all the other <dependency> child resources which have the logic attribute of value NECESSARY match their filterCriteria attribute. If so, go to step 5.

Step 5:	Retrieve the input resource if the input attribute of the <action> resource is a resource reference.

Step 6:	Compose the operation depending on the operation attribute of the <action> resource and the retrieved input from step 5.

Step 7:	Send the composed operation to the object resource according to the resourceID obtained from the objectResource attribute of the <action> resource.

Step 8:	After receiving the response of the request in step 7, if outputResource attribute of the <action> resource is set, retrieve the resource representation of the outputResource and set the representation as the actionResult. Otherwise, put the state of the response in the actionResult attribute.

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?