| Input Contribution |
| --- |
| Meeting ID* | TP#25 |
| Title:* | CIoT interworking architecture |
| Source:* | Xubei, Huawei, Echo.xubei@huawei.com |
| Uploaded Date:* | 2016-09-13 |
| Document(s) Impacted* | < ARC-2016-0394R01-New_TS_on_3GPP-interworking_Draft_Baseline> |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | <A concise statement of the decision required or the recommended action to be taken> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Header

Text here.

## 5.1 oneM2M Architecture for 3GPP cellular IoT interworking with oneM2M

The oneM2M device support the following modes:

- The device node which is resource constrained devices can support a light and compact protocol ADN, such as NB-IoT device,  and the AND-AE communication with IN-CSE by Mca interface.

- The device node which is not resource constrained device can support ASN, such as e-LTE device, and ASN-CSE communication with 3GPP module in the device by Mcn interface.

.

The non-oneM2M Device Node (such as LWM2M  device) can connect to oneM2M platform from Interworking Proxy Entities(IPEs)

This architecture supports the following interworking modes:

- The NSSE may be deployed as SCEF using 3GPP defined interfaces (e.g. Rx, S6a etc.) bound to Mcn reference point. This model is applicable to the case where the oneM2M service provider and the underlying network provider is the same or there is trust relation between both service providers if they are different.

- The NSSE use APIs (OMA or other organization) bound to Mcn reference point with SCEF. This model is applicable to case when the oneM2M service provide and the underlying network provider is not the same;.

The functionality supported by the NSSE is different depending on the interworking mode.