| Input Contribution |
| --- |
| Meeting ID* | ARC #25 |
| Title:* | Senarios for DDS protocol binding with central control |
| Source:* | Jessie, Huawei, lijing80@huawei.com Sarah, Huawei, changhongna@huawei.com |
| Uploaded Date:* | 2016/10/9 |
| Document(s) Impacted* | WI-0047 TR-0027 v0.0.1 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | It is proposed to agree the content in this contribution. |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

### -----------------------start of change 1---------------------------------------------

## 7.1	Senarios for DDS protocol binding with central control

In oneM2M system, M2M devices (ASN or ADN) which belongs to different gatways (MN) communicate with each other, the data flow needs to be transferred through oneM2M service platform (IN-CSE), as shown in the Figure 7.1-1. In the future, more and more M2M devices will be inteterated to the oneM2M system, if all the data flows are forwarded through the oneM2M platform, it may cause the over load of the oneM2M platform. In order to reduce the traffic load of the oneM2M platform, peer to peer communication can be implemented by using the DDS protocol binding, which is illustrated in figure 7.1-2. When a M2M device accesses the oneM2M system, it first sends topics (which can be represented as oneM2M resource), that it wants to publish or subscribe, to DDS repository. DDS repository stores these topics and establishes the pub-sub relationship according to the matching of topics and the local configured policies, which defined whether the publisher and the subscriber are allowed to establish the pub-sub relationship. Simply speaking, a device who wants to publish a topic is called a publisher, a device who wants to subscribe the topic is called a subscriber. In case the topic name of a publisher is same with the topic name of a subscriber and the policies configured at the DDS repository are met, then the DDS repository establishes a pub-sub relationship for the publisher and the subscriber. Then the DDS repository sends the relationship information to notify the publisher the location of the subscriber. Once the publisher knows the location of subscriber, it will send the data to the subscriber directly.

Figure 7.1-1: Data Exchange within oneM2M Systme

Figure 7.1-2: Data Exchange using DDS Protocol

DDS Repository: It is used to provide the centralized discovery sevice. When an application requests a subscription for a topic, the DDS repository locates the publisher of the certain topic and notifies the publisher the location of the subscriber. The DDS repository can be deployed on MN or oneM2M sevice platform.

For specific scenarios, such as internet of vehicles (the communication model is shown in the Figure 7.1-3), vehicles communicate with each other directly, without the need of a broker (e.g. oneM2M Services Platform) to forward the data flow. In this communication model, every vehicle reports topics, it wants to publish or subscribe, to the DDS repository which is deployed on oneM2M service platform. The DDS repository establishs a pub-sub relationship according to the reported topics. Then the DDS repository sends this relationship information to vehicles. Then a vehicle can directly publish data to the other vehicles. This architecture can reduce the load of the platform, while it can improve the central control capability of the platform.

Figure 7.1-3: The communication modle of Internet of Vehicles

## 7.2	Solution 1

### 7.2.1	Use of DDS

This solution makes use of the Data Distribution Service protocol [i.5] and the RTPS [i.6] to transport serialized representations of oneM2M request and response primitives over the Mca or Mcc reference points, and provide reliable, real time communications between two parties e.g. AEs, CSEs.

In order to better manage the topics, an optimized dynamic discovery mechanism is introduced. In the optimized dynamic discovery mechanism, the DDS repository which is an logical function module is introduced. The main role of the DDS repository is to establish the pub-sub relationship between two parties (AEs and CSEs). When the pub-sub relationship is established, the two parties directly communicate with each other without forwarding the data to the DDS repository. The specific process and deployment of the DDS repository are presented in following sub-clauses.

### 7.2.2	Overview

#### 7.2.2.1	Introduction

The DDS protocol binding with topic control solution can be employed for communication between any two endpoints which can be connected over the Mca, Mcc or Mcc' interface reference points supported by the oneM2M Architecture as shown in figure 6.1-1 of oneM2M TS-0001 [i.2].

It is assumed that all the communication parties (AEs and CSEs) make use of DDS middleware, and the policies for establishing the pub-sub relationship are pre-configured in the DDS repository. Prior to the communication, parties need to send the topics to the DDS repository, and then the DDS repository establishs the pub-sub relationship between parties according the mapping of the topics and the local policy. Once the relationship is established, the parties can directly communicate each other without being mediated via the DDS repository.

There are two options for deploying the DDS repository:

- DDS repository is co-located within oneM2M nodes, and there may exist multiple repositories.

-	DDS repository is deployed independently from oneM2M nodes.

#### 7.2.2.2	DDS repository co-located within oneM2M nodes

Figure 7.2.2.2.1-1: DDS repository co-located scenario

Figure 7.2.2.2.1-1 shows a protocol segment view of the DDS repository co-located scenario. In this scenario, all oneM2M nodes (ADN, ASN, MN, IN) include one or more DDS Middleware. DDS repositories are provided within MN and IN. DDS global data space is a virtual concept, which represents the data pool of the whole system where the data exchange between the publisher and the subscriber happens. Assuming that ADN1, ASN2 and MN2 are registered to IN-CSE, ADN2 and ASN1 are registered to MN1, and MN1 is registered to MN2.

An oneM2M node sends its own information of topics to the DDS repository, which is pre-configured in the oneM2M node. The DDS repository records the discovery route of the oneM2M node, which reflects the registration relation of the oneM2M node. The node, that performs as the DDS repository, can also send the topics and the discovery routes that recorded locally to its registrar CSE. Table 7.2.2.2-1 shows the discovery route of the oneM2M nodes stored in the DDS repositories co-located in the MN nodes and the IN node.

Table 7.2.2.2-1: Discovery Routes stored in the DDS repositories

| DDS repository | Discovery Route | Corresponding oneM2M Node |
| --- | --- | --- |
| DDS Repository in IN | PS1 | ADN1 |
| DDS Repository in MN1 | PS2 | ADN2 |
| DDS Repository in MN1 | PS3 | ASN1 |
| DDS Repository in IN | PS4 | ASN2 |
| DDS Repository in MN2 | PS5 | MN1 |
| DDS Repository in IN | PS6 | MN2 |
| DDS Repository in IN | PS2-PS5-PS6 | ADN2 |
| DDS Repository in IN | PS3-PS5-PS6 | ASN1 |

#### 7.2.2.3	DDS repository deployed independently from oneM2M nodes

Figure 7.2.2.3-1: DDS repository located independently from nodes

Figure 7.2.2.3-1 shows a protocol segment view of the DDS repository located independently from nodes. In this scenario, all oneM2M nodes (ADN, ASN, MN, IN) include one or more DDS Middleware. DDS repository exists independently, which means the DDS repository is located outside of the nodes. Assuming that ADN1, ASN2 and MN2 are registered to IN-CSE, ADN2 and ASN1 are registered to MN1, and MN1 is registered to MN2. The main difference between the scenario of DDS repository co-located and the scenario of DDS repository located independently from nodes is the discovery route of topics reported by oneM2M nodes.

In this scenario,oneM2M nodes send information of topics to the DDS repositories according to the discovery routes illustrated in table 7.2.2.3-1.

Table 7.2.2.2.2-1: Discovery Routes stored in the independent DDS repository

| Discovery Route | Corresponding oneM2M Node |
| --- | --- |
| PS1–PS7 | ADN1 |
| PS2–PS5–PS6–PS7 | ADN2 |
| PS3–PS5–PS6–PS7 | ASN1 |
| PS4–PS7 | ASN2 |
| PS5 – PS6 – PS7 | MN1 |
| PS6 – PS7 | MN2 |

### -----------------------End of change 1---------------------------------------------