| Input Contribution |
| --- |
| Meeting ID* | ARC #25 |
| Title:* | DDS backgrounds |
| Source:* | Jessie, Huawei, lijing80@huawei.com Sarah, Huawei, changhongna@huawei.com |
| Uploaded Date:* | 2016/10/9 |
| Document(s) Impacted* | WI-0047 TR-0027 v0.0.1 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | It is proposed to agree the content in this contribution as the background of DDS in TR-0027. |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

### -----------------------start of change 1---------------------------------------------

# 5.1	Backgrounds

The Data Distribution Service (DDS) is a middleware protocol and API standard for data-centric connectivity specified by Object Management Group (OMG). DDS provides low-latency data connectivity, high reliability, and a scalable architecture that business and mission-critical Internet of Things (IoT) applications need. DDS standards can be found on the OMG DDS website, where several features of DDS are illustrated, e.g. data centricity, global data space, quality of service, dynamic discovery and scalable architecture.

The core standards of DDS are the Data-Centric Publish-Subscribe (DCPS) [i.5] and the Real-time Publish-Subscribe Protocol (RTPS) [i.6]. The DCPS builds on the concept of a "global data space" that is accessible to all interested applications. Applications that want to contribute information to this data space declare their intent to become "Publishers". Similarly, applications that want to access portions of this data space declare their intent to become "Subscribers". This standard also specifies how Publishers and Subscribers refer to portions of this space. However, the DCPS does not address the protocol used by the implementation to exchange messages over transports such as TCP/UDP/IP, so different implementations of DCPS will not interoperate with each other unless vendor-specific "bridges" are provided. So the RTPS was specifically developed to be a standard publish/subscribe wire-protocol. The RTPS defines the message formats, interpretation, and usage scenarios that underlie all messages exchanged by applications.

OMG DDS Standards include the following series:

- Core

  - DDS [i.5] v1.4 – the DDS specification describes a DCPS model for distributed application communication and integration.

    - DDS-DLRL [i.7] v1.4 – describes a high-level Data Local Reconstruction Layer (DLRL) interface to DDS that allows a simple integration of the DDS Service into the application layer. The content of this specification is original part of the DCPS specification before v1.4, and was separated to construct a new specification in v1.4.

  - DDSI-RTPS [i.6] v2.2 – defines the RTPS DDS Interoperability Wire Protocol.

- Extensions

  - DDS-XTypes [i.8] v1.1 – defines Extensible and DynamicTopic Types for DDS

  - DDS-Security [i.9] v1.0 Beta 1 – defines the Security Model and Service Plugin Interface (SPI) architecture for compliant DDS implementations.

  - DDS-RPC [i.10] v1.0 Beta 1 – Defines a distributed services framework providing language-independent service defintion and service/remote procedure invokation using DDS. Supports automatic discovery, synchronous and asynchronous invocations, and QoS.

- Services

  - DDS-Web [i.11] v1.0 Beta 1 – defines a platform-independent Abstract Interaction Model of how web clients should access a DDS System and a set of mappings to specific web platforms that realize the Platform Independent Model (PIM) in terms of standard web technologies and protocols.

- API

  - ISO/IEC C++ 2003 Language PSM for DDS [i.12] – defines  a C++  API only for the Data-Centric Publish-Subscribe (DCPS) portion of the DDS specification

  - Java 5 Language PSM for DDS [i.13] – defines a Java API for the Data-Centric Publish-Subscribe (DCPS) portion of the DDS specification.

  - Other language APIs for C, Java, Traditional C++, and other Languages are derived from the DDS API in IDL using the respective IDL to language Mappings

- Work in Progress

  - TCP/IP DDSI-RTPS PSM

## 5.2	Status

The work of the present document is based on the DDS released or in process specifications from OMG. The latest version and the correspongding time of the specifications are listed in table 5.2-1.

| SPECIFICATION | acronym | version | Document state/date |
| --- | --- | --- | --- |
| Data Distribution Service | DDS | 1.4 | Released/2015-04 |
| DDS Data Local Reconstruction Layer | DDS-DLRL | 1.4 | Released/2015-04 |
| Real-time Publish-Subscribe Wire Protocol DDS Interoperability Wire Protocol | DDSI-RTPS | 2.2 | Released/2014-09 |
| Extensible and Dynamic Topic Types for DDS | DDS-XTypes | 1.1 | Released/2014-11 |
| DDS-SECURITY | DDS-SECURITY | 1.0 - Beta 2 | In Process/2016-06 |
| Remote Procedure Calls over DDS | DDS-RPC | 1.0 - Beta 2 | In Process/2016-06 |
| Web-Enabled DDS | DDS-WEB | 1.0 - Beta 2 | In Process/2015-12 |
| ISO/IEC C++ 2003 Language DDS PSM | DDS-PSM-Cxx | 1.0 | Released/2013-11 |
| Java 5 Language PSM for DDS | DDS-Java | 1.0 | Released/2013-11 |

## 5.3	Architecture and protocol stack

### 5.3.1	Data-Centric Publish-Subscribe (DCPS)

DCPS is specific to a "Data Centric" style of distributed communications, which leverages a publish/subscribe communications model to connect anonymous information producers with information consumers. The overall distributed application is composed of processes called "participants", each running in a separate global data space, possibly on different computers. Applications that want to contribute information to this data space declare their intent to become "Publishers". Similarly, applications that want to access portions of this data space declare their intent to become "Subscribers". Each time a publisher posts new data into this "global data space", the RTPS propagates the information to all interested subscribers.

The unit of information exchanged between publishers and subscribers is constructed following certain data model, which is identified by a topic and a type. The topic provides an identifier that uniquely identifies some data items within the global data space. The type provides structural information needed to tell the DCPS how to manipulate the data.

The "datawriter" is an logic function module, which is usually called "object" in DDS specifications, the application must use to communicate to a publisher. The publication is defined as the association of a datawriter to a publisher. To access the received data, the application must use a typed "datareader" attached to the subscriber. A subscriber may receive and dispatch data of different specified types to different datareader. Thus, a subscription is defined as the association of a datareader with a subscriber. When an application wishes to publish data of a given type, it must create a publisher (or reuse an already created one) and a datawriter with all the characteristics of the desired publication. Similarly, when an application wishes to receive data, it must create a subscriber (or reuse an already created one) and a datareader to define the subscription.

The overall DCPS entities is shown in Figure 5.3.1-1. All these DCPS entities are attached to a participant. A participant represents the local membership of the application in a domain. A domain is a distributed concept that links all the applications able to communicate with each other. It represents a communication plane: only the publishers and the subscribers attached to the same domain may interact.

Figure 5.3.1-1 DCPS Entities

### 5.3.2	Real Time Publish subscribe (RTPS)

Real-time Publish-Subscribe Protocol (RTPS) allows Data Distribution Service (DDS) implementations from multiple vendors to interoperate. The RTPS protocol is designed to be able to run over multicast and connectionless best-effort transports such as UDP/IP.

The main features of the RTPS protocol include:

• Performance and quality-of-service properties to enable best-effort and reliable publish-subscribe communications for real-time applications over standard IP networks.

• Fault tolerance to allow the creation of networks without single points of failure.

• Extensibility to allow the protocol to be extended and enhanced with new services without breaking backwards compatibility and interoperability.

• Plug-and-play connectivity so that new applications and services are automatically discovered and applications can join and leave the network at any time without the need for reconfiguration.

• Configurability to allow balancing the requirements for reliability and timeliness for each data delivery.

• Modularity to allow simple devices to implement a subset of the protocol and still participate in the network.

• Scalability to enable systems to potentially scale to very large networks.

• Type-safety to prevent application programming errors from compromising the operation of remote nodes.

## 5.4	Key features

### 5.4.1 Quality of Service (QoS) Policy

DDS provides a rich set of Quality of Service (QoS) policies to allows applications to control/optimize network & computing resources. These QoS policies can be used individually or together to affect a variety aspects of communications, including reliability, performance, persistence of data, and amount of system resources used. These QoS policies makes DDS different from other communication middleware solutions.

The qualities of service (QoS) can be classified into six categories, such as data availability, data delivery, data timeliness, lifecycle, configuration and resources. The table below shows the full list of QoS policies available.

Table 5.4.1-1 DDS QoS Policies

| QosPolicy | Meaning | Concerns | RxO | Changeable | Categories |
| --- | --- | --- | --- | --- | --- |
| USER DATA | Attaches arbitrary application data (a buffer of bytes) to discovery meta-data. | DP,DR,DW | NO | YES | Configuration |
| TOPIC DATA | Attaches arbitrary application data (a buffer of bytes) to discovery meta-data. | T | NO | YES |  |
| GROUP DATA | Attaches arbitrary application data (a buffer of bytes) to discovery meta-data. | P,S | NO | YES |  |
| LIVELINESS | Determine whether an Entity is "active" (alive). | T,DR,DW | YES | NO |  |
| ENTITY FACTORY | Controls Entity behavior as a factory for other entities (i.e., if child entities are created enabled) | DP, P, S | NO | YES |  |
| DEADLINE | Maximum duration within which an instance is expected to be updated. | T,DR,DW | YES | YES | Data Timeliness |
| LATENCY BUDGET | Specifies the maximum acceptable delay from the time the data is written until the data is inserted in the receiver's applicationcache and the receiving application is notified of the fact. | T,DR,DW | YES | YES |  |
| TRANSPORT PRIORITY | This policy is a hint to the infrastructure as to how to set the priority of the underlying transport used to send the data. | T,DW | N/A | YES |  |
| READER_DATA_LIFECYCLE | Specifies the behavior of the DataReader with regards to the lifecycle of the datainstances it manages. | DR | N/A | YES | Lifecycle |
| WRITER_DATA_LIFECYCLE | Specifies the behavior of the DataWriter with regards to the lifecycle of the datainstances it manages. | DW | N/A | YES |  |
| LIFESPAN | Specifies the maximum duration of validity of the data written by the DataWriter | T,DW | N/A | YES | Data Availability |
| DURABILITY | Specifies if Connext will store and deliver previously published data to new/late-joining Readers. | T,DR,DW | YES | NO |  |
| DURABILITY_SERVICE | Configures external Persistence Service for Writers with PERSISTENT or TRANSIENT Durability. | T,DW | NO | NO |  |
| HISTORY | Controls how much data to store and how stored data is managed for the DataWriter/Reader within specified resource limits. | T,DR,DW | NO | NO |  |
| TIME_BASED_FILTER | Sets minimum time period before new data for an instance is provided to a DataReader. | DR | N/A | YES | Resources |
| RESOURCE_LIMITS | Limits amount of data cached by the middleware. | T,DR,DW | NO | NO |  |
| RELIABILITY | Indicates the level of reliability offered/requested by the Service. | T,DR,DW | YES | NO | Data Delivery |
| DESTINATION_ORDER | Controls the criteria used to determine the logical order among changes made by Publisher entities to the same instance of data. | T,DR | NO | NO |  |
| PRESENTATION | Controls how Connext presents data received by an application to DataReaders | P,S | YES | NO |  |
| OWNERSHIP | Specifies whether it is allowed for multiple DataWriters to write the same instance of the data and if so, how these modifications should be arbitrated. | T,DR,DW | YES | NO |  |
| OWNERSHIP_STRENGTH | Specifies strength used to arbitrate among multiple DataWriters of same instance. | DW | N/A | YES |  |
| PARTITION | Set of strings that introduces a logical partition among the topics visible by the Publisher and Subscriber. | P,S | NO | YES |  |
| RxO = Request/Offered Semantics, T = Topic, DP = DomainParticipan, DR = DataReader, DW = DataWriter, P = Publisher, S = Subscriber |

### 5.4.2	Dynamic Discovery

DDS provides a dynamic discovery service. Based on the discovery service, entities can discover and possibly keep track of the presence of remote entities. This discovery information is made available to the application through DDS built-in topics. Built-in Topics are a special kind of topics that are used by applications to discover each other. These Topics are handled automatically by the DDS middleware.

The dynamic discovery makes the DDS applications extensible. The application does not need to know or preconfigure the information of other entities for communication, e.g. IP address, because these information can be automatically discovered by dynamic discovery mechanism.

The dynamic discovery takes place using "built-in" DDS DataReaders and DataWriters with pre-defined Topics and QoS. There are four pre-defined built-in Topics: "DCPSParticipant", "DCPSSubscription", "DCPSPublication", and "DCPSTopic". For each of the built-in Topics, there exists a corresponding DDS built-in DataWriter and DDS built-in DataReader. The built-in DataWriters are used to announce the presence and QoS of the local DDS Participant and the DDS entities it contains (DataReaders, DataWriters and Topics) to the rest of the network. Likewise, the built-in DataReaders collect this information from remote Participants, which is then used by the DDS implementation to identify matching remote entities. The built-in DataReaders act as regular DDS DataReaders and can also be accessed by the user through the DDS API.

The RTPS Simple Participant Discovery Protocol (SPDP) uses a simple approach to announce and detect the presence of Participants in a domain. For each participant, the SPDP creates two RTPS built-in Endpoints: the SPDPbuiltinParticipantWriter and the SPDPbuiltinParticipantReader. The SPDPbuiltinParticipantWriter periodically sends SPDPdiscoveredParticipantData to a pre-configured list of locators to announce the participant’s presence on the network. The pre-configured list of locators may include both unicast and multicast locators. These locators simply represent possible remote Participants in the network, no Participant need actually be present. By sending the SPDPdiscoveredParticipantData periodically, participants can join the network in any order.

## 5.5	Security

The security specification defines five Service Plugin Interfaces (SPIs) that when combined together provide Information Assurance to DDS systems:

• Authentication Service Plugin. Provides the means to verify the identity of the application and/or user that invokes operations on DDS. Includes facilities to perform mutual authentication between participants and establish a shared secret.

• AccessControl Service Plugin. Provides the means to enforce policy decisions on what DDS related operations an authenticated user can perform. For example, which domains it can join, which Topics it can publish or subscribe to, etc.

• Cryptographic Service Plugin. Implements (or interfaces with libraries that implement) all cryptographic operations including encryption, decryption, hashing, digital signatures, etc. This includes the means to derive keys from a shared secret.

• Logging Service Plugin. Supports auditing of all DDS security-relevant events

• Data Tagging Service Plugin. Provides a way to add tags to data samples.

## 5.6	Benefits of introducing DDS to oneM2M

It is considered that oneM2M can utilize the advantages of DDS in the following three different ways to adapt various scenarios.

  - The DDS binding makes use of DDS to provide reliable communications between two parties (AEs and CSEs). Similar to MQTT binding, the pub-sub relationship is established according to the topic names. Moreover, in DDS protocol binding, the pub-sub relationship is also established based on the dynamic discovery mechanism. Parties broadcast the information of topics which they want to publish or subscribe and receive the information of topics broadcasted by other parties. Once a topic which will be published by a party matches a topic which will be subscribed to by other parties, the pub-sub relationship is established. The establishment of a pub-sub relationship between Parties totally depends on the matching of topic names. However, this DDS binding solution may lead to some problem. If the setting of topic name is restricted to the format of "/<originator>/<receiver>" and the and the communication of parties depends on the registration relationship, the advantages of DDS protocol can not be fully utilized. On the other hand, if there is no restriction on the format of the topic name and the establishment of communication entirely depends on the dynamic discovery mechanism, the communication mechanism in oneM2M system will not depend on the registration relationship anymore and the central control capability of the oneM2M platform will be weakened. For example, two ADNs can communicate with each other directly through the dynamic discovery. This straight forward DDS protocol binding solution will be studied in clause 6.

  - For the above-mentioned problem, an optimized dynamic discovery solution is introduced in clause 7 for DDS based direct change of data between oneM2M parties. The optimized dynamic discovery mechanism is used to establish pub-sub relationship between parties using DDS repository which is the logic function module. The DDS repository is similar to the broker of MQTT. But there are two differences. Firstly, the DDS repository is only used to establish the pub-sub relationship, and doesn't forward the data from one party to another. Secondly, the DDS repository establishes the pub-sub relationship not only rely on topic name, but also taking the communication rules or policies into account. The communication rules or policies can be pre-configured according to the actual deployment scenario requirement, e.g. whether or not allowing two nodes without registration relation establish pub-sub relationship. The DDS repository can be implemented by different oneM2M nodes and can be deployed either distributed or in a central mode. In addition of enabling the oneM2M system to achieve low latency and high reliability adavantage of DDS protocol, this solution maintains the central control capability of the platform to the whole oneM2M system.

  - The DDS interworking solution will be studied in clause 8. It enables the oneM2M application to access the data of an existing DDS system. It enhances the interoperability of the oneM2M system, and thus oneM2M system can be used in more high demand scenarios, such as medical, smart energy, industry and so on. More real time systems and devices can be integrated into the oneM2M system.

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of Changes to References Section -------------

## 2.2	Informative references

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

[i.1]	oneM2M Drafting Rules (http://www.onem2m.org/images/files/oneM2M-Drafting-Rules.pdf)

[i.2]	oneM2M TS-0001: "Functional Architecture".

[i.3]	oneM2M TS-0004: "Service Layer Core Protocol Specification".

[i.4]	oneM2M TS-0003: "Security Solutions".

[i.5]	Data Distribution Service (DDS)

NOTE:	Available at http://www.omg.org/spec/DDS/.

[i.6]     Real-time Publish-Subscribe Wire Protocol DDS Interoperability Wire Protocol

NOTE:	Available at http://www.omg.org/spec/DDSI-RTPS/.

[i.7]     DDS Data Local Reconstruction Layer (DDS-DLRL)

NOTE:	Available at http://www.omg.org/spec/DDS-DLRL/.

[i.8]     Extensible and Dynamic Topic Types for DDS

NOTE:	Available at http://www.omg.org/spec/DDS-XTypes/.

[i.9]     DDS Security

NOTE:	Available at http://www.omg.org/spec/DDS-SECURITY/.

[i.10]     Remote Procedure Calls over DDS

NOTE:	Available at http://www.omg.org/spec/DDS-RPC/.

[i.11]     Web-Enabled DDS

NOTE:	Available at http://www.omg.org/spec/DDS-WEB/.

[i.12]     ISO/IEC C++ 2003 Language DDS PSM

NOTE:	Available at http://www.omg.org/spec/DDS-PSM-Cxx/.

[i.13]     Java 5 Language PSM for DDS

NOTE:	Available at http://www.omg.org/spec/DDS-Java/.

### -----------------------End of Changes to References  -------------

### -Start of Changes changes to Definitions, Symbols, Abbreviations, Acronyms-

## 3.3	Abbreviations and Acronyms

For the purposes of the present document, the abbreviations given in oneM2M TS-0001 [i.2] and the following apply:

DDS	Data Distribution Service

IoT	Internet of Things

DCPS	Data-Centric Publish-Subscribe

RTPS 	Real-time Publish-Subscribe

DLRL	Data Local Reconstruction Layer

QoS	Quality of Service

### ---End of changes to Definitions, Symbols, Abbreviations, Acronyms ---