| CHANGE REQUEST |
| --- |
| Meeting:* | ARC 25 |
| Source:* | Datang |
| Date:* | 2016-10-17 |
| Contact:* | Wei Zhou, Datang, zhouwei@catt.cn Hui Xu, Datang, xuhui@catt.cn |
| Reason for Change/s:* | Redefine <accessControlPolicy> resource type for supporting distributed authorization system |
| CR against: Release* | Release 3 |
| CR against: WI* | Active WI-0061 - Distributed Authorization MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0001 V2.10.0 |
| Clauses/Sub Clauses* | 9.6.2 Resource Type accessControlPolicy |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This contribution is about how to implement distributed authorization in the oneM2M System.

The major comments received in last TP meeting (TP22) are:

- Using normal resources to replace the virtual resources (addressed by this contribution);

- Authorization requests shall conform to RESTful (addressed by this contribution);

- Shall provide a whole solution, for example, how the PEP find a PDP to which an access control decision request shall be sent (addressed by another contribution).

According to these comments, this contribution proposes 3 new resource types representing PDP, PRP and PIP respectively. These resource types are <authorizationDecision>, <authorizationPolicy> and <authorizationInformation>. They are oneM2M normal resource.

The following figure shows the new solution for implementing distributed authorization:

- RETRIEVE <authorizationDecision> for obtaining access control decision;

- RETRIEVE <authorizationPolicy> for obtaining access control policy;

- RETRIEVE <authorizationInformation> for obtaining access control information.

This contribution is about how to find an authorization entity, i.e. a PDP, PRP or PIP.

This contribution proposes redesign the <accessControlPolicy> so that it can provide such kind of information. The new added resource attributes are

- pdpAddresses: provide PDP addresses;

- prpAddresses: provide PRP addresses;

- pipAddresses: provide PIP addresses.

The basic processes of using these resource attributes are:

- The Hosting CSE (PEP) gets local applicable ACP, if the privileges attribute is empty, then it read pdpAddresses attribute for getting a PDP address.

- The PDP CSE gets local applicable ACP, if the privileges attribute is empty, then it read prpAddresses attribute for getting a PRP address.

- In case the PDP CSE needs to obtain some access control information (e.g. role, token) that cannot be provided locally, it reads pipAddresses attribute for getting a PIP address.

### -----------------------Start of change 1---------------------------------------------

### 9.6.2	Resource Type accessControlPolicy

#### 9.6.2.0	Introduction

The Access Control Policies (ACPs) shall be used by the CSE to control access to the resources as specified in the present document and in oneM2M TS-0003 [2].

The ACP is designed to fit different access control models such as access control lists, role or attribute based access control.

The <accessControlPolicy> resource is comprised of privileges and selfPrivileges attributes which represent a set of access control rules defining which entities (defined as accessControlOriginators) have the privilege to perform certain operations (defined as accessContolOperations) within specified contexts (defined as accessControlContexts) and are used by the CSEs in making Access Decision to all or specific parts of the targeted resource(defined as accessControlObjectDetails).

In a privilege, each access control rule defines which AE/CSE is allowed for which operation. So for sets of access control rules an operation is permitted if it is permitted by one or more access control rules in the set.

For a resource that is not of <accessControlPolicy> resource type, the common attribute accessControlPolicyIDs for such resources (defined in table 9.6.1.3.2-1) contains a list of identifiers which link that resource to <accessControlPolicy> resources. The CSE Access Decision for such a resource shall follow the evaluation of the set of access control rules expressed by the privileges attributes defined in the <accessControlPolicy> resources.

The selfPrivileges attribute shall represent the set of access control rules for the <accessControlPolicy> resource itself.

The CSE Access Decision for <accessControlPolicy> resource shall follow the evaluation of the set of access control rules expressed by the selfPrivileges attributes defined in the <accessControlPolicy> resource itself.

Logically an authorization system may comprise four sub-functions: enforcing access control decision, making access control decision, providing access control policies and providing access control information (e.g. roles). As specified in TS-0003 [2], these sub-functions are modelled as policy enforcement point (PDP), Policy Decision Point (PDP), Policy Retrieval Point (PRP) and Policy Information Point (PIP) respectively. In oneM2M System these authorization sub-functions may coexist in one CSE or may be distributed in different CSEs in different combinations.

In <accessControlPolicy> resource three operational attributes are defined for holding the information about where to find the distributed authorization sub-functions. These attributes are: pdpAddresses, prpAddresses and pipAddresses.

The pdpAddresses attribute contains a list of addresses of <authorizationDecision> resources. Each <authorizationDecision> resource represents a PDP to which an access control decision request shall be sent in order to obtain an access control decision. See clause 9.6.x for further details of <authorizationDecision> resource type.

The prpAddresses attribute contains a list of addresses of <authorizationPolicy> resources. Each <authorizationPolicy> resource represents a PRP to which an access control policy request shall be sent in order to obtain access control policies. See clause 9.6.y for further details of <authorizationPolicy> resource type.

The pipAddresses attribute contains a list of addresses of <authorizationInformation> resources. Each <authorizationInformation> resource represents a PIP to which an access control information request shall be sent in order to obtain requested access control information (e.g. role and/or token) for making an access control decision. See clause 9.6.z for further details of <authorizationInformation> resource type.

The applicability of the pdpAddresses, prpAddresses and pipAddresses  attributes depends on the deployment form of authorization sub-functions:

In case the privileges attribute is present, the access control rules in the privileges attribute shall be used for access control, and the pdpAddresses, prpAddresses and pipAddresses attributes shall not be present.  If sufficient privileges do not exist to grant access to the Originator and dynamic authorization is supported, then dynamic authorization shall be used to perform consultation-based dynamic access control to resources.

In case the privileges attribute is not present, how to process further depends on which authorization method is adopted. In the case distributed authorization method is supported, pdpAddresses or prpAddresses attribute shall be considered for obtaining access control decision or access control policies from another CSE. However, pdpAddresses and prpAddresses attributes shall not be present at the same time. In case dynamic authorization method is used, pdpAddresses and prpAddresses attributes shall not be present, and the <dynamicAuthorizationConsultation> resource associated with the target resource shall be used to perform consultation-based dynamic access control to resources.

In case the pipAddresses attribute is present, the access control information request (e.g. for role information) related to the access control policy specified in the privileges attribute shall be sent to one of the addresses listed in this attribute.

The details of distributed authorization procedures are described in TS-0003 [2].

Figure 9.6.2.0-1: Structure of <accessControlPolicy> resource

The <accessControlPolicy> resource shall contain the child resource specified in table 9.6.2.0-1.

Table 9.6.2.0-1: Child resources of <accessControlPolicy> resource

| Child Resources of <accessControlPolicy> | Child Resource Type | Multiplicity | Description | <accessControlPolicyAnnc> Child Resource Types |
| --- | --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 | <subscription> |

The <accessControlPolicy> resource shall contain the attributes specified in table 9.6.2.0-2.

Table 9.6.2.0-2: Attributes of <accessControlPolicy> resource

| Attributes of <accessControlPolicy> | Multiplicity | RW/ RO/ WO | Description | <accessControlPolicyAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3. | NA |
| resourceID | 1 | RO | See clause 9.6.1.3. | NA |
| resourceName | 1 | WO | See clause 9.6.1.3. | NA |
| parentID | 1 | RO | See clause 9.6.1.3. | NA |
| expirationTime | 1 | RW | See clause 9.6.1.3. | MA |
| labels | 0..1(L) | RW | See clause 9.6.1.3. | MA |
| creationTime | 1 | RO | See clause 9.6.1.3. | NA |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3. | NA |
| announceTo | 0..1 (L) | RW | See clause 9.6.1.3. | NA |
| announcedAttribute | 0..1 (L) | RW | See clause 9.6.1.3. | NA |
| privileges | 0..1 | RW | A set of access control rules that applies to resources referencing this <accessControlPolicy> resource using the accessControlPolicyID attribute. | MA |
| selfPrivileges | 1 | RW | A set of access control rules that apply to the <accessControlPolicy> resource itself. | MA |
| pdpAddresses | 0..1 (L) | RW | A list of addresses of <authorizationDecision> resources. See clause 9.6.x for further details. | MA |
| prpAddresses | 0..1 (L) | RW | A list of addresses of <authorizationPolicy> resources. See clause 9.6.y for further details. | MA |
| pipAddresses | 0..1 (L) | RW | A list of addresses of <authorizationInformation> resources. See clause 9.6.z for further details. | MA |

The set of access control rules represented in privileges and selfPrivileges attributes are comprised of 4-tuples (accessControlOriginators, accessControlContexts, accessControlOperations, accessControlObjectDetails) with parameters shown in table 9.6.2.0-3 which are further described in the following clauses.

If the privileges attribute contains no 4-tuples then this represents an empty set of the access control rules.

The selfPrivileges attribute shall contain at least one tuple.

The CSE access granting mechanism shall follow the procedure described in oneM2M TS-0003 [2] in clause 7.1 (Access Control Mechanism).

Table 9.6.2.0-3: Parameters in access-control-rule-tuples

| Name | Description |
| --- | --- |
| accessControlOriginators | See clause 9.6.2.1 |
| accessControlContexts | See clause 9.6.2.2 |
| accessControlOperations | See clause 9.6.2.3 |
| accessControlObjectDetails | See clause 9.6.2.4 |
| accessControlAuthenticationFlag | See clause 9.6.2.5 |

### -----------------------End of change 1---------------------------------------------