| Input Contribution |
| --- |
| Meeting ID* | ARC #25 |
| Title:* | Senarios for DDS protocol binding with central control |
| Source:* | Jessie, Huawei, lijing80@huawei.com Sarah, Huawei, changhongna@huawei.com Echo,Huawei,echo.xubei@huawei.com |
| Uploaded Date:* | 2016/10/9 |
| Document(s) Impacted* | WI-0047 TR-0027 v0.0.1 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | It is proposed to agree the content in this contribution. |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

### R05: Delete the description about the peer to peer communication directly.

Make clear that the discovery and data change both comply the oneM2M architecture.

Update the section number based on TR0027 skeleton.

Update the secarios of DDS usage in factory.

R06: Add the descrtipion of change history of R05.

R07: Delete the two tables and delete the discovery route information.

Update the line description in Figure 6.2.2-1 and Figure 6.2.3-1.

R08: Update the PS7 to black line in Figure 6.2.3-1 and all the blue dot line from CSE/AE to CSE/AE in Figure 6.2.2-1 and Figure 6.2.3-1.

### -----------------------start of change 1---------------------------------------------

# 6	DDS protocol binding

## 6.1	DDS configuration within oneM2M Architecture

When oneM2M system supports DDS, if a M2M device accesses the oneM2M system, it should firstly send topics (which can be represented as oneM2M resource), that it wants to publish or subscribe, to DDS repository which is used to provide the centralized control sevice and can be deployed on MN or oneM2M sevice platform. DDS repository stores these topics and establishes the pub-sub relationship according to the matching of topics based on the oneM2M architecure, which defined whether the publisher and the subscriber are allowed to establish the pub-sub relationship. Simply speaking, an entity  publishes a topic is called a publisher, an entity subscribes the topic is called a subscriber. In case the topic name of a publisher is same with the topic name of a subscriber and the policies configured at the DDS repository are met, then the DDS repository establishes a pub-sub relationship for the publisher and the subscriber. Then the DDS repository sends the relationship information to notify the publisher the location of the subscriber. Once the publisher knows the location of subscriber, it will send the data to the subscriber based on the subscriber registration path.

Figure 6.1-1: Data Exchange within oneM2M System

For specific scenarios, such as data exchange between different factories (the communication model is shown in the Figure 6.1-2). In this communication model, the M2M devices and MNs in factory A and factoryB reports topics, which it wants to publish or subscribe, to the DDS repository which is deployed on oneM2M service platform. The DDS repository establishs a pub-sub relationship according to the reported topics and the oneM2M architecure. If one M2M device in factory A wants to send data to a M2M device in factory B, the DDS repository can establish the pub-sub relationships between M2M devices and MNs, and between MNs and oneM2M service platform. The data exchange path is shown by the red dotted line in figure 6.1-2. This architecture can  improve the central control capability of the platform.

Figure 6.1-2: The communication model  between different factories

## 6.2	Solution 1

### 6.2.1	Overview

This solution makes use of the Data Distribution Service protocol [i.5] and the RTPS [i.6] to transport serialized representations of oneM2M request and response primitives over the Mca or Mcc reference points, and provide reliable, real time communications

Figure 6.2.1-1: Protocol Stack

The protocol stack is composed of four parts:oneM2M Primitives DCPS, RTPS, and TCP or UDP, as shown in figure 6.2.1-1.

In order to better manage the topics, an central control mechanism is introduced. In the central control mechanism, the DDS repository which is an logical function module is introduced. The main role of the DDS repository is to establish the pub-sub relationship between oneM2M entities (AEs and CSEs) based on oneM2M architecture. After the pub-sub relationship is established, the oneM2M entities can directly communicate with each other without forwarding the data to the DDS repository.The communication between the publisher and subscriber do comply with the oneM2M architecture. The specific process and deployment of the DDS repository are presented in following sub-clauses.

There are two options for deploying the DDS repository:

- DDS repository is co-located within oneM2M nodes, and there may exist multiple repositories.

-	DDS repository is deployed independently from oneM2M nodes.

### 6.2.2	DDS repository co-located within oneM2Mnodes

Figure 6.2.2-1: DDS repository co-located scenario

Figure 6.2.2-1 shows a protocol segment view of the DDS repository co-located scenario. In this scenario, all oneM2M nodes (ADN, ASN, MN, IN) include one or more DDS Middleware. DDS repositories are implement on MN and IN.

An oneM2M node sends its own information of topics to the DDS repository, which is pre-configured in the oneM2M node. The DDS repository can store the topic and manage the pub-sub relationship.

### 6.2.3	DDS repository deployed independently from oneM2M nodes

Figure 6.2.3-1: DDS repository located independently from nodes

Figure 6.2.3-1 shows a protocol segment view of the DDS repository located independently from nodes. In this scenario, all oneM2M nodes (ADN, ASN, MN, IN) include one or more DDS Middleware. DDS repository exists independently, which means the DDS repository is located outside of the nodes .The DDS repository acts MN/IN-CSE to communication with IN by Mcc interface. Editor’s note: whether PS7 is a oneM2M reference point or a DDS interface is FFS.

### -----------------------End of change 1---------------------------------------------