| Input Contribution |
| --- |
| Meeting ID* | TP#26 |
| Title:* | Structure of catalogue |
| Source:* | Jiaxin Yin, Huawei Technologies Co., Ltd., Yinjiaxin@huawei.com |
| Uploaded Date:* | 2016-11-23 |
| Document(s) Impacted* | TR-0032 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree to be incorporated into the document. |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## 5.2	Structure of catalog

5.2.1	Introduction

Features of oneM2M are organized into a tree structure and separated by Entity, Common Services Function and Feature Sets at each layer. Entity, CSF and Feature Sets have their dedicated abbreviations and identities. Feature is uniquely identified by Feature ID. Feature ID is a combination of abbreviation of Entity and CSF as well as the identity of Feature Sets and the sieral number of Feature and separated by dots “.” in the form as the following.

{Abbr of Entity}.{Abbr of CSF}.{ID of Feature Set}.{Sieral number of Feature}

5.2.2	Entity

Entity is oneM2M defined Entities which could be AE or CSE as feature is implemented differently from the perspective of AE and CSE. There may some other features that are common for both AE and CSE like the binding and serialization. There may be some features that are different between CSEs as well. For example, when MN-CSE is registering to IN-CSE, the procedure of MN-CSE and IN-CSE is different. As a result, the following Entities for feature catalogue is defined.

- GO	-	General feature for all oneM2M Entities

- GC	-	General feature for CSE

- GA	-	General feature for AE

- IC	-	Feature for IN-CSE

- MC	-	Feature for MN-CSE

- AC	-	Feature for ASN-CSE

- IA	-	Feature for IN-AE

- MA	-	Feature for MN-AE

- AA	-	Feature for ADN-AE

5.2.3	Common Services Function

In the document, oneM2M defined CSFs are used to categorize features. Besides, a new category is added to organize features that are common to the oneM2M system.

- GEN	-	General capability

- ASM	-	Application and Service Layer Management

- CMH	-	Communication Management and Delivery Handling

- DMR	-	Data Management and Repository

- DMG	-	Device Management

- DIS	-	Discovery

- GMG	-	Group Management

- LOC	-	Location

- NSE	-	Network Service Exposure, Service Execution and Triggering

- REG	-	Registration

- SEC	-	Security

- SCA	-	Service Charging and Accounting

- SUB	-	Subscription

5.2.4	Feature Set

CSF is composed of Feature Sets. Feature Set is a set of Features that are closely related that serves for the same service. For example, in group management CSF, the configuration of group and the fan out of operation through a group are regarded as two separate services. Thus these are Feature Sets that belong to group management (GMG). Under each CSF, Feature Set is identified by a three digital number starting from 001.

5.2.5	Feature

Feature Set is composed of Features. Feature is the atomic operation that is defined by oneM2M. On the consideration of service, it’s meaningless to divide the operation anymore. For example, set the max number of instance of a container or application registration. Under each Feature Set, Feature is identified by a five digital number starting from 00001.